## Slide 1: Maximizing Speed and Density of Tiled FPGA Overlays via Partitioning
Charles Eric LaForest
J. Gregory Steffan
University of Toronto
ICFPT 2013

## Slide 2: FPGA Overlay Architectures
Layer of abstraction over FPGA
  Easier development
  Compile software rather than design hardware
  Typically a soft-processor
Provides parallelism through “tiling”
  Multiple Cores
  Multiple Datapaths (Vector Processors)

## Slide 3: Scalar Core: Octavo
A soft-processor on Stratix IV
  10 stages, 8 threads, 550 MHz in many cases
  Highly configurable and customizable
Published at FPGA 2012
  “Octavo: an FPGA-Centric Processor Family”
0
1
2
3
4
5
6
7
8
9
ALU0
ALU1
ALU2
ALU3
CTL0
CTL1
I
A/B
A/B

## Slide 4: Tiling Datapaths
Attach SIMD Lanes
  Copies of the Scalar Datapath
Private data memories
Replicated instruction logic
  Pipelined distribution and decoding
  Not the critical path!
Intuition: Fmax stays “constant”
Scalar Core
SIMD
SIMD
SIMD
SIMD

## Slide 5: Experimental Framework
Quartus 12.1 targeting Stratix IV E230
Test harness to isolate paths to outside
Synthesize for speed
  Including full physical synthesis
Maximum Place & Route effort
550 MHz clock target (BRAM Fmax)
Average results over 10 runs
Measure area as equivalent ALMs (eALMs)

## Slide 6: Fmax with Increasing SIMD Lanes
Scalar Core
32 SIMD Lanes
Optimized instruction
logic fan-out!

## Slide 7: Disabling Duplicate Register Removal
467 MHz
370 MHz
+26% Fmax

## Slide 8: A Better Way: Partitioning
Logical division of a design
  Synthesize as separate netlists
  Generally, optimizations do not cross partitions
    Register retiming
    Register de-duplication
    Boolean simplification

## Slide 9: Partitioning Each SIMD Lane

## Slide 10: Impact on Critical Paths
Flat
373 MHz
21 Nodes
Duplicate Registers
456 MHz
43 Nodes
Partitioned
489 MHz
64 Nodes
32-Lane SIMD Core
Source node fan-out of
top 100 failing paths

## Slide 11: Improving Compute Density
Beneficial optimization
Excessive fan-out

## Slide 12: Improving Compute Density
Lost
optimization
Duplicated registers: less excessive fan-out

## Slide 13: Improving Compute Density
Lost
optimization
Partitioning: local optimizations!

## Slide 14: Area Impact
(Relative to Flat)
Partitioned (solid)
Duplicate Registers
(dashed)

## Slide 15: Area Impact
Dup. Registers
+5% area
Partitioning:
+11-14% area

## Slide 16: Summary: SIMD Partitioning
Scalar Core with 0 to 32 SIMD Lanes
  Tiling datapaths
Replicated instruction logic
  Pipelined distribution and decoding in each Lane
Placing each Lane in a Partition
  32 Lanes: 372 MHz  482 MHz (+30%)
Area increase from partitioning: 11-14%
  Reflects area of preserved replicated logic
Better to not partition for a few Lanes!
  4 lanes or less have better compute density
  Local optimizations outweigh increased fanout

## Slide 17: Partitioning!? Really!?
Can we get the same results in another way?
“Layering” replicated logic:
  Introducing sequential dependency via pipelining
    Not about breaking critical paths!
    Isolating instances of replicated logic
  Prevents optimization of replicated logic
  Staggers execution of each layer

## Slide 18: Layering a SIMD Core
1 Layer with 4 Lanes
Scalar
SIMD
SIMD
SIMD
SIMD

## Slide 19: Layering a SIMD Core
2 Layers with 2 Lanes
Scalar
SIMD
SIMD
SIMD
SIMD

## Slide 20: Layering a SIMD Core
4 Layer with 1 Lane
Scalar
SIMD
SIMD
SIMD
SIMD
Staggered SIMD execution!

## Slide 21: Layering a SIMD Core
2
4
8
16
32
1
Flat: +65 MHz (+17%)

## Slide 22: Layering a SIMD Core
Partitioned: +30 MHz (+6%)
Flat: +65 MHz (+17%)

## Slide 23: Replicating Entire Processors
Connect processors in a pipelined Mesh
Entire processors replicated
No critical paths between processors
Intuition: Fmax stays “constant”
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD

## Slide 24: Critical Paths of Meshes
Flat
331 MHz
2 nodes
Partitioned
489 MHz
61 nodes
Mesh of 102 Cores
Source node fan-out
of top 100 failing paths

## Slide 25: Partitioning Meshes
Mesh of 102 Scalar Cores
Bottleneck: optimized 3-bit counter
  Round-robin thread counter in each Scalar Core
  No inputs, but identical and synchronized states
Placing each Core in a Partition
  Avg. Fmax: 284 MHz  437 MHz (54%)
    Only a 22% Fmax drop over 102x scaling!
Area increase from partitioning: 0.85%
  No relation between Fmax and area increases
  Mysterious 10-11% area overhead from CAD tool
No significant increase to CAD time!

## Slide 26: Summary
Tiled designs contain replicated logic
  Forms the critical paths in large tilings
    Useless optimizations causing excessive fanout
  Becomes significant at higher speeds
Partitioning avoids this problem
  Simpler than per-node management
  Lower area than disabling duplicate removal
  Better performance than sequential dependencies
  Benefit scales with the number of tiles
  Area increase only proportional to replicated logic
  No significant change to total CAD time

## Slide 27: Further Work
The CAD tools could automatically…
  Detect repeated optimizations across modules
    Tag the replicated logic and/or alert the designer
  “Restart” optimization
    Keep performance and save (some) area
    Only if substantial replicated logic area
  Partition modules containing replicated logic
Power Analysis of Partitioning
  Could go either way…
CAD tool mysteriously adds area when tiling
  Main source of density reduction when tiling

## Slide 28: Acknowledgements
Funding:
  Queen Elizabeth II World Telecom. Congress
  Walter C. Sumner Foundation
  Altera
  NSERC
Computing:
  SciNet GPC supercomputer
    24 CPU-years of Quartus runs
  Altera

## Slide 29: Extra Slides

## Slide 30: FPGA Overlay Architectures
Layer of abstraction over FPGA
  Easier development
  Compile software rather than design hardware
  Typically a soft-processor
    Nios, MicroBlaze (Altera, Xilinx)
    iDEA (NTU, Xilinx),
    Octavo (UofT, Altera)
Provides parallelism through tiling
  Multi-Cores
  Vector Processors
    VEGAS (UofT)
    VENICE (UBC)

## Slide 31: Multi-Local Logic
Multiple instances of equivalent logic
  Each instance operates locally and identically
Tiling introduces multi-local logic
Different tilings  Different multi-local logic
  Connected (SIMD)
  Unconnected (Mesh)
CAD tools de-duplicate multi-local logic
  Removes redundancy in small circuits
  Introduces critical paths in large circuits!
    Especially at high speeds
Preserve with different partitioning schemes

## Slide 32: Area Impact
Relative to Flat: 1,027 to 25,799 eALMs

## Slide 33: Floorplanning a Scalar Core

## Slide 34: Floorplanning
Spatial pre-allocation of area
  Avoids placement interference
  Preserves timing closure
  Used to manage large projects
A
B
D
C

## Slide 35: Floorplanning a Scalar Core
Floorplan to match logic and routing aspects
  Tall, narrow logic blocks, more horizontal wires
  Maybe improve compute density
Place a Scalar Core in range of floorplans
Results:
  4 to 14% lower compute density!
  Harder P&R problem, same hardware
  Use only for project management

## Slide 36: Floorplanning a Scalar Core
Floorplan to match logic and routing aspects
  Tall, narrow logic blocks, more horizontal wires
  Maybe improve compute density
Scalar Core in 4x4 to 20x20 LAB floorplans
  1 Logic Array Block = 10 ALMs, plus local routing
  Needs ~64 LABs minimum to fit
4 to 14% lower compute density!
  Harder P&R problem, same hardware
Use only for project management

## Slide 37: Floorplanning a Scalar Core
14% lower vs.
no floorplan
4% lower
6x12 12x6
9x8 8x9,
but no gain

## Slide 38: Experimental Framework
Quartus 12.1 targeting Stratix IV E230
Design enclosed by test harness
Synthesize for speed
Maximum Place & Route effort
550 MHz clock target (BRAM Fmax)
Average results over 10 runs
Measure area as equivalent ALMs (eALMs)
  ALM  two 6-LUTs, two flip-flops, two full-adders
  M9K BRAM  28.7 ALMs
  DSP Block  29.75 ALMs
“Comparing FPGA vs. Custom CMOS and the Impact on Processor Microarchitecture”, Wong, Betz, Rose, FPGA 2011

## Slide 39: Partitioning
Logical division of a design
  Synthesize as separate netlists
  Generally, optimizations do not cross partitions
    Register retiming
    Register de-duplication
    Boolean simplification
A
B

## Slide 40: Tiling
Replicating in two dimensions
Multiple copies for parallelism
  SIMD: tiled datapaths
  MIMD: tiled processors
Scalar Core
SIMD
SIMD
SIMD
SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD
Scalar/SIMD