Title
Microbenchmarking the GT200 GPU

---
Objective
- Measure low-level performance
- Speculate about the microarchitecture of the GT200 GPU

---
Objective
- Pipeline
  - Several pipelines
  - Pipeline latency and throughput
- Memory hierarchy
  - Caches
  - Off-chip DRAM latency and throughput

---
Pipeline Benchmarks
- Use clock() for timing
  - Two instructions: move and left shift
- Unrolled sequence of arithmetic ops
  - One thread for latency measurement
  - 512 threads for throughput
uint start_time = clock();
repeat256(a = a + b;)
uint stop_time = clock();
[Save timers to global memory]

---
Pipeline Benchmark Caveats
- Unrolled loop must fit in 8 KB icache
  - Variable instruction length (32- and 64-bit)
- Instruction cache cold misses
  - Measure only second iteration of loop
- PTX “instructions” to real instructions mapping not one-to-one
- Optimization by nvopencc and ptxas
  - Need to circumvent optimizations by clever coding

---
Pipeline Functional Units
Functional unit		Latency (clocks)	Throughput / (ops/clock)
SP	add, sub, / (int, float)	24	8
SFU	rsqrt, log2f, / (float)	28	2
DPU	add, sub, / (double)	48	1

---
SP Pipeline

---
32-Bit Multiplication
32-Bit Multiplication
r1 = r1 * r2
  - r5 = r2.lo * r1.hi	(mul24)
  - r5 = (r2.h1 * r1.lo) + r5	(mad24)
  - r5 = r5 << 16	(shl)
  - r1 = (r2.lo * r1.lo) + r5	(mad24)
Latency is 96 cycles
Throughput is 2 operations per cycle

---
Instruction Cache
- Sequence of independent 64-bit SP instructions (cvt)
- Loop over of varying amount of code
  - Cache misses increase measured runtime
- L2 icache is supposed to be shared with L2 constant cache

---
Instruction Cache
32KB L2
8KB L1

---
Register File Allocation

---
Register File Allocation
- Register file has 64 banks
  - Can not utilize entire register file if not a multiple of 64 threads
  - No bank conflicts, as alluded to in manual
- 8 banks per SP allows single-ported memories to be used for register files
  - ½ bandwidth for ALU
  - ½ bandwidth for memory fetch

---
Global Memory
Global Memory
Read Latency
  - 435 - 450 cycles
  - Chain of dependent reads
    - repeat1024 (j=array[j])
    - where array[j]=j+stride