## Slide 1: Hardware Acceleration of A Boolean Satisfiability Solver
Xander Chin
Braiden Brousseau
Bill Teng

## Slide 2: Motivation
SAT Solvers are core computational engine for major applications
  EDA: testing and verification, logic synthesis, technology mapping, …
  AI: knowledge base deduction, automatic theorem proving, …
Software SAT Solvers has improved a lot in the last ten years, but performance is saturating
Further speed it up through hardware acceleration!
Notes: EDA - Electronic design automation

## Slide 3: SAT in a Nutshell (a very tiny nutshell)
Given a boolean formula, find variable assignments such that the formula is true or prove that no satisfying assignment exists
Conjunctive Normal Form: e.g. φ(a,b,c) = (a+b)(a’+b+c)
literal
clause
NP – Complete
For n variables, there are 2n possible truth assignments to be checked

## Slide 4: Algorithmic Pruning
X4
X2
X3
X1
0
1
S
U
U
U
U
U
U
U
U
U
S
S
S
S
U
S
Resolve Conflict !

## Slide 5: Some Solver Techniques
Propagation
  Literal watches – literal to clause mapping
  Decision heuristics – which variable should be assigned next?
Pruning
  Conflict analysis – which assignments will never work?
  Non-chronological backtracking – undoing failed decisions quickly

## Slide 6: Flexibility of Software
Software can easily implement complex pruning techniques that would be extremely difficult in hardware
New pruning techniques are demonstrating only incremental gains
Some of the complex techniques must be omitted in hardware
We must still implement the core techniques

## Slide 7: Hardware Architecture
Parts of SAT are memory-bound
  Random access data patterns to clauses
Hardware acceleration by streaming burst accesses to memory to maximize bandwidth and custom intermediate caching
DDR
Memory Bound Logic
Memory Bound Logic
Custom Cache
Pipeline Direction
microBlaze
Processor
Memory Bound Logic
Custom Cache
Custom Cache

## Slide 8: Conclusions
Trade-off between
  High-level complex algorithms in software
  Low-level algorithms in hardware
Critical to performance!
Novel new software algorithms could potentially outperform our hardware system
  System flexibility with soft-processor
  Core techniques not likely going away any time soon