## Slide 1: Independence ISA
Conventional ISA
  Instructions execute in order
No way of stating
  Instruction A is independent of B
    Must detect at runtime  cost: time, power, complexity
Idea:
  Change Execution Model at the ISA model
  Allow specification of independence
VLIW Goals:
  Flexible enough
  Match well technology
Vectors and SIMD
  Only for a set of the same operation

## Slide 2: VLIW
Very Long Instruction Word
#1 defining attribute
  The four instructions are independent
Some parallelism can be expressed this way
Extending the ability to specify parallelism
  Take into consideration technology
  Recall, delay slots
  This leads to 
#2 defining attribute: NUAL
  Non-unit assumed latency
ALU1
ALU2
MEM1
control
Instruction format

## Slide 3: NUAL vs. UAL
Unit Assumed Latency (UAL)
  Semantics of the program are that each instruction is completed before the next one is issued
  This is the conventional sequential model
Non-Unit Assumed Latency (NUAL):
  At least 1 operation has a non-unit assumed latency, L, which is greater than 1
  The semantics of the program are correctly understood if exactly the next L-1 instructions are understood to have issued before this operation completes
NUAL: Result observation is delayed by L cycles

## Slide 4: #2 Defining Attribute: NUAL
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
Assumed latencies for all operations
visible
visible
visible
visible
Glorified delay slots
Additional opportunities for specifying parallelism

## Slide 5: #3 DF: Resource Assignment
The VLIW also implies allocation of resources
The spec. inst format maps well onto the following datapath:
ALU1
ALU2
MEM1
control
ALU
ALU
cache
Control
Flow
Unit

## Slide 6: VLIW: Definition
Multiple independent Functional Units
Instruction consists of multiple independent instructions
Each of them is aligned to a functional unit
Latencies are fixed
  Architecturally visible
Compiler packs instructions into a VLIW also schedules all hardware resources
Entire VLIW issues as a single unit
Result: ILP with simple hardware
  compact, fast hardware control
  fast clock
  At least, this is the goal

## Slide 7: VLIW Example
I-fetch &
Issue
FU
FU
Memory
Port
Memory
Port
Multi-ported
Register
File

## Slide 8: VLIW Example
ALU1
ALU2
MEM1
control
Instruction format
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
ALU1
ALU2
MEM1
control
Program order and execution order
Instructions in a VLIW are independent
Latencies are fixed in the architecture spec.
Hardware does not check anything
Software has to schedule so that all works

## Slide 9: Compilers are King
VLIW philosophy:
  “dumb” hardware
  “intelligent” compiler
Key technologies
  Predicated Execution
  Trace Scheduling
    If-Conversion
  Software Pipelining

## Slide 10: Predicated Execution
Instructions are predicated
  if (cond) then perform instruction
  In practice
    calculate result
    if (cond) destination = result
Converts control flow dependences to data dependences
if ( a == 0)
  b = 1;
  else b = 2;
true; pred = (a == 0)
pred; b = 1
!pred; b = 2

## Slide 11: Predicated Execution: Trade-offs
Is predicated execution always a win?
Is predication meaningful for VLIW only?

## Slide 12: Trace Scheduling
Goal:
  Create a large continuous piece or code
  Schedule to the max: exploit parallelism
“Fact” of life:
  Basic blocks are small
  Scheduling across BBs is difficult
But:
  While many control flow paths exist
  There are few “hot” ones

## Slide 13: Trace Scheduling
Trace Scheduling
  Static control speculation
  Assume specific path
  Schedule accordingly
  Introduce check and repair code where necessary
First used to compact microcode
  FISHER, J. Trace scheduling: A technique for global microcode compaction. IEEE Transactions on Computers C-30, 7 (July 1981), 478--490.

## Slide 14: Trace Scheduling: Example
Expand the scope/flexibility of code motion
A
B
C
A
C
Assume AC is the common path
A&C
schedule
Repair
B

## Slide 15: Trace Scheduling: Example #2
bA
bB
bC
bD
bE
bA
bB
bC
bD
check
all OK
repair
bC
bD
repair
bE

## Slide 16: Trace Scheduling Example
test = a[i] + 20;
If (test > 0) then
  sum = sum + 10
else
  sum = sum + c[i]
c[x] = c[y] + 10
test = a[i] + 20
sum = sum + 10
c[x] = c[y] + 10
if (test <= 0) then goto repair
…
Straight code
assume delay
repair:
sum = sum – 10
sum = sum + c[i]

## Slide 17: If-Conversion
Predicate large chunks of code
  No control flow
Schedule
  Free motion of code since no control flow
  All restrictions are data related
Reverse if-convert
  Reintroduce control flow
N.J. Warter, S.A. Mahlke, W.W. Hwu, and B.R. Rau. Reverse if-conversion. In Proceedings of the SIGPLAN'93 Conference on Programming Language Design and Implementation, pages 290-299, June 1993.

## Slide 18: Software Pipelining
A loop
  for i = 1 to N
  a[i] = b[i] + C
Loop Schedule
  0: LD f0, 0(r16) ; addi r16, r16, sizeof(double)
  1:
  2:
  3: ADD f16, f30, f0
  4:
  5:
  6: ST f16, 0(r17); addi r17, r17, sizeof(double)
  Assume f30 holds C

## Slide 19: Software Pipelining – Unroll the loop
Assume latency = 3 cycles for all ops
  0: LD f0, 0(r16)
  1: LD f1, 8(r16)
  2: LD f2, 16(r16)
  3: ADD f16, f30, f0 LD f3, 24(r16)
  4: ADD f17, f30, f1
  5: ADD f18, f30, f2
  6: ST f16, 0(r17) ADD f19, f30, f3
  7: ST f17, 8(r17)
  8 : ST f18, 16(r17
  9: ST f19, 24(r17)
Steady State:
LD (i+3), ADD (i),ST (i – 3)
  3 “pipeline” stages: LD, ADD and ST

## Slide 20: Software Pipelining – What We Want
L 0
A 0
S 0
L 1
A 1
S 1
L 2
A 2
S 2
L 3
A 3
S 3
L 4
A 4
S 4
L 5
A 5
S 5
L 6
A 6
S 6
L 7
A 7
S 7
L 8
A 8
S 8

## Slide 21: “Complete” Code
PROLOG
LD f0, 0(r16) ADD r16, r16, 24
LD f1, 8(r16)
LD f2, 16(r16)
ADD f16, f0,C LD f0, 0(r16) ADD r16, r16, 24
ADD f17, f1,C LD f1, 8(r16)
ADD f18, f2,C LD f2, 16(r16)
KERNEL
ST f16, 0(r17) ADD f16, f0,C LD f0, 0(r16) ADD r16, r16, 24 (& r17)
ST f17, 8(r17) ADD f17, f1,C LD f1, 8(r16)
ST f18, 16(r17) ADD f18, f2,C LD f2, 16(r16)
EPILOGUE
ST f16, 0(r17) ADD f16, f0,C ADD r17, r17, 24
ST f17, 8(r17) ADD f17, f1,C
ST f18, 16(r17) ADD f18, f2,C
ST f16, 0(r17)
ST f17, 8(r17)
ST f18, 16(r17)
Lots of register names needed + code

## Slide 22: Architectural Support for Software Pipelining
Rotating Register File
  LD f0, 0(r16) means LD fx, 0(ry) where
  x = 0 + baseReg and y = 16+baseReg
(p0): LD f0, 0(r1) STAGE 1
(p0): ADD r1, r1, 8
(p3) ADD f3, f3, C STAGE 2
(p6) ST f6, 0(r8) STAGE 3
(p6) ADD r7, r8, 8
Loopback: BaseReg--
Think of this
as one instruction

## Slide 23: Software Pipelining with Rotating Register Files
Assume BaseReg = 8, i in r8 and j in r10, initially p8 is true
(p8): LD f8, 0(r9), (p8): ADD r8, r9, 8, (p11) ADD f11, f11, C (p14) ST f14, 0(r16), (p14) ADD r15, r16, 8
(p7): LD f7, 0(r8), (p7): ADD r7, r8, 8, (p10) ADD f10, f10, C (p13) ST f13, 0(r15), (p13) ADD r14, r15, 8
(p6): LD f6, 0(r7), (p6): ADD r6, r7, 8, (p9) ADD f9, f9, C (p12) ST f12, 0(r14), (p12) ADD r13, r14, 8
(p5): LD f5, 0(r6), (p5): ADD r5, r6, 8, (p8) ADD f8, f8, C (p11) ST f11, 0(r13), (p11) ADD r12, r13, 8
(p4): LD f4, 0(r5), (p4): ADD r4, r5, 8, (p7) ADD f7, f7, C (p10) ST f10, 0(r12), (p10) ADD r11, r12, 8
(p3): LD f3, 0(r4), (p3): ADD r3, r4, 8, (p6) ADD f6, f6, C (p9) ST f9, 0(r11), (p9) ADD r10, r11, 8
(p2): LD f2, 0(r3), (p2): ADD r2, r3, 8, (p5) ADD f5, f5, C (p8) ST f8, 0(r10), (p8) ADD r9, r10, 8
time

## Slide 24: How to Set the Predicates
CTOP: Special Branch + Registers Loop Count + Epilog Count (LC/EC)
Branch.ctop predicate, target address
LC: How many times to run the loop
  Ctop: LC--, predicate = TRUE
EC: How many stages to run the epilogue for
  Used only when LC reaches 0
  Ctop: if (LC ==0) EC--, predicate = FALSE
In our example:
  B.ctop p0, label
Net Effect: Predicated are set incrementally while LC >0 and then turned off by EC
CTOP assumes we know loop count
WTOP for while loops (read paper)
“Overlapped Loop Support in the Cydra 5” Dehnert et. al, 1989
  http://www.crhc.uiuc.edu/impact/ece512/papers/p26-dehnert.pdf
  http://portal.acm.org/citation.cfm?id=70082.68185

## Slide 25: VLIW – A bit of History
Floating Point Systems Array Processor
  very successful in 70’s
  all latencies fixed; fast memory
Multiflow
  Josh Fisher (now at HP)
  1980’s Mini-Supercomputer
Cydrome
  Bob Rau (was at HP)
  1980’s Mini-Supercomputer
Tera
  Burton Smith
  1990’s Supercomputer
  Multithreading
Intel IA-64 (Intel & HP)

## Slide 26: EPIC philosphy
Compiler creates complete plan of run-time execution
  At what time and using what resource
  POE communicated to hardware via the ISA
  Processor obediently follows POE
  No dynamic scheduling, out of order execution
    These second guess the compiler’s plan
Compiler allowed to play the statistics
  Many types of info only available at run-time
    branch directions, pointer values
  Traditionally compilers behave conservatively  handle worst case possibility
  Allow the compiler to gamble when it believes the odds are in its favor
    Profiling
Expose micro-architecture to the compiler
  memory system, branch execution

## Slide 27: Defining feature I - MultiOp
Superscalar
  Operations are sequential
  Hardware figures out resource assignment, time of execution
MultiOp instruction
  Set of independent operations that are to be issued simultaneously
    no sequential notion within a MultiOp
  1 MultiOp issued every cycle
    Provides notion of time
  Resource assignment indicated by position in MultiOp
  POE communicated to hardware via MultiOps
  POE = Plan of Execution

## Slide 28: Defining feature II - Exposed latency
Superscalar
  Sequence of atomic operations
  Sequential order defines semantics (UAL)
  Each conceptually finishes before the next one starts
EPIC – non-atomic operations
  Register reads/writes for 1 operation separated in time
  Semantics determined by relative ordering of reads/writes
Assumed latency (NUAL if > 1)
  Contract between the compiler and hardware
  Instruction issuance provides common notion of time

## Slide 29: EPIC Architecture Overview
Many specialized registers
  32 Static General Purpose Registers
  96 Stacked/Rotated GPRs
    64 bits
  32 Static FP regs
  96 Stacked/Rotated FPRs
    81 bits
  8 Branch Registers
    64 bits
  16 Static Predicates
  48 Rotating Predicates

## Slide 30: ISA
128-bit Instruction Bundles
Contains 3 instructions
6-bit template field
  FUs instructions go to
  Termination of independence bundle
  WAR allowed within same bundle
  Independent instructions may spread over multiple bundles
op
op
op
Bundling info

## Slide 31: Other architectural features of EPIC
Add features into the architecture to support EPIC philosophy
  Create more efficient POEs
  Expose the microarchitecture
  Play the statistics
Register structure
Branch architecture
Data/Control speculation
Memory hierarchy
Predicated execution
  largest impact on the compiler

## Slide 32: Register Structure
Superscalar
  Small number of architectural registers
  Rename using large pool of physical registers at run-time
EPIC
  Compiler responsible for all resource allocation including registers
  Rename at compile time
    large pool of regs needed

## Slide 33: Rotating Register File
Overlap loop iterations
  How do you prevent register overwrite in later iterations?
  Compiler-controlled dynamic register renaming
Rotating registers
  Each iteration writes to r13
  But this gets mapped to a different physical register
  Block of consecutive regs allocated for each reg in loop corresponding to number of iterations it is needed

## Slide 34: Rotating Register File Example
r13
r14
iteration n
RRB = 10
r13
r14
iteration n + 1
RRB = 9
actual reg = (reg + RRB) % NumRegs
At end of each iteration, RRB--
r13
r14
iteration n + 2
RRB = 8
R23
R22
R21

## Slide 35: Branch Architecture
Branch actions
  Branch condition computed
  Target address formed
  Instructions fetched from taken, fall-through or both paths
  Branch itself executes
  After the branch, target of the branch is decoded/executed
Superscalar processors use hardware to hide the latency of all the actions
  Icache prefetching
  Branch prediction – Guess outcome of branch
  Dynamic scheduling – overlap other instructions with branch
  Reorder buffer – Squash when wrong

## Slide 36: EPIC Branches
Make each action visible with an architectural latency
  No stalls
  No prediction necessary (though sometimes still used)
Branch separated into 3 distinct operations
  1. Prepare to branch
      Compute target address
      Prefetch instructions from likely target
    Executed well in advance of branch
  2. Compute branch condition – comparison operation
  3. Branch itself
Branches with latency > 1, have delay slots
  Must be filled with operations that execute regardless of the direction of the branch

## Slide 37: Predication
If a[i].ptr != 0
b[i] = a[i].left;
else
b[i] = a[i].right;
i++
Conventional
load a[i].ptr
p2 = cmp a[i].ptr != 0
Jump if p2 nodecr
load r8 = a[i].left
store b[i] = r8
jump next
nodecr:
load r9 = a[i].right
store b[i] = r9
next:
i++
IA-64
load a[i].ptr
p1, p2 = cmp a[i].ptr != 0
<p1> load a[i].l <p2> load.a[i].r
<p1> store b[i] <p2>store b[i]
i++

## Slide 38: Speculation
Allow the compiler to play the statistics
  Reordering operations to find enough parallelism
  Branch outcome
    Control speculation
  Lack of memory dependence in pointer code
    Data speculation
  Profile or clever analysis provides “the statistics”
General plan of action
  Compiler reorders aggressively
  Hardware support to catch times when its wrong
  Execution repaired, continue
    Repair is expensive
    So have to be right most of the time to or performance will suffer

## Slide 39: “Advanced” Loads
t1=t1+1
if (t1 > t2)
j = a[t1 + t2] ; expected to be slow
add t1 + 1
comp t1 > t2
Jump donothing
load a[t1 – t2]
donothing:
add t1 + 1
ld.s r8=a[t1 – t2]
comp t1>t2
jump
check.s r8
Not IA-64 specific

## Slide 40: “Advanced” Loads
t1=t1+1
if (t1 > t2)
j = a[t1 + t2] ; expected to be slow
add t1 + 1
comp t1 > t2
Jump donothing
load a[t1 – t2]
donothing:
add t1 + 1
ld.s r8=a[t1 – t2]
comp t1>t2
jump
check.s r8
ld.s: load and record
Exception
Check.s check for
Exception
Allows load to be
Performed early
Not IA-64 specific

## Slide 41: Speculative Loads
Memory Conflict Buffer (illinois)
Goal: Move load before a store when unsure that a dependence exists
Speculative load:
  Load from memory
  Keep a record of the address in a table
Stores check the table
  Signal error in the table if conflict
Check load:
  Check table for signaled error
  Branch to repair code if error
How are the CHECK and SPEC load linked?
  Via the target register specifier
Similar effect to dynamic speculation/synchornization

## Slide 42: Exposed Memory Hierarcy
Conventional Memory Hierarchies have storage presence speculation mechanism built-in
Not always effective
  Streaming data
  Latency tolerant computations
EPIC:
  Explicit control on where data goes to:
  Conventional: C1/C1
L_B_C3_C2 S_H_C1
Source cache specifier – where its coming from  latency
Target cache specifier – where to place the data

## Slide 43: VLIW Discussion
Can one build a dynamically scheduled processor with a VLIW instruction set?
What parts of hardware VLIW simplifies? How about the rest?
Is there enough parallelism visible to the compiler?
  What are the trade-offs?
Many DSPs are VLIW
  Why?