## Slide 1: ECE552: Computer Architecture Virtual Memory Instructor: Andreas Moshovos moshovos@eecg.toronto.edu Fall 2015 This is said only on this slide deck but will apply to all others: The base slide set was developed by Prof. Tor Aamodt. based on material profs. Mark Hill, David Woord, Guri Sohi and Jim Smith at the University of Wisconsin-Madison, and Dave Patterson at the University of California Berkeley. Some slides/material developed by Amir Roth of University of Pennsylvania with sources that included University of Wisconsin slides by Mark Hill, Guri Sohi, Jim Smith, and David Wood. Some material enhanced by Milo Martin, Mark Hill, and David Wood with sources that included Profs. Aamodt, Asanovic, Falsafi, Hoe, Lipasti, Shen, Smith, Sohi, Vijaykumar, and Wood.

## Slide 2: Multitasking
A
B
A
B
time

## Slide 3: Multitasking (reference)
Most OS’s multitask
  Run Program A and B at the same time
Most CPUs must support multitasking
  Not run at exactly the same time:
    Run Program A for 20ms
    Run Program B for 20ms
    Run Program A for 20ms, etc
NOTE: Multitasking is different than “hardware multithreading”. Hardware multithreading means hardware can run instructions from two or more threads at exactly the same time. Multitasking involves providing short “time slices” to programs (so at any time only instructions from one thread are running if the hardware is single threaded).

## Slide 4: Multiple Programs Using Memory
My laptop has 8GB MB DRAM
  Memory Usage when creating this slide:
    Chrome 800 MB
    Powerpoint 147 MB
    Firefox 441 MB
    Windows 200 MB
    Others: 3.7 GB
    Total: 4.2GB
Luckily all fit in memory

## Slide 5: Virtual Memory
Chrome
Main Memory

## Slide 6: Virtual Memory
Chrome
Main Memory
Firefox

## Slide 7: Virtual Memory
Chrome
Main Memory
Firefox
Powerpoint

## Slide 8: Virtual Memory
Chrome
Main Memory
Firefox
Powerpoint
Windows
Calculator
Application X

## Slide 9: Virtual Memory
Chrome
Main Memory
Firefox
Powerpoint
Windows
Calculator
Application X
How do they all agree which portion of memory to use?
What if I ran another app and the total exceeds main memory?
What if I open one more tab in chrome?

## Slide 10: Multiple Programs Using Memory
It gets even worse
  Win starts using 1280 MB
  IE starts using 30 MB
  Word starts using 20 MB
  User opens web page (cnn.com), IE wants + 72MB
  User opens document (ps3 soln) Word wants +30MB
  User opens 2nd web page(youtube), IE wants +40MB
  User edits document, Word wants +10MB
  TOTAL
    Win 1280MB, IE 142 MB, Word 60 MB
Main
Mem
OS
IE
Word
IE
IE
Word
Word

## Slide 11: How can we divide up memory between programs?
It gets even worse
  Exit Word
  Start engineering program
    Wants 300MB for a matrix
    Must be contiguous!
    How?
    Move IE? Not realistic
Solution?
  Divide Main Memory into pages, say 4KB each
  Divide Programs into pages (same size)
  Map Program Pages into Main Memory Pages
  Store extra Program Pages on disk
Main
Mem
OS
IE
IE
IE

## Slide 12: Solution: Virtual Memory
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
e
s
D
i
s
k
a
d
d
r
e
s
s
e
s
V
i
r
t
u
a
l
a
d
d
r
e
s
s
e
s
A
d
d
r
e
s
s
t
r
a
n
s
l
a
t
i
o
n
IE
IE
IE
IE
IE
IE
IE
IE
IE sees this
Main Memory sees this
Can store some on disk!
Pages
Fragmented:
Non-contiguous (holes), out-of-order, some on disk
IE

## Slide 13: Virtual Memory
Application A
Main Memory

## Slide 14: Virtual Memory
Application A
Main Memory
Application B

## Slide 15: Virtual Memory
Application A
Main Memory
Application B
Application C

## Slide 16: Virtual Memory
Application A
Main Memory
Application B
Application C

## Slide 17: Virtual Memory
Application A
Main Memory
Application B
Application C
Application D
Application E
Application X

## Slide 18: Mine and Yours & Devices
Application A
NIOS II Memory
Application B
Application C
Disk
Isolation: A process cannot access the values of another process

## Slide 19: What an Application Sees
Application A
Virtual Memory
F()
Actual Memory
Physical Memory = Actual Memory

## Slide 20: How is it done?
A
Virtual
Physical
Page: aligned, continuous
2^n sized
Typical sizes 4K – 8K today
Assume:
Fixed at design time
Reality: adjustable, few sizes
let’s first understand
w/ fixed size
Physical
PAGE
Virtual
PAGE

## Slide 21: Two Apps
A
Virtual
Physical
B
Virtual

## Slide 22: How are pages mapped?
Who keeps the arrows?
A
Virtual
Physical
Physical
PAGE
Virtual
PAGE
VPN
OFF
Page Table
PPN
OFF

## Slide 23: Virtual Memory (reference)
Program Viewpoint
  Addresses start at 0
  Malloc() gives program contiguous memory (consecutive addresses)
  Malloc(), Free(), Malloc(), Free()
    Can malloc() re-use parts that are freed?
    Causes internal fragmentation within one program
  There is lots of free memory available
CPU/OS Viewpoint
  Keep all programs separate
    Don’t all start at 0
    Security implications…. programs should not read each other’s data!
  Dynamic program behavior cause memory fragmentation
    Starting & ending programs, swapping to disk
    Causes external fragmentation between programs
  Limited memory available
    Use Disk to hold extra data
    Use Main Memory like a cache for the program data stored on disk
New structure: Page Table

## Slide 24: Page Table Entries
VPN
OFF
Page Table
PPN
OFF
PPN
v
V = valid
PPN = Physical Page Number
VPN = Virtual Page Number

## Slide 25: Page Table Entries
VPN
OFF
Page Table
PPN
OFF
PPN
v
MIPS I 4GB address space with 4KB pages
OFF = 12 bits
VPN = 32 – 12 = 20
PPN = 20
Physical memory could be larger or smaller
More on this later on

## Slide 26: Address Translation
3
2
1
0
1
1
1
0
9
8
1
5
1
4
1
3
1
2
3
1
3
0
2
9
2
8
2
7
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
3
2
1
0
1
1
1
0
9
8
1
5
1
4
1
3
1
2
2
9
2
8
2
7
P
a
g
e
o
f
f
s
e
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
T
r
a
n
s
l
a
t
i
o
n
Table Lookup
Page Size: 2^12 = 4096 bytes

## Slide 27: Page Table Translation Structure
Size of Page Table?
2^20 or ~1 million entries
1 Page Table Per Program
Page Table Register
2
0
1
2
1
8
3
1
3
0
2
9
2
8
2
7
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
2
9
2
8
2
7
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
Virtual Address
Page Offset
Virtual Page Number
Physical Page Number
Physical Address
Physical Page Number
Page Offset
Page Table
Valid
If 0 then page is on disk

## Slide 28: Address Translation Example
LW $2, 0($4)  read from addr 0x10004123
VPN = 0x1000 4, Page_offset = 0x123
Access:
  PageTable[VPN] get PPN
  PageTable[0x10004]  0xFA00 2 (example)
PA = 0xFA00 2123

## Slide 29: Permissions
VPN
OFF
Page Table
PPN
OFF
PPN
perm
v
Perm = permissions
Read, Write, Execute
V = valid
PPN = Physical Page Number
VPN = Virtual Page Number

## Slide 30: Page Table (reference)
Holds virtual-to-physical address translations
Access like a memory
  Input: Virtual Address
    Only need Virtual PageNumber portion (upper bits)
    Lower bits are PageOffset, ie which byte inside the page
  Output: Physical Address
    Lookup gives a Physical PageNumber
    Combine with PageOffset to form entire Physical Address
Where to hold the PageTable for a program?
  Dedicated memory inside CPU? Too big! not done!
  Instead, store it in main memory

## Slide 31: How are Virtual Pages Mapped?
A attempts to access 0x1000, VPN = 0x1
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 32: How are Virtual Pages Mapped?
PT[0x1] = not valid, Translation finds an invalid entry
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 33: How are Virtual Pages Mapped?
PAGE FAULT: Interrupt to OS, PC = Handler
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 34: How are Virtual Pages Mapped?
OS finds an empty page and allocates PT[0x1] entry
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 35: How are Virtual Pages Mapped?
Page Fault return and application retries fetch from 0x1000
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 36: How are Virtual Pages Mapped?
Application tries to do a load from another page
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 37: How are Virtual Pages Mapped?
Page Fault, OS allocates, return and retry
A
OS
Physical
PAGE
Virtual
Page
VPN
OFF
PT
PPN
OFF

## Slide 38: Where is the Page Table?
Page Table is in memory:
  32 b Address space  2^20 = 1M entries
One page table per process
A
Virtual
Physical
Physical
PAGE
Virtual
PAGE
OS
VPN
OFF
PT
PPN
OFF

## Slide 39: Page Table: Big Lookup Table
D
i
s
k
a
d
d
r
e
s
s
e
s
IE
IE
IE
IE
IE
IE
IE
IE
IE sees this
Main Memory sees this
Fragmented:
Non-contiguous (holes), out-of-order, some on disk
Page Table
Virtual Addresses
Physical Addresses
Address Translation
IE
Pages

## Slide 40: Who accesses the page table?
NIOS II does:
  ldw r8, 0(r10)
This is in virtual memory
  Has to be translated to a physical address first
Must access the PT
  But the PT is in memory
Must do another load 
  Who does that?
  Isn’t this slow?
Every Virtual Memory Access becomes two accesses
  Page Translation
  Actual Access

## Slide 41: Page Table Implications
CPU executes “Load” instruction
  Recall: address is now a Virtual Address
  First step: Lookup address translation
    Where is page table? In main memory
    Special CPU register called Page Table Register (PTR)
      Holds starting address of page table
    Read DataMem from PTR+PageNumber to get Physical Address
  Second step: Access the data
    Read DataMem from Physical Address
Every load/store requires TWO memory accesses
  Slow
  Can we speed up the translation step? Yes, use a cache

## Slide 42: Translation Lookaside Buffer
Cache of Page Table Entries
PPN
perm
v
VPN
PPN
perm
v
VPN
PPN
perm
v
VPN
VPN
OFFSET
PPN
OFFSET
perm

## Slide 43: TLB: Translation Looksaside Buffer (A special cache for the Page Table)
1
1
1
1
0
1
1
0
1
1
0
1
1
1
1
1
0
1
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
TLB
Page Table
Tag
Physical Page Number
V
V
Physical Page Number or Disk Address
Physical Memory
Disk

## Slide 44: Combined TLB & Cache Structure
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
C
a
c
h
e
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
T
L
B
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
1. TLB lookup
3. Access data cache
2. Convert VA to PA
set

## Slide 45: Memory Access:TLB Usage Algorithm
Both hardware and software solutions are possible for TLB miss
NOTICE: software designates some memory pages as READ-ONLY
Example: pages holding instructions.
It will may share some read-only pages with multiple programs, eg you run Firefox twice.

## Slide 46: TLB Notes
TLB Miss
  If handled by software: raises exception on TLB miss.
  If handled by hardware: special hardware unit will check DRAM for translation
  If page is not in DRAM, then need OS to transfer it in (“page fault”).
  OS handles security issues (invalidating TLB entries, etc…)
Read-only pages
  Can share non-sensitive data, e.g., instructions and pre-compiled data tables in a program such as Firefox
  Writes to read-only pages cause exception
  OS handles, possible outcomes:
    Illegal to write to this page
    Change page to writable
    If page is shared, make a new writable copy of this page for this program only. Remaining program share the original read-only copy. This is called “copy on write”

## Slide 47: TLB Operation
Like a Cache
  Processor does “reads”
  OS does “writes”
Initially Empty
On Page Fault cache PT entry
When full evict TLB entry
On Hit no need to access PT
On Miss access PT
  Software (e.g., SPARC) or hardware (x86)
OS manages the TLB

## Slide 48: TLB Typical Organization
32-128 Fully Associative L1 TLB
256-1024 2- to 8-way Set-Associative L2 TLB

## Slide 49: Superpages
Framebuffer
  1920 x 1200 x 3 bytes ~ 6.6 Mbytes
  Accessed frequently
    Refresh rate say 100Hz
    Every pixel (3 bytes) accessed times a second
    But there are millions of pixels
  With 4K pages
    1688 pages
OS can support large pages to avoid allocating multiple entries

## Slide 50: Paging to Secondary Storage
Not all pages need to stay resident
Think of many apps running
Think of one app that “needs” 4G but system has only 2G
“SWAP file”: evict pages from physical memory to disk
Page table extended to keep track of both

## Slide 51: Permissions?
Read/Write/Execute
Devices?
  Cacheable / Non-Cacheable
Can we swapped?
  Pageable vs. Non-Pageable
  Lock pages in memory
    OS, performance

## Slide 52: How it all works?
OS
Part of Memory Space Belongs to OS
Application cannot touch
Special Call Instructions
System Calls

## Slide 53: How it all works?
OS
OS Maintains
Free list of pages
Page Table per Process

## Slide 54: How it all works?
OS
Part of the OS is always resident
  Non-Pageable memory
The rest is pageable
  This includes page tables for processes
OS

## Slide 55: Multi-Level Page Tables
Usually Processes are like this
A
In use
in use
Page Table
Lots of “Empty”

## Slide 56: Multilevel Page Tables
In use
in use
Page Table
VPN
offset
L1 idx
L2 idx
PPN
offset
L2 Tables
Where in memory is the L2 table
(address, valid)
Actual Translation

## Slide 57: Multi-Level Page Table Example
4GB address space, 4K pages
  1M pages
  VPN = PPN = 20 bits
Flat PT:
  1M entries, all allocated
2-level PT with 2K fist level (2^11)
  1st level 2K entries
  2K 2nd level tables
  Each with 512 entries (20 (VPN) – 11 (1st level index))

## Slide 58: Page tables may not fit in memory!
A table for 4KB pages for a 32-bit address space has 1M entries
Each process needs its own address space!
P1 index
P2 index
Page Offset
31
12
11
0
21
22
32 bit virtual address
Top-level table wired in main memory
Subset of 1024 second-level tables in main memory; rest are on disk or unallocated
Two-level Page Tables

## Slide 59: Combined TLB & Cache Structure
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
C
a
c
h
e
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
T
L
B
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
1. TLB lookup
3. Access data cache
2. Convert VA to PA
NOTE: TLB is now slowing our cache
set

## Slide 60: 6th Cache Optimization: Fast hits by Avoiding Address Translation
CPU
TB
$
MEM
VA
PA
PA
Naive
Organization
Virtually Addressed Cache?
CPU
$
TB
MEM
VA
PA
Tags
PA
Overlap $ access
with VA translation:
requires $ index to
remain invariant
across translation
CPU
$
TB
MEM
VA
VA
PA
VA
Tags
L2 $

## Slide 61: Use virtual addresses for cache?
“Physical Addresses”
CPU
Main Memory
A0-A31
A0-A31
D0-D31
D0-D31
Only use TLB on a cache miss
Translation
Look-Aside
Buffer
(TLB)
Virtual
Physical
“Virtual Addresses”
Cache
Virtual
D0-D31
CPU
$
TB
MEM
VA
VA
PA
VA
Tags

## Slide 62: Problems: VA indexed VA tagged
What happens on a context switch?
  Process 1: VA 0x0  PA 0x100
  Process 2: VA 0x0  PA 0x200
  Same VA from different processors pointing to difference Pas.
What if P1 accesses VA 0x0 and then we context switch to P2?
  What will P2 read if it accesses VA 0x0?
Solution?
  #1: Flush the cache
    What about a multiprocessor? Coherence?
  #2: Add ASID: address space identifier (which processes is running)
    Any problems with this?

## Slide 63: Sharing of Memory
Same Physical Page can be shared: why?
A
B

## Slide 64: Sharing of Memory
Same Physical Page can be shared:
  Common Code
  Think shared libraries
  Inter-process communication
Virtual Address may be different for A and B
A
B

## Slide 65: VA-indexed VA-tagged
Need to worry about synonym problem (two different virtual addresses for same physical address)
Example:
  64 KB DM cache, 16 B lines, 4KB pages
Proc 1 VA 0x00000000 -> PA 0xFF000000
Proc 2 VA 0x0000F000 -> PA 0xFF000000
Will ASIDs solve the problem?
What if this is a multiprocessor?

## Slide 66: Virtually-Indexed Physically-Tagged
TLB first, Cache second strategy is slow
  Called Physically Indexed, Physically Tagged
VA-indexed VA-Tagged has problems
To improve performance:
  Lookup TLB, Lookup Cache at same time
  Must use Virtual Address to lookup in cache
  Compare Physical Address (output of TLB) to TAG (output of cache) when checking cache hit
  If OK, we can use the data
  Called Virtually Indexed, Physically Tagged

## Slide 67: Virtual Indexed / Physically Tagged Caches
Used extensively (TLB lookup in parallel with cache lookup --> faster hit time)
Need to worry about synonym problem (two different virtual addresses for same physical address)
Example:
  64 KB DM cache, 16 B lines, 4KB pages
Proc 1 VA 0x00000000 -> PA 0xFF000000
Proc 2 VA 0x0000F000 -> PA 0xFF000000
Coherence?
Can use Physical Addresses

## Slide 68: Set index using VA bits?
Assume: 64 KB direct mapped cache with 16 B lines
  block offset lower 4 bits (3...0)
  cache index next 12 bits (15...4)
Assume: 4KB pages
  page offset lower 12 bits (11...0)
16 ‘synonym’ locations in cache due to 4 virtual address bits (15...12)
Proc. 1 VA 0x0000 000 0 -> PA 0xFF000000
Proc. 2 VA 0x0000 F00 0 -> PA 0xFF000000
Index Proc. 1 = 0x000 (tag = 0xFF000)
Index Proc. 2 = 0xF00 (tag = 0xFF000)
What if Proc. 1 writes, yield, Proc. 2 reads?
… …
Valid Tag Data
000
F00
… …

## Slide 69: VA indexed PA tagged
Valid
Cache Tags
Cache Data
Data out
Virtual Page Number | Page Offset
Translation
Look-Aside
Buffer
(TLB)
Virtual
Physical
=
Hit
Cache Tag
This works, but ...
Q. What is the downside?
A. Inflexibility. Size of cache limited by page size.
 | Set | Byte Select
Cache Block
Cache Block

## Slide 70: VA-indexed PA-Tagged: OS help
Restrict page placement in OS
  make sure index(VA) = index(PA)
  Called page coloring
  Used in many SPARC processors
This is instead of restricting cache set index to use just page offset bits

## Slide 71: VA indexed PA tagged
Valid
Cache Tags
Cache Data
Data out
Virtual Page Number | Page Offset
Translation
Look-Aside
Buffer
(TLB)
Virtual
Physical
=
Hit
Cache Tag
This works, but ...
Q. What is the downside?
A. Inflexibility. Size of cache limited by page size.
 | Set | Byte Select
Cache Block
Cache Block