## Slide 1: SIMD
Single Instruction Multiple Data

## Slide 2: SIMD: Motivation Contd.
Recall:
  Part of architecture is understanding application needs
Many Apps:
  for i = 0 to infinity
    a(i) = b(i) + c
Same operation over many tuples of data
Mostly independent across iterations

## Slide 3: Some things are naturally parallel

## Slide 4: Sequential Execution Model / SISD
int a[N]; // N is large
for (i =0; i < N; i++)
  a[i] = a[i] * fade;
time
Flow of control / Thread
One instruction at the time
Optimizations possible at the machine level

## Slide 5: Data Parallel Execution Model / SIMD
int a[N]; // N is large
for all elements do in parallel
  a[i] = a[i] * fade;
time
This has been tried before: ILLIAC III, UIUC, 1966
http://ieeexplore.ieee.org/xpls/abs_all.jsp?arnumber=4038028&tag=1
http://ed-thelen.org/comp-hist/vs-illiac-iv.html

## Slide 6: SIMD Processing
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
add r3, r1, r2
SIMD
(N operations)
+
r1
r2
r3
+
r1
r2
r3
+
r1
r2
r3
+
r1
r2
r3
+
r1
r2
r3

## Slide 7
TIME
fetch
decode
rf
exec
wb
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
exec
exec
wb
wb
fetch
decode
rf
exec
wb
exec
exec
wb
wb

## Slide 8
TIME
fetch
decode
rf
exec
wb
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
exec
exec
wb
wb
fetch
decode
rf
exec
wb
exec
exec
wb
wb
fetch
decode
rf
exec
wb
exec
exec
wb
wb

## Slide 9: SIMD Architecture
Replicate Datapath, not the control
All PEs work in tandem
CU orchestrates operations
CU
PE
MEM
PE
MEM
PE
MEM
ALU
μCU
regs

## Slide 10: Multimedia extensions
SIMD in “modern” CPUs

## Slide 11: MMX: Basics
Multimedia applications are becoming popular
Are current ISAs a good match for them?
Methodology:
  Consider a number of “typical” applications
  Can we do better?
  Cost vs. performance vs. utility tradeoffs
Net Result: Intel’s MMX
Can also be viewed as an attempt to maintain market share
  If people are going to use these kind of applications we better support them

## Slide 12: Multimedia Applications
Most multimedia apps have lots of parallelism:
  for I = here to infinity
    out[I] = in_a[I] * in_b[I]
  At runtime:
    out[0] = in_a[0] * in_b[0]
    out[1] = in_a[1] * in_b[1]
    out[2] = in_a[2] * in_b[2]
    out[3] = in_a[3] * in_b[3]
    …..
Also, work on short integers:
  in_a[i] is 0 to 256 for example (color)
  or, 0 to 64k (16-bit audio)

## Slide 13: Observations
32-bit registers are wasted
  only using part of them and we know
  ALUs underutilized and we know
Instruction specification is inefficient
  even though we know that a lot of the same operations will be performed still we have to specify each of the individually
  Instruction bandwidth
  Discovering Parallelism
  Memory Ports?
    Could read four elements of an array with one 32-bit load
    Same for stores
    The hardware will have a hard time discovering this
      Coalescing and dependences

## Slide 14: MMX Contd.
Can do better than traditional ISA
  new data types
  new instructions
Pack data in 64-bit words
  bytes
  “words” (16 bits)
  “double words” (32 bits)
Operate on packed data like short vectors
  SIMD
  First used in Livermore S-1 (> 20 years)

## Slide 15: MMX:Example
Up to 8 operations (64bit) go in parallel
Potential improvement: 8x
In practice less but still good
Besides another reason to think your machine
is obsolete

## Slide 16: Data Types

## Slide 19: Vector Processors
Scalar processors operate on single numbers (scalars)
Vector processors operate on vectors of numbers
  Linear sequences of numbers
Does not say that they have to be done in parallel
+
r1
r2
r3
add r3, r1, r2
SCALAR
(1 operation)
v1
v2
v3
+
vector
length
vadd.vv v3, v1, v2
VECTOR
(N operations)
From. Christos Kozyrakis, Stanford

## Slide 20
TIME
fetch
decode
rf
exec
wb
C1
C2
C3
C4
C5
C6
C7
C8
C9
C10
exec
exec
wb
wb
rf
rf
fetch
decode
rf
exec
wb
exec
exec
wb
wb
rf
rf
fetch
decode
rf
exec
wb
exec
exec
wb
wb
rf
rf
a[i] = a[i] + 10
b[i] = b[i] * a[i]
c[i] = c[i] + b[i]
a[i] = a[i] + 10
b[i] = b[i] * a[i]
c[i] = c[i] + b[i]

## Slide 21: Example of Simple Vector Processor

## Slide 22: What’s in a Vector Processor
A scalar processor (e.g., a MIPS processor)
  Scalar register file (32 registers)
  Scalar functional units (arithmetic, load/store, etc)
A vector register file (a 2D register array)
  Each register is an array of elements
    E.g., 32 registers with 32 64-bit elements per register
  MVL = maximum vector length = max # of elements per register
A set for vector functional units
  Integer, FP, load/store, etc
  Some times vector and scalar units are combined (share ALUs)

## Slide 23: Vector Code Example
Y[0:63] = Y[0:63] + a * X[0:63]
LD R0, a
VLD V1, 0(Rx) V1 = X[]
VLD V2, 0(Ry) V2 = Y[]
VMUL.SV V3, R0, V1 V3 = X[]*a
VADD.VV V4, V2, V3 V4 = Y[]+V3
VST V4, 0(Ry) store in Y[]

## Slide 24: Modern Multimedia Instruction Extensions
AVX  Vector extension
256 bit registers
  8 32b floating-point
  4 64b floating-point
Many new instructions