## Slide 1: Insertion Policies
Adaptive Insertion Policies for High-Performance Caching
Moinuddin K. Qureshi Yale N. Patt
Aamer Jaleel Simon C. Steely Jr. Joel Emer

## Slide 2: Dead on Arrival (DoA) Lines
DoA Lines: Lines unused between insertion and eviction
  For the 1MB 16-way L2, 60% of lines are DoA
   Ineffective use of cache space
(%) DoA Lines

## Slide 3: Working Set > Cache Size Example
for (j = 0; j < M; j++)
for (i = 0; i < LARGE_N; i++)
a[i] = a[i] x 10;
Cache
a[]

## Slide 4: Why DoA Lines ?
Streaming data  Never reused. L2 caches don’t help.
Working set of application greater than cache size
Soln: if working set > cache size, retain some working set
art
Misses per 1000 instructions
Cache size in MB
mcf
Misses per 1000 instructions
Cache size in MB

## Slide 5: Working Set > Cache Size Example
for (j = 0; j < M; j++)
for (i = 0; i < LARGE_N; i++)
a[i] = a[i] x 10;
Cache
a[]
Keep this in the cache

## Slide 6: Cache Insertion Policy
Simple changes to insertion policy can greatly improve cache performance for memory-intensive workloads
Two components of cache replacement:
Victim Selection: Which line to replace for incoming line? (E.g. LRU, Random, FIFO, LFU)
Insertion Policy: Where is incoming line placed in replacement list? (E.g. insert incoming line at MRU position)

## Slide 7: LRU-Insertion Policy (LIP)
a
b
c
d
e
f
g
h
MRU
LRU
i
a
b
c
d
e
f
g
Reference to ‘i’ with traditional LRU policy:
a
b
c
d
e
f
g
i
Reference to ‘i’ with LIP:
Choose victim. Do NOT promote to MRU
Lines do not enter non-LRU positions unless reused

## Slide 8: How it works for our example?
for (j = 0; j < M; j++)
for (i = 0; i < LARGE_N; i++)
a[i] = a[i] x 10;
Cache
a[]
Keep this in the cache
Assume Cache is empty
First set of accesses will fill
In all ways,
Thrashing will occur only on the
last way of each set

## Slide 9: What about a change in working set?
Cache
a[]
Keep this in the cache
First this
b[]
Keep this in the cache
Followed by this
a[] will occupy all N-1 sets and will not leave. b[] does not stand a chance.

## Slide 10: Bimodal-Insertion Policy (BIP)
if ( rand() < e ) Insert at MRU position; else Insert at LRU position;
LIP does not age older lines
Infrequently insert lines in MRU position
Let e = Bimodal throttle parameter
For small e , BIP retains thrashing protection of LIP while responding to changes in working set
Think two streaming working sets
Back to back

## Slide 11: Results for LIP and BIP
Changes to insertion policy increases misses for LRU-friendly workloads
LIP
BIP(e=1/32)
(%) Reduction in L2 MPKI

## Slide 12: Bigger Lesson
Interesting programs run for a long time
Billions of instructions per second
  Several orders of magnitude larger than your cache size
Don’t have to rush to do the “right thing” immediately
  Event “infrequent” changes will eventually affect the whole cache

## Slide 13: Dynamic-Insertion Policy (DIP)
Two types of workloads: LRU-friendly or BIP-friendly
DIP can be implemented by:
Monitor both policies (LRU and BIP)
Choose the best-performing policy
Apply the best policy to the cache
Need a cost-effective implementation  “Set Dueling”

## Slide 14: DIP via “Set Dueling”
LRU-sets
Follower Sets
BIP-sets
    Divide the cache in three:
      Dedicated LRU sets
      Dedicated BIP sets
      Follower sets (winner of LRU,BIP)
    n-bit saturating counter
    misses to LRU-sets: counter++
    misses to BIP-set: counter--
    Counter decides policy for Follower sets:
      MSB = 0, Use LRU
      MSB = 1, Use BIP
n-bit cntr
+
miss
–
miss
MSB = 0?
YES
No
Use LRU
Use BIP
monitor  choose  apply
(using a single counter)

## Slide 15: Results for DIP
DIP reduces average MPKI by 21% and requires < two bytes storage overhead
DIP (32 dedicated sets)
BIP
(%) Reduction in L2 MPKI