## Slide 1: Some things are naturally parallel

## Slide 2: Sequential Execution Model / SISD
int a[N]; // N is large
for (i =0; i < N; i++)
  out[i] = out[i] * fade;
time
Flow of control / Thread
One instruction at the time
Optimizations possible at the machine level

## Slide 3: Data Parallel Execution Model / SIMD
int a[N]; // N is large
for all elements do in parallel
  out[i] = a[i] * fade;
time
This has been tried before: ILLIAC III, UIUC, 1966
http://ieeexplore.ieee.org/xpls/abs_all.jsp?arnumber=4038028&tag=1
http://ed-thelen.org/comp-hist/vs-illiac-iv.html

## Slide 4: Single Program Multiple Data / SPMD
int a[N]; // N is large
for all elements do in parallel
new = a[i] * fade
  if (new > 255) out[i] = new;
time
Code is statically identical across all threads
Execution path may differ
The model used in today’s Graphics Processors

## Slide 5: SPMD Execution Order Undefined
All in parallel
Sequential
Any other order

## Slide 6: Programming Model
for index in RANGE
  Kernel(index)
RANGE can be 1D, 2D, or 3D
Use 1D for the time being

## Slide 7: 1D Range – Execution Model
int a[N]; // N is large
for all elements of an array
  a[i] = a[i] * fade
Lots of independent computations
Kernel
THREADs
RANGE (grid)

## Slide 8: Why are threads useful? Parallelism
Concurrency:
  Do multiple things in parallel
  Uses more hardware  Gets higher performance
  Application must have parallelism
Needs more functional units

## Slide 9: Why are threads useful #2 – Tolerating stalls
Often a thread stalls, e.g., memory access
Multiplex the same functional unit
Get more performance at a fraction of the cost

## Slide 10: The Realities of Semiconductor Technology

## Slide 11: What to build then?

## Slide 12: But threads may need to communicate… Compromise
RANGE (grid)
block
thread 10 thread 11
a[10] = in[10] a[11] = in[11]
barrier barrier
a[10] += a[11]
communication
synchronization

## Slide 13: GPGPU Processor – Basic Unit
SHARED MULTIPROCESSOR
FETCH
DECODE SCHEDULE
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
WARP
32
REG
REG
REG
REG
MEM
REG
REG
REG
REG
LOCAL
MEM
REG
REG
REG
REG
CACHE

## Slide 14: GPGPU Processor – Overall Architecture
SHARED MULTIPROCESSOR
FETCH
DECODE SCHEDULE
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
WARP
32
REG
REG
REG
REG
MEM
REG
REG
REG
REG
LOCAL
MEM
REG
REG
REG
REG
CACHE
SHARED MULTIPROCESSOR
FETCH
DECODE SCHEDULE
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
WARP
32
REG
REG
REG
REG
MEM
REG
REG
REG
REG
LOCAL
MEM
REG
REG
REG
REG
CACHE
SHARED MULTIPROCESSOR
FETCH
DECODE SCHEDULE
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
WARP
32
REG
REG
REG
REG
MEM
REG
REG
REG
REG
LOCAL
MEM
REG
REG
REG
REG
CACHE
Block Scheduler
Shared Cache
Global Memory

## Slide 15: GPGPU Processor – Basic Unit
SHARED MULTIPROCESSOR
FETCH
DECODE SCHEDULE
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
EXEC
REG
WARP
32
REG
REG
REG
REG
MEM
REG
REG
REG
REG
LOCAL
MEM
REG
REG
REG
REG
CACHE
Warp Pool

## Slide 16: Fade example
Each thread will process one pixel
for all elements do in parallel
  out[i] = a[i] * fade;

## Slide 17: Decompose into blocks

## Slide 18: Assign Each block to an SMX

## Slide 19: Decompose a Block into Warps
thread

## Slide 20: Execute Warps onto SMX
thread

## Slide 21: Warp vs. Thread vs. Instructions
Warp is 32 Threads
Each Thread has the same program
Each thread will execute many instructions
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + f;
}

## Slide 22: Warp scheduling – Hiding Stalls

## Slide 23: Exposing Locality to Programmer
RANGE (grid)
block
Threads within a group can co-operate and coordinate

## Slide 24: Communication and Synchronization
RANGE (grid)
block
thread 10 thread 11
a[10] = in[10] a[11] = in[11]
barrier barrier
a[10] += a[11]
communication
synchronization

## Slide 25: WARP Execution and Control Flow Divergence
if (in[i] == 0) out[i] = sqrt(x);
else out[i] = 10;
in[i] == 0
out[i] = sqrt(x)
out[i] = 10
in[i] == 0
idle
WARP
TIME

## Slide 26: Control Flow Divergence Contd.
TIME
BAD SCENARIO
in[i] == 0
WARP #1
Good Scenario
in[i] == 0
idle
WARP
in[i] == 0
WARP #2

## Slide 27: GPU: bandwidth optimized – latencies are long
A GPU ADD takes 24 GPU cycles (true of GTX280)
  CPU ADD 1 cycle
The GPU cycle is roughly 4x of a CPU cycle
  For the systems in the lab (GTX480)
Need ~100 threads to break even
1000s of threads for GPU to be better

## Slide 28: Architecture Scalability

## Slide 29: GF100 Architecture Overview -- Compute
64-bit

## Slide 30: GF100 Architecture - Complete
512 CUDA cores
16 PolyMorph Engines
4 raster units
64 texture units
48 ROP units
384-bit GDDR5
  6 channels
  64-bit / channel

## Slide 31: SM Architecture
Streaming Multiprocessor (SM)
  32 Streaming Processors (SP)
    32 INT or FP (32-bit)
    16 DP (64-bit)
  4 Super Function Units (SFU)
  16 Load/Store Units
Multi-threaded instruction dispatch
  Up to1536 threads active
    32 (threads) x 48
  24,576 threads for all SMs
  Up to 8 concurrent blocks
    1024 threads/block limit
  Shared instruction fetch per 32 threads
  Cover latency of texture/memory loads
80+ GFLOPS
16K/48K KB shared memory
48K/16K L1 cache
DRAM texture and memory access

## Slide 32: GK110 Architecture GTX7xx series

## Slide 34: Why GPUs now? Why not before?

## Slide 35: Programmer’s view
GPU as a co-processor
(CPU data is from 2008 – matches our lab machines)
CPU
Memory
GPU
GPU Memory
1GB / 3GB
3GB/s – 8GB.s
6.4GB/sec – 31.92GB/sec
8B per transfer
177.4GB/sec / 288.4GB/sec
Key Suppliers: Nvidia and AMD
GTX480 / GTX780 (6 of those)

## Slide 36: Execution Timeline
time
1. Copy to GPU mem
2. Launch GPU Kernel
GPU / Device
2’. Synchronize with GPU
3. Copy from GPU mem
CPU / Host

## Slide 37: Programmer’s view
First create data on CPU memory
CPU
Memory
GPU
GPU Memory

## Slide 38: Programmer’s view
Then Copy to GPU
CPU
Memory
GPU
GPU Memory

## Slide 39: Programmer’s view
GPU starts computation  runs a kernel
CPU can also continue
CPU
Memory
GPU
GPU Memory

## Slide 40: Programmer’s view
CPU and GPU Synchronize
CPU
Memory
GPU
GPU Memory

## Slide 41: Programmer’s view
Copy results back to CPU
CPU
Memory
GPU
GPU Memory
GTX780: kernels can spawn kernels

## Slide 42: Programming Languages
CUDA
  NVidia
  Has market lead
OpenCL
  Many including Nvidia
  CUDA superset
  Somewhat different syntax
  Can target many different devices, e.g., CPUs + programmable accelerators
  Fairly new
Both are evolving

## Slide 43: Computation partitioning:
At the highest level:
  Think of computation as a series of loops:
    for (i = 0; i < big_number; i++)
      a[i] = some function
    for (i = 0; i < big_number; i++)
      a[i] = some other function
    for (i = 0; i < big_number; i++)
      a[i] = some other function
Kernels

## Slide 44: Some things are naturally parallel

## Slide 45: My first CUDA Program
__global__ void arradd (float *a, float fade, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] * fade;
}
int main()
{
float h[N];
float *d;
cudaMalloc ((void **) &a, SIZE);
cudaThreadSynchronize ();
cudaMemcpy (d, a, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d, 10.0, N);
cudaThreadSynchronize ();
cudaMemcpy (a, d, SIZE, cudaMemcpyDeviceToHost));
CUDA_SAFE_CALL (cudaFree (a));
}
GPU
CPU

## Slide 46: Per Kernel Computation Partitioning
Computation Grid: 2D Case
  Threads within a block can communicate/synchronize
  Run on the same core
Threads across blocks can’t communicate
  Shouldn’t touch each others data
  Behavior undefined
Block
thread

## Slide 47: Per Kernel Computation Partitioning
Computation Grid: 2D Case
  One thread can process multiple data elements
  Other mappings are possible and often desirable
    More on this when we talk about how to optimize for performance
Block
thread

## Slide 48: Fade example
Each thread will process one pixel
for all elements do in parallel
  out[i] = a[i] * fade;

## Slide 49: Code Skeleton
CPU:
  Initialize image from file
  Allocate IN and OUT buffers on GPU
  Copy image to
  Launch GPU kernel
    Reads IN
    Produces OUT
  Copy Out back to CPU
  Write image to a file
GPU:
  Launch a thread per pixel

## Slide 50: GPU Kernel pseudo-code
__global__ void fade (unsigned char *in, unsigned char *out, float f, int xmax, int ymax)
{
unsigned int v = in[x][y];
v = v * f;
if (v > 255) v = 255;
out[x][y] = v;
}
This is the program for one thread
It processes one pixel

## Slide 51: How does a thread know which pixel to process?
blockDim.y
gridDim.y
blockDim.x
gridDim.x
threadIdx.y
threadIdx.x
blockIdx.x
blockIdx.y

## Slide 52: gridDim
gridDim.x = 7, gridDim.y = 6
How many blocks per dimension

## Slide 53: blockDim
blockDim.x= 7, blockDim.y = 7
How many threads in a block per dimension

## Slide 54: blockIdx
blockIdx = coordinates of block in the grid
blockIdx.x = 2, blockIdx.y = 3
blockIdx.x = 5, blockIdx.y = 1
(0,0)

## Slide 55: threadIdx
threadIdx = coordinates of thread in the block
threadidx.x= 2, threadIdx.y = 3
threadIdx.x = 5, threadIdx.y = 4
(0,0)

## Slide 56: How does a thread know which pixel to process?
blockDim.y
gridDim.y
blockDim.x
gridDim.x
threadIdx.y
threadIdx.x
blockIdx.x
blockIdx.y
x = blockIdx.x * blockDim.x + threadIdx.x
y = blockIdx.y * blockDim.y + threadIdx.y

## Slide 57: GPU Kernel pseudo-code
__global__ void fade (unsigned char *in, unsigned char *out, float f, int xmax, int ymax)
{
int x = blockDim.x * blockIdx.x + threadIdx.x;
int y = blockDim.y * blockIdx.y + threadIdx.y;
unsigned int v = in[x * row_size + y];
v = v * f;
if (v > 255) v = 255;
out[x * row_size + y] = v;
}

## Slide 58: GPU Kernel pseudo-code w/ limits
__global__ void fade (unsigned char *in, unsigned char *out, float f, int xmax, int ymax)
{
int x = blockDim.x * blockIdx.x + threadIdx.x;
int y = blockDim.y * blockIdx.y + threadIdx.y
if ( (x >= xmax) || (y>= ymax) ) return;
unsigned int v = in[x * row_size + y]
v = v * f;
if (v > 255) v = 255;
out[x * row_size + y] = v;
}

## Slide 59: Programmer’s view: Memory Model

## Slide 60: CUDA API: Example
int a[N];
for (i =0; i < N; i++)
  a[i] = a[i] + x;
Allocate CPU Data Structure
Initialize Data on CPU
Allocate GPU Data Structure
Copy Data from CPU to GPU
Define Execution Configuration
Run Kernel
CPU synchronizes with GPU
Copy Data from GPU to CPU
De-allocate GPU and CPU memory

## Slide 61: My first CUDA Program / Skeleton
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + float;
}
int main()
{
float h_a[N];
float *d_a;
cudaMalloc ((void **) &a_d, SIZE);
cudaMemcpy (d_a, h_a, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d_a, 10.0, N);
cudaThreadSynchronize ();
cudaMemcpy (h_a, d_a, SIZE, cudaMemcpyDeviceToHost));
cudaFree (a_d);
}
GPU
CPU

## Slide 62: 1. Allocate CPU Data container
float *ha;
main (int argc, char *argv[])
{
int N = atoi (argv[1]);
ha = (float *) malloc (sizeof (float) * N);
...
}
No memory allocated on the GPU side
Pinned memory allocation results in faster CPU to/from GPU copies
But pinned memory cannot be paged-out
cudaMallocHost (…)

## Slide 63: 2. Initialize CPU Data (dummy)
float *ha;
int i;
for (i = 0; i < N; i++)
ha[i] = i;

## Slide 64: 3. Allocate GPU Data container
float *da;
cudaMalloc ((void **) &da, sizeof (float) * N);
Notice: no assignment side
  NOT: da = cudaMalloc (…)
Assignment is done internally:
  That’s why we pass &da
Space is allocated in Global Memory on the GPU

## Slide 65: GPU Memory Allocation
The host manages GPU memory allocation:
  cudaMalloc (void **ptr, size_t nbytes)
  Must explicitly cast to (void **)
    cudaMalloc ((void **) &da, sizeof (float) * N);
  cudaFree (void *ptr);
    cudaFree (da);
  cudaMemset (void *ptr, int value, size_t nbytes);
    cudaMemset (da, 0, N * sizeof (int));
Check the CUDA Reference Manual

## Slide 66: 4. Copy Initialized CPU data to GPU
float *da;
float *ha;
cudaMemCpy ((void *) da, // DESTINATION
(void *) ha, // SOURCE
sizeof (float) * N, // #bytes
cudaMemcpyHostToDevice); // DIRECTION

## Slide 67: Host/Device Data Transfers
The host initiates all transfers:
cudaMemcpy( void *dst, void *src, size_t nbytes, enum cudaMemcpyKind direction)
Asynchronous from the CPU’s perspective
  CPU thread continues
In-order processing with other CUDA requests
enum cudaMemcpyKind
  cudaMemcpyHostToDevice
  cudaMemcpyDeviceToHost
  cudaMemcpyDeviceToDevice

## Slide 68: 5. Define Execution Configuration
How many blocks and threads/block
int threads_block = 64;
int blocks = N / threads_block;
if (blocks % N != 0) blocks += 1;
Alternatively:
blocks = (N + threads_block – 1) / threads_block;

## Slide 69: 6. Launch Kernel & 7. CPU/GPU Synchronization
Instructs the GPU to launch blocks x threads_block threads:
arradd <<<blocks, threads_block>> (da, 10f, N);
cudaThreadSynchronize (); // forces CPU to wait
arradd: kernel name
<<<…>>> execution configuration
(da, x, N): arguments
  256 byte limit / No variable arguments
    Not sure this is still true (will check)

## Slide 70: CPU/GPU Synchronization
CPU does not block on cuda…() calls
  Kernel/requests are queued and processed in-order
  Control returns to CPU immediately
Good if there is other work to be done
  e.g., preparing for the next kernel invocation
Eventually, CPU must know when GPU is done
Then it can safely copy the GPU results
cudaThreadSynchronize ()
  Block CPU until all preceding cuda…() and kernel requests have completed

## Slide 71: 8. Copy data from GPU to CPU & 9. DeAllocate Memory
float *da;
float *ha;
cudaMemCpy ((void *) ha, // DESTINATION
(void *) da, // SOURCE
sizeof (float) * N, // #bytes
cudaMemcpyDeviceToHost); // DIRECTION
cudaFree (da);
// display or process results here
free (ha);

## Slide 72: The GPU Kernel
__global__ darradd (float *da, float x, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) da[i] = da[i] + x;
}
BlockIdx: Unique Block ID.
  Numerically asceding: 0, 1, …
BlockDim: Dimensions of Block = how many threads it has
  BlockDim.x, BlockDim.y, BlockDim.z
  Unused dimensions default to 0
ThreadIdx: Unique per Block Index
  0, 1, …
  Per Block

## Slide 73: My first CUDA Program
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + float;
}
int main()
{
float h_a[N];
float *d_a;
cudaMalloc ((void **) &a_d, SIZE);
cudaThreadSynchronize ();
cudaMemcpy (d_a, h_a, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d_a, 10.0, N);
cudaThreadSynchronize ();
cudaMemcpy (h_a, d_a, SIZE, cudaMemcpyDeviceToHost));
CUDA_SAFE_CALL (cudaFree (a_d));
}
GPU
CPU

## Slide 74: Texture Unit
Painting with images