## Slide 1: Out-of-Order Execution Structure Optimizations

## Slide 2: Tag Elimination

## Slide 3: Conventional Schedulers are Overdesigned
For MIPS-like ISA
  Two source tags
  One destination tag
Not all instructions use two source operands
  E.g., addi $1, $2, 10
Not all instructions produce a result that is interesting for scheduling
  E.g., beq
Some operands are ready when the instruction enters the scheduler
Source: Efficient Dynamic Scheduling Through Tag Elimination, Dan Ernst and Todd Austin, ISCA 2002

## Slide 4: Some Operands are Ready when the Instruction Enters the Scheduler

## Slide 5: Window Specialization
Have reservation stations with different source operand wait capabilities

## Slide 6: Window Specialization
At rename check how many source operands are not ready
If there is an appropriate slot proceed to schedule
If not, stall at rename
Advantages:
  Destination bus only runs over reservation stations with comparators
  Load on the destination bus is reduced
Disadvantages:
  Stalls due to unavailability of reservation stations
  Complexity of res. Station assignment

## Slide 7: Window Specialization - Performance
Performance as IPC – Actual Clock Frequency not considered

## Slide 8: Window Specialization - Performance
Performance as IPC per ns

## Slide 9: Last Tag Prediction
Observe:
  Instruction becomes ready after the last tag it waits for appears
Last Tag prediction
  Predict which of the two tags will that be
Speculatively execute
  Correct speculation: that was the last tag
  Incorrect speculation:
    Need to reschedule
    Detection? Try to read a value that is not available

## Slide 10: GShare-Style Last Tag Prediction
Two-bit saturating counters

## Slide 11: Accuracy
Over all instructions with two outstanding operands

## Slide 12: Window Specialization - Performance
Performance as IPC – Actual Clock Frequency not considered
Predictive schedulers

## Slide 13: Window Specialization - Performance
Performance as IPC per ns

## Slide 14: Prescheduling
Data-flow prescheduling for large
instruction windows in out-of-order
processors
Pierre Michaud, André Seznec, HPCA 2001

## Slide 15: Prescheduling
Predict latencies
Put scheduled instructions into a FIFO
Slide into a smaller window

## Slide 16: Prescheduling Method

## Slide 17: Prescheduling Example

## Slide 18: Latency Prediction

## Slide 19: Latency Prediction Contd.

## Slide 20: Broadcast Free Scheduler

## Slide 21: Broadcast Free Scheduler
Cyclone design
  D. Ernst, A. Hamel, T. Austin
  ISCA 2003
Preschedule Instructions
Put them into a dual strip cyclical FIFO
Vertical paths allow for motion between the strips

## Slide 22: Cyclone Architecture
Will be ready in cycle + 6

## Slide 23: Cyclone Architecture – Cycle +1

## Slide 24: Cyclone Architecture – Cycle + 2

## Slide 25: Cyclone Architecture – Cycle + 3

## Slide 26: Cyclone Architecture – Cycle + 4

## Slide 27: Cyclone Architecture – Cycle + 5

## Slide 28: Cyclone Architecture – Cycle + 6

## Slide 29: Cyclone Architecture – Cycle + 6

## Slide 30: Cyclone Architecture – Mis-scheduling
Estimate new latency

## Slide 31: Pre-scheduler
Insert instruction with predicted latency N at the front of the FIFO
Have it switch at N/2
Can only do two cascaded MAX calculations
Due to timing considerations

## Slide 32: Cyclone IPC Performance

## Slide 33: Cyclone True Performance and Area

## Slide 34: Matrix Schedulers

## Slide 35: Conventional Scheduler
WS requests
IW grants

## Slide 36: Conventional Scheduler Timing
A2
A2
B1
B1
B3
B3
Source: A High-Speed Dynamic Instruction Scheduling Scheme
for Superscalar Processors
Masahiro Goshima Kengo Nishino Yasuhiko Nakashima Shin-ichiro Mori
Toshiaki Kitamura Shinji Tomita
MICRO 2001
Can’t pipeline without introducing
Bubbles between dependent
Instructions:

## Slide 37: Towards a Matrix Scheduler
Observe:
  In conventional scheduling dependences are discovered twice:
    Once at renaming
    Once during scheduling
  Why? Dependences are implicitly represented
    Producer and Consumer link via a name
    This is indirect
Matrix Scheduler idea:
  Represent dependences explicitly

## Slide 38: Dependence Matrix
Who am I
Who do I depend upon?
Left source
Right source

## Slide 39: Matrix Scheduler
wakeup
Write port
One cell

## Slide 40: Inserting an entry
Write port

## Slide 41: Wakeup
wakeup

## Slide 42: Mispeculation Recovery
Do not cleanup
Use external logic to inhibit request signals

## Slide 43: Delay
Partial wakeup lines
0.18um
1.8V
85C

## Slide 44: Delay measurement points

## Slide 45: Scheduling Priorities

## Slide 46: Conflict Resolution
More instructions ready than available issue slots
  Which get to go?
Age vs. Pseudo-Random Resolution
Age is important
Priority Enforcer picks the oldest
  Complex
Source:
Matrix Scheduler Reloaded
ISCA 2007

## Slide 47: Compacting Scheduler
Implemented in the Alpha 21264
Physical order within scheduler corresponds to age
Entry freed:
  Shift up all younger entries

## Slide 48: Virtual Physical Registers
Physical register names are used for two purposes
  Scheduling
  Communicating
A physical register is held much in advance than needed
  We need the register only after the value is produced
De-couple scheduling from communication names

## Slide 49: Used vs. Allocated Registers

## Slide 50: Goal

## Slide 51: Virtual Physical Registers

## Slide 52: Deadlock
Older instruction completes later than younger ones
  No registers available
Steal a register and re-execute

## Slide 53: Performance vs. Physical Registers