## Slide 1: SCNN: An Accelerator for Compressed-sparse Convolutional Neural Networks
Parashar et al., ISCA 2017
Advanced Computer Architecture, A. Moshovos, Feb 2018

## Slide 2: Motivation
Significant redundancy in CNNs
Weights:
  Can be pruned during training w/o affecting accuracy
  Convert to 0: 20% to 80% across diff layers
Activations:
  Due to ReLU: 50% to 70%
Past work:
  Computation:
    Either zero weights or zero activations
    Not Both
    This work: both
  Communication/Storage:
    Tiling + Compression:
      Compressed weights + activations
      No external references for activations: stay on chip

## Slide 3: Networks Evaluated
Assumes standard ImageNet images: 224 x 224 pixels
More for higher resolution images

## Slide 4: Motivation: AlexNet
Lower is better
Significant potential of we target both IW and IA
  I = ineffectual = zero-valued in this work

## Slide 5: Motivation: GoogLeNet

## Slide 6: Motivation: VGGNet

## Slide 7: Computation Structure/Terminology
Batching/Images
Filters
Channels
Input Image Dim. W
Input H
Filter W
Filter H
Stride?
Notation:
N=1 for this study, typical for real-time

## Slide 8: Design Philosophy
Communication is more important than Computation
Primary goal:
  Avoid moving inputs around
  Emphasis on activations
  Avoid off-chip accesses as much as possible
We’ll discuss at the end what is the end result

## Slide 9: How to Partition the Computation
SCNN: grid of PEs
  Local weight+Activation memories
  Goal avoid off-chip accesses
  Reduce cross PE communication of inputs
Dataflow  greatly impacts overall energy
Their solution:
Planar Tiled – Input Stationary – Cartesian Product – Sparse

## Slide 10: Planar Tiled – Input Stationary – Cartesian Product – Sparse

## Slide 11: Planar Tiled – Input Stationary – Cartesian Product – Sparse
Weights replicated
Activations partitioned
Each W x A
Computed only once

## Slide 12: Baseline: Dense Dataflow
PT-IS-DP-dense
Input A stays at one PE
Multiplied with all Ws needed for all output activations needed
  K x R x S output activation subvolume
    R x S: windows that include this activation
    K: filters  output channels  output activation planes
  Input channels:
window
Planar?

## Slide 13: Reusing Activations
Avoid accesses to the local Activation buffer
  Register to hold an activation
  As long as necessary to do all calculations
K x R x S output activations  input weights as well

## Slide 14: What happens to each product
Some PE calculates an A x W
  Partial sum
Where does it go?
  Needs to be accumulated into a specific output activation
Accumulator Banks

## Slide 15: Implications for weights and outputs
Minimize input activation traffic
Increased accesses to:
  Weights
  Accumulator Banks
Solution:
  Blocking along the K/C dimension
  Calculate only Kc planes at a time
    Output blocking  fewer partial outputs to store in the accumulators at any given point of time
    Input weight blocking  fewer filters to store as well
  K/Kc groups

## Slide 16: K/Kc blocking for weights and outputs
Only some filters
Only some output planes
Storage Needed:
Kc
at a time
Dataflow:

## Slide 17: Intra-PE Parallelism
Fetch two vectors of non-zero inputs
  I: activations
  F: weights
Calculate the Cartesian Product
  Wi x Ai for each Wi in F and each Ai in I
Weights reused over all I activations
Each Product is useful
  No extraneous fetches or computation

## Slide 18: Inter-PE Parallelism
W x H activation plane
  Wt x Ht planar tiles  distribute over the PEs
  Each tile: all of C
  C x Wt x Ht per partition
Does not work exactly for both activations and weights
Cannot have both assigned completely to the same PE
Not all Windows will strictly
fit on onto one PE

## Slide 19: Halos
First definition:
  A x W products that are needed by multiple PEs
Solutions:
  @ at the input:
    replicate A and W across all PEs that need them
  @ the output:
    calculate A x W at one PE, communicate to others
Revised definition:
  Partial sums of A x W that are needed by another PE
  A and W are partitioned across PEs
  A appear at only one PE

## Slide 20: Resulting Dataflow/Compute
Kc Filter chunks
Input
I=A width of mult array
Wt x Ht tile pe PE
For each filter
F = W width of mult array
One A x W
Where it goes?
(x,y,k) = (x,y,channel)
Accumulate
Final output
Could be at
a different PE
Planar: Per input Channel

## Slide 21: SCNN Architecture

## Slide 22: PE Detail

## Slide 23: Routing Results with the PE
F x I products per cycle
Conflicts
F x I x 2 xbar enough
  Needs arbitration still

## Slide 24: Halos and Input/Output
Halos: need to route to neighbors
Current Output = Next Layer’s Input
  Two buffers w/ alternating role

## Slide 25: Data Compression/Representation
Non-zero + how many zeros (4-bit)
  Plane-Row major
  May have to store some zero values if more than 15 zeros

## Slide 26: Temporal Tiling for Large Models
Trying to fit all inputs on chip
On a few cases not possible
Operate only on a subvolume of input and hence output
Send to off-chip in-between
  Temporal tiling
  Vs. Spatial tiling: distribute activations across PEs

## Slide 27: Evaluation: Configuration(s)

## Slide 28: Evaluation: Area
16nm FinFET

## Slide 29: Energy and Performance vs. Density
How relevant is this?
Pro: shows the tradeoffs
Cons: Random input?
Think of caches?

## Slide 30: Performance
Oracle:
  Compute ratio

## Slide 31: Where time goes: Array Ultilization
Intra-PE fragmentation
  Not enough useful work within the PE
Inter-PE imbalance
  Sync at output C groups

## Slide 32: Energy Efficiency

## Slide 33: Effects of input sparsity w/ GoogLeNet

## Slide 34: Other Layers
Fully-Connected
  No weight reuse
  F x I multiply array
    Only the diagonal
    For the 4x4 only 4
Other layers:
  Extra logic
Only 1% of the total compute for GoogLeNet