## Slide 1: Critical Path Prediction
Focusing processor policies via critical-path prediction
B. Fields, S. Rubin and R. Bodik
ISCA 2001
some slides/content from the original presentation

## Slide 2: Motivation
Identify the Critical Path
  Instructions that if accelerated would improve overall performance
Exploit to improve the processor
  This work seems to focus on performance?
  “Make processor policies sensitive to performance”

## Slide 3: Applications Shown
Resource Arbitration
  Scheduler Priorities
  Give critical instructions priority for execution
Misspeculation Reduction
  Value prediction only for critical instructions

## Slide 4: Instruction Slack
Slack of an instruction:
  How long can we delay the instruction before performance decreases?
It’s zero only for instructions on the critical path
Can be used to tolerate latencies

## Slide 5: Using Data Dependency Analysis
Used in compilers
  Determine the data dependencies
  Observe the time of arrival for each value
  Find the longest path

## Slide 6: Using Dependence Analysis
A: ld r1, 0(r2)
B: beq r1, r3, ELSE
C: ELSE: ld r4, 0(r1)
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
A | F | D | S | E | M | M | W | C |  |  |  |  |  | 
B |  | F | D | S | S | S | E | M | W | C |  |  |  | 
C |  |  | F | D | S | S | E | M | W | C |  |  |  | 
A
C
B
3
3
0

## Slide 7: Determining the critical path is hard
A: ld r1, 0(r2)
B: beq r1, r3, ELSE
C: ELSE: ld r4, 0(r1)
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
A | F | D | S | E | M | M | W | C |  |  |  |  |  | 
B |  | F | D | S | S | S | E | M | W | C |  |  |  | 
w |  |  | F | D | S | E | M |  |  |  |  |  |  | 
w |  |  |  | F | D | S | E |  |  |  |  |  |  | 
w |  |  |  |  | F | D | S |  |  |  |  |  |  | 
w |  |  |  |  |  | F | D |  |  |  |  |  |  | 
w |  |  |  |  |  |  | F |  |  |  |  |  |  | 
C |  |  |  |  |  |  | F | D | S | E | M | W | C | 
A
C
B
3
3
0

## Slide 8: Determining Slack is hard
“Probe the processor” approach: Delay and observe
  Delay dynamic instruction by n cycles
  See if execution time increased
    No, increase n; restart; go to step 1
Srinivasan and Lebeck approximation, for loads (MICRO ’98)
  heuristics to predict execution time increase
Microprocessors are complex:
Sometimes slack is determined by resources (e.g., ROB)

## Slide 9: Determining slack
  Alternative approach: Dependence-graph analysis
  Build resource-sensitive dependence graph
  Analyze to find slack
Casmira and Grunwald’s solution (Kool Chips Workshop ’00)
Graphs only with instructions in issue window
  But, how to build resource-sensitive graph?

## Slide 10: Casmira and Grunwald’s solution
A takes longer – performance
Stays the same

## Slide 11: Data-Dependence Graph
Observe latency to produce a result
1
1
1
1
1
2
3
Slack = 0 cycles
Misses microarchitectural effects – limited window -- mispredictions

## Slide 12: Our Dependence Graph Model (ISCA ‘01)
Three nodes: Fetch, Decode, Execute
Imperfect – Good enough  experimental result
E
E
E
E
E
F
F
F
F
F
C
C
C
C
C
Slack = 0 cycles
F = Fetch synonymous to D = Dispatch in the paper

## Slide 13: Our Dependence Graph Model (ISCA ‘01)
E
1
E
E
E
E
1
1
1
1
2
3
F
F
F
F
F
C
C
C
C
C
1
1
1
1
1
1
1
1
1
1
10
0
0
1
1
0
0
1
Slack = 6 cycles
Modeling resources increases observable slack

## Slide 14: An Example
Wrong path not modeled  validation shows this is an OK approximation
Should it be 2? yes

## Slide 15: Within Each Instruction: Execution Follows Dispatch
Execution Follows Dispatch: Di Ei

## Slide 16: Within Each Instruction: Commit Follows Execution
Commit Follows Execution: Ei Ci

## Slide 17: Across Instructions: In-Order Dispatch
In-order Dispatch: Di-1 Di
  Superscalar
  Program Order
  D0  D1: latency 0? 2-way Superscalar

## Slide 18: Across Instructuions: In-Order Commit
In-Order Commit: Ci-1 Ci
  Program Order
  Superscalar
    Notice 0 and 1 alternating pattern across CC edges

## Slide 19: Across Instructions: True Data Dependencies
Data Dependencies: Ei-1 Ej

## Slide 20: Across Instructions: Finite Window
Finite Reorder Buffer: Ci-w Di
  C0  D4: ROB size = 4
  w = window size = 4

## Slide 21: Across Instructions: Branch Mispredictions
Control Dependencies/Branch Mispredictions:
Ei-1 Di
  Instruction cannot be fetched before branch is resolved
  E7  D8: 4 cycles

## Slide 22: No Edge Can Span More than Window Size Instructions
By construction only EE edges could
  D and C nodes are restricted by window size (ROB)
    Wrong path instructions are not included
An EE edge that spans more than WS insts?
  Producer and Consumer not concurrently in the processor
  Producer has committed by the time the consumer enters
  Consumer finds the values it needs in the RF
    Hence EE cannot be critical

## Slide 23: Constructing the Model
Phase 1: Simulate:
Record latency per edge
  More on this on the next slide
Dump these out
Phase 2: Post Processing
Construct graph
Traverse – find longest path
May be able to do so on-the-fly
Impractical for implementation
This is for validation

## Slide 24: Edge Latencty
Time to resolve the edge
  EE: time from decode to execute finish for producer
    FU latency + wait time after ready (structural hazard)
  CD: 0 commit takes no time
  DD: 0 if dispatched together, otherwise?
Why 3?

## Slide 25: Why D8D9 is 3?
D8 got an instruction miss
  Took 3 cycles to get it from L2
  D9 had to wait for D8 hence the latency
  The miss is on D8

## Slide 26: Validating the Model
If the critical instructions are correctly identified then reducing their latency should improve performance
Simulate baseline with +1 latency for all instructions
Two experiments:
  ExpA: Reduce latency to normal for “critical”
  ExpB: Reduce latency to normal for “non-critical”
Expected result
  Performance should improve for ExpA
  Ideally, not for ExpB
  But performance improvement should be higher for ExpA than for ExpB

## Slide 27: Validating the Model
Have 15 insts
Takes N cycles to execute
10 are critical
Run time reduces by 7 cycles
M,easurement will be 0.7

## Slide 28: Discussion of Results
Why does performance improve for ExpB
  Model is incomplete/imperfect
    Prefetching down the wrong path
Why is the performance improvement different?
  Different programs have different behavior
    Could be closer to peak performance for some
  Near-Critical paths
    Eliminating one critical path exposes another
    Must eliminate both for maximum effect

## Slide 29: Criticality Breakdown Per Instruction
Commit Critical
Execute Critical
Fetch Critical
Commit Non-Critical
Execute Non-Critical
Non critical instructions
No node is part of the CP

## Slide 30: Criticality Breakdown Per Instruction
Execute Critical
  Execute node part of the critical path
    E2: result of ld needed by multiply

## Slide 31: Criticality Breakdown Per Instruction
Dispatch Critical
  Dispatch node part of the critical path
    D8: I$ miss delays fetching I9

## Slide 32: Criticality Breakdown Per Instruction
Commit Critical
  Window full
  Must commit to be able to fetch
  I3? CC or EC? Both  Instruction is critical
    How do they account? One of the two. May be the earliest? Other cases

## Slide 33: Non-Critical Instruction
Commit Non-Critical
  Overlaps with a critical CD edge
  Window is full while they execute
  An earlier instruction holds up the window

## Slide 34: Non-Critical Instruction
Execute Non-Critical
  Overlaps with a critical EE edge
  Even if it executed earlier the other instruction would take longer
  None in the example below

## Slide 35: Criticality Breakdown

## Slide 36: Determining the Critical Path
All we have to do is observe the order in which edges arrive
Last-arriving edge per instruction:
  Only these can be part of the critical path
What’s the critical path:
  Start at the last instruction
  Traverse backward following last-arriving edges
This is precise but requires keeping all instructions
How about an approximation?

## Slide 37: Determining the last arriving edge
For each instruction
  For each node: D, E, and C
  Determine the last arriving edge
So, for each instruction there will be three last arriving edges one for each of its nodes

## Slide 38: Determining the Last-Arriving Edge

## Slide 39: Determining the Last-Arriving Edge

## Slide 40: Determining the Last-Arriving Edge

## Slide 41: Determining the Last-Arriving Edge

## Slide 42: Determining the Last-Arriving Edge

## Slide 43: Determining the Last-Arriving Edge

## Slide 44: Determining the Last-Arriving Edge
Why not last arriving?

## Slide 45: Determining the Last-Arriving Edge
Why not last arriving?

## Slide 46: Need for Prediction
Method requires backward traversal
  Too expensive
How about an approximation
  Idea: sample each instruction for criticality
  Plant token
  Propagate token along last arriving edges  forward’
    If no outgoing last arriving edge token dies
  After a while check if token is alive
    Declare instruction as critical
    Approximation
    Forward propagation  easy

## Slide 47: Predictor Organization

## Slide 48: An Approximation

## Slide 49: Plant Tokens at I4’s D, E, and C, propagate

## Slide 50: Implementation
1. Inst commits
2. Which were the last arriving
edges per node
3. Read out the tokens from the
Source insts per node
4. Write them into this inst’s nodes

## Slide 51: Accuracy

## Slide 52: Performance
Assume originally all insts latencies + 1, reduce critical by 1

## Slide 53: Application #1 – Focused Instruction Steering
Wire delays dominate – can’t build large windows
Solution: clusters
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
DEC’s Alpha 21264

## Slide 54: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
How would assign these?

## Slide 55: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
Clustering: no delay

## Slide 56: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
How about this? Assume not enough resources to place all in the same cluster

## Slide 57: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
Critical path matters

## Slide 58: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
Critical path matters

## Slide 59: Focused Steering and Scheduling

## Slide 60: Comparison to heuristic-based Prediction

## Slide 61: Value Prediction
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e

## Slide 62: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'

## Slide 63: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B

## Slide 64: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B
C
b'
D
c'
E
d'

## Slide 65: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B
C
b'
D
c'
E
d'
a
b''
c''
d''
e''

## Slide 66: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B
C
b'
D
c'
E
d'
a
b''
c''
d''
e''
==
==
==
==

## Slide 67: Application #2: Focusing Value Prediction

## Slide 68: Virtual Physical Registers
Physical register names are used for two purposes
  Scheduling
  Communicating
A physical register is held much in advance than needed
  We need the register only after the value is produced
De-couple scheduling from communication names

## Slide 69: Used vs. Allocated Registers

## Slide 70: Goal

## Slide 71: Virtual Physical Registers

## Slide 72: Deadlock
Older instruction completes later than younger ones
  No registers available
Steal a register and re-execute

## Slide 73: Performance vs. Physical Registers