## Slide 1: Long Short Term Memory & Efficient Speech Engine
Andreas Moshovos, Feb 2019

## Slide 2: Feed Forward Neural Nets: Recap
  Outputs y are Correlations of inputs x
  Hidden state h is various features of x

## Slide 3: Typical Activation Functions
  Sigmoid σ(x): squashes range to (0,1)
      Think: thou shall not pass
      ~AND gate
  Hyperbolic Tangent tanh(x): squashes range to (-1, +1)
      Think: you are correlated: positively, negatively, by this much including not at all (zero)
  Rectifier Linear Unit ReLU(x): max(0, x)
      Not correlated, or correlated this much
      Variations: attenuate negative values (x < 0) ? x * scale : x
        Easier to train for

## Slide 4: Recurrent Neural Nets
  Bob arrives at grocery store
  Bob holding bacon
    Infer: Bob is shopping and not cooking
  Inputs
    xt: input @ time t
    ht-1: hidden state @ time t
  Outputs
    yt: output @ time t
    ht: new hidden state

## Slide 5: Vanishing/Exploding Gradient Problem
  Hidden state: long term memory
  At every step it goes through an activation function, tanh
    Small values vanish
    High values explode

## Slide 6: Long Short Term Memory
  Hidden state: Working memory – ephemeral
  Cell state: Long term memory
  Input
  Output

## Slide 7: Remember Gate
  Hidden state: Working memory – ephemeral
  Cell state: Long term memory
  Input
  Output
Based on
current input
Based on
working memory
Which long term features to pass (0,1)

## Slide 8: Candidate for addition to Long Term Memory
from
current input
from
working memory
Correlation of features

## Slide 9: Candidate for addition to Long Term Memory
from
current input
from
working memory
Correlation of features
Which are worth adding/saving into long term memory
from
current input
from
working memory

## Slide 10: Updating Long Term Memory
o is element-wise multiplication

## Slide 11: What to focus on for short term memory (working)
from
current input
from
working memory
Correlation of features

## Slide 12: What Updating Short Term Memory (working)
from
current input
from
working memory
Correlation of features
yt = focus t (not exactly right)
from
current input
from
working memory

## Slide 13: Standard Terminology
ltm = cell state
wm = hidden state
Focus = output gate
Remember = forget gate
Save = input gate

## Slide 14: Another View
Recurrent Neural Nets
  Structure and Unrolled in time
From: https://colah.github.io/posts/2015-08-Understanding-LSTMs

## Slide 15: RNNs: memory and output through a single layer

## Slide 16: LSTMs

## Slide 17: LSTM: Gate
Optionally let information through
    Sigmoid + pointwise multiplication

## Slide 18: What Information to throw away from cell state (long term mem)
Forget gate: what to keep from Ct-1, based on short term memory (ht-1) and current input (xt)

## Slide 19: What new information to remember in long term memory
Input gate: what info from current short term memory (ht-1) and input (xt) to remember for the long term (Cell state)

## Slide 20: Create the new Cell state (long term memory)
New Cell State:
  Forget from Ct-1 and merge new info from ht-1 and xt

## Slide 21: New short term memory and output
Output Gate: based on previous short term memory (ht-1) and current input (xt) what to output from Cell state (long term memory)
    Note that Ct includes past memory and new info from ht-1 and xt

## Slide 22: Peephole Connections in LSTMs
Gates depend also on long term memory (Ct-1)
    Gers & Schmidhuber ftp://ftp.idsia.ch/pub/juergen/TimeCount-IJCN2000.pdf

## Slide 23: Coupled Forget and Input Gates

## Slide 24: Gated Recurrent Unit
Combine Forget and Input gates into a single Update gate
Others: Depth Gated RNNs, Clockwork RNNs
Follow ups: Attention, Grid LSTMs
Check:

## Slide 25: Efficient Speech Engine
Andreas Moshovos, Feb 2019

## Slide 26: Pruning & Compression + Hardware Acceleration on FPGA

## Slide 27: Speech Recognition Engine
LSTM takes 90% of total time
Focus of this work

## Slide 28: LSTM used
diagonal

## Slide 29: Model Compression
Train Regularly
|W| < threshold  prune
Threshold  empirical
Around 93% accuracy drops / non-monotonic behavior

## Slide 30: Load Balance Aware Pruning
Each PE processes a row?
Rows with more elements delay all others
Effort to avoid one row being 5% and another at 15%
Instability around 70%, more experiments at 90%

## Slide 31: Quantization
Pruning 10x reduction in weight parameters
Quantization another 2x  from 32 float to 12b+4b fixed point

## Slide 32: Quantization
Dynamic Range of Weights
    length of fractional part to avoid overflow
    Shouldn’t that be the integer part?

## Slide 33: Quantization of Activation Functions
Determine input range
    Derive sampling strategy

## Slide 34: Encoding in Memory
Data Transfers through:
    DDR3 512b & PCI-E 128b

## Slide 35: ESE: Architecture Overview
Clusters (Channels) of Pes

## Slide 36: Channel Architecture Detail

## Slide 37: Basic Operations: Sparse Matrix x Vector, Element-wise Vector

## Slide 39: Scheduling: From Han’s slides
Get input and first Matrix, plus pointers
Three Channels:
Matrix
Pointers
Vector
Initialization of Activation Tables

## Slide 40: Architecture: Who does what

## Slide 41: Scheduling: From Han’s slides
Get input and first Matrix, plus pointers

## Slide 42: Scheduling
Overlap Computation with Fetching of next Weight Matrix

## Slide 43: Scheduling
Next SpMxV overlapped with next Weight Matrix plus Vector

## Slide 44: Scheduling: and so on…

## Slide 55: Handling Sparsity
Matrix rows interleaved over Pes (modulo)
PE processes one activation at a time: column
    Some Pes will have more work than others
    FIFOs per PE help
  Per Row Pointers help the PE locate the next NZ element per column
  Or is it a pointer per non-zero element?

## Slide 56
Each PE processes some rows
Each row corresponds to a different output activation
Element-wise: take all activations and multiply with another vector

## Slide 57: Speedup and Energy Efficiency