## Slide 1: CEASER: Mitigating Conflict-Based Attacks via Encrypted-Address and Remapping
Moinuddin Qureshi
MICRO-2018

## Slide 2: Background: Resource Sharing
B
LLC
CORE
CORE
Modern systems share LLC for improving resource utilization
Sharing the LLC allows system to dynamically allocate LLC capacity

## Slide 3: Conflict-Based Cache Attacks
B
LLC
CORE
(Spy)
CORE
(Victim)
A
B
V
Co-running spy can infer access pattern of victim by causing cache conflicts
Conflicts leak access pattern, used to infer secret [AES – Bernstein’05]
Miss for B
Victim Accessed Set
Notes: TODO: More attacks

## Slide 4: Prior Solutions
Way Partitioning
Mapping Table
(MT)
NoMo [TACO’12], CATalyst [HPCA’16]
Table-Based Randomization
RPCache[ISCA’07], NewCache[MICRO’08]
Not scalable to many core
Mapping Table large for LLC (MBs)
OS support needed to protect Table
Inefficient use of cache space

## Slide 5: Our Goal
Protect the LLC from conflict-based attacks, while incurring
        Negligible storage overhead
        Negligible performance overhead
        No OS support
        No restriction on capacity sharing
        Localized Implementation

## Slide 6: Outline
Why?
CEASE
CEASER
Effective?

## Slide 7: CEASE: Cache using Encrypted Address Space
Insight: Don’t memorize the random mapping, compute it
LLC
xCAFE0000
Physical Line
Address (PLA)
Encrypt
Key
Dirty Evict
ELA
(ELA)
Decrypt
Key
0xa17b20cf
CEASE
Localized change (ELA visible only within the cache)
Cache operations (access, coherence, prefetch) all remain unchanged
Notes: TAGS are also of ELA
Say that none of the operations change
Before writeback, motivate why decryption

## Slide 8: Randomization via Encryption
Lines that mapped to the same set, get scattered to different sets
A’
B’
LLC
Encrypt
Key
CEASE
B’’
A’’
LLC
Encrypt
Key
CEASE
A
B
LLC
Mapping depends on the key, different machines have different keys

## Slide 9: Encryption: Need Fast, Small-Width Cipher
Block
Cipher
B
B
PlainText
CipherText
Small-width Ciphers deemed insecure:
  Brute-force attack on key
  Memorize all input-output pairs
PLA is ~40 bits
(up-to 64TB memory)
Insight: ELA not visible to attacker (okay to use 40-bit block cipher)
Larger tag (80+ bits)
Latency of 10+ cycles

## Slide 10: Low-Latency Block Cipher (LLBC)
LLBC incurs a delay of 24 XOR gates (approximately 2-cycle latency)
Four-Stage Feistel-Network (with Substitution-Permutation Network)
*inspired by DES and BlowFish Encryption

## Slide 11: Outline
Why?
CEASE
CEASER
Effective?

## Slide 12: Let’s Break CEASE …
D
B
A
C
LLC
E
Attacker can break CEASE within 22 seconds (8MB LLC)
[Liu et al. S&P, 2015]
Form pattern such that cache has a conflict miss
Removed line NOT
in conflicting set
Removed line MAPS
to conflicting set
Remove one line from pattern & check conflict
Conflict Miss?
No
Yes
Notes: TODO: Make this animated

## Slide 13: CEASER: CEASE with Remapping
CEASER uses gradual remapping to periodically change the keys
Split time into Epoch of N accesses (change Key every Epoch)
CACHE
Key
Key
Key
CurrKey
NextKey
CurrKey
NextKey
CurrKey
NextKey
EPOCH
BULK
GRADUAL
time

## Slide 14: CEASER: CEASE with Remapping
SetPtr
Remap-Rate of 1 %  Remap W-way set after (100*W) accesses
Access=0
Epoch=0
CurrKey
NextKey
Access=200
Epoch=0
B0
A1
B1
A0
X0
X1
Access=400
Epoch=0
Access=600
Epoch=0
Y0
Y1
Access=800
Epoch=0
Z0
Z1
Access=0
Epoch=1
CurrKey
NextKey
Cache Access: If (Set[CurrKey] < Sptr) Use NextKey
CEASER with gradual remap needs negligible hardware (one bit per line)
Notes: EMPHASIZE 1%

## Slide 15: Outline
Why?
CEASE
CEASER
Effective?

## Slide 16: Security Analysis
CEASER can tolerate years of attack (Even with remap-rate of 1%)
Time to learn “Eviction Set” for one set (vulnerability removed after remap, <1ms)
Remap-Rate | 8MB LLC | 1 MB LLC-Bank
1% (default) | 100+ years | 100+ years
0.5% | 100+ years | 21 years
0.1% | 100+ years | 5 hours
0.05% | 37 years | 5 minutes
No-Remap (CEASE) | 22 seconds | 0.4 seconds
Limits impact on missrate, energy, accesses to ~1%
Notes: EMPHASIZE 1% (POWER, ENERGY, PERFORAMNCE, MISSRATE)

## Slide 17: Performance and Storage Overheads
CEASER incurs negligible slowdown (~1% ) and storage overheads (24 bytes)
Chart: 
CEASE | 99.684 | 99.198 | 99.321
CEASER | 99.263 | 98.784 | 98.905
Rate-34
Mix-100
ALL-134
Norm Performance (%)
8 cores with 8MB LLC 16-way
(34 workloads, SPEC + Graph)
Structures | Cost
80-bit key (2 LLBC) | 20 bytes
SPtr | 2 bytes
Access Counter | 2 bytes
Total | 24 bytes

## Slide 18: Summary
Robust to attacks (years)
Negligible slowdown (~ 1%)
No OS support needed
Negligible storage (24 bytes)
Localized change (within cache)
Cache
Line Address
Encrypt
Key1
Key2
Change Key, Periodically
Need practical solution to protect LLC from conflict-based attacks
Appealing for Industrial Adoption

## Slide 19: What About Flush-Based Attacks?
Flush-Based Attack: Use clflush to evict shared line, wait, and test
Partitioning
Randomization
Restriction
SHARP [ISCA’17]
Line Duplication
NewCache [MICRO’17]
Compatible with CEASER

## Slide 20: Diffusion Properties of LLBC
Diffusion: Single bit change in input causes lots of bits to change in output
Proposed LLBC has close-to-ideal diffusion properties

## Slide 21: Determining Set Index
Cache index function determines the line to set mapping
Proprietary index functions can be learned [Liu et al., S&P 2015]
Breaking one machine gives information for ALL other machines
B
B
Line Address
Proprietary
Function
?
Line Address
Notes: TODO: More attacks