## Slide 1: Review of Modern Processor Architectures
Andreas Moshovos
moshovos@eecg.toronto.edu
EA310

## Slide 2: Review of Modern Processor Architectures

## Slide 3: Sequential Execution Semantics
Contract: How the machine appears to behave

## Slide 4: Dissecting Instructions
Data Movement
Data Manipulation
Control Flow

## Slide 5: An Instruction in a Processor’s Lifetime

## Slide 6: How to Improve Performance?
Increase concurrency
  Do more things simultaneously
Instruction Level Parallelism
  Find concurrency in instruction processing
    Within the instruction
    Across multiple instructions
Dynamic – User Transparent
    The machine discovers it
Static – User/Compiler Specifies
    Machine is build to execute multiple instructions
Parallelism – thread level
  Duplicate units / processors
  Rely on programmer to write parallel program

## Slide 7: Pipelining

## Slide 8: Sequential Semantics are Preserved

## Slide 9: Superscalar - In-order
Two or more consecutive instructions in the original program order can execute in parallel
  This is the dynamic execution order
N-way Superscalar
  Can issue up to N instructions per cycle
  2-way, 3-way, …
fetch
decode
ld
fetch
decode
add
fetch
decode
sub
fetch
decode
bne

## Slide 10: Data Dependences

## Slide 11: Superscalar vs. Pipelining
loop: ld r2, 10(r1)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
Pipelining:
sum += a[i--]
fetch
decode
ld
fetch
decode
add
fetch
decode
sub
fetch
decode
bne
time
Superscalar:
fetch
decode
ld
fetch
decode
add
fetch
decode
sub
fetch
decode
bne

## Slide 12: Superscalar Performance
Performance Spectrum?
  What if all instructions were dependent?
    Speedup = 0, Superscalar buys us nothing
  What if all instructions were independent?
    Speedup = N where N = superscalarity
Again key is typical program behavior
  Some parallelism exists

## Slide 13: “Real-Life” Performance
OLTP = Online Transaction Processing
SOURCE:
Partha Ranganathan
Kourosh Gharachorloo**
Sarita Adve*
Luiz André Barroso**
Performance of Database Workloads on
Shared-Memory Systems with Out-of-Order
Processors
ASPLOS98

## Slide 14: “Real Life” Performance - Superscalar
SPEC CPU 2000: Simplescalar sim: 32K I$ and D$, 8K bpred

## Slide 15: Issue Mechanism – A Group of Instructions at Decode
Assume 2 source & 1 target max per instr.
  comparators for 2-way:
    3 for tgt and 2 for src (tgt: WAW + WAR, src: RAW)
  comparators for 4-way:
    2nd instr: 3 tgt and 2 src
    3rd instr: 6 tgt and 4 src
    4th instr: 9 tgt and 6 src
tgt
src1
src1
tgt
src1
src1
tgt
src1
src1
simplifications
may be possible
resource checking
not shown
Program order

## Slide 16: Preserving Sequential Semantics
In principle not much different than pipelining
Program order is preserved in the pipeline
Some instructions proceed in parallel
  But order is clearly defined
Defer interrupts to commit stage (i.e., writeback)
  Flush all subsequent instructions
    may include instructions committing simultaneously
  Allow all preceding instructions to commit
Recall comparisons are done in program order
Must have sufficient time in clock cycle to handle these
See next slide

## Slide 17: Interrupts Example
fetch
decode
ld
fetch
decode
add
fetch
decode
div
fetch
decode
bne
Exception
raised
Exception
taken
fetch
decode
bne
fetch
decode
ld
fetch
decode
add
fetch
decode
div
fetch
decode
bne
Exception
raised
Exception
taken
fetch
decode
bne
Exception
raised

## Slide 18: 21164

## Slide 19: Case Study: Alpha 21164

## Slide 20: 21164: Int. Pipe

## Slide 21: 21164: Memory Pipeline

## Slide 22: 21164: Floating-Point Pipe

## Slide 23: Performance Comparison
Source:

## Slide 24: CPI Comparison: Ideal 0.25

## Slide 25: Compiler Impact
Optimized
Base
Performance

## Slide 26: Stall Cycles - 21164
No instructions
Data Dependences/Data Stalls

## Slide 27: Issue Cycle Distribution - 21064

## Slide 28: Issue Cycle Distribution - 21164

## Slide 29: Superscalar/Pipeline challenges
Must have multiple instructions in-flight
  How to find them?
    Branch/Jump instructions
Must fetch multiple instructions

## Slide 30: Instruction Decode/Issue – Alpha 21164 Solution
Up to four insts/cycle
Naturally aligned groups
  Must start at 16 byte boundary (INT16)
  Simplifies Fetch path
CPU needs:
I-Cache:
Where instructions come from?

## Slide 31: Fetching Four Instructions
CPU needs:
I-Cache:
Where instructions come from?
Software must guarantee alignment at 16 byte boundaries
Lots of NOPs

## Slide 32: Instruction Decode/Issue
Up to four insts/cycle
Naturally aligned groups
  Must start at 16 byte boundary (INT16)
  Simplifies Fetch path
All of group must issue before next group gets in
Simplifies Scheduling
  No need for reshuffling

## Slide 33: Good Design Practice
Optimize for the common case
Make sure all cases work correctly
Have a problem
  Think of the ideal solution
    Is it too expensive/complex  may lead to slower clock cycle
  Think of alternatives
    Simpler to implement  may lead to faster clock cycle
  Performance = IPC x Freq
  Reason/measure performance difference
  Which is best?

## Slide 34: Sequential Semantics - Review
Instructions appear as if they executed:
  In “program order”
    As if they executed one after the other
Program
Order
Pipelining
Superscalar
Out-of-Order

## Slide 35: Out-of-Order Execution
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
do {
sum += a[++m];
i--;
} while (i != 0);
out-of-order
loop: add r4, r4, 1
ld r2, 10(r4)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
Superscalar

## Slide 36: Sequential Semantics?
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
Execution does NOT adhere to sequential semantics
To be precise: Eventually it may
Simplest solution:
  Define problem away
  IBM 360 did this
Not acceptable today: e.g., Virtual Memory
Three-phase Instruction execution
  In-Progress, Completed and Committed
inconsistent
consistent

## Slide 37: Preserving Sequential Semantics: Three phases
Instr. exec. in 3 phases:
  In-progress, Completed, Committed
  OOO for in-progress and Completed
  In-order Commits
Completed - out-of-order: ”Visible only inside”
  Results visible to subsequent instructions
  Results not visible to outsiders
    On interrupts completed results are discarded
Committed - in-order: ”Visible to all”
  Results visible to subsequent instructions
  Results visible to outsiders
    On interrupt committed results are preserved

## Slide 38: How Completes Help w/ Performance
Time
DIV R3, _, _
ADD R1, _, _
ADD _, R1, _
In-order
commits
in-order
completes
out-of-order completes
in-order commits
complete
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
commit
commit
commit
commit
commit

## Slide 39: Implementing Completes/Commits
Key idea:
  Maintain sufficient state around to be able to roll-back when necessary
  Roll-back:
    Discard (aka Squash) all not committed
One solution (conceptual): History File
  Upon Complete instruction records previous value of target register
  Upon Discard, instruction restores target value
  Upon Commit, nothing to do
Focus on scheduling mechanisms

## Slide 40: Solution #2: Future File
Two states:
  Architectural
    Updated only on commit
  Speculative
    Updated on complete
Normally use Speculative
On exception:
  Flush Speculative
  Use Architectural
Implementing precise interrupts in pipelined processors
J. E. Smith and A. Pleszkun,
http://www.eecg.toronto.edu/~moshovos/ACA07/readings/smith-interrupts.pdf

## Slide 41: Out-of-Order Execution Overview
Program Form
Processing Phase
Static program
dynamic inst.
Stream (trace)
execution
window
completed
instructions
Dispatch/ dependences
inst. Issue
inst execution
inst. Reorder &
commit
In-Progress
Completed
Committed

## Slide 42: Out-of-Order Execution: Stages
Fetch: get instruction from memory
Decode/Dispatch: what is it? What are the dependences
Issue: go – all dependences satisfied
Execute: perform operation
Complete: result available to other insts.
Commit: result available to outsiders

## Slide 43: OOO Scheduling
Instruction @ Decode:
  Do I have dependences yet to be satisfied?
  Yes, stall until they are
  No, clear to issue
When Do I Wakeup?
  Producer Completes and notifies me
  If All dependences satisfied
  I can proceed
Dependence:
  (later instruction, earlier instruction) & type
We’ll first consider RAW and then move on to WAW and WAR

## Slide 44: Stalling @ Decode for RAW
Are there unsatisfied dependences?
  RAW: have to wait for register value
  We don’t really care who is producing the value
  Only whether it is available
Can use the Register Availability Vector as in pipelining/superscalar
  Also known as scoreboard
At Decode
  Reset bit corresponding to your target
  At writeback set
  Check all bits for source regs: if any is 0 stall

## Slide 45: Issuing Instructions: Scheduling
Determine when an instruction can issue
  Ignore resources for the time being
Stalled because of RAW w/ preceding instruction
Concept:
  Producer (write) notifies consumers (read)
Requirements:
  Consumers need to be able to identify producer
  The register name is one possible link
Mechanism
  Consumer placed in a reservation station
  Producers on complete broadcasts identity
  Waiting instructions observe
  Update Operand Availability
  Issue if all operands now available

## Slide 46: Reservation Station
State pertaining to an instruction
  What registers it reads
  Whether they are available
  What is the destination register
  What state is the instruction in
    Waiting
    Executing

## Slide 47: Out-Of-Order Exec. Example
loop: add r4, r4, 4
ld r2, 10(r4) 4 cycles lat
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
Cycle 0
status

## Slide 48
Out-Of-Order Exec. Example: Cycle 0
1
1
1
0
r1
r2
r3
r4
RAV
op
src1
src2
tgt
Cycle 0
add
r4/1
NA/1
r4/0
Rdy
status
loop: add r4, r4, 4
ld r2, 10(r4)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
Ready to be
executed

## Slide 49
Cycle 1
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Exec
status
ld
r4/1
NA/1
r2
Rdy
R4 gets produced now
Notify those waiting for R4

## Slide 50
Cycle 2
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait

## Slide 51
Cycle 3
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
0
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Rdy
No dependences

## Slide 52
Cycle 4
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Exec
r1 produced now
Notify consumers
bne
r1/1
r0/1
NA
Rdy
r1 will be available next cycle

## Slide 53
Cycle 5
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Exec
executing

## Slide 54
Cycle 6
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
Notify consumers
add
r3/1
r2/1
r3
Rdy
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Exec
executing

## Slide 55
Cycle 7
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Cmtd
Executing
Notify consumers
add
r3/1
r2/1
r3
Exec
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Compl

## Slide 56
Cycle 8
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Cmtd
add
r3/1
r2/1
r3
Cmtd
sub
r1/1
NA/1
r1
Cmtd
bne
r1/1
r0/1
NA
Cmtd

## Slide 57: Window vs. Scheduler
Window
  Distance between oldest and youngest instruction that can co-exist inside the CPU
  Larger window  Potential for more ILP
Scheduler
  Number of instructions that are waiting to be issued
Window
  Instructions enter at Fetch
  Exit at Commit
Scheduler
  Instructions enter at Decode
  Leave at writeback/complete
Window >= Scheduler
  Can be the same structure
In window but not in scheduler  completed
instructions

## Slide 58: Speculative Execution
Why?
  1 every 5 insts is a branch (control flow)
  Today’s processors have a window of 128 insts
  Can’t wait until a branch is resolved to fetch next set of insts
  Solution: Speculate
Fetch branch
Resolve branch
Wrong
squash

## Slide 59: Beyond Simple OoO
A
B
C
D
E
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F2, F7, F4
E will wait for B, C and D.
WAR w/ C and D
WAW w/ B
Can we do better?

## Slide 60: What if we had infinite registers
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F2, F7, F4
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F9, F7, F4
No false dependences anymore
Since we do not reuse a name we can’t have WAW and WAR

## Slide 61: Register Renaming
Register Version
  Every Write creates a new version
  Uses read the last version
  Need to keep a version until all uses have read it.
Register Renaming:
  Architectural vs. Physical Registers
    more phys. than arch.
  Maintain a map of arch. to phys. regs.
  Use in-order decoding to properly identify dependences.
  Instructions wait only for input op. availability.
  Only last version is written to reg. file.

## Slide 62: Register renaming example
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p1

## Slide 63: Register renaming example
First rename input operands:
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p1

## Slide 64: Register renaming example
Then rename destination
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p4
From free list
r1
p2
ROB
For recovery purposes

## Slide 65: Register renaming example
Rename inputs
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p4
From free list
r1
p2
ROB
For recovery purposes

## Slide 66: Register renaming example
Rename destination
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p5
p4
p5
p5
p4
From free list
r1
p2
ROB
For recovery purposes
r3
p3

## Slide 67: MIPS R10000 Pipeline Overview

## Slide 68: MIPS R10000 Architecture

## Slide 69: MIPS R10000 Pipelines

## Slide 70: Instruction Fetch
Must feed core with instructions
  Window is 32
Start with this

## Slide 71: Instruction Fetch
Address translation
Instruction Cache Tags
Instruction Cache Data
Branch Prediction
Instruction buffer
timeline

## Slide 72: Fetching Multiple Instructions?

## Slide 73: Fetching Multiple Instructions & the I-Cache
4 instructions (4 bytes each) out of 32-byte line
  Continuous chunk
  Alignment restrictions also limit possible cases
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
selection/alignment network
to scheduler
i-0
i-1
i-2
i-3

## Slide 74: MIPS R1000 Solution: Fetching 4 continuous insts
5
6
7
8
to scheduler
rotate
0
4
8
12
3
7
11
15
1
5
9
13
2
6
10
14
4 instructions (4 bytes each) out of 16-inst line (64 bytes)
Four banks: read one instruction from each
Calculate addr+0, …, addr+3 and send its MOD 4 to four read ports
  Only one inst. per set per cycle (for up to 4 insts fetched)
Select the 4 words
Then rotate into place
8
7
5
6

## Slide 75: Control Flow
Speculative Branches
  4-entry stack
  4-bit vector one-hot encoding of which is which
    Every instruction tagged with this
  Take snapshot of some structures
    History file – coarse grain
Resolving Branches
  Correct
    Discard entry from stack
    Clear the corresponding bit from all instructions in the pipe
  Incorrect
    Discard all instructions following branch
    Broadcast one-hot encoded branch ID
    Flush everything

## Slide 76: Register Renaming
Doing things early
Reduces critical path
Reorder buffer
From decode
To Scheduler
Link to ROB
Register
Alias
Table
scoreboard

## Slide 77: Scheduler
Reservation
Station
select
WAKEUP
Control Speculation

## Slide 78: Back-to-Back Scheduling

## Slide 79: Optimistic Scheduling
ld r1
add _, r1
F
E
M
D
W
F
E
M
D
W
Cache hit
D
M
E
D
add should start execution here
Must decide that add should execute
Start making scheduling decisions
Hit/miss known here

## Slide 80: Optimistic Scheduling #2
ld r1
add _, r1
F
E
M
D
W
F
E
M
D
W
Cache hit
D
M
E
D
add should start execution here
Must decide that add should execute
Start making scheduling decisions
Hit/miss known here
Guess Hit/Miss

## Slide 81: Data Cache Datapath