## Slide 1: Out-of-Order Execution Structure Optimizations

## Slide 2: Tag Elimination

## Slide 3: Conventional Schedulers are Overdesigned
For MIPS-like ISA
  Two source tags
  One destination tag
Not all instructions use two source operands
  E.g., addi $1, $2, 10
Not all instructions produce a result that is interesting for scheduling
  E.g., beq
Some operands are ready when the instruction enters the scheduler
Source: Efficient Dynamic Scheduling Through Tag Elimination, Dan Ernst and Todd Austin, ISCA 2002

## Slide 4: Some Operands are Ready when the Instruction Enters the Scheduler

## Slide 5: Window Specialization
Have reservation stations with different source operand wait capabilities

## Slide 6: Window Specialization
At rename check how many source operands are not ready
If there is an appropriate slot proceed to schedule
If not, stall at rename
Advantages:
  Destination bus only runs over reservation stations with comparators
  Load on the destination bus is reduced
Disadvantages:
  Stalls due to unavailability of reservation stations
  Complexity of res. Station assignment

## Slide 7: Window Specialization - Performance
Performance as IPC – Actual Clock Frequency not considered

## Slide 8: Window Specialization - Performance
Performance as IPC per ns

## Slide 9: Last Tag Prediction
Observe:
  Instruction becomes ready after the last tag it waits for appears
Last Tag prediction
  Predict which of the two tags will that be
Speculatively execute
  Correct speculation: that was the last tag
  Incorrect speculation:
    Need to reschedule
    Detection? Try to read a value that is not available

## Slide 10: GShare-Style Last Tag Prediction
Two-bit saturating counters

## Slide 11: Accuracy
Over all instructions with two outstanding operands

## Slide 12: Window Specialization - Performance
Performance as IPC – Actual Clock Frequency not considered
Predictive schedulers

## Slide 13: Window Specialization - Performance
Performance as IPC per ns

## Slide 14: Prescheduling
Data-flow prescheduling for large
instruction windows in out-of-order
processors
Pierre Michaud, André Seznec, HPCA 2001

## Slide 15: Prescheduling
Predict latencies
Put scheduled instructions into a FIFO
Slide into a smaller window

## Slide 16: Prescheduling Method

## Slide 17: Prescheduling Example

## Slide 18: Latency Prediction

## Slide 19: Latency Prediction Contd.

## Slide 20: Broadcast Free Scheduler

## Slide 21: Broadcast Free Scheduler
Cyclone design
  D. Ernst, A. Hamel, T. Austin
  ISCA 2003
Preschedule Instructions
Put them into a dual strip cyclical FIFO
Vertical paths allow for motion between the strips

## Slide 22: Cyclone Architecture
Will be ready in cycle + 6

## Slide 23: Cyclone Architecture – Cycle +1

## Slide 24: Cyclone Architecture – Cycle + 2

## Slide 25: Cyclone Architecture – Cycle + 3

## Slide 26: Cyclone Architecture – Cycle + 4

## Slide 27: Cyclone Architecture – Cycle + 5

## Slide 28: Cyclone Architecture – Cycle + 6

## Slide 29: Cyclone Architecture – Cycle + 6

## Slide 30: Cyclone Architecture – Mis-scheduling
Estimate new latency

## Slide 31: Pre-scheduler
Insert instruction with predicted latency N at the front of the FIFO
Have it switch at N/2
Can only do two cascaded MAX calculations
Due to timing considerations

## Slide 32: Cyclone IPC Performance

## Slide 33: Cyclone True Performance and Area

## Slide 34: Matrix Schedulers

## Slide 35: Conventional Scheduler
WS requests
IW grants

## Slide 36: Conventional Scheduler Timing
A2
A2
B1
B1
B3
B3
Source: A High-Speed Dynamic Instruction Scheduling Scheme
for Superscalar Processors
Masahiro Goshima Kengo Nishino Yasuhiko Nakashima Shin-ichiro Mori
Toshiaki Kitamura Shinji Tomita
MICRO 2001
Can’t pipeline without introducing
Bubbles between dependent
Instructions:

## Slide 37: Towards a Matrix Scheduler
Observe:
  In conventional scheduling dependences are discovered twice:
    Once at renaming
    Once during scheduling
  Why? Dependences are implicitly represented
    Producer and Consumer link via a name
    This is indirect
Matrix Scheduler idea:
  Represent dependences explicitly

## Slide 38: Dependence Matrix
Who am I
Who do I depend upon?
Left source
Right source

## Slide 39: Matrix Scheduler
wakeup
Write port
One cell

## Slide 40: Inserting an entry
Write port

## Slide 41: Wakeup
wakeup

## Slide 42: Mispeculation Recovery
Do not cleanup
Use external logic to inhibit request signals

## Slide 43: Delay
Partial wakeup lines
0.18um
1.8V
85C

## Slide 44: Delay measurement points

## Slide 45: Scheduling Priorities

## Slide 46: Conflict Resolution
More instructions ready than available issue slots
  Which get to go?
Age vs. Pseudo-Random Resolution
Age is important
Priority Enforcer picks the oldest
  Complex
Source:
Matrix Scheduler Reloaded
ISCA 2007

## Slide 47: Compacting Scheduler
Implemented in the Alpha 21264
Physical order within scheduler corresponds to age
Entry freed:
  Shift up all younger entries

## Slide 48: Critical Path Prediction
Focusing processor policies via critical-path prediction
B. Fields, S. Rubin and R. Bodik
ISCA 2001
some slides/content from the original presentation

## Slide 49: Instruction Slack
Slack of an instruction:
  How long can we delay the instruction before performance decreases?
It’s zero only for instructions on the critical path
Can be used to tolerate latencies
Work motivation:
  Machines are non-uniform: time, power, etc.
  Need a control policy to tolerate the variance

## Slide 50: Determining slack is hard
“Probe the processor” approach: Delay and observe
  Delay dynamic instruction by n cycles
  See if execution time increased
    No, increase n; restart; go to step 1
Srinivasan and Lebeck approximation, for loads (MICRO ’98)
  heuristics to predict execution time increase
Microprocessors are complex:
Sometimes slack is determined by resources (e.g. ROB)

## Slide 51: Determining slack
  Alternative approach: Dependence-graph analysis
  Build resource-sensitive dependence graph
  Analyze to find slack
Casmira and Grunwald’s solution (Kool Chips Workshop ’00)
Graphs only with instructions in issue window
  But, how to build resource-sensitive graph?

## Slide 52: Data-Dependence Graph
1
1
1
1
1
2
3
Slack = 0 cycles
Misses microarchitectural effects – limited window -- mispredictions

## Slide 53: Data-Dependence Graph
Assume WS = 3
1
1
1
1
1
2
3
Slack = 0 cycles
Misses microarchitectural effects – limited window -- mispredictions
1. Can’t get to this
2. Before fetching this
3.Or retiring this

## Slide 54: Our Dependence Graph Model (ISCA ‘01)
E
E
E
E
E
F
F
F
F
F
C
C
C
C
C
Slack = 0 cycles
F = Fetch synonymous to D = Dispatch in the paper

## Slide 55: Our Dependence Graph Model (ISCA ‘01)
E
1
E
E
E
E
1
1
1
1
2
3
F
F
F
F
F
C
C
C
C
C
1
1
1
1
1
1
1
1
1
1
10
0
0
1
1
0
0
1
Slack = 6 cycles
Modeling resources increases observable slack

## Slide 56: An Example
Wrong path not modeled  validation shows this is an OK approximation

## Slide 57: Validating the Model

## Slide 58: Criticality Breakdown Cases
ROB full ROB Empty
  (1) Exec/Not Committed:
  (2) Executing:
I_(n)
I_(n-1)
I_(0)
I_(0)
oldest
fetching

## Slide 59: Criticality Breakdown
Commit non-critical:
  sits in ROB while there is an ROB stall
  Some other CD edge is critical
  Even if this commits a younger instruction will keep the ROB full long enough to be in the critical path
Execute non-critical:
  Another EE edge is more critical

## Slide 60: Criticality Breakdown

## Slide 61: Determining the Critical Path
All we have to do is observe the order in which edges arrive
Last-arriving edge per instruction:
  Only these can be part of the critical path
What’s the critical path:
  Start at the last instruction
  Traverse backward following last-arriving edges
This is precise but requires keeping all instructions
How about an approximation?

## Slide 62: An Example

## Slide 63: Organization

## Slide 64: An Approximation

## Slide 65: An Example

## Slide 66: Implementation
1. Inst commits
2. Which were the last arriving
edges per node
3. Read out the tokens from the
Source insts per node
4. Write them into this inst’s nodes

## Slide 67: Accuracy

## Slide 68: Performance
Assume originally all insts latencies + 1, reduce critical by 1

## Slide 69: Application #1 – Focused Instruction Steering
Wire delays dominate – can’t build large windows
Solution: clusters
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
DEC’s Alpha 21264

## Slide 70: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
How would assign these?

## Slide 71: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
Clustering: no delay

## Slide 72: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
How about this? Assume not enough resources to place all in the same cluster

## Slide 73: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
Critical path matters

## Slide 74: Application #1 – Focused Instruction Steering
Cluster #1
FE
Cluster #2
Latency: 1 within cluster 2 inter-cluster
Critical path matters

## Slide 75: Focused Steering and Scheduling

## Slide 76: Comparison to heuristic-based Prediction

## Slide 77: Value Prediction
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e

## Slide 78: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'

## Slide 79: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B

## Slide 80: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B
C
b'
D
c'
E
d'

## Slide 81: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B
C
b'
D
c'
E
d'
a
b''
c''
d''
e''

## Slide 82: What if we predict outputs?
Chain of dependent instructions
A
B
D
C
E
a
b
c
d
e
A
a'
B
C
b'
D
c'
E
d'
a
b''
c''
d''
e''
==
==
==
==

## Slide 83: Application #2: Focusing Value Prediction

## Slide 84: Virtual Physical Registers
Physical register names are used for two purposes
  Scheduling
  Communicating
A physical register is held much in advance than needed
  We need the register only after the value is produced
De-couple scheduling from communication names

## Slide 85: Used vs. Allocated Registers

## Slide 86: Goal

## Slide 87: Virtual Physical Registers

## Slide 88: Deadlock
Older instruction completes later than younger ones
  No registers available
Steal a register and re-execute

## Slide 89: Performance vs. Physical Registers