## Slide 1: Tensor Processing Unit ISCA 2017
First two slides text from:
  https://www.slideshare.net/AntoniosKatsarakis/tensor-processing-unit-tpu
  Andreas Moshovos, Advanced Computer Architecture, Winter 2018, U. of Toronto

## Slide 2: Motivation
2006: only a few applications could run on custom H/W (ASIC, FPGA, GPUs) —> thus you could easily find those resources in a datacenter (due to under-utilization)
2013: predictions on the wide applicability of another computational paradigm called Neural Networks (NN), could double the computation demands on datacenters.
It would be very expensive to increase the GPUs in order to satisfy those needs

## Slide 3: Goals
Proposal:
  Design a custom ASIC for the inference phase of NN (training still happens using GPUs)
Principles:
  improve cost-performance by 10X compared to GPUs
  simple design for response time guarantees
  (single-thread, no prefetching, no OOO etc)
Characteristics:
  More like a co-processor to reduce time-to market delays
  Host sends instructions to TPU
  connected through PCIe I/O bus

## Slide 4: This Paper
Overview of the TPU architectufre
Compare to CPU + GPU in a datacenter setting
Not the latest designs but the designs contemporary at the time

## Slide 5: Quantization & Datatypes
Quantization:
  IEEE FP  8bit fixed point
  8b multiply  6x energy-efficiency / 6x area
  8b addition  13x energy-eff. / 38x area

## Slide 6: Target NNs
Multi-level Perceptrons
  Fully-connected layer
Convolutional Networks
  Chain/DAG of Conv/Activation/Pooling/Fully-Connected
Recursive Neural Networks
  LSTM most popular
  Fully-connected + vector

## Slide 7: Models

## Slide 8: Main Take-aways
Inference apps usually emphasize response-time over throughput since they are often user-facing.
Due to latency limits, the K80 GPU is underutilized for inference, and is just a little faster than a Haswell CPU.
A smaller and lower power chip, the TPU has 25X as many MACs and 3.5X as much on-chip memory as the K80 GPU.
The TPU is about 15X - 30X faster at inference than the K80 GPU and the Haswell CPU.

## Slide 9: Main Take-aways #2
Four of the six NN apps are memory-bandwidth limited on the TPU;
  if the TPU were revised to have the same memory system as the K80 GPU, it would be about 30X - 50X faster than the GPU and CPU.
The performance/Watt of the TPU is 30X - 80X that of contemporary products;
  the revised TPU with K80 memory would be 70X - 200X better.
While most architects have been accelerating CNNs, they represent just 5% of our datacenter workload.

## Slide 10: TPU Architecture
All internal buses are 256B wide

## Slide 11: TPU Architecture
Main Block: MMU 256 x 256 MACs, 8b signed or unsigned ints.
256 partial sums per cycle

## Slide 12: TPU Architecture
16bit products accumulated in the Accumulators 

## Slide 13: TPU Architecture
4MiB: 4K x 256 x 32b accumulators (vectors)

## Slide 14: Why 4K vectors in the Accumulators
Calculated for Peak performance;
  Need ~1350
  Rounded that up to 2048
  Double that so that we can have double buffering:
    Reading past results while calculating the next set

## Slide 15: TPU Architecture
MMU: can do mix of 8b, or 16b
½ speed for 8b x 16b, ¼ speed for 16b x 16b

## Slide 16: MMU contd.
Contains 64KiB weights x 2
One tile is the active the other is for double buffering
  Loading the next while calculating with the current one
  Needs 256 cycles to load next one
Can do Matrix Multiply or Convolution
Can read or write 256 values per cycle
Targets Dense networks, Sparse later revisions

## Slide 17: Loading Weights
8GiB off-chip DRAM, Weight FIFO 64KiB x 4

## Slide 18: Activations/Intermediate Results
Unified Buffer: 24MiB, data from/to host CPU
Connects on 16x PCIE 3.0 through Sata interface

## Slide 19: Other Layers
Specialized Units for; Activation Functions, Normalization and
Pooling

## Slide 20: Layout

## Slide 21: CISC Instructions
About a dozen
5 are the most important ones
1. Read_Host_Memory reads data from the CPU host memory into the Unified Buffer (UB).
2. Read_Weights reads weights from Weight Memory into the Weight FIFO as input to the Matrix Unit.
3. MatrixMultiply/Convolve causes the Matrix Unit to perform a matrix multiply or a convolution from the Unified Buffer into the Accumulators.
  A matrix operation takes a variable-sized B*256 input, multiplies it by a 256x256 constant weight input, and produces a B*256 output, taking B pipelined cycles to complete.

## Slide 22: Instructions Contd.
4. Activate performs the nonlinear function of the artificial neuron, with options for ReLU, Sigmoid, and so on. Its inputs are the Accumulators, and its output is the Unified Buffer. It can also perform the pooling operations needed for convolutions using the dedicated hardware on the die, as it is connected to nonlinear function logic.
5. Write_Host_Memory writes data from the Unified Buffer into the CPU host memory.

## Slide 23: Design Philosophy
Keep the Matrix Unit busy
4-stage pipeline
  Instructions can occupy pipeline “stages” for thousands of cycles
Overlap instructions with MatrixMultiply
Read_weights uses access/decoupling

## Slide 24: Systolic Array Approach
Software “thinks” that 256 input data is read once and updates the output accumulators in a single cycle.
In reality, the data propagates as a wave, and values accumulate accordingly

## Slide 25: Hardware Being Compared

## Slide 26: Roofline Model
The closer we are to the roofline the better the machine is utilized

## Slide 27: What’s going on with CNN1?
Half of the cycles doing MACs
Only half of those are active due to shallow feature depths
35% of cycles waiting for weights to load from off-chip

## Slide 28: CPU plot

## Slide 29: GPU Plot

## Slide 30: Combined Roofline Plots

## Slide 31: Performance/Watt

## Slide 32: Scaling