## Slide 1: Introduction to CUDA Programming
CUDA Programming Introduction #2
Andreas Moshovos
Winter 2015
Some slides/material from:
UIUC course by Wen-Mei Hwu and David Kirk
UCSB course by Andrea Di Blas
Universitat Jena by Waqar Saleem
NVIDIA by Simon Green

## Slide 2: Execution Timeline
time
1. Copy to GPU mem
2. Launch GPU Kernel
GPU / Device
2’. Synchronize with GPU
3. Copy from GPU mem
CPU / Host

## Slide 3: Programmer’s view
First create data on CPU memory
CPU
Memory
GPU
GPU Memory

## Slide 4: Programmer’s view
Then Copy to GPU
CPU
Memory
GPU
GPU Memory

## Slide 5: Programmer’s view
GPU starts computation  runs a kernel
CPU can also continue
CPU
Memory
GPU
GPU Memory

## Slide 6: Programmer’s view
CPU and GPU Synchronize
CPU
Memory
GPU
GPU Memory

## Slide 7: Programmer’s view
Copy results back to CPU
CPU
Memory
GPU
GPU Memory

## Slide 8: My first CUDA Program
__global__ void arradd (float *a, float fade, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] * fade;
}
int main()
{
float h[N];
float *d;
cudaMalloc ((void **) &d, SIZE);
cudaThreadSynchronize ();
cudaMemcpy (d, h_a, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d, 10.0, N);
cudaThreadSynchronize ();
cudaMemcpy (h, d, SIZE, cudaMemcpyDeviceToHost));
cudaFree (d);
}
GPU
CPU

## Slide 9: How does a thread know which pixel to process?
blockDim.y
gridDim.y
blockDim.x
gridDim.x
threadIdx.y
threadIdx.x
blockIdx.x
blockIdx.y
x = blockIdx.x * blockDim.x + threadIdx.x
y = blockIdx.y * blockDim.y + threadIdx.y

## Slide 10: GBT: Grids of Blocks of Threads
Why? Realities of integrated circuits:
need to cluster computation and storage to achieve high speeds
Philosophy is:
We’ll tell you about the hardware – you figure out how to make the best of it
Programmers view of data and computation partitioning
Time

## Slide 11: Programmer’s view: Memory Model

## Slide 12: Grids of Blocks of Threads: Dimension Limits
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Grid of Blocks 1D, 2D, or 3D
  Max x, y and z: 65535
Block of Threads: 1D, 2D, or 3D
  Max number of threads: 1024
  Max x: 1024
  Max y: 1024
  Max z: 64
Limits apply to Compute Capability 2.0
  GTX480 = 2.0

## Slide 13: Grids of Blocks of Threads: Dimension Limits
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)
Grid of Blocks 1D, 2D, or 3D
  Max x: 2^32 – 1= 4G
  Max y and z: 2^16 -1 = 65535
Block of Threads: 1D, 2D, or 3D
  Max number of threads: 1024
  Max x: 1024
  Max y: 1024
  Max z: 64
Limits apply to Compute Capability 5.3
  GTX980= 5.3?

## Slide 14: Compute Capability

## Slide 15: Compute Capability

## Slide 16: Thread Batching
A kernel is executed as a grid of thread blocks
  All threads share data memory space
    But cannot communicate through it
A thread block:
Threads that can cooperate with each other by:
  Synchronizing their execution
    For hazard-free shared memory accesses
  Efficiently sharing data through a low latency shared memory
Two threads from two different blocks cannot cooperate
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 17: Thread Coordination Overview
Race-free access to data
Only across threads within the same block
No communication across blocks

## Slide 18: Programmer’s view: Memory Model: Thread vs. Host
Arrows show whether read and/or write is possible

## Slide 19: Memory Model Summary
Memory | Location | Cached | Access | Scope
Local | off-chip | No | R/W | thread
Shared | on-chip | N/A | R/W | all threads in a block
Global | off-chip | Yes | R/W | all threads + host
Constant | off-chip | Yes | RO | all threads + host
Texture | off-chip | Yes | RO | all threads + host

## Slide 20: Memory Model: Global, Constant, and Texture Memories
Global memory
  Main means of communicating R/W Data between host and device
  Contents visible to all threads
  Officially not cached (GTX280)
    Little locality – 3D graphics origin
  GTX480 caches it
  GTX980 caches it
Texture and Constant Memories
  Constants initialized by host
  Contents visible to all threads
  Cached (GTX280)
  GTX980 (cached in L1 same for global)

## Slide 21: Execution Model: Ordering
Execution order is undefined
Do not assume and use:
    block 0 executes before block 1
    Thread 10 executes before thread 20
    And any other ordering even if you can observe it
  Future implementations may break this ordering
  It’s not part of the CUDA definition
  Why? More flexible hardware options

## Slide 22: CUDA Software Architecture
cuda…()
cu…()
e.g., fft()

## Slide 23: Reasoning about CUDA call ordering
GPU communication via cuda…() calls and kernel invocations
  cudaMalloc, cudaMemCpy
Asynchronous from the CPU’s perspective
  CPU places a request in a “CUDA” queue
  requests are handled in-order
Streams allow for multiple queues
  Order within each queue honored
  No order across queues
  More on this much later on

## Slide 24: Execution Model Summary (for your reference)
Grid of blocks of threads
  1D/2D/3D grid of blocks
  1D/2D/3D blocks of threads
All blocks are identical:
  same structure and # of threads
Block execution order is undefined
Same block threads:
  can synchronize and share data fast (shared memory)
Threads from different blocks:
  Cannot cooperate
  Communication through global memory
Threads and Blocks have IDs
  Simplifies data indexing
  Can be 1D, 2D, or 3D (threads)
Blocks do not migrate: execute on the same processor
Several blocks may run over the same processor

## Slide 25: CUDA API: Example
int a[N];
for (i =0; i < N; i++)
  a[i] = a[i] + x;
Allocate CPU Data Structure
Initialize Data on CPU
Allocate GPU Data Structure
Copy Data from CPU to GPU
Define Execution Configuration
Run Kernel
CPU synchronizes with GPU
Copy Data from GPU to CPU
De-allocate GPU and CPU memory

## Slide 26: My first CUDA Program / Skeleton
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + float;
}
int main()
{
float h[N];
float *d;
cudaMalloc ((void **) &d, SIZE);
cudaMemcpy (d, h, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d_a, 10.0, N);
cudaThreadSynchronize ();
cudaMemcpy (h, d, SIZE, cudaMemcpyDeviceToHost));
cudaFree (a_d);
}
GPU
CPU

## Slide 27: 1. Allocate CPU Data container
float *ha;
main (int argc, char *argv[])
{
int N = atoi (argv[1]);
h = (float *) malloc (sizeof (float) * N);
...
}
No memory allocated on the GPU side
Pinned memory allocation results in faster CPU to/from GPU copies
But pinned memory cannot be paged-out
cudaMallocHost (…)
More on this later on

## Slide 28: 2. Initialize CPU Data (dummy)
float *h;
int i;
for (i = 0; i < N; i++)
h[i] = i;

## Slide 29: 3. Allocate GPU Data container
float *d;
cudaMalloc ((void **) &d, sizeof (float) * N);
Notice: no assignment side
  NOT: da = cudaMalloc (…)
Assignment is done internally:
  That’s why we pass &da
Space is allocated in Global Memory on the GPU

## Slide 30: GPU Memory Allocation
The host manages GPU memory allocation:
  cudaMalloc (void **ptr, size_t nbytes)
  Must explicitly cast to (void **)
    cudaMalloc ((void **) &da, sizeof (float) * N);
  cudaFree (void *ptr);
    cudaFree (da);
  cudaMemset (void *ptr, int value, size_t nbytes);
    cudaMemset (da, 0, N * sizeof (int));
Check the CUDA Reference Manual:
  http://docs.nvidia.com/cuda/pdf/CUDA_C_Programming_Guide.pdf

## Slide 31: 4. Copy Initialized CPU data to GPU
float *d;
float *h;
cudaMemCpy ((void *) d, // DESTINATION
(void *) h, // SOURCE
sizeof (float) * N, // #bytes
cudaMemcpyHostToDevice); // DIRECTION

## Slide 32: Host/Device Data Transfers
The host initiates all transfers:
cudaMemcpy( void *dst, void *src, size_t nbytes, enum cudaMemcpyKind direction)
Synchronous from the CPU’s perspective
  CPU thread blocks
    Asynchronous, if less than 64KB, otherwise blocks
  More on this later on
In-order processing with other CUDA requests
enum cudaMemcpyKind
  cudaMemcpyHostToDevice
  cudaMemcpyDeviceToHost
  cudaMemcpyDeviceToDevice

## Slide 33: 5. Define Execution Configuration
How many blocks and threads/block
int threads_block = 64;
int blocks = N / threads_block;
if (blocks % N != 0) blocks += 1;
Alternatively:
blocks = (N + threads_block – 1) / threads_block;

## Slide 34: 6. Launch Kernel & 7. CPU/GPU Synchronization
Instructs the GPU to launch blocks x threads_block threads:
darradd <<<blocks, threads_block>> (d, 10f, N);
cudaThreadSynchronize (); // forces CPU to wait
darradd: kernel name
<<<…>>> execution configuration
(da, x, N): arguments
  256 byte limit / No variable arguments
  Not sure this still applies
Asynchronous, CPU continues

## Slide 35: CPU/GPU Synchronization
CPU does not block on cuda…() calls
  Kernel/requests are queued and processed in-order
  Control returns to CPU immediately
Good if there is other work to be done
  e.g., preparing for the next kernel invocation
Eventually, CPU must know when GPU is done
Then it can safely copy the GPU results
cudaThreadSynchronize ()
  Block CPU until all preceding cuda…() and kernel requests have completed

## Slide 36: 8. Copy data from GPU to CPU & 9. DeAllocate Memory
float *d;
float *h;
cudaMemCpy ((void *) h, // DESTINATION
(void *) d, // SOURCE
sizeof (float) * N, // #bytes
cudaMemcpyDeviceToHost); // DIRECTION
cudaFree (d);
// display or process results here
free (h);

## Slide 37: The GPU Kernel
__global__ darradd (float *d, float x, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) d[i] = d[i] + x;
}
BlockIdx: Unique Block ID.
  Numerically asceding: 0, 1, …
BlockDim: Dimensions of Block = how many threads it has
  BlockDim.x, BlockDim.y, BlockDim.z
  Unused dimensions default to 0
ThreadIdx: Unique per Block Index
  0, 1, …
  Per Block

## Slide 38: CUDA Function Declarations
__global__ defines a kernel function
  Must return void
  Can only call __device__ functions
__device__ and __host__ can be used together
  Two difference versions generated
 | Executed on the: | Only callable from the:
__device__ float DeviceFunc() | device | device
__global__ void KernelFunc() | device | host
__host__ float HostFunc() | host | host

## Slide 39: My first CUDA Program
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + float;
}
int main()
{
float h[N];
float *d;
cudaMalloc ((void **) &d, SIZE);
cudaMemcpy (d, h, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d_a, 10.0, N);
cudaDeviceSynchronize ();
cudaMemcpy (h, d, SIZE, cudaMemcpyDeviceToHost));
cudaFree (a_d);
}
GPU
CPU

## Slide 40: How to get high-performance #1
Programmer managed Scratchpad memory
  Bring data in from global memory
  Reuse
  16KB or 36KB/banked (GTX480/GTX780)
  96KB (GTX980)
  Accessed in parallel by 32 threads
  “shared memory”
Programmer needs to:
  Decide what to bring and when
  Decide which thread accesses what and when
  Coordination paramount

## Slide 41: How to get high-performance #2
Global memory accesses
  32 threads access memory together
  Can coalesce into a single reference
  E.g., a[threadID] works well
Control flow
  32 threads run together
  If they diverge there is a performance penalty

## Slide 42: Textures
Texture cache (GTX480/GTX780)
  When you think there is locality
  Cached in GTX980
Interpolation for free
  Given two values (x, y) and (x’,y’)
  You can ask for (X,Y) between [x,x’] and [y,y’]
Scaling:
  Can use normalized coordinates [0,1]

## Slide 43: Numerical Accuracy
Can do FP
  Mostly OK some minor discrepancies (older0
  No issues with GTX980/GTX780
Can do DP
  1/8 the bandwidth (older)
  GTX980 1/32 (need to double-check this)
Mixed methods
  Break numbers into two single-precision values
Older: Must carefully check for stability/correctness
Is better w/ current generation hardware

## Slide 44: Are GPUs really that much faster than CPUs
50x – 200x speedups typically reported
“Recent” work found
  Not enough effort goes into optimizing code for CPUs
  Intel paper (ISCA 2010)
    http://portal.acm.org/ft_gateway.cfm?id=1816021&type=pdf
But:
  The learning curve and expertise needed for CPUs is much larger
  Then, so is the potential and flexibility

## Slide 45: Material
Programming Massively Parallel Processors: A Hands-on Approach Paperback – Dec 14 2012
by David B. Kirk (Author), Wen-mei W. Hwu (Author)
Heterogeneous Computing with OpenCL 2.0 – May 18 2015
by David R. Kaeli (Author), Perhaad Mistry (Author), Dana Schaa (Author), Dong Ping Zhang (Author)
We’ll cover CUDA for GTX980

## Slide 46: Checking for errors
cudaSuccess variable
cudaPeekAtLastError(void):
  Returns the last error
  Does not change the cudaSuccess value
cudaGetLastError(void0
  Returns the error status
  Clears it

## Slide 47: How to use
#define gpuErrchk(rv) { gpuAssert((rv), __FILE__, __LINE__); }
inline void gpuAssert(cudaError_t code, const char *file, int line, bool abort=true)
{
if (code != cudaSuccess)
{
fprintf(stderr,"GPUassert: %s %s %d\n", cudaGetErrorString(code), file, line);
if (abort) exit(code);
}
}
How to use: gpuErrchk( cudaMalloc(&a_d, size*sizeof(int)) );
From: http://stackoverflow.com/questions/14038589/what-is-the-canonical-way-to-check-for-errors-using-the-cuda-runtime-api

## Slide 48: Kernel Error Checking
kernel<<<1,1>>>(a);
gpuErrchk( cudaPeekAtLastError() );
// check for launch errors
gpuErrchk( cudaDeviceSynchronize() );
gpuErrchk(cudaGetLastError() );
// check for other errors??
Try and let me know

## Slide 49: Measuring Time – Coarse Grain
cudaEvent_t start, stop;
float elapsedTime;
cudaEventCreate(&start);
cudaEventRecord(start,0);
WHAT YOU WANT TO MEASURE
cudaEventCreate(&stop);
cudaEventRecord(stop,0);
cudaEventSynchronize(stop); // wait before printing
cudaEventElapsedTime(&elapsedTime, start,stop);
printf("Elapsed time : %f ms\n" ,elapsedTime);

## Slide 50: Measuring Time: Clock() example
__global__ static void timedkernel(clock_t * timer_start, clock_t *timer_end)
{
tmid = blockIdx.x * blockDim.x + threadIdx.x;
timer_start[tmid] = clock();
do something
timer_end[tmid] = clock();
}
You’ll get one measurement per thread

## Slide 51: Clock() example 2
__global__ static void timedkernel(clock_t * timer_start, clock_t * timer_end)
{
tmid = blockIdx.x;
// first thread in block if (threadIdx.x == 0) timer_start[tmid] = clock();
do something
_syncthreads(); // wait for all threads in block – if you wish to measure all
if (threadIdx.x == 0) timer_end[tmid] = clock();
}
You’ll get one measurement per block
SDK uses a timer array with twice as many elements as blocks
timer_end[] becomes timer[bid+gridDim.x]

## Slide 52: Measurement Methodology
You will not get exactly the same time measurements every time
  Other processes running / external events (e.g., network activity)
  Cannot control
  “Non-determinism”
Must take sufficient samples
  say 10 or more
  There is theory on what the number of samples must be
Measure average

## Slide 53: Introduction to CUDA Programming
Hardware Overview
Andreas Moshovos
Winter 2016
Updated Winter 2009
Updated Winter 2002
Most slides/material from:
UIUC course by Wen-Mei Hwu and David Kirk
Real World Technologies by David Kanter
HotChips 22 Presentation by C. M. Wittenbrink, E. Kilgariff and A. Prabhu

## Slide 54: Our lab systems
All now have GTX980
  Ug51.eecg to ug75.eecg
CUDA 7.0
Debian Jesse
AMD Machines
  Ug81.eecg to ug90.eecg
  Currently off – OS stability – software not hardware

## Slide 55: Programmer’s view of a CPU+GPU system
GPU as a co-processor (data is from 2008)
CPU
Memory
GPU
GPU Memory
1GB on our systems
3GB/s – 8GB.s
6.4GB/sec – 31.92GB/sec
8B per transfer
Our system is 12.8GB/s
177GB/sec
Key Suppliers: Nvidia and AMD
GTX480 characteristics
Top of the line in 2010

## Slide 56: Our Lab Systems: Processor, board and memory
i7 4790 @ 3.6GHz (4Ghz Turbo – one core)
  Launched Q4’14
  Cores: 4, two threads/core
  L1D/L1I: 32/32KB (64B/cycle read 32B/cycle write)
  L2: 256KB
  L3: 8MB
  Mem Bus: 1333Mhz
  45nm, 95W
ASUS Q87M-E
  Intel Q87 Chipset
16GB memory
  No details on bandwidth

## Slide 57: Lab Motherboard

## Slide 58: System Architecture of a Typical PC / Intel (2008)

## Slide 59: Current (2014) Intel System Architecture (desktop)

## Slide 60: PCI-E 1.x Architecture
Switched, point-to-point connection
  Each card has a dedicated “link” to the central switch, no bus arbitration.
  Packet switches messages form virtual channel
  Prioritized packets for QoS
    E.g., real-time video streaming
IO
IO
IO
BUS: PCI or older
NB
IO
IO
IO
NB
PCI-E

## Slide 61: PCI-E
From Wikipedia: By V4711This vector graphics image was created with Adobe Illustrator.
- Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=37527913
Point to point links

## Slide 62: PCI-E
PCI Express version | Line code | Transfer rate[a] | Bandwidth | 
 |  |  | Per lane[a] | In a ×16 (16-lane) slot[a]
1.0 | 8b/10b | 2.5 GT/s | 2 Gbit/s (250 MB/s) | 32 Gbit/s (4 GB/s)
2.0 | 8b/10b | 5 GT/s | 4 Gbit/s (500 MB/s) | 64 Gbit/s (8 GB/s)
3.0 | 128b/130b | 8 GT/s | 7.877 Gbit/s (984.6 MB/s) | 126.032 Gbit/s (15.754 GB/s)
4.0 | 128b/130b | 16 GT/s | 15.754 Gbit/s (1969.2 MB/s) | 252.064 Gbit/s (31.508 GB/s)

## Slide 63: CUDA Refresher
Grids of Blocks
Blocks of Threads
Why? Realities of integrated circuits: need to cluster computation and storage
to achieve high speeds

## Slide 64: Execution model guarantees
Only that threads will execute
Says nothing about the order
Extreme cases:
  #1: All threads run in parallel
  #2: All threads run sequentially
    Interleaving at synchronization points
A CUDA program can run:
  On the CPU
  On a GPU with 1 and on one with N units
    Different models/price points

## Slide 65: Architecture Scalability

## Slide 66: Thread Blocks Refresher
Programmer declares (Thread) Block:
  Block size 1 to 1024 concurrent threads
  Block shape 1D, 2D, or 3D
  Block dimensions in threads
All threads in a Block execute the same thread program
Threads have thread id numbers within Block
Threads share data and synchronize while doing their share of the work
Thread program uses thread id to select work and address shared data
Thread Id #: 0 1 2 3 … m
Thread program

## Slide 67: My first CUDA Program
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + float;
}
int main()
{
float h[N];
float *d;
cudaMalloc ((void **) &d, SIZE);
cudaMemcpy (d, h, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d_a, 10.0, N);
cudaDeviceSynchronize ();
cudaMemcpy (h, d, SIZE, cudaMemcpyDeviceToHost));
cudaFree (a_d);
}
GPU
CPU

## Slide 68: Architecture Goals
Use multithreading to hide DRAM latency
Support fine-grain parallel processing
Virtualize the processors to achieve scalability
  Multiple blocks and threads per processor
Simplify programming.
  Develop program for one thread
Conventional Processors
  Latency optimized
  ILP
  Caches 99% hit rate
GPU
  Caches 90% or less. Not a good option 
  Throughput optimized
  ILP + TLP

## Slide 69: GF100 Specifications
3 Billion Transistors in 40 nm process (TSMC)
Up to 512 CUDA / unified shader cores
384-bit GDDR5 memory interface
6GB capacity
GeForce GTX480: Graphics Enthusiast

## Slide 70: GF100 Architecture Overview -- Compute
64-bit

## Slide 71: GF100 Architecture - Complete
512 CUDA cores
16 PolyMorph Engines
4 raster units
64 texture units
48 ROP units
384-bit GDDR5
  6 channels
  64-bit / channel

## Slide 72: Terminology
SPA
  Streaming Processor Array
TPC
  Texture Processor Cluster
    3 SM + TEX
SM
  Streaming Multiprocessor (32 SP)
  Multi-threaded processor core
  Fundamental processing unit for CUDA thread block
SP
  Streaming Processor
  Scalar ALU for a single CUDA thread

## Slide 73: SM Architecture
Streaming Multiprocessor (SM)
  32 Streaming Processors (SP)
    32 INT or FP (32-bit)
    16 DP (64-bit)
  4 Super Function Units (SFU)
  16 Load/Store Units
Multi-threaded instruction dispatch
  Up to1536 threads active
    32 (threads) x 48
  24,576 threads for all SMs
  Up to 8 concurrent blocks
    1024 threads/block limit
  Shared instruction fetch per 32 threads
  Cover latency of texture/memory loads
80+ GFLOPS
16K/48K KB shared memory
48K/16K L1 cache
DRAM texture and memory access

## Slide 74: Decompose into blocks
float d[X,Y] where X = R * H and Y = C * W
arradd <<< RxC_blocks, HxW_threads >>> (d, 10.0, N);

## Slide 75: Assign Each block to an SMX
Check that there are enough resources
Before assigning
e.g., registers, thread holders

## Slide 76: Decompose a Block into Warps
thread

## Slide 77: Execute Warps onto SMX
thread

## Slide 78: Warp vs. Thread vs. Instructions
Warp is 32 Threads
Each Thread has the same program
Each thread will execute many instructions
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + f;
}

## Slide 79: Understanding Control Flow Divergence
if (in[i] == 0) out[i] = sqrt(x);
else out[i] = 10;
in[i] == 0
out[i] = sqrt(x)
out[i] = 10
in[i] == 0
idle
WARP
TIME

## Slide 80: Control Flow Divergence Contd.
TIME
BAD SCENARIO
in[i] == 0
WARP #1
Good Scenario
in[i] == 0
idle
WARP
in[i] == 0
WARP #2

## Slide 81: Warp Scheduling: Hiding Thread stalls

## Slide 82: Thread Life
Grid is launched on the SPA
Thread Blocks are serially distributed to all the SM’s
  Potentially >1 Thread Block per SM
Each SM launches Warps of Threads
  2 levels of parallelism
SM schedules and executes Warps that are ready to run
As Warps and Thread Blocks complete, resources are freed
  SPA can distribute more Thread Blocks
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 83: Stream Multiprocessors Execute Blocks
Threads are assigned to SMs at Block granularity
  Up to 8 Blocks to each SM as resource allows
  SM in GF100 can take up to 1536 threads
    Could be 256 (threads/block) * 6 blocks
    Could be 512 (threads/block) * 3 blocks, etc.
    At least 192 threads/block to fully utilize an SM
Threads run concurrently
  SM assigns/maintains thread id #s
  SM manages/schedules thread execution

## Slide 84: Thread Scheduling and Execution
Each Thread Blocks is divided in 32-thread Warps
  This is an implementation decision, not part of the CUDA programming model
Warp: primitive scheduling unit
All threads in warp:
  same instruction
  control flow causes some to become inactive
…
t0 t1 t2 … t31
…
…
t0 t1 t2 … t31
…
Block 1 Warps
Block 2 Warps

## Slide 85: Cooperative Thread Array
Break Blocks into warps
Allocate Resources
  Registers, Shared Mem, Barriers
Then allocate for execution

## Slide 86: Warp Scheduling
SM hardware implements zero-overhead Warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a Warp execute the same instruction when selected
2 clock cycles needed to dispatch the same instruction for all threads in a Warp in GF100
warp 8 instruction 11
SM multithreaded
Warp scheduler
warp 1 instruction 42
warp 3 instruction 95
warp 8 instruction 12
. . .
time
warp 3 instruction 96

## Slide 87: How many warps are there?
If 3 blocks are assigned to an SM and
each Block has 256 threads,
how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
  At any point in time, only one of the 24 Warps will be selected for instruction fetch and execution.
    More on this later

## Slide 88: Warp Scheduling Ramifications
If one global memory access is needed for every 4 instructions
  A minimal of 25 Warps are needed to fully tolerate a 200-cycle memory latency
Why?
  Need to hide 200 cycles every four instructions
  Every Warp occupies 2 cycles during which the same instruction executes
  Every 4 insts a thread stalls
  Every 8 cycles a thread stalls
  200/8 =25 or at least 25 warps

## Slide 89: Granularity Considerations: Block & Thread limits per SM
For Matrix Multiplication or any 2D-type of computation, should I use 8X8, 16X16 or 32X32 tiles?
  For 8X8, we have 64 threads per Block.
    Thread/SM limit = 1536 up to 24 Blocks.
    Blocks/SM limit = 8  only 512 threads will go into each SM
  For 16X16, we have 256 threads per Block.
    Thread/SM limit = 1536  up to 6 Blocks.
    Blocks/SM limit = 8  full capacity unless other resource considerations overrule.
  For 32X32, we have 1024 threads per Block.
    Thread/SM limit = 1536  up to 1 Block.
    Blocks/SM limit = 8  Only 1024 threads will go to each SM
  For 64x64, we have 4096 threads per Block.
    Thread/block limit = 1024  Not even one can fit into an SM.

## Slide 90: SM Instruction Buffer – Warp Scheduling (ref)
Fetch one warp instruction/cycle
  from instruction L1 cache
  into any instruction buffer slot
Issue one “ready-to-go” warp instruction/cycle
  from any warp - instruction buffer slot
  operand scoreboarding used to prevent hazards
Issue selection based on round-robin/age of warp: not public
SM broadcasts the same instruction to 32 Threads of a Warp
That’s the theory  warp scheduling may use heuristics
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 91: Maxwell Architecture – GTX980 – GT204
Q4, 2014
28nm
5.2B xtors
398mm^2
PCIE3.0
1.126 Ghz
2048 cores
16 SMs
96KB Shared Memory per SM/2MB L2 cache
Mem bandwidth: 224.3 GB/sec
Compute Capability 5.2

## Slide 92: Maxwell GT204 SMM
Register File: 64K 32-bit
Max regs per thread: 255
Active thread blocks per SM: 32

## Slide 93: GT204 SMM

## Slide 94: GT204 chip

## Slide 95: Scoreboarding (ref)
All register operands of all instructions in the Instruction Buffer are scoreboarded
  Status becomes ready after the needed values are deposited
  prevents hazards
  cleared instructions are eligible for issue
Decoupled Memory/Processor pipelines
  any thread can continue to issue instructions until scoreboarding prevents issue
  allows Memory/Processor ops to proceed in shadow of Memory/Processor ops

## Slide 96: WARP scheduling & scoreboarding
add r1, r2, 10  r1 = r2 + 10
add r3, r1, r1  r3 = r1 + r1
time
Scoreboard[r1] = 0
Scoreboard[r1] = 1
Scoreboard[r1]?
stall

## Slide 97: WARP scheduling & scoreboarding
add r1, r2, 10  r1 = r2 + 10
add r3, r2, r2  r3 = r2 + r2
time
Scoreboard[r1] = 0
Scoreboard[r1] = 1
Scoreboard[r2]?

## Slide 98: SM Architecture Detail
Two 16-thread units
Two warps one per unit
2 cycle per warp
Only one warp for memory
4 SFUs
Only one warp for DFP

## Slide 99: Dual Issue Detail
Image from: http://stanford-cs193g-sp2010.googlecode.com/svn/trunk/lectures/lecture_11/the_fermi_architecture.pdf

## Slide 100: Scalar Units
32 bit ALU and Multiply-Add
IEEE Single-Precision Floating-Point
Integer

## Slide 101: Special Function Units
Transcendental function evaluation and per-pixel attribute interpolation
Function evaluator:
  rcp, rsqrt, log2, exp2, sin, cos approximations
  Uses quadratic interpolation based on Enhanced Minimax Approximation
Latency is 16 cycles
Some are synthesized: 32 cycles or so

## Slide 102: Memory System Goals
High-Bandwidth
As much parallelism as possible
wide. 384 pins in GF100 / Many DRAM chips
fast signalling. max data rate per pin.
maximize utilization
  Multiple bins of memory requests
  Coalesce requests to get as wide as possible
  Goal to use every cycle to transfer from/to memory
Compression: lossless and lossy
Caches where it makes sense. Small

## Slide 103: Optimize Memory Access Ordering for Coalescing
Coalesced Accesses:
  A single access for all requests in a warp
Coalesced vs. Non-coalesced
  Global device memory
    order of magnitude
  Shared memory
    Avoid bank conflicts

## Slide 104: Caching Loads (default)
Warp requests 32 aligned, consecutive 4-byte words
Addresses fall within 1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%

## Slide 105: Caching loads – Permuted accesses
Warp requests 32 aligned, permuted 4-byte words
Addresses fall within 1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%

## Slide 106: Caching Load – misaligned continuous region
Warp requests 32 misaligned, consecutive 4-byte words
Addresses fall within 2 cache-lines
  Warp needs 128 bytes
  256 bytes move across the bus on misses
  Bus utilization: 50%

## Slide 107: Caching Load – One word by all
All threads in a warp request the same 4-byte word
Addresses fall within a single cache-line
  Warp needs 4 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 3.125%

## Slide 108: Caching Load – Worst Case Scatter
Warp requests 32 scattered 4-byte words
Addresses fall within N cache-lines
  Warp needs 128 bytes
  N*128 bytes move across the bus on a miss
  Bus utilization: 128 / (N*128)

## Slide 109: Parallelism in the Memory System
Local Memory: per-thread
  Private per thread
  Auto variables, register spill
Shared Memory: per-Block
  Shared by threads of the same block
  Inter-thread communication
Global Memory: per-application
  Shared by all threads
  Inter-Grid communication
Thread
Local Memory
Grid 0
. . .
Global
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory

## Slide 110: SM Memory Architecture
Threads in a Block share data & results
  In Memory and Shared Memory
  Synchronize at barrier instruction
Per-Block Shared Memory Allocation
  Keeps data close to processor
  Minimize trips to global Memory
  SM Shared Memory dynamically allocated to Blocks, one of the limiting resources

## Slide 111: SM Register File
Register File (RF)
  256KB
  64K 32-bit registers
  Provides 4 operands/clock
TEX pipe can also read/write RF
Load/Store pipe can also read/write RF
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 112: Programmer’s View of Register File
There are 32K registers in each SM in GF100
  This is an implementation decision, not part of CUDA
  Registers are dynamically partitioned across all Blocks assigned to the SM
  Once assigned to a Block, the register is NOT accessible by threads in other Blocks
  Each thread in the same Block only access registers assigned to itself
4 blocks
3 blocks

## Slide 113: Register Use Implications Example
Matrix Multiplication
  Assume there were 16K registers for this example
If each Block has 32X32 threads and each thread uses 10 registers, how many threads can run on each SM?
  Each Block requires 10*32*32 = 10240 registers
  32768= 3 * 10240+ change
  So,3 blocks can run on an SM as far as registers are concerned
How about if each thread increases the use of registers by 1?
  Each Block now requires 11*256 = 11264 registers
  23768 = 2 * 11264
  Only 2 Blocks can run on an SM, 2/3 reduction of parallelism

## Slide 114: Dynamic Partitioning
Dynamic partitioning gives more flexibility to compilers/programmers
  One can run a smaller number of threads that require many registers each or a large number of threads that require few registers each
    This allows for finer grain threading than traditional CPU threading models.
  The compiler can tradeoff between instruction-level parallelism and thread level parallelism

## Slide 115: ILP example
a = a + bmem
c = c + 10 * b
load r1, 0(r3)
add r2, r2, r1
mul r1, r4, 10
add r5, r1, r1
r1 is a temporary
a in r2
b in r4
c in r5
One more register:
load r1, 0(r3)
add r2, r2, r1
mul r6, r4, 10
add r5, r6, r6
Final version:
load r1, 0(r3)
mul r6, r4, 10
add r5, r6, r6
add r2, r2, r1

## Slide 116: Within or Across Thread Parallelism (ILP vs. TLP) (ref)
Assume:
  kernel: 256-thread Blocks
  4 independent instructions for each global memory load,
  thread: 21 registers
  global loads: 400 cycles
  6 Blocks can run on each SM (32K / (256 * 21))
  Need 400 / (4 * 2) 50 Warps to hide latency
  6 Blocks have 256 / 32 x 6 = 48 warps
If a Compiler can use one more register to change the dependence pattern so that 8 independent instructions exist for each global memory load
  Only 5 blocks can run on each SM
  Need 400/(8*2) = 25 Warps to tolerate the memory latency
  Five Blocks have 40 Warps.
  Conclusion: could be better

## Slide 117: How many registers is my kernel using?
NVCC flag: -ptxas-options="-v“
ptxas info : Compiling entry function 'acos_main' ptxas info : Used 4 registers, 60+56 bytes lmem, 44+40 bytes smem, 20 bytes cmem[1], 12 bytes cmem[14]
For shared memory per block:
  44 bytes explicitly allocated by the user
  40 were implicitly allocated by the system/compiler
Lmem:
  local memory per thread
Constant:
  Program variables [1]
  Compiler generated constants [14]
Double-check this please

## Slide 118: CUDA Occupancy Calculator
http://developer.download.nvidia.com/compute/cuda/3_2_prod/sdk/docs/CUDA_Occupancy_Calculator.xls

## Slide 119: Constants
Immediate address constants
Indexed address constants
Constants stored in DRAM, and cached on chip
  L1 per SM
  64KB total in DRAM
A constant value can be broadcast to all threads in a Warp
  Extremely efficient way of accessing a value that is common for all threads in a Block
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 120: Shared Memory
Each SM has 16 KB or 48KB or 96KB of Shared Memory
  32 banks of 32-bit words
CUDA uses Shared Memory as shared storage visible to all threads in a thread block
  read and write access
Not used explicitly for pixel shader programs
  we dislike pixels talking to each other
Key Performance Enhancement
  Move data in Shared memory
  Operate in there
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 121: Shared Memory
In a parallel machine, many threads access memory
  Therefore, memory is divided into banks
  Essential to achieve high bandwidth
Each bank can service one address per two cycles
  A memory can service as many simultaneous accesses as it has banks
Multiple simultaneous accesses to a bank result in a bank conflict
  Conflicting accesses are serialized
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0

## Slide 122: Shared Memory Conflicts
Uses:
  Inter-thread communication within a block
  Cache data to reduce redundant global memory accesses
  Use it to improve global memory access patterns
Organization:
  32 banks, 4-byte wide banks
  Successive 4-byte words belong to different banks
Performance:
  4 bytes per bank per 2 clocks per multiprocessor
  smemaccesses are issued per 32 threads (warp)
    per 16-threads for GPUs prior to Fermi
  serialization: if n threads of 32 access different 4-byte words in the same bank, n accesses are executed serially
  multicast: n threads access the same word in one fetch
    Could be different bytes within the same word
    Prior to Fermi, only broadcast was available, sub-word accesses within the same bank caused serialization

## Slide 123: Shared Memory Accesses
THREAD
WARP EXECUTION
Memory References
Half-Warp

## Slide 124: Bank Addressing Examples
No Bank Conflicts
  Linear addressing stride == 1
No Bank Conflicts
  Random 1:1 Permutation
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 31
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 31
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0

## Slide 125: Bank Addressing Examples
2-way Bank Conflicts
  Linear addressing stride == 2
16-way Bank Conflicts
  Linear addressing stride == 16
Thread 18
Thread 17
Thread 16
Thread 15
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 31
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 16
Bank 15
Bank 31
Bank 14
Bank 2
Bank 1
Bank 0
x8
x8

## Slide 126: How Addresses Map to Banks on G200
Each bank has a bandwidth of 32 bits per clock cycle
Successive 32-bit words are assigned to successive banks
GF100 has 16 banks
  So bank = address % 32
  Same as the size of a warp
    No bank conflicts between different warps, only within a single warp

## Slide 127: How to get high-performance #1
Programmer managed Scratchpad memory
  Bring data in from global memory
  Reuse
  16KB or 48KB /banked
  Accessed in parallel by 16 threads
  “shared memory”
Programmer needs to:
  Decide what to bring and when
  Decide which thread accesses what and when
  Coordination paramount

## Slide 128: How to get high-performance #2
Global memory accesses
  32 threads access memory together
  Can coalesce into a single reference
  E.g., a[threadID] works well
Control flow
  32 threads run together
  If they diverge there is a performance penalty
  Filtering for free