## Slide 1: Introduction to CUDA Programming
Hardware Overview
Andreas Moshovos
Winter 2016
Updated Winter 2009
Updated Winter 2002
Most slides/material from:
UIUC course by Wen-Mei Hwu and David Kirk
Real World Technologies by David Kanter
HotChips 22 Presentation by C. M. Wittenbrink, E. Kilgariff and A. Prabhu

## Slide 2: Our lab systems
All now have GTX980
  Ug51.eecg to ug75.eecg
CUDA 7.0
Debian Jesse
AMD Machines
  Ug81.eecg to ug90.eecg
  Currently off – OS stability – software not hardware

## Slide 3: Programmer’s view of a CPU+GPU system
GPU as a co-processor (data is from 2008)
CPU
Memory
GPU
GPU Memory
6GB on our systems
15.75GB/s
6.4GB/sec – 31.92GB/sec
8B per transfer
Our system is 25.6GB/s
224.3GB/sec
Key Suppliers: Nvidia and AMD
GTX980 characteristics
Top of the line in 2010

## Slide 4: Our Lab Systems: Processor, board and memory
i7 4790 @ 3.6GHz (4Ghz Turbo – one core)
  Launched Q4’14
  Cores: 4, two threads/core
  L1D/L1I: 32/32KB (64B/cycle read 32B/cycle write)
  L2: 256KB
  L3: 8MB
  Mem Bus: 1333Mhz
  45nm, 95W
ASUS Q87M-E
  Intel Q87 Chipset
16GB memory
  No details on bandwidth

## Slide 5: Lab Motherboard

## Slide 6: System Architecture of a Typical PC / Intel (2008)

## Slide 7: Current (2014) Intel System Architecture (desktop)

## Slide 8: PCI-E 1.x Architecture
Switched, point-to-point connection
  Each card has a dedicated “link” to the central switch, no bus arbitration.
  Packet switches messages form virtual channel
  Prioritized packets for QoS
    E.g., real-time video streaming
IO
IO
IO
BUS: PCI or older
NB
IO
IO
IO
NB
PCI-E

## Slide 9: PCI-E
From Wikipedia: By V4711This vector graphics image was created with Adobe Illustrator.
- Own work, CC BY-SA 4.0, https://commons.wikimedia.org/w/index.php?curid=37527913
Point to point links

## Slide 10: PCI-E
PCI Express version | Line code | Transfer rate[a] | Bandwidth | 
 |  |  | Per lane[a] | In a ×16 (16-lane) slot[a]
1.0 | 8b/10b | 2.5 GT/s | 2 Gbit/s (250 MB/s) | 32 Gbit/s (4 GB/s)
2.0 | 8b/10b | 5 GT/s | 4 Gbit/s (500 MB/s) | 64 Gbit/s (8 GB/s)
3.0 | 128b/130b | 8 GT/s | 7.877 Gbit/s (984.6 MB/s) | 126.032 Gbit/s (15.754 GB/s)
4.0 | 128b/130b | 16 GT/s | 15.754 Gbit/s (1969.2 MB/s) | 252.064 Gbit/s (31.508 GB/s)

## Slide 11: CUDA Refresher
Grids of Blocks
Blocks of Threads
Why? Realities of integrated circuits: need to cluster computation and storage
to achieve high speeds

## Slide 12: Execution model guarantees
Only that threads will execute
Says nothing about the order
Extreme cases:
  #1: All threads run in parallel
  #2: All threads run sequentially
    Interleaving at synchronization points
A CUDA program can run:
  On the CPU
  On a GPU with 1 and on one with N units
    Different models/price points

## Slide 13: Architecture Scalability

## Slide 14: Thread Blocks Refresher
Programmer declares (Thread) Block:
  Block size 1 to 1024 concurrent threads
  Block shape 1D, 2D, or 3D
  Block dimensions in threads
All threads in a Block execute the same thread program
Threads have thread id numbers within Block
Threads share data and synchronize while doing their share of the work
Thread program uses thread id to select work and address shared data
Thread Id #: 0 1 2 3 … m
Thread program

## Slide 15: My first CUDA Program
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + float;
}
int main()
{
float h[N];
float *d;
cudaMalloc ((void **) &d, SIZE);
cudaMemcpy (d, h, SIZE, cudaMemcpyHostToDevice));
arradd <<< n_blocks, block_size >>> (d, 10.0, N);
cudaDeviceSynchronize ();
cudaMemcpy (h, d, SIZE, cudaMemcpyDeviceToHost));
cudaFree (a);
}
GPU
CPU

## Slide 16: Architecture Goals
Use multithreading to hide DRAM latency
Support fine-grain parallel processing
Virtualize the processors to achieve scalability
  Multiple blocks and threads per processor
Simplify programming.
  Develop program for one thread
Conventional Processors
  Latency optimized
  ILP
  Caches 99% hit rate
GPU
  Caches 90% or less. Not a good option 
  Throughput optimized
  ILP + TLP

## Slide 17: GF100 Specifications
3 Billion Transistors in 40 nm process (TSMC)
Up to 512 CUDA / unified shader cores
384-bit GDDR5 memory interface
6GB capacity
GeForce GTX480: Graphics Enthusiast

## Slide 18: GF100 Architecture Overview -- Compute
64-bit

## Slide 19: GF100 Architecture - Complete
512 CUDA cores
16 PolyMorph Engines
4 raster units
64 texture units
48 ROP units
384-bit GDDR5
  6 channels
  64-bit / channel

## Slide 20: Terminology
SPA
  Streaming Processor Array
TPC
  Texture Processor Cluster
    3 SM + TEX
SM
  Streaming Multiprocessor (32 SP)
  Multi-threaded processor core
  Fundamental processing unit for CUDA thread block
SP
  Streaming Processor
  Scalar ALU for a single CUDA thread

## Slide 21: SM Architecture
Streaming Multiprocessor (SM)
  32 Streaming Processors (SP)
    32 INT or FP (32-bit)
    16 DP (64-bit)
  4 Super Function Units (SFU)
  16 Load/Store Units
Multi-threaded instruction dispatch
  Up to 1536 threads active
    32 (threads) x 48
  24,576 threads for all SMs
  Up to 8 concurrent blocks
    1024 threads/block limit
  Shared instruction fetch per 32 threads
  Cover latency of texture/memory loads
80+ GFLOPS
16K/48K KB shared memory
48K/16K L1 cache
DRAM texture and memory access

## Slide 22: Decompose into blocks
float d[X,Y] where X = R * H and Y = C * W
arradd <<< RxC_blocks, HxW_threads >>> (d, 10.0, N);

## Slide 23: Assign Each block to an SMX
Check that there are enough resources
Before assigning
e.g., registers, thread holders

## Slide 24: Decompose a Block into Warps
thread
Warp = group of threads
0 – 31
32 – 63
64 – 95
…

## Slide 25: Execute Warps onto SMX
thread

## Slide 26: Warp vs. Thread vs. Instructions
Warp is 32 Threads
Each Thread has the same program
Each thread will execute many instructions
__global__ void arradd (float *a, float f, int N)
{
int i = blockIdx.x * blockDim.x + threadIdx.x;
if (i < N) a[i] = a[i] + f;
}

## Slide 27: Understanding Control Flow Divergence
if (in[i] == 0) out[i] = sqrt(x);
else out[i] = 10;
in[i] == 0
out[i] = sqrt(x)
out[i] = 10
in[i] == 0
idle
WARP
TIME

## Slide 28: Control Flow Divergence Contd.
TIME
BAD SCENARIO
in[i] == 0
WARP #1
Good Scenario
in[i] == 0
idle
WARP
in[i] == 0
WARP #2

## Slide 29: What if a thread stalls?
Thread 0 loads from memory:

## Slide 30: Warp Scheduling: Hiding Latencies

## Slide 31: Warp Scheduling: Hiding Thread stalls

## Slide 32: Thread Life
Grid is launched on the SPA
Thread Blocks are serially distributed to all the SM’s
  Potentially >1 Thread Block per SM
Each SM launches Warps of Threads
  2 levels of parallelism
SM schedules and executes Warps that are ready to run
As Warps and Thread Blocks complete, resources are freed
  SPA can distribute more Thread Blocks
Host
Kernel 1
Kernel 2
Device
Grid 1
Block
(0, 0)
Block
(1, 0)
Block
(2, 0)
Block
(0, 1)
Block
(1, 1)
Block
(2, 1)
Grid 2
Block (1, 1)
Thread
(0, 1)
Thread
(1, 1)
Thread
(2, 1)
Thread
(3, 1)
Thread
(4, 1)
Thread
(0, 2)
Thread
(1, 2)
Thread
(2, 2)
Thread
(3, 2)
Thread
(4, 2)
Thread
(0, 0)
Thread
(1, 0)
Thread
(2, 0)
Thread
(3, 0)
Thread
(4, 0)

## Slide 33: Stream Multiprocessors Execute Blocks
Threads are assigned to SMs at Block granularity
  Up to 8 Blocks to each SM as resource allows
  SM in GF100 can take up to 1536 threads
    Could be 256 (threads/block) * 6 blocks
    Could be 512 (threads/block) * 3 blocks, etc.
    At least 192 threads/block to fully utilize an SM
For GTX980
  Up to 32 blocks per SM
  Up to 2048 threads per SM
Threads run concurrently
  SM assigns/maintains thread id #s
  SM manages/schedules thread execution

## Slide 34: Cooperative Thread Array
Break Blocks into warps
Allocate Resources
  Registers, Shared Mem, Barriers
Then allocate for execution

## Slide 35: Warp Scheduling
SM hardware implements zero-overhead Warp scheduling
  Warps whose next instruction has its operands ready for consumption are eligible for execution
  Eligible Warps are selected for execution on a prioritized scheduling policy
  All threads in a Warp execute the same instruction when selected
2 clock cycles needed to dispatch the same instruction for all threads in a Warp in GF100 (older)
GTX980: single cycle per warp
warp 8 instruction 11
SM multithreaded
Warp scheduler
warp 1 instruction 42
warp 3 instruction 95
warp 8 instruction 12
. . .
time
warp 3 instruction 96

## Slide 36: How many warps are there?
If 3 blocks are assigned to an SM and
Each Block has 256 threads,
how many Warps are there in an SM?
  Each Block is divided into 256/32 = 8 Warps
  There are 8 * 3 = 24 Warps
  At any point in time, only one of the 24 Warps will be selected for instruction fetch and execution.
    More on this later

## Slide 37: Warp Scheduling Ramifications
If one global memory access is needed for every 4 instructions
  A minimal of 25 Warps are needed to fully tolerate a 200-cycle memory latency (older hardware)
Why?
  Need to hide 200 cycles every four instructions
  Every Warp occupies 2 cycles during which the same instruction executes (Older Hardware)
  Every 4 insts a thread stalls
  Every 8 cycles a thread stalls
  200/8 =25 or at least 25 warps

## Slide 38: Warp Scheduling Ramifications
If one global memory access is needed for every 4 instructions
  A minimal of 50 Warps are needed to fully tolerate a 200-cycle memory latency (older hardware)
Why?
  Need to hide 200 cycles every four instructions
  Every Warp occupies 1 cycle during which the same instruction executes
  Every 4 insts a thread stalls
  Every 4 cycles a thread stalls
  200/4 = 50 or at least 50 warps

## Slide 39: Granularity Considerations: Block & Thread limits per SM
For Matrix Multiplication or any 2D-type of computation, should I use 8X8, 16X16 or 32X32 tiles?
Older hardware
  For 8X8, we have 64 threads per Block.
    Thread/SM limit = 2048 up to 24 Blocks.
    Blocks/SM limit = 8  only 512 threads will go into each SM
  For 16X16, we have 256 threads per Block.
    Thread/SM limit = 1536  up to 6 Blocks.
    Blocks/SM limit = 8  full capacity unless other resource considerations overrule.
  For 32X32, we have 1024 threads per Block.
    Thread/SM limit = 1536  up to 1 Block.
    Blocks/SM limit = 8  Only 1024 threads will go to each SM
  For 64x64, we have 4096 threads per Block.
    Thread/block limit = 1024  Not even one can fit into an SM.

## Slide 40: Granularity Considerations: Block & Thread limits per SM
For Matrix Multiplication or any 2D-type of computation, should I use 8X8, 16X16 or 32X32 tiles?
  For 8X8, we have 64 threads per Block.
    Thread/SM limit = 2048  up to 32 Blocks.
    Blocks/SM limit = 32  2048 threads unless other resource considerations overrule.
  For 16X16, we have 256 threads per Block.
    Thread/SM limit = 2048  up to 16 Blocks.
    Blocks/SM limit = 32  2048 threads unless other resource considerations overrule.
  For 32X32, we have 1024 threads per Block.
    Thread/SM limit = 2048  up to 2 Blocks.
    Blocks/SM limit = 32  Only 2048 threads will go to each SM
  For 64x64, we have 4096 threads per Block.
    Thread/block limit = 2048  Not even one can fit into an SM.

## Slide 41: SM Instruction Buffer – Warp Scheduling (ref)
Fetch one warp instruction/cycle
  from instruction L1 cache
  into any instruction buffer slot
Issue one “ready-to-go” warp instruction/cycle
  from any warp - instruction buffer slot
  operand scoreboarding used to prevent hazards
Issue selection based on round-robin/age of warp: not public
SM broadcasts the same instruction to 32 Threads of a Warp
That’s the theory  warp scheduling may use heuristics
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 42: Maxwell Architecture – GTX980 – GT204
Q4, 2014
28nm
5.2B xtors
398mm^2
PCIE3.0
1.126 Ghz
2048 cores
16 SMs
96KB Shared Memory per SM/2MB L2 cache
Mem bandwidth: 224.3 GB/sec
Compute Capability 5.2

## Slide 43: Maxwell GT204 SMM
Register File: 64K 32-bit
Max regs per thread: 256
Active thread blocks per SM: 32
Max Shared Memory Per Block: 48K

## Slide 44: GT204 SMM

## Slide 45: GT204 chip

## Slide 46: Scoreboarding (ref)
All register operands of all instructions in the Instruction Buffer are scoreboarded
  Status becomes ready after the needed values are deposited
  prevents hazards
  cleared instructions are eligible for issue
Decoupled Memory/Processor pipelines
  any thread can continue to issue instructions until scoreboarding prevents issue
  allows Memory/Processor ops to proceed in shadow of Memory/Processor ops

## Slide 47: WARP scheduling & scoreboarding
add r1, r2, 10  r1 = r2 + 10
add r3, r1, r1  r3 = r1 + r1
time
Scoreboard[r1] = 0
Scoreboard[r1] = 1
Scoreboard[r1]?
stall

## Slide 48: WARP scheduling & scoreboarding
add r1, r2, 10  r1 = r2 + 10
add r3, r2, r2  r3 = r2 + r2
time
Scoreboard[r1] = 0
Scoreboard[r1] = 1
Scoreboard[r2]?

## Slide 49: SM Architecture Detail
Two 16-thread units
Two warps one per unit
2 cycle per warp
Only one warp for memory
4 SFUs
Only one warp for DFP

## Slide 50: Dual Issue Detail
Image from: http://stanford-cs193g-sp2010.googlecode.com/svn/trunk/lectures/lecture_11/the_fermi_architecture.pdf

## Slide 51: Functional Units/Execution Bandwidth

## Slide 54: Scalar Units
32 bit ALU and Multiply-Add
IEEE Single-Precision Floating-Point
Integer

## Slide 55: Special Function Units
Transcendental function evaluation and per-pixel attribute interpolation
Function evaluator:
  rcp, rsqrt, log2, exp2, sin, cos approximations
  Uses quadratic interpolation based on Enhanced Minimax Approximation
Latency is 16 cycles
Some are synthesized: 32 cycles or so

## Slide 56: Memory System Goals
High-Bandwidth
As much parallelism as possible
wide. 384 pins in GF100 / Many DRAM chips
fast signalling. max data rate per pin.
maximize utilization
  Multiple bins of memory requests
  Coalesce requests to get as wide as possible
  Goal to use every cycle to transfer from/to memory
Compression: lossless and lossy
Caches where it makes sense. Small

## Slide 57: Optimize Memory Access Ordering for Coalescing
Coalesced Accesses:
  A single access for all requests in a warp
Coalesced vs. Non-coalesced
  Global device memory
    order of magnitude
  Shared memory
    Avoid bank conflicts

## Slide 58: Caching Loads (default)
Warp requests 32 aligned, consecutive 4-byte words
Addresses fall within 1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%

## Slide 59: Caching loads – Permuted accesses
Warp requests 32 aligned, permuted 4-byte words
Addresses fall within 1 cache-line
  Warp needs 128 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 100%

## Slide 60: Caching Load – misaligned continuous region
Warp requests 32 misaligned, consecutive 4-byte words
Addresses fall within 2 cache-lines
  Warp needs 128 bytes
  256 bytes move across the bus on misses
  Bus utilization: 50%

## Slide 61: Caching Load – One word by all
All threads in a warp request the same 4-byte word
Addresses fall within a single cache-line
  Warp needs 4 bytes
  128 bytes move across the bus on a miss
  Bus utilization: 3.125%

## Slide 62: Caching Load – Worst Case Scatter
Warp requests 32 scattered 4-byte words
Addresses fall within N cache-lines
  Warp needs 128 bytes
  N*128 bytes move across the bus on a miss
  Bus utilization: 128 / (N*128)

## Slide 63: Parallelism in the Memory System
Local Memory: per-thread
  Private per thread
  Auto variables, register spill
Shared Memory: per-Block
  Shared by threads of the same block
  Inter-thread communication
Global Memory: per-application
  Shared by all threads
  Inter-Grid communication
Thread
Local Memory
Grid 0
. . .
Global
Memory
. . .
Grid 1
Sequential
Grids
in Time
Block
Shared
Memory

## Slide 64: SM Memory Architecture
Threads in a Block share data & results
  In Memory and Shared Memory
  Synchronize at barrier instruction
Per-Block Shared Memory Allocation
  Keeps data close to processor
  Minimize trips to global Memory
  SM Shared Memory dynamically allocated to Blocks, one of the limiting resources

## Slide 65: SM Register File
Register File (RF)
  256KB
  64K 32-bit registers
  Provides 4 operands/clock
TEX pipe can also read/write RF
Load/Store pipe can also read/write RF
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 66: Programmer’s View of Register File
There are 32K registers in each SM in GF100
  This is an implementation decision, not part of CUDA
  Registers are dynamically partitioned across all Blocks assigned to the SM
  Once assigned to a Block, the register is NOT accessible by threads in other Blocks
  Each thread in the same Block only access registers assigned to itself
4 blocks
3 blocks

## Slide 67: Register Use Implications Example
Matrix Multiplication
  Assume there were 16K registers for this example
If each Block has 32X32 threads and each thread uses 10 registers, how many threads can run on each SM?
  Each Block requires 10*32*32 = 10240 registers
  32768= 3 * 10240+ change
  So,3 blocks can run on an SM as far as registers are concerned
How about if each thread increases the use of registers by 1?
  Each Block now requires 11*256 = 11264 registers
  23768 = 2 * 11264
  Only 2 Blocks can run on an SM, 2/3 reduction of parallelism

## Slide 68: Dynamic Partitioning
Dynamic partitioning gives more flexibility to compilers/programmers
  One can run a smaller number of threads that require many registers each or a large number of threads that require few registers each
    This allows for finer grain threading than traditional CPU threading models.
  The compiler can tradeoff between instruction-level parallelism and thread level parallelism

## Slide 69: ILP example
a = a + bmem
c = c + 10 * b
load r1, 0(r3)
add r2, r2, r1
mul r1, r4, 10
add r5, r1, r1
r1 is a temporary
a in r2
b in r4
c in r5
One more register:
load r1, 0(r3)
add r2, r2, r1
mul r6, r4, 10
add r5, r6, r6
Final version:
load r1, 0(r3)
mul r6, r4, 10
add r5, r6, r6
add r2, r2, r1

## Slide 70: Within or Across Thread Parallelism (ILP vs. TLP) (ref)
Assume:
  kernel: 256-thread Blocks
  4 independent instructions for each global memory load,
  thread: 21 registers
  global loads: 400 cycles
  6 Blocks can run on each SM (32K / (256 * 21))
  Need 400 / (4 * 2) 50 Warps to hide latency
  6 Blocks have 256 / 32 x 6 = 48 warps
If a Compiler can use one more register to change the dependence pattern so that 8 independent instructions exist for each global memory load
  Only 5 blocks can run on each SM
  Need 400/(8*2) = 25 Warps to tolerate the memory latency
  Five Blocks have 40 Warps.
  Conclusion: could be better

## Slide 71: How many registers is my kernel using?
NVCC flag: -ptxas-options="-v“
ptxas info : Compiling entry function 'acos_main' ptxas info : Used 4 registers, 60+56 bytes lmem, 44+40 bytes smem, 20 bytes cmem[1], 12 bytes cmem[14]
For shared memory per block:
  44 bytes explicitly allocated by the user
  40 were implicitly allocated by the system/compiler
Lmem:
  local memory per thread
Constant:
  Program variables [1]
  Compiler generated constants [14]
Double-check this please

## Slide 72
__global__ void __launch_bounds__(maxThreadsPerBlock, minBlocksPerMultiprocessor) MyKernel(...) { ... }

## Slide 73: CUDA Occupancy Calculator
http://developer.download.nvidia.com/compute/cuda/3_2_prod/sdk/docs/CUDA_Occupancy_Calculator.xls

## Slide 74: Constants
Immediate address constants
Indexed address constants
Constants stored in DRAM, and cached on chip
  L1 per SM
  64KB total in DRAM
A constant value can be broadcast to all threads in a Warp
  Extremely efficient way of accessing a value that is common for all threads in a Block
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 75: Shared Memory
Each SM has 16 KB or 48KB or 96KB of Shared Memory
  32 banks of 32-bit words
CUDA uses Shared Memory as shared storage visible to all threads in a thread block
  read and write access
Not used explicitly for pixel shader programs
  we dislike pixels talking to each other
Key Performance Enhancement
  Move data in Shared memory
  Operate in there
I
$
L
1
Multithreaded
Instruction Buffer
R
F
C
$
L
1
Shared
Mem
Operand Select
MAD
SFU

## Slide 76: Shared Memory
In a parallel machine, many threads access memory
  Therefore, memory is divided into banks
  Essential to achieve high bandwidth
Each bank can service one address per two cycles
  A memory can service as many simultaneous accesses as it has banks
Multiple simultaneous accesses to a bank result in a bank conflict
  Conflicting accesses are serialized
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0

## Slide 77: Shared Memory Conflicts
Uses:
  Inter-thread communication within a block
  Cache data to reduce redundant global memory accesses
  Use it to improve global memory access patterns
Organization:
  32 banks, 4-byte wide banks
  Successive 4-byte words belong to different banks
Performance:
  4 bytes per bank per 2 clocks per multiprocessor
  smemaccesses are issued per 32 threads (warp)
    per 16-threads for GPUs prior to Fermi
  serialization: if n threads of 32 access different 4-byte words in the same bank, n accesses are executed serially
  multicast: n threads access the same word in one fetch
    Could be different bytes within the same word
    Prior to Fermi, only broadcast was available, sub-word accesses within the same bank caused serialization

## Slide 78: Shared Memory Accesses
THREAD
WARP EXECUTION
Memory References
Half-Warp

## Slide 79: Bank Addressing Examples
No Bank Conflicts
  Linear addressing stride == 1
No Bank Conflicts
  Random 1:1 Permutation
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 31
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 31
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0

## Slide 80: Bank Addressing Examples
2-way Bank Conflicts
  Linear addressing stride == 2
16-way Bank Conflicts
  Linear addressing stride == 16
Thread 18
Thread 17
Thread 16
Thread 15
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 31
Bank 7
Bank 6
Bank 5
Bank 4
Bank 3
Bank 2
Bank 1
Bank 0
Thread 31
Thread 7
Thread 6
Thread 5
Thread 4
Thread 3
Thread 2
Thread 1
Thread 0
Bank 16
Bank 15
Bank 31
Bank 14
Bank 2
Bank 1
Bank 0
x8
x8

## Slide 81: How Addresses Map to Banks on G200
Each bank has a bandwidth of 32 bits per clock cycle
Successive 32-bit words are assigned to successive banks
GF100 has 16 banks
  So bank = address % 32
  Same as the size of a warp
    No bank conflicts between different warps, only within a single warp

## Slide 82: How to get high-performance #1
Programmer managed Scratchpad memory
  Bring data in from global memory
  Reuse
  16KB or 48KB /banked
  Accessed in parallel by 16 threads
  “shared memory”
Programmer needs to:
  Decide what to bring and when
  Decide which thread accesses what and when
  Coordination paramount

## Slide 83: How to get high-performance #2
Global memory accesses
  32 threads access memory together
  Can coalesce into a single reference
  E.g., a[threadID] works well
Control flow
  32 threads run together
  If they diverge there is a performance penalty
  Filtering for free