## Slide 1: A Vulnerability-Tolerant Secure Architecture Based on Ensembles of Moving Target Defenses with Churn
M. Gallagher, L. Biernacki, S. Chen, Z.B. Aweke, S.F. Yitbarek, M.T. Aga, A. Harris, Z. Xu, B. Kasikci, V. Bertacco, S. Malik, M. Tiwari, T. Austin
ASPLOS 2019 – Security II – 2019.04.16
1

## Slide 2: A Vulnerability-Tolerant Secure Architecture Based on Ensembles of Moving Target Defenses with Churn
M. Gallagher, L. Biernacki, S. Chen, Z.B. Aweke, S.F. Yitbarek, M.T. Aga, A. Harris, Z. Xu, B. Kasikci, V. Bertacco, S. Malik, M. Tiwari, T. Austin
ASPLOS 2019 – Security II – 2019.04.16
2

## Slide 3: Secure System Design Now
Secure design “loop”:
  For-each vulnerability:
  Attackers exploit vulnerability
  Defenders patch vulnerability
List of vulnerabilities increasing…
Not typically possible to prove security against all vulnerabilities
:(
Notes: Attackers finding more ways in (CVE database growing)
How to be vulnerability-tolerant

## Slide 4: Characteristics of Exploits
Benign programs may have vulnerabilities 
Defenses need to be vulnerability-tolerant
Vulnerabilities + Information Assets = Exploit
Attackers use internal program assets:
  Byproduct of system implementation
  Usually not relied-on by programmers

## Slide 5: Exploits: Abusing Program Assets
0xdeadbeef
gg ez game
Benign Use-Case
char buf[30];
strcpy(buf, arg);
arg = “gg ez game”
Stack
Return Addr.
buf
Notes: - Seen this example “beef beaten to death….deadbeef”
- Vulnerability: unchecked call: strcpy() doesn’t know length of buffer

## Slide 6: Exploits: Abusing Program Assets
Malicious Use-Case
char buf[30];
strcpy(buf, arg);
arg = “AAAAA…\xf0\x01\x01\x00”
Address of target()
Stack
buf
0xdeadbeef
0xf0010100
AAAAAA …
… AAAAA
AAAAAAAAAAAAAA
Return Addr.
buf
Information Assets:
Location of target()
Pointer Representation

## Slide 7: Semantics
Program-level: defined used by programmers.
Undefined: not explicitly documented, often properties of the implementation:
  Out-of-bounds array accesses, uninitialized values, execution timing, micro-arch sharing characteristics (think cache)
Programs use the program-level and typically not the undefined ones
  Sometimes they do use the undefined ones too.
Goal:
keep well-defined semantics as such and randomize undefined semantics.

## Slide 8: Protecting Information Assets
An Approach:
Randomize assets
Moving Target Defenses (MTDs)
Load-time MTDs: 64-bit ASLR, ISR, …
Attackers defeat load-time MTDs with Derandomization Attacks
 Load-Time MTDs have LOW durability
Notes: - Control-flow attacks
- Derandomization // Side-Channel

## Slide 9: ASLR attacks

## Slide 10: Protecting Information Assets
An Approach:
Randomize assets
Moving Target Defenses (MTDs)
Load-time MTDs: 64-bit ASLR, ISR, …
Attackers defeat load-time MTDs with Derandomization Attacks
 Load-Time MTDs have LOW durability
Morpheus uses H/W‐supported re‐randomization (Churn) to give high‐entropy MTDs better durability
Notes: - High durability with churn + high entropy

## Slide 11: Attacks vs. (Re-)Randomization
Probe
Weaponize
Attack
Probe
Weaponize
Attack
…
t
Load-time
MTDs
Re-Randomized
MTDs
(Churn)
No MTDs
Probe
Probe
!
Probe
!
Probe
!
Probe
!
!
…

## Slide 12: Context/Goal
a trusted but vulnerable victim program processes untrusted inputs that exploit memory errors to hijack control-flow of the victim.
make use of buffer overflows, format-string, heap-spray, double-free, return/jump-oriented programming, and other execution-level semantics to override language-level protections and hijack control flow.
Denial-of-service (DoS) and side-channel attacks, while good future targets for Morpheus, are outside the scope of this work

## Slide 13: Assumptions
We assume the following about the attacker:
i)they can-not physically threaten the system via power analysis, fault injection,etc.;
ii)they cannot manipulate the system’s boot sequence or anticipate the output of the random number generator;
iii)they interact with the system via an interface such as the network or keyboard;
iv)they cannot modify the original binary;
v)they are able to locate a memory corruption or disclosure vulnerability in the target program to exploit.

## Slide 14
Morpheus Architecture
Evaluations
Parting Thoughts
Introduction

## Slide 15
Introduction
Parting Thoughts
Morpheus Architecture
Evaluations

## Slide 16: Morpheus: Ensemble of MTDs
Churn
Encryption
Displacement
Tagged Memory
Code
Code Ptrs
Data Ptrs
Encryption:
Obfuscate information assets
Displacement:
Shift code & data segments
Information Assets
EMTD
Notes: When do we churn?

## Slide 17: Defense #1
Change the mapping of virtual addresses as seen by the program
  +OFFSET to addresses
    DATA
    CODE
  The offsets are different per program
    Attacker cannot easily guess where a code or data may be placed
    Not easy to find out what the pointer should be
buf
0xdeadbeef
0xf0010100
AAAAAA …
… AAAAA
AAAAAAAAAAAAAA
Return Addr.
buf

## Slide 18: Displacement
Introduces entropy to Code & Data location
Shift address space into 2 independent spaces
  Add d, a 60 bit displacement, to pointers
VAS
Data
Code
DASD
Data
DASC
Code
Data
dDATA
dCODE
64-bit Space
48-bit Space

## Slide 19: How do we know smth is a PTR?
Domain Tagging
And PTR updates

## Slide 20: Domain Tagging
Four distinct domains/ uses 2b domain tags:
code (C), code pointers(CP), data pointers (DP), and other data (D).
The pipeline is responsible for propagating tags; specifically, domain tags are fetched into the pipeline and used to compute the tag of the output value for every instruction. Initial tag values come from the compiler, while the microarchitecture is augmented to support tag storage.

## Slide 21: Tagging Support
registers: 2b tag
memory 2b tag per 64b word
tag information resides in physical DRAM at an offset @ start+phyaddr/32, where @start is the address of the tags in DRAM
tags are cached throughout the memory hierarchy. The 64-byte tag groups read from DRAM are cached in a tag cache, and all data cache blocks are extended with 2-bits per 64-bit word, to store the additional domain tag bits with each cache block.

## Slide 22: Executing Mem Ops
First map the pointers to VAS.
memory system sees the regular virtual address map.
* However, from the program’s perspective the correct DASD or DASC address must be given.
Translating from DAS to VAS:
  subtracting from the current offset.

## Slide 23: Latency Implications & Impl
Load: offset+base register
VAS = (offset+BASE) – dDATA
Implemented as:
  tmp = offset – dDATA @ decode
  Base + tmp @ execute

## Slide 24: Morpheus: Ensemble of MTDs
Churn
Encryption
Displacement
Tagged Memory
Code
Code Ptrs
Data Ptrs
Encryption:
Obfuscate information assets
Displacement:
Shift code & data segments
Information Assets
EMTD
Notes: When do we churn?

## Slide 25: Encryption
Introduces entropy to Code & Pointer values
Encrypt domains under own keys
  Code
  Code Pointer
  Data Pointer
QARMA Block Cipher
  Fast cipher used in Arm’s PAC
  Used in counter-mode here
Asset
KC/CP/DP
Encrypted/Decrypted
Asset
bad
f00
Addr of Asset
QARMA [ToSC’17]
64-bit block cipher
128-bit keys
Notes: - Overhead can be hidden due to parallel access

## Slide 26: Domain Encryption
Domain Encryption Defense
Decrypt in the L1 Encrypt before going to the L2. Goal encrypted in MEMORY as viewed by OTHERS:
The three keys used for domain encryption (KC,KC P, andKDP) are stored in microarchitectural
registers that are not accessible by software, so they are private to a process’s ad-dress space

## Slide 27: Morpheus: Key Mechanisms
Domain tagging (Section 4.1) to precisely track the do-main of all memory objects at runtime. Morpheus leverages these tags to implement two moving target defenses
Pointer displacement(Section 4.2), which obscures pointer values by adding a random displacement to them by domain
Domain encryption(Section 4.3), which encrypts all domains in the program under their own keys.

## Slide 28: Tagging & Attack Detection
Tags enable behavior tracking
Illegal Ops
  Clearly dangerous
Suspicious Ops
  Normal programs may perform
  May be probes or attacks
Attack Detector
Operand Tags
Opcode
Illegal
Suspicious
Executing non-code
Jump to non-CP
…
Terminate Program
Churn
CP arithmetic
Arith. overflow
…
Otherwise, churn every 50ms

## Slide 29: Churning EMTDs
Program
Churn
Flush
Key
Gen
Reg
Asset Updates
Stale
Flush
Key
Gen
Churn Period
Stale: Under OLD key
Clean: Updated to NEW key
!
!
Asset Updates
Clean
Threshold
t
Notes: - Churn period: Fixed interval OR Variable (Attack detector)

## Slide 30: μArch Additions
Tagged Memory
Tag Propagation
Attack Detector
Displacement
Translate DASVAS
Encryption
QARMA Engines
Churn Unit
State Machine
RNG (Key-Gen)
Threshold Register
Churn Unit
L1 D-cache
Tags
ENC/DEC
L2 Cache
Tags
Displacement Translation
To DRAM
Pipeline
Tag Support
Churn Support
Registers
Tags
Attack Detector
Notes: Displacement – preserve original VAS

## Slide 31
Introduction
Parting Thoughts
Morpheus Architecture
Evaluations

## Slide 32
Introduction
Evaluations
Parting Thoughts
Morpheus Architecture

## Slide 33: Evaluation Framework
gem5 + DRAMSim2
  RISC-V – RV64IMA ISA
  Implements churn unit
  Simulate tag fetch & Tag$
Benchmarks:
  SPEC 2006, INT+FP, C-only
  Subset of MiBench
Core Type | MinorCPU (InO)
CPU Freq. | 2.5GHz
L1 I$ | 32KB 2-cycle
L1 D$ | 32KB 2-cycle
L2 Unified | 256KB 20-cycle
Tag Cache | 4KB

## Slide 34: Security in Morpheus
How long to penetrate Morpheus defenses?
Difficult to attack a system that is
  Constantly changing
  Has high entropy
Approach: Attack a weaker Morpheus
Churn Disabled
Shared Key for Defenses
De-featured Morpheus
Notes: - Shared key: No multi-domain or multi-process keys

## Slide 35: Attacking a Weakened Morpheus
Chart: Average Attack Probe Time (s)
| EP | EP | EP | EP
AnC Address De-randomization | 150000 | 147400 | 0 | 0
High bit probes | 3459.3 | 3459.3 | 0 | 0
Code search | 0 | 1511.44 | 0 | 1511.44
Blind code search | 98653.27 | 0 | 98653.27 | 0
0.01s
98.6s
152s
251s
Defenses Enabled
bad
f00
5,020x 50ms Churn Cycle
251s to penetrate a Morpheus system with high entropy & no churn!
Notes: No churn: using load-time MTD!

## Slide 36: Effects of Churn Period
Normal Churn Period
< 1%
avg. slowdown
Notes: - Performance vs security trade-offs

## Slide 37: Evaluation Summary
Keys change 5020x faster than time-to-penetrate with advanced probes
Low performance impact (<1%) on system
With network latencies of ~1ms/36miles, churn invalidates information before attackers can use it
Notes: - 10ms churn == 360mi network separation

## Slide 38
Introduction
Evaluations
Parting Thoughts
Morpheus Architecture

## Slide 39
Introduction
Parting Thoughts
Morpheus Architecture
Evaluations

## Slide 40: Limitations of Morpheus
Relative Address Attacks
  Distance between code & data churns
  Distance within segments is preserved
Reliance on Tagged Memory
  Enables powerful EMTDs + Churn
  Attacks missed by tag-checks are mitigated by EMTDs
  Additional complexity of tagging
Future Work
Churn relative distance
Support churn without tags

## Slide 41: Conclusions
EMTDs + Churn provide vulnerability tolerance
  Attackers exploit vulnerabilities & information assets
  EMTDs protect assets by churning them to stop derandomization
Morpheus shows that with H/W support, we achieve:
  High entropy defenses
  High durability with churn
  Low performance overhead (<1%)
Future directions of EMTDs + Churn
  Achieve stronger control-flow protections
  Hinder side-channels
  Create additional ensemble defenses
?
?
?

## Slide 42: // BACKUP
Beep Beep

## Slide 43: SPEC 2006 Detail
Should be Rarely Encountered!

## Slide 44: Penetration Testing
RIPE testing suite
  Used a subset of attacks ported to RISC-V
  Code injection
    Code is encrypted → injected code is invalid
  Code reuse (ROP)
    Locations shifted → injected return addresses invalid
Back-Call-Site Attack (breaks Active-Set CFI)

## Slide 45: Hardware Area Estimate
[Not in paper]
Baseline: SiFive U54 - 28nm estimate
  CACTI 7 for cache sizes
  QARMA estimated from original work
  Churn Support  smaller 64-bit core from SiFive
 | SiFive U54-MC | Morpheus | 
U54 w/ Caches | 2.249 mm2 | 2.249 mm2 | -
+ Tagged Memory | - | 0.084 mm2 | 3.74%
+ QARMA | - | 0.044 mm2 | 1.96%
+ Churn Support | - | 0.082 mm2 | 3.65%
Total | 2.249 mm2 | 2.459 mm2 | 9.34%

## Slide 46: Full μArch