## Slide 1: Chip-Multiprocessor Caches: Placement and Management
Andreas Moshovos
University of Toronto/ECE
Short Course, University of Zaragoza, July 2009
Most slides are based on or directly taken from material and slides by the original paper authors

## Slide 2: Modern Processors Have Lots of Cores and Large Caches
Sun Niagara T1
From http://jinsatoh.jp/ennui/archives/2006/03/opensparc.html

## Slide 3: Modern Processors Have Lots of Cores and Large Caches
Intel i7 (Nehalem)
From http://www.legitreviews.com/article/824/1/

## Slide 4: Modern Processors Have Lots of Cores and Large Caches
From http://www.chiparchitect.com
AMD Shanghai

## Slide 5: Modern Processors Have Lots of Cores and Large Caches
From http://www.theinquirer.net/inquirer/news/1018130/ibms-power5-the-multi-chipped-monster-mcm-revealed
IBM Power 5

## Slide 6: Why?
Helps with Performance and Energy
  Find graph with perfect vs. realistic memory system

## Slide 7: What Cache Design Used to be About
L2: Worst Latency == Best Latency
Key Decision: What to keep in each cache level
Core
L1I
L1D
L2
Main Memory
1-3 cycles / Latency Limited
10-16 cycles / Capacity Limited
> 200 cycles

## Slide 8: What Has Changed
ISSCC 2003

## Slide 9: What Has Changed
Where something is matters
More time for longer distances

## Slide 10: NUCA: Non-Uniform Cache Architecture
Tiled Cache
Variable Latency
Closer tiles = Faster
Key Decisions:
  Not only what to cache
  Also where to cache
Core
L1I
L1D
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2

## Slide 11: NUCA Overview
Initial Research focused on Uniprocessors
Data Migration Policies
  When to move data among tiles
L-NUCA: Fine-Grained NUCA

## Slide 12: Another Development: Chip Multiprocessors
Easily utilize on-chip transistors
Naturally exploit thread-level parallelism
Dramatically reduce design complexity
Future CMPs will have more processor cores
Future CMPs will have more cache
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
Text from Michael Zhang & Krste Asanovic, MIT

## Slide 13: Initial Chip Multiprocessor Designs
core
L1$
Layout: “Dance-Hall”
  Core + L1 cache
  L2 cache
Small L1 cache: Very low access latency
Large L2 cache
Intra-Chip Switch
core
L1$
core
L1$
core
L1$
L2
Cache
A 4-node CMP with a large L2 cache
Slide from Michael Zhang & Krste Asanovic, MIT

## Slide 14: Chip Multiprocessor w/ Large Caches
core
L1$
Layout: “Dance-Hall”
  Core + L1 cache
  L2 cache
Small L1 cache: Very low access latency
Large L2 cache: Divided into slices to minimize access latency and power usage
Intra-Chip Switch
core
L1$
core
L1$
core
L1$
A 4-node CMP with a large L2 cache
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
Slide from Michael Zhang & Krste Asanovic, MIT

## Slide 15: Chip Multiprocessors + NUCA
L2 Slice
core
L1$
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
Current: Caches are designed with (long) uniform access latency for the worst case:
  Best Latency == Worst Latency
Future: Must design with non-uniform access latencies depending on the on-die location of the data:
  Best Latency << Worst Latency
Challenge: How to minimize average cache access latency:
  Average Latency  Best Latency
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
L2 Slice
Intra-Chip Switch
core
L1$
core
L1$
core
L1$
A 4-node CMP with a large L2 cache
Slide from Michael Zhang & Krste Asanovic, MIT

## Slide 16: Tiled Chip Multiprocessors
Tiled CMPs for Scalability
  Minimal redesign effort
  Use directory-based protocol for scalability
Managing the L2s to minimize the effective access latency
  Keep data close to the requestors
  Keep data on-chip
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
core
L1$
L2$
Slice
Data
Switch
L2$
Slice
Tag
Slide from Michael Zhang & Krste Asanovic, MIT

## Slide 17: Option #1: Private Caches
+ Low Latency
- Fixed allocation
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2
Main Memory

## Slide 18: Option #2: Shared Caches
Higher, variable latency
One Core can use all of the cache
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2
Main Memory

## Slide 19: Data Cache Management for CMP Caches
Get the best of both worlds
  Low Latency of Private Caches
  Capacity Adaptability of Shared Caches

## Slide 20: NUCA: A Non-Uniform Cache Access Architecture for Wire-Delay Dominated On-Chip Caches
  Changkyu Kim, D.C. Burger, and S.W. Keckler,
  10th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS-X), October, 2002.

## Slide 21: NUCA: Non-Uniform Cache Architecture
Tiled Cache
Variable Latency
Closer tiles = Faster
Key Decisions:
  Not only what to cache
  Also where to cache
Interconnect
  Dedicated busses
  Mesh better
Static Mapping
Dynamic Mapping
  Better but more complex
  Migrate data
Core
L1I
L1D
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2

## Slide 22: Distance Associativity for High-Performance Non-Uniform Cache Architectures
Zeshan Chishti, Michael D Powell, and T. N. Vijaykumar
36th Annual International Symposium on Microarchitecture (MICRO), December 2003.
Slides mostly directly from their conference presentation

## Slide 23: Problem with NUCA
Couples Distance Placement with Way Placement
NuRapid:
  Distance Associativity
Centralized Tags
  Extra pointer to Bank
  Achieves 7% overall processor E-D savings
Core
L1I
L1D
L2
L2
L2
L2
L2
L2
L2
L2
Way 1
Way 2
Way 3
Way 4
fastest
slowest
fast
slow

## Slide 24: Light NUCA: a proposal for bridging the inter-cache latency gap
Darío Suárez 1, Teresa Monreal 1, Fernando Vallejo 2, Ramón Beivide 2, and Victor Viñals 1
1 Universidad de Zaragoza and 2 Universidad de Cantabria

## Slide 25: L-NUCA: A Fine-Grained NUCA
3-level conventional cache vs. L-NUCA and L3
D-NUCA vs. L-NUCA and D-NUCA

## Slide 26: Managing Wire Delay in Large CMP Caches
Bradford M. Beckmann and David A. Wood
Multifacet Project
University of Wisconsin-Madison
MICRO 2004
12/8/04

## Slide 27: Managing Wire Delay in Large CMP Caches
Managing wire delay in shared CMP caches
Three techniques extended to CMPs
    On-chip Strided Prefetching
      Scientific workloads: 10% average reduction
      Commercial workloads: 3% average reduction
    Cache Block Migration (e.g. D-NUCA)
      Block sharing limits average reduction to 3%
      Dependence on difficult to implement smart search
    On-chip Transmission Lines (e.g. TLC)
      Reduce runtime by 8% on average
      Bandwidth contention accounts for 26% of L2 hit latency
Combining techniques
    Potentially alleviates isolated deficiencies
      Up to 19% reduction vs. baseline
    Implementation complexity
D-NUCA search technique for CMPs
  Do it in steps

## Slide 28: Where do Blocks Migrate to?
Scientific Workload:
Block migration successfully separates
the data sets
Commercial Workload:
Most Accesses go in the middle

## Slide 29
A NUCA Substrate for Flexible CMP Cache Sharing
Jaehyuk Huh, Changkyu Kim †, Hazim Shafi, Lixin Zhang§,
Doug Burger , Stephen W. Keckler †
Int’l Conference on Supercomputing, June 2005
§Austin Research Laboratory IBM Research Division | †Dept. of Computer Sciences The University of Texas at Austin

## Slide 30: What is the best Sharing Degree? Dynamic Migration?
Determining sharing degree
  Miss rates vs. hit latencies
Latency management for increasing wire delay
  Static mapping (S-NUCA) and dynamic mapping (D-NUCA)
Best sharing degree is 4
Dynamic migration
  Does not seem to be worthwhile in the context of this study
  Searching problem is still yet to be solved
L1 prefetching
  7 % performance improvement (S-NUCA)
  Decrease the best sharing degree slightly
Per-line sharing degrees provide the benefit of both high and low sharing degree
Core
L1I
L1D
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
  Sharing Degree (SD):
  number of processors in a shared L2

## Slide 31: Victim Replication: Maximizing Capacity while Hiding Wire Delay in Tiled Chip Multiprocessors
Michael Zhang & Krste Asanovic
Computer Architecture Group
MIT CSAIL
Int’l Conference on Computer Architecture, June 2005
Slides mostly directly from the author’s presentation

## Slide 32: Victim Replication: A Variant of the Shared Design
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Sharer i
Sharer j
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Home Node
Implementation: Based on the shared design
Get for free:
  L1 Cache: Replicates shared data locally for fastest access latency
L2 Cache: Replicates the L1 capacity victims  Victim Replication

## Slide 33: Optimizing Replication, Communication, and Capacity Allocation in CMPs
Z. Chishti, M. D. Powell, and T. N. Vijaykumar
Proceedings of the 32nd International Symposium on Computer Architecture, June 2005.
Slides mostly by the paper authors and by Siddhesh Mhambrey’s course presentation CSE520

## Slide 34: CMP-NuRAPID: Novel Mechanisms
Controlled Replication
  Avoid copies for some read-only shared data
In-Situ Communication
  Use fast on-chip communication to avoid coherence miss of read-write-shared data
Capacity Stealing
  Allow a core to steal another core’s unused capacity
Hybrid cache
  Private Tag Array and Shared Data Array
  CMP-NuRAPID(Non-Uniform access with Replacement and Placement using Distance associativity)
  Local, larger tags
Performance
  CMP-NuRAPID improves performance by 13% over a shared cache and 8% over a private cache for three commercial multithreaded workloads
  Three novel mechanisms to exploit the changes in Latency-Capacity tradeoff

## Slide 35: Cooperative Caching for Chip Multiprocessors
Jichuan Chang and Guri Sohi
Int’l Conference on Computer Architecture, June 2006

## Slide 36: CC: Three Techniques
Don’t go off-chip if on-chip (clean) data exist
  Existing protocols do that for dirty data only
    Why? When clean-shared have to decide who responds
    No significant benefit in SMPs  CMPs protocols are build on SMP protocols
Control Replication
  Evict singlets only when no invalid or replicates exist
  “Spill” an evicted singlet into a peer cache
Approximate global-LRU replacement
  First become the LRU entry in the local cache
  Set as MRU if spilled into a peer cache
  Later become LRU entry again: evict globally
  1-chance forwarding (1-Fwd)
    Blocks can only be spilled once if not reused

## Slide 37: Cooperative Caching
Two probabilities to help make decisions
  Cooperation probability: Prefer singlets over replicates?
    When replacing within a set
      Use probability to select whether a singlet can be evicted or not
    control replication
  Spill probability: Spill a singlet victim?
    If a singlet was evicted should it be replicated?
    throttle spilling
No method for selecting this probability is proposed

## Slide 38: Managing Distributed, Shared L2 Caches through OS-Level Page Allocation
Sangyeun Cho and Lei Jin
Dept. of Computer Science
University of Pittsburgh
Int’l Symposium on Microarchitecture, 2006

## Slide 39: Page-Level Mapping
The OS has control of where a page maps to

## Slide 40: OS Controlled Placement – Potential Benefits
Performance management:
  Proximity-aware data mapping
Power management:
  Usage-aware slice shut-off
Reliability management
  On-demand isolation
On each page allocation, consider
  Data proximity
  Cache pressure
  e.g., Profitability function P = f(M, L, P, Q, C)
    M: miss rates
    L: network link status
    P: current page allocation status
    Q: QoS requirements
    C: cache configuration

## Slide 41: OS Controlled Placement
Hardware Support:
  Region-Table
  Cache Pressure Tracking:
    # of actively accessed pages per slice
    Approximation  power-, resource-efficient structure
Results on OS-directed:
  Private
  Clustered

## Slide 42: ASR: Adaptive Selective Replication for CMP Caches
Brad Beckmann, Mike Marty, and David Wood
Multifacet Project
University of Wisconsin-Madison
Int’l Symposium on Microarchitecture, 2006
12/13/06

## Slide 43: Adaptive Selective Replication
Sharing, Locality, Capacity Characterization of Workloads
  Replicate only Shared read-only data
  Read-write: little locality  written and read a few times
  Single Requestor: little locality
Adaptive Selective Replication: ASR
  Dynamically monitor workload behavior
  Adapt the L2 cache to workload demand
  Up to 12% improvement vs. previous proposals
Mechanisms for estimating Cost/Benefit of less/more replication
Dynamically adjust replication probability
  Several replication prob. levels
Use probability to “randomly” replicate blocks

## Slide 44: An Adaptive Shared/Private NUCA Cache Partitioning Scheme for Chip Multiprocessors
Haakon Dybdahl & Per Stenstrom
Int’l Conference on High-Performance Computer Architecture, Feb 2007

## Slide 45: Adjust the Size of the Shared Partition in Each Local Cache
Divide ways in Shared and Private
  Dynamically adjust the # of shared ways
Decrease?  Loss: How many more misses will occur?
Increase?  Gain: How many more hits?
Every 2K misses adjust ways according to gain and loss
No massive evictions or copying to adjust ways
  Replacement algorithm takes care of way adjustment lazily
Demonstrated for multiprogrammed workloads

## Slide 46
Dynamic Spill-Receive for Robust High-Performance Caching in CMPs
Moinuddin K. Qureshi
T. J. Watson Research Center, Yorktown Heights, NY

## Slide 47: Cache Line Spilling
Spill evicted line from one cache to neighbor cache
- Co-operative caching (CC) [ Chang+ ISCA’06]
Problem with CC:
Performance depends on the parameter (spill probability)
All caches spill as well as receive  Limited improvement
  Spilling helps only if application demands it
  Receiving lines hurts if cache does not have spare capacity
Cache A
Cache B
Cache C
Cache D
Spill
Goal:
Robust High-Performance Capacity Sharing with Negligible Overhead

## Slide 48: Spill-Receive Architecture
Each Cache is either a Spiller or Receiver but not both
- Lines from spiller cache are spilled to one of the receivers
- Evicted lines from receiver cache are discarded
Dynamic Spill Receive (DSR)  Adapt to Application Demands
Dynamically decide whether a cache should be a Spill or a Receive one
Cache A
Cache B
Cache C
Cache D
Spill
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)
Set Dueling: A few sampling sets follow one or the other policy
Periodically select the best and use for the rest
Underlying Assumption: The behavior of a few sets is reasonably representative of that of all sets

## Slide 49: PageNUCA: Selected Policies for Page-grain Locality Management in Large Shared CMP Caches
Mainak Chaudhuri, IIT Kanpur
Int’l Conference on High-Performance Computer Architecture, 2009
Some slides from the author’s conference talk

## Slide 50: PageNUCA
Most Pages accessed by a single core and multiple times
  That core may change over time
  Migrate page close to that core
Fully hardwired solution composed of four central algorithms
  When to migrate a page
  Where to migrate a candidate page
  How to locate a cache block belonging to a migrated page
  How the physical data transfer takes place
Shared pages: minimize average latency
Solo pages: move close to core
Dynamic migration better than first-touch: 12.6%
  Multiprogrammed workloads

## Slide 51: Dynamic Hardware-Assisted Software-Controlled Page Placement to Manage Capacity Allocation and Sharing within Caches
Manu Awasthi, Kshitij Sudan, Rajeev Balasubramonian, John Carter
University of Utah
Int’l Conference on High-Performance Computer Architecture, 2009

## Slide 52: Conclusions
Last Level cache management at page granularity
  Previous work: First-touch
Salient features
  A combined hardware-software approach with low overheads
    Main Overhead : TT  page translation for all pages currently cached
  Use of page colors and shadow addresses for
    Cache capacity management
    Reducing wire delays
    Optimal placement of cache lines.
  Allows for fine-grained partition of caches.
Up to 20% improvements for multi-programmed, 8% for multi-threaded workloads

## Slide 53: R-NUCA: Data Placement in Distributed Shared Caches
Nikos Hardavellas, M. Ferdman, B. Falsafi, and A. Ailamaki
Int’l Conference on Computer Architecture, June 2009
Slides from the authors and by Jason Zebchuk, U. of Toronto

## Slide 54: R-NUCA
Private L2
Core
Core
Core
Core
Private L2
Private L2
Private L2
Shared L2
Core
Core
Core
Core
L2 cluster
Core
Core
Core
Core
L2 cluster
Private Data Sees This
Shared Data Sees This
Instructions
See This
OS enforced replication at the page level

## Slide 55: NUCA: A Non-Uniform Cache Access Architecture for Wire-Delay Dominated On-Chip Caches
  Changkyu Kim, D.C. Burger, and S.W. Keckler,
  10th International Conference on Architectural Support for Programming Languages and Operating Systems (ASPLOS-X), October, 2002.
Some material from slides by Prof. Hsien-Hsin S. Lee ECE, GTech

## Slide 56: Conventional – Monolithic Cache
UCA: Uniform Access Cache
UCA
Best Latency = Worst Latency
  Time to access the farthest possible bank

## Slide 57: UCA Design
Partitioned in Banks
Conceptually a single address and a single data bus
  Pipelining can increase throughput
See CACTI tool:
  http://www.hpl.hp.com/research/cacti/
  http://quid.hpl.hp.com:9081/cacti/
Tag Array
Data Bus
Address Bus
Bank
Sub-bank
Predecoder
Sense
amplifier
Wordline driver
and decoder

## Slide 58: Experimental Methodology
SPEC CPU 2000
Sim-Alpha
CACTI
8 FO4 cycle time
132 cycles to main memory
Skip and execute a sample
Technology Nodes
  130nm, 100nm, 70nm, 50nm

## Slide 59: UCA Scaling – 130nm to 50nm
Chart: 
| 130nm/2MB | 100nm/4MB | 70nm/8MB | 50nm/16MB
Miss Rate | 0.23 | 0.2 | 0.17 | 0.13
Chart: 
| 130nm/2MB | 100nm/4MB | 70nm/8MB | 50nm/16MB
Unloaded Latency | 13 | 18 | 26 | 41
Chart: 
| 130nm/2MB | 100nm/4MB | 70nm/8MB | 50nm/16MB
Loaded Latency | 67.7 | 91.1 | 144.2 | 255.1
Chart: 
| 130nm/2MB | 100nm/4MB | 70nm/8MB | 50nm/16MB
IPC | 0.41 | 0.39 | 0.34 | 0.26
Relative Latency and Performance Degrade as Technology Improves

## Slide 60: UCA Discussion
Loaded Latency: Contention
  Bank
  Channel
    Bank may be free but path to it is not

## Slide 61: Multi-Level Cache
Conventional Hierarchy
L3
Common Usage:
  Serial-Access for Energy and Bandwidth Reduction
This paper:
  Parallel Access
  Prove that even then their design is better
L2

## Slide 62: ML-UCA Evaluation
Better than UCA
Performance Saturates at 70nm
No benefit from larger cache at 50nm
Chart: Latency
| 130nm/512K/2MB | 100nm/512K/4M | 70nm/1M/8M | 50nm/1M/16M
Unloaded L2 | 6 | 7 | 9 | 10
Unloaded L3 | 13 | 21 | 26 | 41
Chart: 
| 130nm/512K/2MB | 100nm/512K/4M | 70nm/1M/8M | 50nm/1M/16M
IPC | 0.55 | 0.57 | 0.64 | 0.64

## Slide 63: S-NUCA-1
Static NUCA with per bank set busses
Data Bus
Address Bus
Bank
Sub-bank
Use private per bank set channel
Each bank has its distinct access latency
A given address maps to a given bank set
  Lower bits of block address
Tag
Set
Offset
Bank Set

## Slide 64: S-NUCA-1
How fast can we initiate requests?
  If c = scheduler delay
Conservative /Realistic:
  Bank + 2 x interconnect + c
Aggressive / Unrealistic:
  Bank + c
What is the optimal number of bank sets?
  Exhaustive evaluation of all options
  Which gives the highest IPC
Data Bus
Address Bus
Bank

## Slide 65: S-NUCA-1 Latency Variability
Variability increases for finer technologies
Number of banks does not increase beyond 4M
  Overhead of additional channels
  Banks become larger and slower
Chart: 
| 130nm/2M/16 | 100nm/4M/32 | 70nm/8M/32 | 50nm/16M/32
Unloaded min S2 | 4 | 4 | 6 | 9
Unloaded avg S2 | 10 | 15 | 19 | 29
Unloaded max S2 | 13 | 21 | 26 | 41

## Slide 66: S-NUCA-1 Loaded Latency
Better than ML-UCA
Chart: 
| 130nm/2M/16 | 100nm/4M/32 | 70nm/8M/32 | 50nm/16M/32
Aggr. Loaded | 10 | 15.3 | 19.3 | 30.2

## Slide 67: S-NUCA-1: IPC Performance
Per bank channels become an overhead
Prevent finer partitioning @70nm or smaller
Chart: 
| 130nm/2M/16 | 100nm/4M/32 | 70nm/8M/32 | 50nm/16M/32
IPC S1 | 0.55 | 0.57 | 0.63 | 0.62

## Slide 68: S-NUCA2
Use a 2-D Mesh P2P interconnect
Bank
Data bus
Switch
Tag Array
Wordline driver
and decoder
Predecoder
Wire overhead much lower:
  S1: 20.9% vs. S2: 5.9% at 50nm and 32banks
Reduces contention
128-bit bi-directional links

## Slide 69: S-NUCA2 vs. S-NUCA1 Unloaded Latency
S-NUCA2 almost always better
Chart: 
| 130nm/2M/16 | 100nm/4M/32 | 70nm/8M/32 | 50nm/16M/32
Unloaded min S1 | 7 | 3 | 5 | 8
Unloaded min S2 | 4 | 4 | 6 | 9
Unloaded avg S1 | 10 | 15 | 19 | 29
Unloaded avg S2 | 8 | 10 | 18 | 21
Unloaded max S1 | 13 | 21 | 26 | 41
Unloaded max S2 | 11 | 15 | 29 | 32
Hmm

## Slide 70: S-NUCA2 vs. S-NUCA-1 IPC Performance
S2 better than S1
Chart: 
| 130nm/2M/16 | 100nm/4M/32 | 70nm/8M/32 | 50nm/16M/32
IPC S1 | 0.55 | 0.57 | 0.63 | 0.62
IPC S2 | 0.55 | 0.58 | 0.62 | 0.65

## Slide 71: Dynamic NUCA
Data can dynamically migrate
Move frequently used cache lines closer to CPU
One way of each set in fast d-group; compete within set
Cache blocks “screened” for fast placement
data
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
d-group
Processor Core
Part of slide from Zeshan Chishti, Michael D Powell, and T. N. Vijaykumar

## Slide 72: Dynamic NUCA – Mapping #1
Simple Mapping
All 4 ways of each bank set need to be searched
Farther bank sets  longer access
8 bank sets
way 0
way 1
way 2
way 3
one set
bank
Where can a block map to?

## Slide 73: Dynamic NUCA – Mapping #2
Fair Mapping
Average access times across all bank sets are equal
8 bank sets
way 0
way 1
way 2
way 3
one set
bank

## Slide 74: Dynamic NUCA – Mapping #3
Shared Mapping
Sharing the closest banks  every set has some fast storage
If n bank sets share a bank then all banks must be n-way set associative
8 bank sets
way 0
way 1
way 2
way 3
bank

## Slide 75: Dynamic NUCA - Searching
Where is a block?
Incremental Search
  Search in order
Multicast
  Search all of them in parallel
Partitioned Multicast
  Search groups of them in parallel
way 0
way 1
way 2
way 3

## Slide 76: D-NUCA – Smart Search
Tags are distributed
  May search many banks before finding a block
  Farthest bank determines miss determination latency
Solution: Centralized Partial Tags
  Keep a few bits of all tags (e.g., 6) at the cache controller
  If no match  Bank doesn’t have the block
  If match  Must access the bank to find out
Partial Tags  R.E. Kessler, R. Jooss, A. Lebeck, and M.D. Hill. Inexpensive
implementations of set-associativity. In Proceedings of
the 16th Annual International Symposium on Computer Architecture,
pages 131–139, May 1989.

## Slide 77: Partial Tags / Smart Search Policies
SS-Performance:
  Partial Tags and Banks accessed in parallel
  Early Miss Determination
  Go to main memory if no match
  Reduces latency for misses
SS-Energy:
  Partial Tags first
  Banks only on potential match
  Saves energy
  Increases Delay

## Slide 78: Migration
Want data that will be accessed to be close
Use LRU?
  Bad idea: must shift all others
MRU
LRU
Generational Promotion
  Move to next bank
  Swap with another block

## Slide 79: Initial Placement
Where to place a new block coming from memory?
Closest Bank?
  May force another important block to move away
Farthest Bank?
  Takes several accesses before block comes close

## Slide 80: Victim Handling
A new block must replace an older block victim
What happens to the victim?
Zero Copy
  Gets dropped completely
One Copy
  Moved away to a slower bank (next bank)

## Slide 81: DN-Best
DN-BEST
  Shared Mapping
  SS Energy
    Balance performance and access account/energy
    Maximum performance is 3% higher
  Insert at tail
    Insert at head  reduces avg. latency but increases misses
  Promote on hit
    No major differences with other polices

## Slide 82: Baseline D-NUCA
Simple Mapping
Multicast Search
One-Bank Promotion on Hit
Replace from the slowest bank
8 bank sets
way 0
way 1
way 2
way 3
one set
bank

## Slide 83: D-NUCA Unloaded Latency
Chart: 
| 130nm/2M/4x4 | 100nm/4MB/8x4 | 70nm/8MB/16x8 | 50nm/16M/16x16
Unloaded min | 4 | 4 | 4 | 3
Unloaded avg | 8 | 10 | 18 | 25
Unloaded Max | 11 | 15 | 31 | 47

## Slide 84: IPC Performance: DNUCA vs. S-NUCA2 vs. ML-UCA
Chart: 
IPC DNUCA | 0.57 | 0.63 | 0.67 | 0.71
IPC S2 | 0.55 | 0.58 | 0.62 | 0.65
IPC ML | 0.55 | 0.57 | 0.64 | 0.64

## Slide 85: Performance Comparison
D-NUCA and S-NUCA2 scale well
D-NUCA outperforms all other designs
ML-UCA saturates – UCA Degrades
UPPER = all hits are
in the closest bank
3 cycle latency

## Slide 86: Distance Associativity for High-Performance Non-Uniform Cache Architectures
Zeshan Chishti, Michael D Powell, and T. N. Vijaykumar
36th Annual International Symposium on Microarchitecture (MICRO), December 2003.
Slides mostly directly from the authors’ conference presentation

## Slide 87: Motivation
Large Cache Design
L2/L3 growing (e.g., 3 MB in Itanium II)
Wire-delay becoming dominant in access time
Conventional large-cache
Many subarrays => wide range of access times
Uniform cache access => access-time of slowest subarray
Oblivious to access-frequency of data
Want often-accessed data faster: improve access time

## Slide 88: Previous work: NUCA (ASPLOS ’02)
Pioneered Non-Uniform Cache Architecture
Access time: Divides cache into many distance-groups
D-group closer to core => faster access time
Data Mapping: conventional
Set determined by block index; each set has n-ways
Within a set, place frequently-accessed data in fast d-group
Place blocks in farthest way; bubble closer if needed

## Slide 89: D-NUCA
One way of each set in fast d-group; compete within set
Cache blocks “screened” for fast placement
data
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
Processor core
d-group

## Slide 90: D-NUCA
One way of each set in fast d-group; compete within set
Cache blocks “screened” for fast placement
data
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
Processor core
d-group

## Slide 91: D-NUCA
data
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
Processor core
d-group
One way of each set in fast d-group; compete within set
Cache blocks “screened” for fast placement

## Slide 92: D-NUCA
data
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
Processor core
d-group
One way of each set in fast d-group; compete within set
Cache blocks “screened” for fast placement

## Slide 93: D-NUCA
Processor core
d-group
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
One way of each set in fast d-group; compete within set
Cache blocks “screened” for fast placement

## Slide 94: D-NUCA
Want to change restriction; more flexible data-placement
data
tag
way 0
way 1
way n-2
way n-1
fast
slow
. . .
...
...
Processor core
d-group

## Slide 95: NUCA
Artificial coupling between s-a way # and d-group
Only one way in each set can be in fastest d-group
  Hot sets have > 1 frequently-accessed way
  Hot sets can place only one way in fastest d-group
Swapping of blocks is bandwidth- and energy-hungry
D-NUCA uses a switched network for fast swaps

## Slide 96: Common Large-cache Techniques
Sequential Tag-Data: e.g., Alpha 21164 L2, Itanium II L3
Access tag first, and then access only matching data
Saves energy compared to parallel access
Data Layout: Itanium II L3
Spread a block over many subarrays (e.g., 135 in Itanium II)
For area efficiency and hard- and soft-error tolerance
These issues are important for large caches

## Slide 97: Contributions
Key observation:
sequential tag-data => indirection through tag array
Data may be located anywhere
Distance Associativity:
Decouple tag and data => flexible mapping for sets
Any # of ways of a hot set can be in fastest d-group
NuRAPID cache: Non-uniform access with Replacement And Placement usIng Distance associativity
Benefits:
More accesses to faster d-groups
Fewer swaps => less energy, less bandwidth
But:
More tags + pointers are needed

## Slide 98: Outline
Overview
NuRAPID Mapping and Placement
NuRAPID Replacement
NuRAPID layout
Results
Conclusion

## Slide 99: NuRAPID Mapping and Placement
Distance-Associative Mapping:
decouple tag from data using forward pointer
Tag access returns forward pointer, data location
Placement: data block can be placed anywhere
Initially place all data in fastest d-group
Small risk of displacing often-accessed block

## Slide 100: NuRAPID Mapping; Placing a block
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
2
3
Atag,grp0,frm1
A
forward pointer
All blocks initially placed in fastest d-group

## Slide 101: NuRAPID: Hot set can be in fast d-group
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
2
3
Atag,grp0,frm1
A
Btag,grp0,frmk
B
Multiple blocks from one set in same d-group

## Slide 102: NuRAPID: Unrestricted placement
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
2
3
Atag,grp0,frm1
A
Btag,grp0,frmk
Ctag,grp2,frm0
Dtag,grp1,frm1
B
C
D
No coupling between tag and data mapping

## Slide 103: Outline
Overview
NuRAPID Mapping and Placement
NuRAPID Replacement
NuRAPID layout
Results
Conclusion

## Slide 104: NuRAPID Replacement
Two forms of replacement:
Data Replacement: Like conventional
  Evicts blocks from cache due to tag-array limits
Distance Replacement: Moving blocks among d-groups
  Determines which block to demote from a d-group
  Decoupled from data replacement
  No blocks evicted
    Blocks are swapped

## Slide 105: NuRAPID: Replacement
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
Btag,grp0,frm1
B
Ztag,grp1,frmk
Z
Place new block, A, in set 0.
Space must be created in the tag set:
Data-Replace Z
Z may not be in the target d-group

## Slide 106: NuRAPID: Replacement
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
Btag,grp0,frm1
B
empty
empty
Place new block, A, in set 0.
Data-Replace Z

## Slide 107: NuRAPID: Replacement
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
Btag,grp0,frm1
B, set1 way0
Atag
empty
Place Atag, in set 0.
Must create an empty data block
B is selected to demote. Use reverse-pointer to locate Btag
reverse pointer

## Slide 108: NuRAPID: Replacement
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
Btag,grp1,frmk
empty
Atag
B, set1 way0
B is demoted to empty frame. Btag updated
There was an empty frame because Z was evicted
This may not always be the case

## Slide 109: NuRAPID: Replacement
fast
slow
d-group 0
d-group 1
d-group 2
Data Arrays
Tag array
...
Way-0
Way-(n-1)
frame #
0
1
k
0
1
k
0
1
k
set #
0
1
Btag,grp1,frmk
A, set0 wayn-1
Atag,grp0,frm1
B, set1 way0
A is placed in d-group 0
pointers updated

## Slide 110: Replacement details
Always empty block for demotion for dist.-replacement
May require multiple demotions to find it
Example showed only demotion
Block could get stuck in slow d-group
Solution: Promote upon access (see paper)
How to choose block for demotion?
Ideal: LRU-group
LRU hard. We show random OK (see paper)
  Promotions fix errors made by random

## Slide 111: Outline
Overview
NuRAPID Mapping and Placement
NuRAPID Replacement
NuRAPID layout
Results
Conclusion

## Slide 112: Layout: small vs. large d-groups
Key: Conventional caches spread block over subarrays
+ Splits the “decoding” into the address decoder and muxes at the output of the subarrays
e.g., 5-to-1 decoder + 2 2-to-1 muxes better than 10-to-1 decoder
?? 9-to-1 decoder ??
+ more flexibility to deal with defects
+ more tolerant to transient errors
Non-uniform cache: can spread over only one d-group
  So all bits in a block have same access time
Small d-groups (e.g., 64KB of 4 16-KB subarrays)
Fine granularity of access times
Blocks spread over few subarrays
Large d-groups (e.g., 2 MB of 128 16-KB subarrays)
Coarse granularity of access times
Blocks spread over many subarrays
Large d-groups superior for spreading data

## Slide 113: Outline
Overview
NuRAPID Mapping and Placement
NuRAPID Replacement
NuRAPID layout
Results
Conclusion

## Slide 114: Methodology
64 KB, 2-way L1s. 8 MSHRs on d-cache
NuRAPID: 8 MB, 8-way, 1-port, no banking
4 d-groups (14-, 18-, 36-, 44- cycles)
8 d-groups (12-, 19-, 20-, . . . 49- cycles) shown in paper
Compare to:
BASE:
  1 MB, 8-way L2 (11-cycles) + 8-MB, 8-way L3 (43-cycles)
8 MB, 16-way D-NUCA (4 – 31 cycles)
  Multi-banked, infinite-bandwidth interconnect

## Slide 115: Results
SA vs. DA placement (paper figure 4)
As high
As possible

## Slide 116: Results
3.0% better than D-NUCA and up to 15% better

## Slide 117: Conclusions
NuRAPID
  leverage seq. tag-data
  flexible placement, replacement for non-uniform cache
  Achieves 7% overall processor E-D savings
over conventional cache, D-NUCA
  Reduces L2 energy by 77% over D-NUCA
NuRAPID an important design for wire-delay dominated caches

## Slide 118: Managing Wire Delay in Large CMP Caches
Bradford M. Beckmann and David A. Wood
Multifacet Project
University of Wisconsin-Madison
MICRO 2004

## Slide 119: Overview
Managing wire delay in shared CMP caches
Three techniques extended to CMPs
    On-chip Strided Prefetching (not in talk – see paper)
      Scientific workloads: 10% average reduction
      Commercial workloads: 3% average reduction
    Cache Block Migration (e.g. D-NUCA)
      Block sharing limits average reduction to 3%
      Dependence on difficult to implement smart search
    On-chip Transmission Lines (e.g. TLC)
      Reduce runtime by 8% on average
      Bandwidth contention accounts for 26% of L2 hit latency
Combining techniques
    Potentially alleviates isolated deficiencies
      Up to 19% reduction vs. baseline
    Implementation complexity

## Slide 120: Baseline: CMP-SNUCA
L1
I $
L1
D $
CPU 2
L1
I $
L1
D $
CPU 3
L1
D $
L1
I $
CPU 7
L1
D $
L1
I $
CPU 6
L1
D $
L1
I $
CPU 1
L1
D $
L1
I $
CPU 0
L1
I $
L1
D $
CPU 4
L1
I $
L1
D $
CPU 5

## Slide 121: Outline
Global interconnect and CMP trends
Latency Management Techniques
Evaluation
  Methodology
  Block Migration: CMP-DNUCA
  Transmission Lines: CMP-TLC
  Combination: CMP-Hybrid

## Slide 122: Block Migration: CMP-DNUCA
L1
I $
L1
D $
CPU 2
L1
I $
L1
D $
CPU 3
L1
D $
L1
I $
CPU 7
L1
D $
L1
I $
CPU 6
L1
D $
L1
I $
CPU 1
L1
D $
L1
I $
CPU 0
L1
I $
L1
D $
CPU 4
L1
I $
L1
D $
CPU 5
B
A
A
B

## Slide 123: On-chip Transmission Lines
Similar to contemporary off-chip communication
Provides a different latency / bandwidth tradeoff
Wires behave more “transmission-line” like as frequency increases
  Utilize transmission line qualities to our advantage
  No repeaters – route directly over large structures
  ~10x lower latency across long distances
Limitations
  Requires thick wires and dielectric spacing
  Increases manufacturing cost
See “TLC: Transmission Line Caches” Beckman, Wood, MICRO’03

## Slide 124: RC vs. TL Communication
Conventional Global RC Wire
On-chip Transmission Line
Voltage
Voltage
Distance
Vt
Driver
Receiver
Voltage
Voltage
Distance
Vt
Driver
Receiver

## Slide 125
RC Wire vs. TL Design
RC delay dominated
Receiver
Driver
On-chip Transmission Line
Conventional Global RC Wire
LC delay dominated
~0.375 mm
~10 mm
Notes: Many RC wire segments separated by intermediate latches and repeaters
Single LC (inductive – capacitance) product over a distance of approximately 10 mm
  We assumed here voltage mode signaling
  Termination with a digital tuned driver resistance

## Slide 126: On-chip Transmission Lines
Why now? → 2010 technology
  Relative RC delay ↑
  Improve latency by 10x or more
What are their limitations?
  Require thick wires and dielectric spacing
  Increase wafer cost
Presents a different Latency/Bandwidth Tradeoff
Notes:   Wires behave more “transmission line like” as frequency increases
  Let’s use these transmission line qualities to our advantage
  Technology provides a lower-k dielectric

## Slide 127: Latency Comparison

## Slide 128: Bandwidth Comparison
2 transmission line signals
50 conventional signals
Key observation
Transmission lines – route over large structures
Conventional wires – substrate area & vias for repeaters
Notes: This is a cross-sectional view
Shielding and reference planes provide noise isolation and low-loss return paths
Key observation is conventional interconnect requires repeaters
  hence vias and intermediate repeaters

## Slide 129: Transmission Lines: CMP-TLC
CPU 3
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
CPU 2
CPU 1
CPU 0
CPU 4
CPU 5
CPU 6
CPU 7
16
8-byte
links

## Slide 130: Combination: CMP-Hybrid
L1
I $
L1
D $
CPU 2
L1
I $
L1
D $
CPU 3
L1
D $
L1
I $
CPU 7
L1
D $
L1
I $
CPU 6
L1
D $
L1
I $
CPU 1
L1
D $
L1
I $
CPU 0
L1
I $
L1
D $
CPU 4
L1
I $
L1
D $
CPU 5
8
32-byte
links

## Slide 131: Outline
Global interconnect and CMP trends
Latency Management Techniques
Evaluation
  Methodology
  Block Migration: CMP-DNUCA
  Transmission Lines: CMP-TLC
  Combination: CMP-Hybrid

## Slide 132: Methodology
Full system simulation
  Simics
  Timing model extensions
    Out-of-order processor
    Memory system
Workloads
  Commercial
    apache, jbb, otlp, zeus
  Scientific
    Splash: barnes & ocean
    SpecOMP: apsi & fma3d

## Slide 133: System Parameters
Memory System |  | Dynamically Scheduled Processor | 
L1 I & D caches | 64 KB, 2-way, 3 cycles | Clock frequency | 10 GHz
Unified L2 cache | 16 MB, 256x64 KB, 16-way, 6 cycle bank access | Reorder buffer / scheduler | 128 / 64 entries
L1 / L2 cache block size | 64 Bytes | Pipeline width | 4-wide fetch & issue
Memory latency | 260 cycles | Pipeline stages | 30
Memory bandwidth | 320 GB/s | Direct branch predictor | 3.5 KB YAGS
Memory size | 4 GB of DRAM | Return address stack | 64 entries
Outstanding memory request / CPU | 16 | Indirect branch predictor | 256 entries (cascaded)

## Slide 134: Outline
Global interconnect and CMP trends
Latency Management Techniques
Evaluation
  Methodology
  Block Migration: CMP-DNUCA
  Transmission Lines: CMP-TLC
  Combination: CMP-Hybrid

## Slide 135: CMP-DNUCA: Organization
Bankclusters
Local
Inter.
Center
CPU 2
CPU 3
CPU 7
CPU 6
CPU 1
CPU 0
CPU 4
CPU 5

## Slide 136: Hit Distribution: Grayscale Shading
CPU 2
CPU 3
CPU 7
CPU 6
CPU 1
CPU 0
CPU 4
CPU 5
Greater %
of L2 Hits

## Slide 137: CMP-DNUCA: Migration
Migration policy
  Gradual movement
  Increases local hits and reduces distant hits
other
bankclusters
my center
bankcluster
my inter.
bankcluster
my local
bankcluster

## Slide 138: CMP-DNUCA: Hit Distribution Ocean per CPU
CPU 0
CPU 1
CPU 2
CPU 3
CPU 4
CPU 5
CPU 6
CPU 7

## Slide 139: CMP-DNUCA: Hit Distribution Ocean all CPUs
Block migration successfully separates the data sets

## Slide 140: CMP-DNUCA: Hit Distribution OLTP all CPUs

## Slide 141: CMP-DNUCA: Hit Distribution OLTP per CPU
Hit Clustering: Most L2 hits satisfied by the center banks
CPU 0
CPU 1
CPU 2
CPU 3
CPU 4
CPU 5
CPU 6
CPU 7

## Slide 142: CMP-DNUCA: Search
Search policy
  Uniprocessor DNUCA solution: partial tags
    Quick summary of the L2 tag state at the CPU
    No known practical implementation for CMPs
      Size impact of multiple partial tags
      Coherence between block migrations and partial tag state
  CMP-DNUCA solution: two-phase search
    1st phase: CPU’s local, inter., & 4 center banks
    2nd phase: remaining 10 banks
    Slow 2nd phase hits and L2 misses

## Slide 143: CMP-DNUCA: L2 Hit Latency

## Slide 144: CMP-DNUCA Summary
Limited success
  Ocean successfully splits
    Regular scientific workload – little sharing
  OLTP congregates in the center
    Commercial workload – significant sharing
Smart search mechanism
  Necessary for performance improvement
  No known implementations
  Upper bound – perfect search

## Slide 145: Outline
Global interconnect and CMP trends
Latency Management Techniques
Evaluation
  Methodology
  Block Migration: CMP-DNUCA
  Transmission Lines: CMP-TLC
  Combination: CMP-Hybrid

## Slide 146: L2 Hit Latency
Bars Labeled
D: CMP-DNUCA
T: CMP-TLC
H: CMP-Hybrid

## Slide 147: Overall Performance
Transmission lines improve L2 hit and L2 miss latency

## Slide 148: Conclusions
Individual Latency Management Techniques
  Strided Prefetching: subset of misses
  Cache Block Migration: sharing impedes migration
  On-chip Transmission Lines: limited bandwidth
Combination: CMP-Hybrid
  Potentially alleviates bottlenecks
  Disadvantages
    Relies on smart-search mechanism
    Manufacturing cost of transmission lines

## Slide 149: Recap
Initial NUCA designs  Uniprocessors
  NUCA:
    Centralized Partial Tag Array
  NuRAPID:
    Decouples Tag and Data Placement
    More overhead
  L-NUCA
    Fine-Grain NUCA close to the core
  Beckman & Wood:
    Move Data Close to User
    Two-Phase Multicast Search
    Gradual Migration
    Scientific: Data mostly “private”  move close / fast
    Commercial: Data mostly “shared”  moves in the center / “slow”

## Slide 150: Recap – NUCAs for CMPs
Beckman & Wood:
  Move Data Close to User
  Two-Phase Multicast Search
  Gradual Migration
  Scientific: Data mostly “private”  move close / fast
  Commercial: Data mostly “shared”  moves in the center / “slow”
CMP-NuRapid:
  Per core, L2 tag array
    Area overhead
    Tag coherence

## Slide 151
A NUCA Substrate for Flexible CMP Cache Sharing
Jaehyuk Huh, Changkyu Kim †, Hazim Shafi, Lixin Zhang§,
Doug Burger , Stephen W. Keckler †
Int’l Conference on Supercomputing, June 2005
§Austin Research Laboratory IBM Research Division | †Dept. of Computer Sciences The University of Texas at Austin

## Slide 152: Challenges in CMP L2 Caches
L2 Coherence Mechanism
P0
I
D
P1
I
D
P2
I
D
P3
I
D
P4
I
D
P5
I
D
P6
I
D
P7
I
D
I
D
P0
P15
I
D
P0
P14
I
D
P0
P13
I
D
P0
P12
I
D
P0
P11
I
D
P0
P10
I
D
P0
P9
I
D
P0
P8
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
L2
Completely Shared L2
  Private L2 (SD = 1)
  + Small but fast L2 caches
  - More replicated cache blocks
  - Can not share cache capacity
  - Slow remote L2 accesses
  Completely Shared L2 (SD=16)
  + No replicated cache blocks
  + Dynamic capacity sharing
  - Large but slow caches
What is the best sharing degree (SD) ?
  Does granularity affect? (per-application and per-line)
  The effect of increasing wire delay
  Do latency managing techniques affect?
  Partially Shared L2
Partially
Shared L2
Partially
Shared L2
Partially
Shared L2
Partially
Shared L2
L2 Caches for CMPs ?

## Slide 153: Sharing Degree

## Slide 154: Outline
Design space
  Varying sharing degrees
  NUCA caches
  L1 prefetching
MP-NUCA design
Lookup mechanism for dynamic mapping
Results
Conclusion

## Slide 155: Sharing Degree Effect Explained
Latency Shorter: Smaller Sharing Degree
  Each partition is smaller
Hit Rate higher: Larger Sharing Degree
  Larger partitions means more capacity
Inter-processor communication: Larger Sharing Degree
  Through the shared cache
L1 Coherence more Expensive: Larger Sharing Degree
  More L1’s share an L2 Partition
L2 Coherence more expensive: Smaller Sharing Degree
  More L2 partitions

## Slide 156: Design Space
Determining sharing degree
  Sharing Degree (SD): number of processors in a shared L2
  Miss rates vs. hit latencies
  Sharing differentiation: per-application and per-line
    Private vs. Shared data
    Divide address space into shared and private
Latency management for increasing wire delay
  Static mapping (S-NUCA) and dynamic mapping (D-NUCA)
  D-NUCA : move frequently accessed blocks closer to processors
  Complexity vs. performance
The effect of L1 prefetching on sharing degree
  Simple strided prefetching
  Hide long L2 hit latencies

## Slide 157: Sharing Differentiation
Private Blocks
  Lower sharing degree better
  Reduced latency
  Caching efficiency maintained
    No one else will have cached it anyhow
Shared Blocks
  Higher sharing degree better
  Reduces the number of copies
Sharing Differentiation
  Address Space into Shared and Private
  Assign Different Sharing Degrees

## Slide 158: Flexible NUCA Substrate
Bank-based non-uniform caches, supporting multiple sharing degrees
Directory-based coherence
  L1 coherence : sharing vectors embedded in L2 tags
  L2 coherence : on-chip directory
P0
I
D
P1
I
D
P2
I
D
P3
I
D
P4
I
D
P5
I
D
P6
I
D
P7
I
D
I
D
P0
P15
I
D
P0
P14
I
D
P0
P13
I
D
P0
P12
I
D
P0
P11
I
D
P0
P10
I
D
P0
P9
I
D
P0
P8
Directory for
L2 coherence
Support SD=1, 2, 4, 8, and 16
L2 Banks
How to find a block?
P4
I
D
P5
I
D
P6
I
D
P7
I
D
Static mapping
S-NUCA
P4
I
D
P5
I
D
P6
I
D
P7
I
D
Static mapping
Dynamic mapping
D-NUCA 1D
P4
I
D
P5
I
D
P6
I
D
P7
I
D
Dynamic mapping
Dynamic mapping
D-NUCA 2D
DNUCA-1D:
block  one column
DNUCA-2D:
block  any column
Higher associativity

## Slide 159: Lookup Mechanism
Use partial-tags [Kessler et al. ISCA 1989]
Searching problem in shared D-NUCA
  Centralized tags : multi-hop latencies from processors to tags
  Fully replicated tags : huge area overheads and complexity
Distributed partial tags: partial-tag fragment for each column
Broadcast lookups of partial tags can occur in D-NUCA 2D
P0
I
D
P1
I
D
P2
I
D
P3
I
D
D-NUCA
Partial tag fragments

## Slide 160: Methodology
MP-sauce: MP-SimpleScalar + SimOS-PPC
Benchmarks: commercial applications and SPLASH 2
Simulated system configuration
  16 processors, 4 way out-of-order + 32KB I/D L1
  16 X 16 bank array, 64KB, 16-way, 5 cycle bank access latency
  1 cycle hop latency
  260 cycle memory latency, 360 GB/s bandwidth
Simulation parameters
Sharing degree (SD) | 1, 2, 4, 8, and 16
Mapping policies | S-NUCA, D-NUCA-1D, and D- NUCA-2D
D-NUCA search | distributed partial tags and perfect search
L1 prefetching | stride prefetching (positive/negative unit and non-unit stride)

## Slide 161: Sharing Degree
L1 miss latencies with S-NUCA (SD=1, 2, 4, 8, and 16)
Hit latency increases significantly beyond SD=4
The best shared degrees: 2 or 4

## Slide 162: D-NUCA: Reducing Latencies
NUCA hit latencies with SD=1 to 16
D-NUCA 2D perfect reduces hit latencies by 30%
Searching overheads are significant in both 1D and 2D D-NUCAs
D-NUCAs with
perfect search
Perfect search 
Auto-magically go to the right
block
Hit latency != performance

## Slide 163: S-NUCA vs. D-NUCA
D-NUCA improves performance but not as much with realistic searching
The best SD may be different compared to S-NUCA

## Slide 164: S-NUCA vs. D-NUCA
Fixed best: fixed shared degree for all applications
Variable best: per-application best sharing degree
D-NUCA has marginal performance improvement due to the searching overhead
Per-app. sharing degrees improved D-NUCA more than S-NUCA
What is the base? Are the bars comparable?

## Slide 165: Per-line Sharing Degree
Per-line sharing degree: different sharing degrees for different classes of cache blocks
Private vs. shared sharing degrees
  Private : place private blocks in close banks
  Shared : reduce replication
Approximate evaluation
  Per-line sharing degree is effective for two applications (6-7% speedups)
  Best combination: private SD= 1 or 2 and shared SD = 16

## Slide 166: Conclusion
Best sharing degree is 4
Dynamic migration
  Does not change the best sharing degree
  Does not seem to be worthwhile in the context of this study
  Searching problem is still yet to be solved
  High design complexity and energy consumption
L1 prefetching
  7 % performance improvement (S-NUCA)
  Decrease the best sharing degree slightly
Per-line sharing degrees provide the benefit of both high and low sharing degree

## Slide 167: Victim Replication: Maximizing Capacity while Hiding Wire Delay in Tiled Chip Multiprocessors
Michael Zhang & Krste Asanovic
Computer Architecture Group
MIT CSAIL
Int’l Conference on Computer Architecture, 2005
Slides mostly directly from the author’s presentation

## Slide 168: Current Research on NUCAs
Intra-Chip Switch
core
L1$
core
L1$
core
L1$
core
L1$
Targeting uniprocessor machines
Data Migration: Intelligently place data such that the active working set resides in cache slices closest to the processor
  D-NUCA [ASPLOS-X, 2002]
  NuRAPID [MICRO-37, 2004]

## Slide 169: Data Migration does not Work Well with CMPs
Problem: The unique copy of the data cannot be close to all of its sharers
Behavior: Over time, shared data migrates to a location equidistant to all sharers
  Beckmann & Wood [MICRO-36, 2004]
core
L1$
Intra-Chip Switch
core
L1$
core
L1$
core
L1$
Intra-Chip Switch
core
L1$
core
L1$
core
L1$
core
L1$

## Slide 170: This Talk: Tiled CMPs w/ Directory Coherence
Tiled CMPs for Scalability
  Minimal redesign effort
  Use directory-based protocol for scalability
Managing the L2s to minimize the effective access latency
  Keep data close to the requestors
  Keep data on-chip
Two baseline L2 cache designs
  Each tile has own private L2
  All tiles share a single distributed L2
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
SW
c
L1
L2$
Data
L2$
Tag
core
L1$
L2$
Slice
Data
Switch
L2$
Slice
Tag

## Slide 171: Private L2 Design Provides Low Hit Latency
core
L1$
Private
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Private
L2$
Data
Switch
DIR
L2$
Tag
Sharer j
Sharer i
The local L2 slice is used as a private L2 cache for the tile
  Shared data is duplicated in the L2 of each sharer
  Coherence must be kept among all sharers at the L2 level
On an L2 miss:
  Data not on-chip
  Data available in the private L2 cache of another chip

## Slide 172: Private L2 Design Provides Low Hit Latency
core
L1$
Private
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Private
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Private
L2$
Data
Switch
DIR
L2$
Tag
Home Node
statically determined by address
Owner/Sharer
Requestor
The local L2 slice is used as a private L2 cache for the tile
  Shared data is duplicated in the L2 of each sharer
  Coherence must be kept among all sharers at the L2 level
On an L2 miss:
  Data not on-chip
  Data available in the private L2 cache of another tile (cache-to-cache reply-forwarding)
Off-chip
Access

## Slide 173: Private L2 Design Provides Low Hit Latency
core
L1$
Private
L2$
Data
Switch
DIR
L2$
Tag
Characteristics:
  Low hit latency to resident L2 data
  Duplication reduces on-chip capacity
Works well for benchmarks with working sets that fits into the local L2 capacity
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2
SW
c
L1
Dir
Private
L2

## Slide 174: Shared L2 Design Provides Maximum Capacity
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Requestor
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Owner/Sharer
Off-chip
Access
All L2 slices on-chip form a distributed shared L2, backing up all L1s
  No duplication, data kept in a unique L2 location
  Coherence must be kept among all sharers at the L1 level
On an L2 miss:
  Data not in L2
  Coherence miss (cache-to-cache reply-forwarding)
Home Node
statically determined by address

## Slide 175: Shared L2 Design Provides Maximum Capacity
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
SW
c
L1
Dir
Shared
L2
Characteristics:
  Maximizes on-chip capacity
  Long/non-uniform latency to L2 data
Works well for benchmarks with larger working sets to minimize expensive off-chip accesses
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2

## Slide 176: Victim Replication:
Shared design characteristics:
  Long/non-uniform L2 hit latency
  Maximum L2 capacity
Private design characteristics:
  Low L2 hit latency to resident L2 data
  Reduced L2 capacity
A Hybrid Combining the Advantages
of Private and Shared Designs

## Slide 177: Victim Replication
Shared design characteristics:
  Long/non-uniform L2 hit latency
  Maximum L2 capacity
Private design characteristics:
  Low L2 hit latency to resident L2 data
  Reduced L2 capacity
Victim Replication: Provides low hit latency while keeping the working set on-chip
A Hybrid Combining the Advantages
of Private and Shared Designs

## Slide 178: Victim Replication: A Variant of the Shared Design
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Sharer i
Sharer j
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Home Node
Implementation: Based on the shared design
L1 Cache: Replicates shared data locally for fastest access latency
L2 Cache: Replicates the L1 capacity victims  Victim Replication

## Slide 179: The Local Tile Replicates the L1 Victim During Eviction
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Sharer i
Sharer j
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Home Node
Replicas: L1 capacity victims stored in the Local L2 slice
Why? Reused in the near future with fast access latency
Which way in the target set to use to hold the replica?

## Slide 180: The Replica should NOT Evict More Useful Cache Blocks from the L2 Cache
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Sharer j
core
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
Home Node
Never evict actively shared home blocks in favor of a replica
Replica is NOT always made
Sharer i
Invalid blocks
Home blocks w/o sharers
Existing replicas
Home blocks w/ sharers

## Slide 181: Victim Replication Dynamically Divides the Local L2 Slice into Private & Shared Partitions
core
L1$
Switch
DIR
L2$
Tag
core
L1$
Switch
DIR
L2$
Tag
core
L1$
Switch
DIR
L2$
Tag
Shared L2$
Private L2$
(filled w/ L1 victims)
Shared
L2$
Private
L2$
Private Design
Shared Design
Victim Replication
Victim Replication dynamically creates a large local private, victim cache for the local L1 cache

## Slide 182: Experimental Setup
Processor Model: Bochs
  Full-system x86 emulator running Linux 2.4.24
  8-way SMP with single in-order issue cores
All latencies normalized to one 24-F04 clock cycle
  Primary caches reachable in one cycle
Cache/Memory Model
  4x2 Mesh with 3 Cycle near-neighbor latency
  L1I$ & L1D$: 16KB each, 16-Way, 1-Cycle, Pseudo-LRU
  L2$: 1MB, 16-Way, 6-Cycle, Random
  Off-chip Memory: 256 Cycles
Worst-case cross chip contention-free latency is 30 cycles
Applications
Linux 2.4.24
DRAM
c
L1
L2
S
D
c
L1
L2
S
D
c
L1
L2
S
D
c
L1
L2
S
D
c
L1
L2
S
D
c
L1
L2
S
D
c
L1
L2
S
D
c
L1
L2
S
D
Notes: OK. Hopefully by now I’ve at least got you thinking that “ok. This maaaaay work”. And let’s move on to the evaluation part of the talk. And also in my opinion, more interesting part. Before that though, we have to first get through some mandatory slides about the system setup.
So for the processor model, … read off.
As for the cache and memory model. We have developed a detailed simulator in-house that models the cache and memory hierarchy of the CMP. The protocol used is the four state MESI.
One problem we faced while evaluating the scheme is the long running time of the benchmarks. So to make the ISCA deadline, we needed to do something about it. Thanks to the SMART group at CMU, we extended their work in statistical sampling to multiprocessors and cut down and simulation time. Another problem we faced was system variation, especially in combination with sampling. So we decided to run each benchmark 10 times and saw that variation is small compared to the results.

## Slide 183: The Plan for Results
Three configurations evaluated:
  Private L2 design  L2P
  Shared L2 design  L2S
  Victim replication  L2VR
Three suites of workloads used:
  Multi-threaded workloads
  Single-threaded workloads
  Multi-programmed workloads
Results show Victim Replication’s Performance Robustness
Notes: OK now time for results and here is the plan. We first present the results for multi-threaded benchmarks. Then we move on to single-threaded benchmarks as a special case of multi-threaded benchmarks. Lastly we will present some multi-programmed benchmarks. Note that the multi-programmed results are not in the paper as we obtained them after the cam-ready deadline. The main result shown here is the average data fetch latency experienced by a processor in 24-FO4 cycles.

## Slide 184: Multithreaded Workloads
8 NASA Advanced Parallel Benchmarks:
  Scientific (computational fluid dynamics)
  OpenMP (loop iterations in parallel)
  Fortran: ifort –v8 –O2 –openmp
2 OS benchmarks
  dbench: (Samba) several clients making file-centric system calls
  apache: web server with several clients (via loopback interface)
  C: gcc 2.96
1 AI benchmark: Cilk checkers
  spawn/sync primitives: dynamic thread creation/scheduling
  Cilk: gcc 2.96, Cilk 5.3.2
Notes: We have a good mix of benchmarks
Read off

## Slide 185: Average Access Latency
Their working set fits in the private L2
Notes: The three metrics are shown in the figures. Please do not pay attention to the details of the results on this slide as I will talk about them in detail later. II just want to introduce what they are. First thing to notice is that the performance of L2VC is always slightly better than L2S but worse than L2VR. Thus we ignore L2VC from the rest of the discussion. The data access breakdown shows how a cache access is serviced, either by a hit in the L1, or a hit in the Local L2, or a hit in the non-local L2, or from Memory. The off-chip miss rate is the same as the off-chip memory accesses in the data access breakdown diagram, just that it is magnified here for ease of reading.

## Slide 186: Average Access Latency
Working set >> all of L2s combined
Lower latency of L2P dominates – no capacity advantage for L2S
Notes: The three metrics are shown in the figures. Please do not pay attention to the details of the results on this slide as I will talk about them in detail later. II just want to introduce what they are. First thing to notice is that the performance of L2VC is always slightly better than L2S but worse than L2VR. Thus we ignore L2VC from the rest of the discussion. The data access breakdown shows how a cache access is serviced, either by a hit in the L1, or a hit in the Local L2, or a hit in the non-local L2, or from Memory. The off-chip miss rate is the same as the off-chip memory accesses in the data access breakdown diagram, just that it is magnified here for ease of reading.

## Slide 187: Average Access Latency
Working set fits in L2
Higher miss rate with L2P than L2S
Still lower latency of L2P dominates since miss rate is relatively low
Notes: The three metrics are shown in the figures. Please do not pay attention to the details of the results on this slide as I will talk about them in detail later. II just want to introduce what they are. First thing to notice is that the performance of L2VC is always slightly better than L2S but worse than L2VR. Thus we ignore L2VC from the rest of the discussion. The data access breakdown shows how a cache access is serviced, either by a hit in the L1, or a hit in the Local L2, or a hit in the non-local L2, or from Memory. The off-chip miss rate is the same as the off-chip memory accesses in the data access breakdown diagram, just that it is magnified here for ease of reading.

## Slide 188: Average Access Latency
Much lower L2 miss rate with L2S
L2S not that much better than L2P
Notes: The three metrics are shown in the figures. Please do not pay attention to the details of the results on this slide as I will talk about them in detail later. II just want to introduce what they are. First thing to notice is that the performance of L2VC is always slightly better than L2S but worse than L2VR. Thus we ignore L2VC from the rest of the discussion. The data access breakdown shows how a cache access is serviced, either by a hit in the L1, or a hit in the Local L2, or a hit in the non-local L2, or from Memory. The off-chip miss rate is the same as the off-chip memory accesses in the data access breakdown diagram, just that it is magnified here for ease of reading.

## Slide 189: Average Access Latency
Working set fits on local L2 slice
Uses thread migration a lot
With L2P most accesses are to remote L2 slices after thread migration
Notes: The three metrics are shown in the figures. Please do not pay attention to the details of the results on this slide as I will talk about them in detail later. II just want to introduce what they are. First thing to notice is that the performance of L2VC is always slightly better than L2S but worse than L2VR. Thus we ignore L2VC from the rest of the discussion. The data access breakdown shows how a cache access is serviced, either by a hit in the L1, or a hit in the Local L2, or a hit in the non-local L2, or from Memory. The off-chip miss rate is the same as the off-chip memory accesses in the data access breakdown diagram, just that it is magnified here for ease of reading.

## Slide 190: Average Access Latency, with Victim Replication
 | BT | CG | EP | FT | IS | LU | MG | SP | apache | dbench | checkers

## Slide 191: Average Access Latency, with Victim Replication
 | BT | CG | EP | FT | IS | LU | MG | SP | apache | dbench | checkers
1st | L2VR | L2P | L2VR | L2P | Tied | L2P | L2VR | L2P | L2P | L2P | L2VR
2nd | L2P 0.1% | L2VR 32.0% | L2S 18.5% | L2VR 3.5% | Tied | L2VR 4.5% | L2S 17.5% | L2VR 2.5% | L2VR 3.6% | L2VR 2.1% | L2S 14.4%
3rd | L2S 12.2% | L2S 111% | L2P 51.6% | L2S 21.5% | Tied | L2S 40.3% | L2P 35.0% | L2S 22.4% | L2S 23.0% | L2S 11.5% | L2P 29.7%

## Slide 192: FT: Private Best When Working Set Fits in Local L2 Slice
Average Data
Access Latency
Access
Breakdown
Off-chip misses
Hits in Non-Local L2
Hits in Local L2
Hits in L1
The large capacity of the shared design is not utilized as shared and private designs have similar off-chip miss rates
The short access latency of the private design yields better performance
Victim replication mimics the private design by creating replicas, with performance within 5%
Why L2VR worse than L2P?
  Must first miss bring in L1 and then replicate
L2P
L2S
L2VR
L2P
L2S
L2VR
Best
Very Good
O.K.
Not Good …

## Slide 193: CG: Large Number of L2 Hits Magnifies Latency Advantage of Private Design
The latency advantage of the private design is magnified by the large number of L1 misses that hits in L2 (>9%)
Victim replication edges out shared design with replicas, by falls short of the private design
Average Data
Access Latency
Access
Breakdown
L2P
L2S
L2VR
L2P
L2S
L2VR
Off-chip misses
Hits in Non-Local L2
Hits in Local L2
Hits in L1

## Slide 194: MG: VR Best When Working Set Does not Fit in Local L2
Off-chip misses
Hits in Non-Local L2
Hits in Local L2
Hits in L1
The capacity advantage of the shared design yields many fewer off-chip misses
The latency advantage of the private design is offset by costly off-chip accesses
Victim replication is even better than shared design by creating replicas to reduce access latency
L2P
L2S
L2VR
L2P
L2S
L2VR
Average Data
Access Latency
Access
Breakdown

## Slide 195: Checkers: Thread Migration  Many Cache-Cache Transfers
Virtually no off-chip accesses
Most of hits in the private design come from more expensive cache-to-cache transfers
Victim replication is even better than shared design by creating replicas to reduce access latency
Average Data
Access Latency
Access
Breakdown
L2P
L2S
L2VR
L2P
L2S
L2VR
Off-chip misses
Hits in Non-Local L2
Hits in Local L2
Hits in L1

## Slide 196: Victim Replication Adapts to the Phases of the Execution
CG
FT
% of replica in cache
0
5.0 Billion Instrs
0
6.6 Billion Instrs
Each graph shows the percentage of replicas in the L2 caches averaged across all 8 caches
Notes: VR has two important properties I hope you can take away. First is that VR is an adaptive algorithm that adapt to the phases of the benchmarks. Shown here are two time-varying graphs of the percentage of victim replicas in the cache. This is the average of all 8 caches. On the left is CG, you clearly observe the two phases, and on the right is FT, where you observe the repetition.
Second is that the size of the “victim cache” is very large, usually on the order of 100 MB, which is much larger than the conventional victim cache in hardware.

## Slide 197: Single-Threaded Benchmarks
SpecINT2000 are used as Single-Threaded benchmarks
  Intel C compiler version 8.0.055
Victim replication automatically turns the cache hierarchy into three levels with respect to the node hosting the active thread
Active
Thread
L1$
Shared
L2$
Data
Switch
DIR
L2$
Tag
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2

## Slide 198: Single-Threaded Benchmarks
SpecINT2000 are used as Single-Threaded benchmarks
  Intel C compiler version 8.0.055
Victim replication automatically turns the cache hierarchy into three levels with respect to the node hosting the active thread
  Level 1: L1 cache
  Level 2: All remote L2 slices
  “Level 1.5”: The local L2 slice acts as a large private victim cache which holds data used by the active thread
Active
Thread
L1$
Mostly
Replica
Data
Switch
DIR
L2$
Tag
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
T
L1
Dir
L1.5
with
replicas
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2
SW
c
L1
Dir
Shared
L2

## Slide 199: Three Level Caching
mcf
bzip
% of replica in cache
0
3.8 Billion Instrs
0
1.7 Billion Instrs
Thread running
on one tile
Thread moving
between two tiles
Each graph shows the percentage of replicas in the L2 caches for each of the 8 caches

## Slide 200: Single-Threaded Benchmarks
Average Data Access Latency
Victim replication is the best policy in 11 out of 12 benchmarks with an average saving of 23% over shared design and 6% over private design

## Slide 201: Multi-Programmed Workloads
Average Data Access Latency
Created using SpecINTs, each with 8 different programs chosen at random
1st : Private design, always the best
2nd : Victim replication, performance within 7% of private design
3rd : Shared design, performance within 27% of private design
Notes: For multi-programmed benchmarks. You’d expect that the result lie somewhere between multi-threaded and single-threaded benchmarks, and they indeed do. And on average savings is 19% over L2S.

## Slide 202: Concluding Remarks
Victim Replication is
Simple: Requires little modification from a shared L2 design
Scalable: Scales well to CMPs with large number of nodes by using a directory-based cache coherence protocol
Robust: Works well for a wide range of workloads
  Single-threaded
  Multi-threaded
  Multi-programmed

## Slide 203: Optimizing Replication, Communication, and Capacity Allocation in CMPs
Z. Chishti, M. D. Powell, and T. N. Vijaykumar
Proceedings of the 32nd International Symposium on Computer Architecture, June 2005.
Slides mostly by the paper authors and by Siddhesh Mhambrey’s course presentation CSE520

## Slide 204: Cache Organization
Goal:
  Utilize Capacity Effectively- Reduce capacity misses
  Mitigate Increased Latencies- Keep wire delays small
Shared
  High Capacity but increased latency
Private
  Low Latency but limited capacity
Neither private nor shared caches achieve both goals

## Slide 205: CMP-NuRAPID: Novel Mechanisms
Controlled Replication
  Avoid copies for some read-only shared data
In-Situ Communication
  Use fast on-chip communication to avoid coherence miss of read-write-shared data
Capacity Stealing
  Allow a core to steal another core’s unused capacity
Hybrid cache
  Private Tag Array and Shared Data Array
  CMP-NuRAPID(Non-Uniform access with Replacement and Placement using Distance associativity)
Performance
  CMP-NuRAPID improves performance by 13% over a shared cache and 8% over a private cache for three commercial multithreaded workloads
  Three novel mechanisms to exploit the changes in Latency-Capacity tradeoff

## Slide 206: CMP-NuRAPID
Non-Uniform Access and Distance Associativity
  Caches divided into d-groups
  D-group preference
  Staggered
4-core CMP with CMP-NuRAPID

## Slide 207: CMP-NuRapid Tag and Data Arrays
Tag arrays snoop on a bus to maintain coherence
Data
Array
Memory
Crossbar or other interconnect
P1
Tag 1
Bus
d-group 0
P2
Tag 2
P0
Tag 0
P3
Tag 3
d-group 1
d-group 2
d-group 3

## Slide 208: CMP-NuRAPID Organization
Private Tag Array
Shared Data Array
Leverages forward and reverse pointers
Single copy of block shared by multiple tags
Data for one core in different d-groups
Extra Level of Indirection for novel mechanisms

## Slide 209: Mechanisms
Controlled Replication
In-Situ Communication
Capacity Stealing

## Slide 210: Controlled Replication Example
0
1
k
0
1
k
A,set0,tagP0
0
1
k
set #
set #
frame #
frame #
P0 has a clean block A in its tag and d-group 0
P0 tag
P1 tag
Data Arrays
d-group 0
d-group 1
Atag,grp0,frm1
0
1
k

## Slide 211: Controlled Replication Example (cntd.)
0
1
k
0
1
k
A,set0,tagP0
0
1
k
set #
set #
frame #
frame #
P1 misses on a read to A
P1’s tag gets a pointer to A in d-group 0
P0 tag
P1 tag
Data Arrays
d-group 0
d-group 1
Atag,grp0,frm1
0
1
k
Atag,grp0,frm1
First access points to the same copy
No replica is made

## Slide 212: Controlled Replication Example (cntd.)
0
1
k
0
1
k
A,set0,tagP0
0
1
k
set #
set #
frame #
frame #
P0 tag
P1 tag
Data Arrays
d-group 0
d-group 1
Atag,grp0,frm1
0
1
k
Atag,grp1,frmk
A,set0,tagP1
P1 reads A again
P1 replicates A in its closest d-group 1
Increases Effective Capacity
Second access makes a copy
Data that is reused is reused multiple times

## Slide 213: Shared Copies - Backpointer
0
1
k
0
1
k
A,set0,tagP0
0
1
k
set #
set #
frame #
frame #
Only P0 can replace A
P0 tag
P1 tag
Data Arrays
d-group 0
d-group 1
Atag,grp0,frm1
0
1
k
Atag,grp0,frm1

## Slide 214: Mechanisms
Controlled Replication
In-Situ Communication
Capacity Stealing

## Slide 215: In-Situ Communication
Write to Shared Data
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2

## Slide 216: In-Situ Communication
Write to Shared Data
  Invalidate all other copies
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2

## Slide 217: In-Situ Communication
Write to Shared Data
  Invalidate all other copies
  Write new value on own copy
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2

## Slide 218: In-Situ Communication
Write to Shared Data
  Invalidate all other copies
  Write new value on own copy
  Readers read on-demand
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2
Communication & Coherence
Overhead

## Slide 219: In-Situ Communication
Write to Shared Data
  Update All Copies
  Waste When Current Readers don’t need the value anymore
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2
Communication & Coherence
Overhead

## Slide 220: In-Situ Communication
Only one copy
Writer Updates the copy
Readers read it directly
Lower Communication and Coherence Overheads
Core
L1I
L1D
L2
Core
L1I
L1D
Core
L1I
L1D
Core
L1I
L1D
L2
L2
L2

## Slide 221: In-Situ Communication
Enforce single copy of read-write shared block in L2 and keep the block in communication (C) state
Requires change in the coherence protocol
Replace M to S transition by M to C transition
Fast communication with capacity savings
Notes: Whenever there is a write in the shared state, the copy of the block in the sharers is invalidated and the writer has the modified copy. On a subsequent read, the reader incurs the penalty of a coherence miss to obtain data from writer and makes new copy in its private cache. This implies slow access. Idea is that each write is read more than once. In C state, writer writes the copy and reader in C state reads it without incurring a miss.

## Slide 222: Mechanisms
Controlled Replication
In-Situ Communication
Capacity Stealing

## Slide 223: Capacity Stealing
Demotion:
  Demote less frequently used data to un-used frames in d-groups closer to core with less capacity demands.
Promotion:
  if tag hit occurs on a block in farther d-group promote it
Data for one core in different d-groups
Use of unused capacity in a neighboring core

## Slide 224: Placement and Promotion
Private Blocks (E)
Initially:
  In the closest d-group
Hit in private data not in closest d-group
  Promote to closets d-group
Shared Blocks
Rules for Controller Replication and In-Situ Communication apply
Never Demoted

## Slide 225: Demotion and Replacement
Data Replacement
  Similar to conventional caches
  Occurs on cache misses
  Data is evicted
Distance Replacement
  Unique to NuRAPID
  Occurs on demotion
  Only data moves

## Slide 226: Data Replacement
A block in the same cache set as the cache miss
Order of preference
  Invalid
    No cost
  Private
    Only one core needs the replaced block
  Shared
    Multiple cores may need the replaced block
LRU within each category
Replacing an invalid block or a block in the farthest d-group creates only space for the tag
  Need to find space for the data as well

## Slide 227: Data Replacement
Private block in farthest d-group
  Evicted
  Space created for data in the farthest d-group
Shared
  Only tag evicted
  Data stays there
  No space for data
  Only the backpointer-referenced core can replace these
Invalid
  No space for data
Multiple demotions may be needed
  Stop at some d-group at random and evict

## Slide 228: Methodology
Full-system simulation of 4-core CMP using Simics
CMP NuRAPID: 8 MB, 8-way
4 d-groups,1-port for each tag array and data d-group
Compare to
  Private 2 MB, 8-way, 1-port per core
  CMP-SNUCA: Shared with non-uniform-access, no replication

## Slide 229: Performance: Multithreaded Workloads
Ideal: capacity of shared, latency of private
CMP NuRAPID: Within 3% of ideal cache on average
Chart: 
 | 1.06 | 1.07 | 1.15 | 1.24 | 0 | 0 | 1.02 | 1.02 | 1.085 | 1.1 | 0 | 0 | 1.06 | 1.07 | 1.14 | 1.16 | 0 | 0 | 1.046 | 1.052 | 1.127 | 1.167
a b c d
Performance relative to shared
a: CMP-SNUCA b: Private c: CMP NuRAPID d: Ideal
oltp
apache
Average
specjbb

## Slide 230: Performance: Multiprogrammed Workloads
CMP NuRAPID outperforms shared, private, and CMP-SNUCA
Chart: 
 | 1.12 | 1.3 | 1.47 | 0 | 0 | 1.04 | 1.1 | 1.14 | 0 | 0 | 1.08 | 1.25 | 1.34 | 0 | 0 | 1.04 | 1.1 | 1.15 | 0 | 0 | 1.07 | 1.187 | 1.275
a b c
a: CMP-SNUCA b: Private c: CMP NuRAPID
MIX1
MIX2
Average
MIX3
MIX4
Performance relative to shared

## Slide 231: Access distribution: Multiprogrammed workloads
CMP NuRAPID: 93% hits to closest d-group
CMP-NuRAPID vs Private: 11- vs 10-cycle average hit latency
a b c
Chart: 
 | 0.92 | 0.85 | 0.913 | 0 | 0 | 0.955 | 0.905 | 0.95 | 0 | 0 | 0.88 | 0.845 | 0.87 | 0 | 0 | 0.89 | 0.86 | 0.88 | 0 | 0 | 0.911 | 0.858 | 0.903
 | 0.08 | 0.15 | 0.087 | 0 | 0 | 0.045 | 0.095 | 0.05 | 0 | 0 | 0.12 | 0.185 | 0.13 | 0 | 0 | 0.11 | 0.14 | 0.12 | 0 | 0 | 0.089 | 0.142 | 0.097
Cache Hits
Cache Misses
Fraction of total accesses
MIX1
MIX2
Average
MIX3
MIX4
a b c
a: Shared/CMP-SNUCA b: Private c: CMP NuRAPID

## Slide 232: Summary

## Slide 233: Conclusions
CMPs change the Latency Capacity tradeoff
Controlled Replication, In-Situ Communication and Capacity Stealing are novel mechanisms to exploit the change in the Latency-Capacity tradeoff
CMP-NuRAPID is a hybrid cache that uses incorporates the novel mechanisms
For commercial multi-threaded workloads– 13% better than shared, 8% better than private
For multi-programmed workloads– 28% better than shared, 8% better than private

## Slide 234: Cooperative Caching for Chip Multiprocessors
Jichuan Chang and Guri Sohi
Int’l Conference on Computer Architecture, June 2006

## Slide 235: Yet Another Hybrid CMP Cache - Why?
Private cache based design
  Lower latency and per-cache associativity
  Lower cross-chip bandwidth requirement
  Self-contained for resource management
  Easier to support QoS, fairness, and priority
Need a unified framework
  Manage the aggregate on-chip cache resources
  Can be adopted by different coherence protocols

## Slide 236: CMP Cooperative Caching
Form an aggregate global cache via cooperative private caches
  Use private caches to attract data for fast reuse
  Share capacity through cooperative policies
  Throttle cooperation to find an optimal sharing point
Inspired by cooperative file/web caches
  Similar latency tradeoff
  Similar algorithms
P
L2
L1I
L1D
P
L2
L1I
L1D
P
L2
L1I
L1D
P
L2
L1I
L1D
Network

## Slide 237: Outline
Introduction
CMP Cooperative Caching
Hardware Implementation
Performance Evaluation
Conclusion

## Slide 238: Policies to Reduce Off-chip Accesses
Cooperation policies for capacity sharing
  (1) Cache-to-cache transfers of clean data
  (2) Replication-aware replacement
  (3) Global replacement of inactive data
Implemented by two unified techniques
  Policies enforced by cache replacement/placement
  Information/data exchange supported by modifying the coherence protocol

## Slide 239: Policy (1) - Make use of all on-chip data
Don’t go off-chip if on-chip (clean) data exist
  Existing protocols do that for dirty data only
    Why? When clean-shared have to decide who responds
    In SMPs no significant benefit to doing that
Beneficial and practical for CMPs
  Peer cache is much closer than next-level storage
  Affordable implementations of “clean ownership”
Important for all workloads
  Multi-threaded: (mostly) read-only shared data
  Single-threaded: spill into peer caches for later reuse

## Slide 240: Policy (2) – Control replication
Intuition – increase # of unique on-chip data
  SINGLETS
Latency/capacity tradeoff
  Evict singlets only when no invalid or replicates exist
    If all singlets pick LRU
  Modify the default cache replacement policy
“Spill” an evicted singlet into a peer cache
  Can further reduce on-chip replication
  Which cache? Choose at Random

## Slide 241: Policy (3) - Global cache management
Approximate global-LRU replacement
  Combine global spill/reuse history with local LRU
Identify and replace globally inactive data
  First become the LRU entry in the local cache
  Set as MRU if spilled into a peer cache
  Later become LRU entry again: evict globally
1-chance forwarding (1-Fwd)
  Blocks can only be spilled once if not reused

## Slide 242: 1-Chance Forwarding
Keep Recirculation Count with each block
Initially RC = 0
When evicting a singlet w/ RC = 0
  Set it’s RC to 1
When evicting:
  RC--
  If RC = 0 discard
If block is touched
  RC = 0
  Give it another chance

## Slide 243: Cooperation Throttling
Why throttling?
  Further tradeoff between capacity/latency
Two probabilities to help make decisions
  Cooperation probability: Prefer singlets over replicates?
    control replication
  Spill probability: Spill a singlet victim?
    throttle spilling
Shared
Private
Cooperative Caching
CC 100%
Policy (1)
CC 0%

## Slide 244: Outline
Introduction
CMP Cooperative Caching
Hardware Implementation
Performance Evaluation
Conclusion

## Slide 245: Hardware Implementation
Requirements
  Information: singlet, spill/reuse history
  Cache replacement policy
  Coherence protocol: clean owner and spilling
Can modify an existing implementation
Proposed implementation
  Central Coherence Engine (CCE)
  On-chip directory by duplicating tag arrays

## Slide 246: Duplicate Tag Directory
2.3% of total

## Slide 247: Information and Data Exchange
Singlet information
  Directory detects and notifies the block owner
Sharing of clean data
  PUTS: notify directory of clean data replacement
  Directory sends forward request to the first sharer
Spilling
  Currently implemented as a 2-step data transfer
  Can be implemented as recipient-issued prefetch

## Slide 248: Outline
Introduction
CMP Cooperative Caching
Hardware Implementation
Performance Evaluation
Conclusion

## Slide 249: Performance Evaluation
Full system simulator
  Modified GEMS Ruby to simulate memory hierarchy
  Simics MAI-based OoO processor simulator
Workloads
  Multithreaded commercial benchmarks (8-core)
    OLTP, Apache, JBB, Zeus
  Multiprogrammed SPEC2000 benchmarks (4-core)
    4 heterogeneous, 2 homogeneous
Private / shared / cooperative schemes
  Same total capacity/associativity

## Slide 250: Multithreaded Workloads - Throughput
CC throttling - 0%, 30%, 70% and 100%
  Same for spill and replication policy
Ideal – Shared cache with local bank latency

## Slide 251: Multithreaded Workloads - Avg. Latency
Low off-chip miss rate
High hit ratio to local L2
Lower bandwidth needed than a shared cache

## Slide 252: Multiprogrammed Workloads
L1
Local L2
Remote L2
Off-chip
L1
Local L2
Remote L2
Off-chip
CC = 100%

## Slide 253: Comparison with Victim Replication
SPECOMP
Single- threaded
Normalized Performance

## Slide 254: Conclusion
CMP cooperative caching
  Exploit benefits of private cache based design
  Capacity sharing through explicit cooperation
  Cache replacement/placement policies for replication control and global management
  Robust performance improvement

## Slide 255: Managing Distributed, Shared L2 Caches through OS-Level Page Allocation
Sangyeun Cho and Lei Jin
Dept. of Computer Science
University of Pittsburgh
Int’l Symposium on Microarchitecture, 2006

## Slide 256: Private caching
2. L2 access
1. L1 miss
L1 miss
L2 access
  Hit
  Miss
Access directory
  A copy on chip
  Global miss
3. Access directory
 short hit latency (always local)
 high on-chip miss rate
long miss resolution time
complex coherence enforcement

## Slide 257: OS-Level Data Placement
Placing “flexibility” as the top design consideration
OS-level data to L2 cache mapping
  Simple hardware based on shared caching
  Efficient mapping maintenance at page granularity
Demonstrating the impact using different policies

## Slide 258: Talk roadmap
Data mapping, a key property
Flexible page-level mapping
  Goals
  Architectural support
  OS design issues
Management policies
Conclusion and future works

## Slide 259: Data mapping, the key
Data mapping = deciding data location (i.e., cache slice)
Private caching
  Data mapping determined by program location
  Mapping created at miss time
  No explicit control
Shared caching
  Data mapping determined by address
    slice number = (block address) % (Nslice)
  Mapping is static
  Cache block installation at miss time
  No explicit control
  (Run-time can impact location within slice)
Mapping granularity = block

## Slide 260: Block-Level Mapping
Used in Shared Caches

## Slide 261: Page-Level Mapping
The OS has control of where a page maps to
  Page-level interleaving across cache slices

## Slide 262: Goal 1: performance management
 Proximity-aware data mapping

## Slide 263: Goal 2: power management
 Usage-aware cache shut-off
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 264: Goal 3: reliability management
 On-demand cache isolation
X
X

## Slide 265: Goal 4: QoS management
 Contract-based cache allocation

## Slide 266: Architectural support
L1 miss
Method 1: “bit selection”
slice_num = (page_num) % (Nslice)
other bits
slice_num
offset
data address
Method 2: “region table”
regionx_low ≤ page_num ≤ regionx_high
page_num
offset
region0_low
slice_num0
region0_high
region1_low
slice_num1
region1_high
Method 3: “page table (TLB)”
page_num «–» slice_num
vpage_num0
slice_num0
ppage_num0
vpage_num1
slice_num1
ppage_num1
reg_table
TLB
 Simple hardware support enough
 Combined scheme feasible
Slice = Collection of Banks
Managed as a unit

## Slide 267: Some OS design issues
Congruence group CG(i)
  Set of physical pages mapped to slice i
  A free list for each i  multiple free lists
On each page allocation, consider
  Data proximity
  Cache pressure
  e.g., Profitability function P = f(M, L, P, Q, C)
    M: miss rates
    L: network link status
    P: current page allocation status
    Q: QoS requirements
    C: cache configuration
Impact on process scheduling
Leverage existing frameworks
  Page coloring – multiple free lists
  NUMA OS – process scheduling & page allocation

## Slide 268: Tracking Cache Pressure
A program’s time-varying working set
Approximated by the number of actively accessed pages
Divided by the cache size
Use a Bloom filter to approximate that
  Empty the filter
  If miss, count++ and insert

## Slide 269: Working example
Program
1
0
2
3
4
5
6
8
7
9
10
11
12
13
14
15
5
5
5
5
P(4) = 0.9
P(6) = 0.8
P(5) = 0.7
…
P(1) = 0.95
P(6) = 0.9
P(4) = 0.8
…
4
1
6
 Static vs. dynamic mapping
 Program information (e.g., profile)
Proper run-time monitoring needed
Profitability Function:

## Slide 270: Simulating private caching
For a page requested from a program running on core i, map the page to cache slice i
L2 cache latency (cycles)
SPEC2k INT
SPEC2k FP
private caching
OS-based
L2 cache slice size
 Simulating private caching is simple
 Similar or better performance

## Slide 271: Simulating shared caching
For a page requested from a program running on core i, map the page to all cache slices (round-robin, random, …)
L2 cache latency (cycles)
SPEC2k INT
SPEC2k FP
L2 cache slice size
shared
OS
129
106
 Simulating shared caching is simple
Mostly similar behavior/performance

## Slide 272: Clustered Sharing
Mid-way between Shared and Private
1
0
2
3
4
5
6
8
7
9
10
11
12
13
14
15

## Slide 273: Simulating clustered caching
For a page requested from a program running on core of group j, map the page to any cache slice within group (round-robin, random, …)
Relative performance (time-1)
private
OS
shared
4 cores used; 512kB cache slice
 Simulating clustered caching is simple
Lower miss traffic than private
Lower on-chip traffic than shared

## Slide 274: Conclusion
“Flexibility” will become important in future multicores
  Many shared resources
  Allows us to implement high-level policies
OS-level page-granularity data-to-slice mapping
  Low hardware overhead
  Flexible
Several management policies studied
  Mimicking private/shared/clustered caching straightforward
  Performance-improving schemes

## Slide 275: Future works
Dynamic mapping schemes
  Performance
  Power
Performance monitoring techniques
  Hardware-based
  Software-based
Data migration and replication support

## Slide 276: ASR: Adaptive Selective Replication for CMP Caches
Brad Beckmann†, Mike Marty, and David Wood
Multifacet Project
University of Wisconsin-Madison
Int’l Symposium on Microarchitecture, 2006
12/13/06
† currently at Microsoft

## Slide 277: Introduction
Previous hybrid proposals
  Cooperative Caching, CMP-NuRapid
    Private L2 caches / restrict replication
  Victim Replication
    Shared L2 caches / allow replication
  Achieve fast access and high capacity
    Under certain workloads & system configurations
    Utilize static rules
  Non-adaptive
    E.g., CC w/ 100% (minimum replication)
      Apache performance improves by 13%
      Apsi performance degrades by 27%

## Slide 278: Adaptive Selective Replication
Adaptive Selective Replication: ASR
  Dynamically monitor workload behavior
  Adapt the L2 cache to workload demand
  Up to 12% improvement vs. previous proposals
Estimates
  Cost of replication
    Extra misses
      Hits in LRU
  Benefit of replication
    Lower hit latency
      Hits in remote caches

## Slide 279: Outline
Beckmann, Marty, & Wood
ASR: Adaptive Selective Replication for CMP Caches
279
Introduction
Understanding L2 Replication
  Benefit
  Cost
  Key Observation
  Solution
ASR: Adaptive Selective Replication
Evaluation
Notes: 279

## Slide 280: Understanding L2 Replication
Three L2 block sharing types
  Single requestor
    All requests by a single processor
  Shared read only
    Read only requests by multiple processors
  Shared read-write
    Read and write requests by multiple processors
Profile L2 blocks during their on-chip lifetime
  8 processor CMP
  16 MB shared L2 cache
  64-byte block size

## Slide 281: Understanding L2 Replication
Shared Read-only
Shared Read-write
Single Requestor
Apache
Jbb
Oltp
Zeus
High Locality
Mid Locality
Low Locality

## Slide 282: Understanding L2 Replication
Shared read-only replication
  High-Locality
  Can reduce latency
  Small static fraction  minimal impact on capacity if replicated
  Degree of sharing can be large  must control replication to avoid capacity overload
Shared read-write
  Little locality
  Data is read only a few times and then updated
  Not a good idea to replicate
Single Requestor
  No point in replicating
  Low locality as well
Focus on replicating Shared Read-Only

## Slide 283: Understanding L2 Replication: Benefit
L2 Hit Cycles
Replication Capacity
The more we replicate the closer the data can be to the accessing core
Hence the lower the latency

## Slide 284: Understanding L2 Replication: Cost
L2 Miss Cycles
Replication Capacity
The more we replicate the lower the effective cache capacity
Hence we get more cache misses

## Slide 285: Understanding L2 Replication: Key Observation
Beckmann, Marty, & Wood
ASR: Adaptive Selective Replication for CMP Caches
285
L2 Hit Cycles
Replication Capacity
Top 3% of Shared Read-only blocks satisfy
70% of Shared Read-only requests
Replicate Frequently
Requested Blocks First
Notes: 285

## Slide 286: Understanding L2 Replication: Solution
Total
Cycle
Curve
Total Cycles
Replication Capacity
Optimal
Property of Workload
Cache Interaction
Not Fixed 
Must Adapt

## Slide 287: Outline
Wires and CMP caches
Understanding L2 Replication
ASR: Adaptive Selective Replication
  SPR: Selective Probabilistic Replication
  Monitoring and adapting to workload behavior
Evaluation

## Slide 288: SPR: Selective Probabilistic Replication
Mechanism for Selective Replication
Replicate on L1 eviction
  Use token coherence
    No need for centralized directory (CC) or home node (victim)
  Relax L2 inclusion property
    L2 evictions do not force L1 evictions
    Non-exclusive cache hierarchy
  Ring Writebacks
    L1 Writebacks passed clockwise between private L2 caches
    Merge with other existing L2 copies
Probabilistically choose between
  Local writeback  allow replication
  Ring writeback  disallow replication
  Always writeback if block already in local L2
Replicates frequently requested blocks

## Slide 289: SPR: Selective Probabilistic Replication
Private
L2
Private
L2
CPU 3
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
CPU 2
CPU 1
CPU 0
CPU 4
CPU 5
CPU 6
CPU 7
Private
L2
Private
L2
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
L1
I $
L1
D $
Private
L2
Private
L2
Private
L2
Private
L2

## Slide 290: SPR: Selective Probabilistic Replication
Replication
Capacity
Replication Levels
0
1
2
3
4
5
Replication Level | 0 | 1 | 2 | 3 | 4 | 5
Prob. of Replication | 0 | 1/64 | 1/16 | 1/4 | 1/2 | 1
Current
Level
How do we choose the probability of replication?

## Slide 291: Implementing ASR
Four mechanisms estimate deltas
  Decrease-in-replication Benefit
  Increase-in-replication Benefit
  Decrease-in-replication Cost
  Increase-in-replication Cost
Triggering a cost-benefit analysis
Four counters  measuring cycle differences

## Slide 292: ASR: Decrease-in-replication Benefit
L2 Hit Cycles
Replication Capacity
current level
lower level

## Slide 293: ASR: Decrease-in-replication Benefit
Goal
  Determine replication benefit decrease of the next lower level
  Local hits that would be remote hits
Mechanism
  Current Replica Bit
    Per L2 cache block
    Set for replications of the current level
    Not set for replications of lower level
  Current replica hits would be remote hits with next lower level
Overhead
  1-bit x 256 K L2 blocks = 32 KB

## Slide 294: ASR: Increase-in-replication Benefit
L2 Hit Cycles
Replication Capacity
current level
higher level

## Slide 295: ASR: Increase-in-replication Benefit
Goal
  Determine replication benefit increase of the next higher level
  Blocks not replicated that would have been replicated
Mechanism
  Next Level Hit Buffers (NLHBs)
    8-bit partial tag buffer
    Store replicas of the next higher when not replicated
  NLHB hits would be local L2 hits with next higher level
Overhead
  8-bits x 16 K entries x 8 processors = 128 KB

## Slide 296: ASR: Decrease-in-replication Cost
L2 Miss Cycles
Replication Capacity
current level
lower level

## Slide 297: ASR: Decrease-in-replication Cost
Goal
  Determine replication cost decrease of the next lower level
  Would be hits in lower level, evicted due to replication in this level
Mechanism
  Victim Tag Buffers (VTBs)
    16-bit partial tags
    Store recently evicted blocks of current replication level
  VTB hits would be on-chip hits with next lower level
Overhead
  16-bits x 1 K entry x 8 processors = 16 KB

## Slide 298: ASR: Increase-in-replication Cost
L2 Miss Cycles
Replication Capacity
current level
higher level

## Slide 299: ASR: Increase-in-replication Cost
Goal
  Determine replication cost increase of the next higher level
  Would be evicted due to replication at next level
Mechanism
  Goal: track the 1K LRU blocks  too expensive
  Way and Set counters [Suh et al. HPCA 2002]
    Identify soon-to-be-evicted blocks
    16-way pseudo LRU
    256 set groups
  On-chip hits that would be off-chip with next higher level
Overhead
  255-bit pseudo LRU tree x 8 processors = 255 B
Overall storage overhead: 212 KB or 1.2% of total storage

## Slide 300: Estimating LRU position
Counters per way and per set
  Ways x Sets x Processors  too expensive
To reduce cost they maintain a pseudo-LRU ordering of set groups
  256 set-groups
  Maintain way counters per group
  Pseudo-LRU tree
How are these updated?

## Slide 301: ASR: Triggering a Cost-Benefit Analysis
Goal
  Dynamically adapt to workload behavior
  Avoid unnecessary replication level changes
Mechanism
  Evaluation trigger
    Local replications or NLHB allocations exceed 1K
  Replication change
    Four consecutive evaluations in the same direction

## Slide 302: ASR: Adaptive Algorithm
Decrease in Replication Benefit vs.
Increase in Replication Cost
  Whether we should decrease replication
Decrease in Replication Cost vs.
Increase in Replication Benefit
  Whether we should increase replication
Decrease in Replication Cost  Would be hits in lower level, evicted due to replication
Increase in Replication Benefit  Blocks not replicated that would have been replicated
Decrease in Replication Benefit  Local hits that would be remote hits if lower
Increase in Replication Cost  Would be evicted due to replication at next level

## Slide 303: ASR: Adaptive Algorithm
 | Decrease in Replication Cost > Increase in Replication Benefit | Decrease in Replication Cost < Increase in Replication Benefit
Decrease in Replication Benefit > Increase in Replication Cost | Go in direction with greater value | Increase Replication
Decrease in Replication Benefit < Increase in Replication Cost | Decrease Replication | Do Nothing
Decrease in Replication Cost  Would be hits in lower level, evicted due to replication
Increase in Replication Benefit  Blocks not replicated that would have been replicated
Decrease in Replication Benefit  Local hits that would be remote hits if lower
Increase in Replication Cost  Would be evicted due to replication at next level

## Slide 304: Outline
Beckmann, Marty, & Wood
ASR: Adaptive Selective Replication for CMP Caches
Wires and CMP caches
Understanding L2 Replication
ASR: Adaptive Selective Replication
Evaluation
Notes: 304

## Slide 305: Methodology
Full system simulation
  Simics
  Wisconsin’s GEMS Timing Simulator
    Out-of-order processor
    Memory system
Workloads
  Commercial
    apache, jbb, otlp, zeus
  Scientific (see paper)
    SpecOMP: apsi & art
    Splash: barnes & ocean

## Slide 306: System Parameters
Memory System |  | Dynamically Scheduled Processor | 
L1 I & D caches | 64 KB, 4-way, 3 cycles | Clock frequency | 5.0 GHz
Unified L2 cache | 16 MB, 16-way | Reorder buffer / scheduler | 128 / 64 entries
L1 / L2 prefetching | Unit & Non-unit strided prefetcher (similar Power4) | Pipeline width | 4-wide fetch & issue
Memory latency | 500 cycles | Pipeline stages | 30
Memory bandwidth | 50 GB/s | Direct branch predictor | 3.5 KB YAGS
Memory size | 4 GB of DRAM | Return address stack | 64 entries
Outstanding memory request / CPU | 16 | Indirect branch predictor | 256 entries (cascaded)
[ 8 core CMP, 45 nm technology ]

## Slide 307: Replication Benefit, Cost, & Effectiveness Curves
Benefit
Cost

## Slide 308: Replication Benefit, Cost, & Effectiveness Curves
Effectiveness

## Slide 309: Comparison of Replication Policies
SPR  multiple possible policies
Evaluated 4 shared read-only replication policies
  VR: Victim Replication
    Previously proposed [Zhang ISCA 05]
    Disallow replicas to evict shared owner blocks
  NR: CMP-NuRapid
    Previously proposed [Chishti ISCA 05]
    Replicate upon the second request
  CC: Cooperative Caching
    Previously proposed [Chang ISCA 06]
    Replace replicas first
    Spill singlets to remote caches
    Tunable parameter 100%, 70%, 30%, 0%
  ASR: Adaptive Selective Replication
    Our proposal
    Monitor and adjust to workload demand
Lack
Dynamic
Adaptation

## Slide 310: ASR: Performance
S: CMP-Shared
P: CMP-Private
V: SPR-VR
N: SPR-NR
C: SPR-CC
A: SPR-ASR

## Slide 311: Conclusions
CMP Cache Replication
  No replications  conservers capacity
  All replications  reduces on-chip latency
  Previous hybrid proposals
    Work well for certain criteria
    Non-adaptive
Adaptive Selective Replication
  Probabilistic policy favors frequently requested blocks
  Dynamically monitor replication benefit & cost
  Replicate benefit > cost
  Improves performance up to 12% vs. previous schemes

## Slide 312: An Adaptive Shared/Private NUCA Cache Partitioning Scheme for Chip Multiprocessors
Haakon Dybdahl & Per Stenstrom
Int’l Conference on High-Performance Computer Architecture, Feb 2007

## Slide 313: The Problem with Previous Approaches
Uncontrolled Replication
  A replicated block evicts another block at random
  This results in Polution
Goal of this work:
  Develop an adaptive replication method
How will replication be controlled?
  Adjust the portion of the cache that can be used for replicas
The paper shows that the proposed method is better than:
  Private
  Shared
  Controlled Replication
Only Multi-Program workloads considered
  The authors argue that the technique should work for parallel workloads as well

## Slide 314: Baseline Architecture
Local and remote partitions
Sharing engine controls replication

## Slide 315: Motivation
Some programs do well with few ways
Some require more ways
 ways

## Slide 316: Private vs. Shared Partitions
Adjust the number of ways:
  Private ways
  Replica ways  can be used by all processors
Private ways only available to local processor
Goal is to minimize the total number of misses
  Size of private partition
  The number of blocks in the shared partition

## Slide 317: Sharing Engine
Three components
  Estimation of private/shared “sizes”
  A method for sharing the cache
  A replacement policy for the shared cache space

## Slide 318: Estimating the size of Private/Shared Partitions
Keep several counters
Should we decrease the number of ways?
  Count the number of hits to the LRU block in each set
  How many more misses will occur?
Should we increase the number of ways?
  Keep shadow tags  remember last evicted block
  Hit in shadow tag  increment the counter
  How many more hits will occur?
Every 2K misses:
  Look at the counters
  Gain: Core with max more ways
  Loss: Core with min less ways
  If Gain > Loss  Adjust ways give more ways to first core
Start with 75% private and 25% shared

## Slide 319: Structures
Core ID with every block
  Used eventually in Shadow Tags
A counter per core
  Max blocks per set  how many ways it can use
Another two counters per block
  Hits in Shadow tags
    Estimate Gain of increasing ways
  Hits in LRU block
    Estimate Loss of decreasing ways

## Slide 320: Management of Partitions
Private partition
  Only accessed by the local core
  LRU
Shared partition
  Can contain blocks from any core
  Replacement algorithm tries to adjust size according to the current partition size
To adjust the shared partition ways only the counter is changed
  Block evictions or introductions are done gradually

## Slide 321: Cache Hit in Private Portion
All blocks involved are from the private partition
  Simply use LRU
  Nothing else is needed

## Slide 322: Cache hit in neighboring cache
This means first we had a miss in the local private partition
Then all other caches are searched in parallel
The cache block is moved to the local cache
  The LRU block in the private portion is moved to the neighboring cache
  There it is set as the MRU block in the shared portion
Local
LRU
Remote
Local
MRU
Remote
MRU

## Slide 323: Cache miss
Get from memory
Place as MRU in private portion
  Move LRU block to shared portion of the local cache
  A block from the shared portion needs to be evicted
Eviction Algorithm
  Scan in LRU order
    If the owning Core has too many blocks in the set evict
  If no block found LRU goes
How can a Core have too many blocks?
  Because we adjust the max number of blocks per set
  The above algorithm gradually enforces this adjustment

## Slide 324: Methodology
Extended Simplescalar
SPEC CPU 2000

## Slide 325: Classification of applications
Which care about L2 misses?

## Slide 326: Compared to Shared and Private
Running different mixes of four benchmarks

## Slide 327: Conclusions
Adapt the number of ways
Estimate the Gain and Loss per core of increasing the number of ways
Adjustment happens gradually via the shared portion replacement algorithm
Compared to private: 13% faster
Compared to shared: 5%

## Slide 328
Dynamic Spill-Receive for Robust High-Performance Caching in CMPs
Moinuddin K. Qureshi
T. J. Watson Research Center, Yorktown Heights, NY

## Slide 329: Background: Private Caches on CMP
Private caches avoid the need for shared interconnect
++ fast latency, tiled design, performance isolation
Core A
I$
D$
CACHE A
Core B
I$
D$
CACHE B
Core C
I$
D$
CACHE C
Core D
I$
D$
CACHE D
Memory
Problem: When one core needs more cache and other core
has spare cache, private-cache CMPs cannot share capacity

## Slide 330: Cache Line Spilling
Spill evicted line from one cache to neighbor cache
- Co-operative caching (CC) [ Chang+ ISCA’06]
Problem with CC:
Performance depends on the parameter (spill probability)
All caches spill as well as receive  Limited improvement
  Spilling helps only if application demands it
  Receiving lines hurts if cache does not have spare capacity
Cache A
Cache B
Cache C
Cache D
Spill
Goal:
Robust High-Performance Capacity Sharing with Negligible Overhead

## Slide 331: Spill-Receive Architecture
Each Cache is either a Spiller or Receiver but not both
- Lines from spiller cache are spilled to one of the receivers
- Evicted lines from receiver cache are discarded
What is the best N-bit binary string that maximizes the performance of Spill Receive Architecture 
Dynamic Spill Receive (DSR)  Adapt to Application Demands
Cache A
Cache B
Cache C
Cache D
Spill
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)
S/R =1
(Spiller cache)
S/R =0
(Receiver cache)

## Slide 332: “Giver” & “Taker” Applications
Some applications
  Benefit from more cache  Takers
  Do not benefit from more cache  Givers
If all Givers  Private cache works well
If mix  Spilling helps
#ways

## Slide 333: Where is a block?
First check the “local” bank
Then “snoop” all other caches
Then go to memory

## Slide 334: Dynamic Spill-Receive via “Set Dueling”
Spiller-sets
Follower Sets
Receiver-sets
    Divide the cache in three:
      Spiller sets
      Receiver sets
      Follower sets (winner of spiller, receiver)
    n-bit PSEL counter
    misses to spiller-sets: PSEL--
    misses to receiver-set: PSEL++
    MSB of PSEL decides policy for Follower sets:
      MSB = 0, Use spill
      MSB = 1, Use receive
PSEL
-
miss
+
miss
MSB = 0?
YES
No
Use Recv
Use spill
monitor  choose  apply
(using a single counter)

## Slide 335: Dynamic Spill-Receive Architecture
Cache A
Cache B
Cache C
Cache D
Set X
Set Y
AlwaysSpill
AlwaysRecv
-
+
Miss in Set X
in any cache
Miss in Set Y
in any cache
PSEL B
PSEL C
PSEL D
PSEL A
Decides policy for all sets of Cache A (except X and Y)

## Slide 336: Outline
Background
Dynamic Spill Receive Architecture
Performance Evaluation
Quality-of-Service
Summary

## Slide 337: Experimental Setup
  Baseline Study:
    4-core CMP with in-order cores
    Private Cache Hierarchy: 16KB L1, 1MB L2
    10 cycle latency for local hits, 40 cycles for remote hits
  Benchmarks:
    6 benchmarks that have extra cache: “Givers” (G)
    6 benchmarks that benefit from more cache: “Takers” (T)
    All 4-thread combinations of 12 benchmarks: 495 total
    Five types of workloads:
G4T0
G3T1
G2T2
G1T3
G0T4

## Slide 338: Performance Metrics
Three metrics for performance:
Throughput  perf = IPC1 + IPC2 can be unfair to low-IPC application
Weighted Speedup  perf = IPC1/SingleIPC1 + IPC2/SingleIPC2  correlates with reduction in execution time
Hmean-fairness  perf = hmean(IPC1/SingleIPC1, IPC2/SingleIPC2)  balances fairness and performance

## Slide 339: Results for Throughput
On average, DSR improves throughput by 18%, co-operative caching by 7%
DSR provides 90% of the benefit of knowing the best decisions a priori
* DSA implemented with 32 dedicated sets and 10 bit PSEL counters
G4T0  Need more capacity for all apps  still DASR helps
No significant degradation of performance for some workloads

## Slide 340: S-Curve
Throughput Improvement

## Slide 341: Results for Weighted Speedup
On average, DSR improves weighted speedup by 13%

## Slide 342: Results for Hmean Fairness
On average, DSR improves Hmean Fairness from 0.58 to 0.78

## Slide 343: DSR vs. Faster Shared Cache
DSR (with 40 cycle extra for remote hits) performs similar to shared cache with zero latency overhead and crossbar interconnect

## Slide 344: Scalability of DSR
DSR improves average throughput by 19% for both systems
(No performance degradation for any of the workloads)

## Slide 345: Outline
Background
Dynamic Spill Receive Architecture
Performance Evaluation
Quality-of-Service
Summary

## Slide 346: Quality of Service with DSR
For 1 % of the 495x4 =1980 apps, DSR causes IPC loss of > 5%
In some cases, important to ensure that performance does not degrade compared to dedicated private cache  QoS
Estimate Misses with vs. without DSR
DSR can ensure QoS: change PSEL counters by weight of miss:
ΔMiss = MissesWithDSR – MissesWithoutDSR
ΔCyclesWithDSR = AvgMemLatency · ΔMiss
Calculate weight every 4M cycles. Needs 3 counters per core
Estimated by Spiller Sets

## Slide 347: QoS DSR Hardware
4-byte cycle counter
  Shared by all cores
Per Core/Cache:
  3 bytes for Misses in Spiller Sets
  3 bytes for Miss in DSR
  1 byte for QoSPenaltyFactor
    6.2 fixed-point
  12 bits for PSEL
    10.2 fixed-point
10 bytes per core
On overflow of cycle counter
  Halve all other counters

## Slide 348: IPC of QoS-Aware DSR
IPC curves for other categories almost overlap for the two schemes.
Avg. throughput improvement across all 495 workloads similar (17.5% vs. 18%)
For Category: G0T4
IPC Normalized To NoSpill

## Slide 349: Summary
  The Problem:
  Need efficient capacity sharing in CMPs with private cache
  Solution: Dynamic Spill-Receive (DSR)
  1. Provides High Performance by Capacity Sharing
  - On average 18% in throughput (36% on hmean fairness)
  2. Requires Low Design Overhead
  - < 2 bytes of HW require per core in the system
  3. Scales to Large Number of Cores
  - Evaluated 16-cores in our study
  4. Maintains performance isolation of private caches
  - Easy to ensure QoS while retaining performance

## Slide 350: DSR vs. TADIP

## Slide 351: PageNUCA: Selected Policies for Page-grain Locality Management in Large Shared CMP Caches
Mainak Chaudhuri, IIT Kanpur
Int’l Conference on High-Performance Computer Architecture, 2009
Some slides from the author’s conference talk

## Slide 352: Baseline System
Manage data placement at the Page Level
C0
B0
B1
L2 bank
control
C1
B2
B3
C2
B4
B5
C3
B6
B7
C4
B8
B9
C5
B10
B11
C6
B12
B13
C7
B14
B15
Memory
control
L2 bank
Ring
Core w/
L1$

## Slide 353: Page-Interleaved Cache
Data is interleaved at the page level
Page allocation determines where data goes on-chip
C0
B0
B1
C1
B2
B3
C2
B4
B5
C3
B6
B7
C4
B8
B9
C5
B10
B11
C6
B12
B13
C7
B14
B15
0
1
3
15
16
pages
0
1
3
15
16

## Slide 354: Preliminaries: Baseline mapping
Virtual address to physical address mapping is demand-based L2 cache-aware bin-hopping
  Good for reducing L2 cache conflicts
An L2 cache block is found in a unique bank at any point in time
  Home bank maintains the directory entry of each block in the bank as an extended state
  Home bank may change as a block migrates
  Replication not explored in this work

## Slide 355: Preliminaries: Baseline mapping
Physical address to home bank mapping is page-interleaved
  Home bank number bits are located right next to the page offset bits
Private L1 caches are kept coherent via a home-based MESI directory protocol
  Every L1 cache request is forwarded to the home bank first for consulting the directory entry
  The cache hierarchy maintains inclusion

## Slide 356: Preliminaries: Observations
Every 100K references
Given a time window:
Most pages are accessed by one core and multiple times
Barnes
Matrix
Equake
FFTW
Ocean
Radix
>= 32
[16, 31]
[8, 15]
[1, 7]
Fraction of all pages or L2$ accesses
0
0.2
0.4
0.6
0.8
1.0
Solo pages
Access
coverage

## Slide 357: Dynamic Page Migration
Fully hardwired solution composed of four central algorithms
  When to migrate a page
  Where to migrate a candidate page
  How to locate a cache block belonging to a migrated page
  How the physical data transfer takes place

## Slide 358: #1: When to Migrate
Keep the following access counts per page:
  Max & core ID
  Second Max & core ID
  Access count since last, new sharer introduced
Maintain two empirically derived threadholds
  T1 = 9  for max and second max
  T2 = 29  for new sharer
Two modes based on DIFF = MAX - SecondMAX
  DIFF < T1  No, single dominant accessing core
    Shared mode:
      Migrate when AC of last sharer > T2
      New sharer dominate
  DIFF >= T1  One core dominates the access count
    Solo Mode:
      Migrate when the dominant core is distant

## Slide 359: #2: Where to Migrate to
Find a destination bank of migration
Find an appropriate “region” in the destination bank for holding the migrated page
Many different pages map to the same bank
Pick one

## Slide 360: #2: Migration – Destination Bank
Sharer Mode:
  Minimize the average access latency
  Assuming all accessing cores equally important
  Proximity ROM:
    Sharing vector  four banks that have lower average latency
      Scalability? Coarse-grain vectors using clusters of nodes
      Pick the bank with the least load
      Load = # pages mapped to the bank
Solo Mode:
  Four local banks
  Pick the bank with the least load

## Slide 361: #2: Migration – Which Physical Page to Map to?
PACT: Page Access Counter Table
One entry per page
  Maintains the information needed by PageNUCA
Ideally all pages have PACT entries
  In practice some may not due to conflict misses

## Slide 362: #2: Migration – Which Physical Page to Map to?
First find an appropriate set of pages
  Look for an invalid PACT entry
    Maintain a bit vector for the sets
If no invalid entry exists
  Select a Non-MRU Set
  Pick the LRU entry
Generate a Physical Address outside the range of installed physical memory
  To avoid potential conflicts with other pages
When a PACT entry is evicted
  The corresponding page is swapped with the new page
One more thing … before describing the actual migration
MRU

## Slide 363: Physical Addresses: PageNUCA vs. OS
Dl1Map: OS PA  PageNUCA PA
FL2Map: OS PA  PageNUCA PA
IL2MAP: PageNUCA PA  OS PA
The rest of the system is oblivious to Page NUCA
  It still uses the PAs assigned by the OS
  Only the L2 sees the PageNUCA PAs
PageNUCA
Uses PAs to change
the mapping of pages
to banks
OS Only
OS & PageNUCA
OS Only
OS Only

## Slide 364: Physical Addresses: PageNUCA vs. OS
Invariant:
  Given page p is mapped to page q
  FL2Map(p)  q
    This is at the home node of p
  IL2Map(q)  p
    This is at the home node of q
PageNUCA
Uses PAs to change
the mapping of pages
to banks
OS Only
OS & PageNUCA
OS Only
OS Only

## Slide 365: Physical Addresses: PageNUCA vs. OS
L1Map:
  Fill on TLB Miss
  On migration notify all relevant L1Maps
    Nodes that had entries for the page being migrated
  On miss:
    Go to FL2Map in the home node
PageNUCA
Uses PAs to change
the mapping of pages
to banks
OS Only
OS & PageNUCA
OS Only
OS Only

## Slide 366: #3: Migration Protocol
First convert the PageNUCA PAs into OS Pas
Eventually we want
  s  D & d  S
Source
Bank
Dest
Bank
iL2
iL2
S
D
Want to migrate S in place of D: Swap S and D
s
d
PageNUCA PA
OS PA
S
D

## Slide 367: #3: Migration Protocol
Update home Forward L2 maps
  s maps now to D and d maps to S
Swap Inverse Maps at the current banks
Source
Bank
Dest
Bank
iL2
iL2
S
D
Want to migrate S in place of D: Swap S and D
Home(s)
Bank
Home(d)
Bank
fL2
fL2
d
s
s
d
S
D
D
S

## Slide 368: #3: Migration Protocol
Lock the two banks
  Swap the data pages
Finally, notify all L1 maps of the change and unlock the banks
Source
Bank
Dest
Bank
iL2
iL2
S
D
Want to migrate S in place of D: Swap S and D
Home(s)
Bank
Home(d)
Bank
fL2
fL2
d
s
s
d
D
S
D
S

## Slide 369: How to locate a cache block in L2$
On-core translation of OS PA to L2 CA (showing the L1 data cache misses only)
dTLB
L1 Data
Cache
dL1
Map
LSQ
VPN
Offset
OS PA
PPN
Miss
L2 CA
Ring
Core outbound
OS PPN to L2 PPN
Exercised by all
L1 to L2 transactions
One-to-one
Filled on dTLB miss

## Slide 370: How to locate a cache block in L2$
Uncore translation between OS PA and L2 CA
L2 Cache
Bank
Forward
L2Map
Inverse
L2Map
PACT
Ring
Ring
L2 CA
L2 PPN
Mig.?
MC
MC
OS PPN
L2 CA
(RING)
L2 PPN
Miss
Offset
OS PPN
OS
PA
Refill/Ext.
Hit

## Slide 371: Other techniques
Block-grain migration is modeled as a special case of page-grain migration where the grain is a single L2 cache block
  The per-core L1Map is now a replica of the forward L2Map so that an L1 cache miss request can be routed to the correct bank
  The forward and inverse L2Maps get bigger (same organization as the L2 cache)
OS-assisted static techniques
  First touch: assign VA to PA mapping such that the PA is local to the first touch core
  Application-directed: one-time best possible page-to-core affinity hint before the parallel section starts

## Slide 372: Simulation environment
Single-node CMP with eight OOO cores
  Private L1 caches: 32KB 4-way LRU
  Shared L2 cache: 1MB 16-way LRU banks, 16 banks distributed over a bidirectional ring
  Round-trip L2 cache hit latency from L1 cache: maximum 20 ns, minimum 7.5 ns (local access), mean 13.75 ns (assumes uniform access distribution) [65 nm process, M5 for ring with optimally placed repeaters]
  Off-die DRAM latency: 70 ns row miss, 30 ns row hit

## Slide 373: Storage overhead
Page-grain: 848.1 KB (4.8% of total L2 cache storage)
Block-grain: 6776 KB (28.5%)
  Per-core L1Maps are the largest contributors
Idealized block-grain with only one shared L1Map: 2520 KB (12.9%)
  Difficult to develop a floorplan

## Slide 374: Performance comparison: Multi-Threaded
Page
Normalized cycles (lower is better)
0.6
0.7
0.8
0.9
1.0
1.1
Barnes
Matrix
Equake
FFTW
Ocean
Radix
gmean
1.46
1.69
Block
First touch
App.-dir.
Perfect
18.7%
22.5%
Lock placement

## Slide 375: Performance comparison: Multi-Program
Page
Normalized avg. cycles (lower is better)
0.6
0.7
0.8
0.9
1.0
1.1
MIX1
MIX2
MIX3
MIX4
MIX5
MIX6
gmean
Block
First touch
Perfect
12.6%
15.2%
Spill effect
MIX7
MIX8

## Slide 376: L1 cache prefetching
Impact of a 16 read/write stream stride prefetcher per core
  L1 Pref. Page Mig. Both
  ShMem 14.5% 18.7% 25.1%
  MProg 4.8% 12.6% 13.0%
Complementary for the most part for multi-threaded apps
Page Migration dominates for multi-programmed workloads

## Slide 377: Dynamic Hardware-Assisted Software-Controlled Page Placement to Manage Capacity Allocation and Sharing within Caches
Manu Awasthi, Kshitij Sudan, Rajeev Balasubramonian, John Carter
University of Utah
Int’l Conference on High-Performance Computer Architecture, 2009

## Slide 378: Executive Summary
Last Level cache management at page granularity
Salient features
  A combined hardware-software approach with low overheads
  Use of page colors and shadow addresses for
    Cache capacity management
    Reducing wire delays
    Optimal placement of cache lines
  Allows for fine-grained partition of caches.

## Slide 379: Baseline System
Core 1
Core 2
Core 4
Core 3
Core/L1 $
Cache Bank
Router
Intercon
Also applicable to other NUCA layouts

## Slide 380: Existing techniques
S-NUCA :Static mapping of address/cache lines to banks (distribute sets among banks)
  Simple, no overheads. Always know where your data is!
  Data could be mapped far off!

## Slide 381: S-NUCA Drawback
Core 1
Core 2
Core 4
Core 3
Increased Wire Delays!!

## Slide 382: Existing techniques
S-NUCA :Static mapping of address/cache lines to banks (distribute sets among banks)
  Simple, no overheads. Always know where your data is!
  Data could be mapped far off!
D-NUCA (distribute ways across banks)
  Data can be close by
  But, you don’t know where. High overheads of search mechanisms!!

## Slide 383: D-NUCA Drawback
Core 1
Core 2
Core 4
Core 3
Costly search Mechanisms!

## Slide 384: A New Approach
Page Based Mapping
  Cho et. al (MICRO ‘06)
  S-NUCA/D-NUCA benefits
Basic Idea –
  Page granularity for data movement/mapping
  System software (OS) responsible for mapping data closer to computation
  Also handles extra capacity requests
Exploit page colors!

## Slide 385: Page Colors
Cache Tag
Cache Index
Offset
Physical Page #
Page Offset
The Cache View
The OS View
Physical Address – Two Views

## Slide 386: Page Colors
Cache Tag
Cache Index
Offset
Physical Page #
Page Offset
Page Color
Intersecting bits of Cache Index and Physical Page Number
Can Decide which set a cache line goes to
Bottomline : VPN to PPN assignments can be manipulated to redirect cache line placements!

## Slide 387: The Page Coloring Approach
Page Colors can decide the set (bank) assigned to a cache line
Can solve a 3-pronged multi-core data problem
  Localize private data
  Capacity management in Last Level Caches
  Optimally place shared data (Centre of Gravity)
All with minimal overhead! (unlike D-NUCA)

## Slide 388: Prior Work : Drawbacks
Implement a first-touch mapping only
  Is that decision always correct?
  High cost of DRAM copying for moving pages
No attempt for intelligent placement of shared pages (multi-threaded apps)
Completely dependent on OS for mapping

## Slide 389: Would like to..
Find a sweet spot
Retain
  No-search benefit of S-NUCA
  Data proximity of D-NUCA
  Allow for capacity management
  Centre-of-Gravity placement of shared data
Allow for runtime remapping of pages (cache lines) without DRAM copying

## Slide 390: Lookups – Normal Operation
CPU
Virtual Addr : A
TLB
A → Physical Addr : B
L1 $
Miss!
B
Miss!
DRAM
B
L2 $

## Slide 391: Lookups – New Addressing
CPU
Virtual Addr : A
TLB
A → Physical Addr : B → New Addr : B1
L1 $
Miss!
B1
Miss!
DRAM
B1→ B
L2 $

## Slide 392: Shadow Addresses
Physical Page Number
Page Offset
OPC
Unused Address Space (Shadow) Bits
Original Page Color (OPC)
SB
Physical Tag (PT)
PT

## Slide 393: Shadow Addresses
Page Offset
OPC
SB
PT
Find a New Page Color (NPC)
Page Offset
SB
PT
Replace OPC with NPC
NPC
Page Offset
SB
PT
NPC
Store OPC in Shadow Bits
OPC
Cache
Lookups
Page Offset
OPC
SB
PT
Off-Chip, Regular Addressing

## Slide 394: More Implementation Details
New Page Color (NPC) bits stored in TLB
Re-coloring
  Just have to change NPC and make that visible
    Just like OPC→NPC conversion!
Re-coloring page => TLB shootdown!
Moving pages :
  Dirty lines : have to write back – overhead!
  Warming up new locations in caches!

## Slide 395: The Catch!
Virt Addr VA
VPN
PPN
NPC
PA1
Eviction
Virt Addr VA
VPN
PPN
NPC
TLB Miss!!
Translation Table (TT)
VPN
PPN
NPC
PROC ID
TLB
TT Hit!

## Slide 396: Advantages
Low overhead : Area, power, access times!
  Except TT
Lesser OS involvement
  No need to mess with OS’s page mapping strategy
Mapping (and re-mapping) possible
Retains S-NUCA and D-NUCA benefits, without D-NUCA overheads

## Slide 397: Application 1 – Wire Delays
Core 1
Core 2
Core 4
Core 3
Address PA
Longer Physical Distance => Increased Delay!

## Slide 398: Application 1 – Wire Delays
Core 1
Core 2
Core 4
Core 3
Address PA
Address PA1
Remap
Decreased Wire Delays!

## Slide 399: Application 2 – Capacity Partitioning
Shared vs. Private Last Level Caches
  Both have pros and cons
  Best solution : partition caches at runtime
Proposal
  Start off with equal capacity for each core
    Divide available colors equally among all
    Color distribution by physical proximity
  As and when required, steal colors from someone else

## Slide 400: Application 2 – Capacity Partitioning
Core 1
Core 2
Core 4
Core 3
1. Need more Capacity
2. Decide on a Color from Donor
3. Map New, Incoming pages of Acceptor to Stolen Color
Proposed-Color-Steal

## Slide 401: How to Choose Donor Colors?
Factors to consider
  Physical distance of donor color bank to acceptor
  Usage of color
For each donor color i we calculate suitability
The best suitable color is chosen as donor
Done every epoch (1000,000 cycles)
color_suitabilityi = α x distancei + β x usagei

## Slide 402: Are first touch decisions always correct?
Core 1
Core 2
Core 4
Core 3
1. Increased Miss Rates!! Must Decrease Load!
2. Choose Re-map Color
3. Migrate pages from Loaded bank to new bank
Proposed-Color-Steal-Migrate

## Slide 403: Application 3 : Managing Shared Data
Optimal placement of shared lines/pages can reduce average access time
  Move lines to Centre of Gravity (CoG)
But,
  Sharing pattern not known apriori
  Naïve movement may cause un-necessary overhead

## Slide 404: Page Migration
Core 1
Core 2
Core 4
Core 3
Cache Lines (Page) shared by cores 1 and 2
No bank pressure consideration : Proposed-CoG
Both bank pressure and wire delay considered : Proposed-Pressure-CoG

## Slide 405: Overheads
Hardware
  TLB Additions
    Power and Area – negligible (CACTI 6.0)
  Translation Table
OS daemon runtime overhead
  Runs program to find suitable color
  Small program, infrequent runs
  TLB Shootdowns
    Pessimistic estimate : 1% runtime overhead
Re-coloring : Dirty line flushing

## Slide 406: Results
SIMICS with g-cache
Spec2k6, BioBench, PARSEC and Splash 2
CACTI 6.0 for cache access times and overheads
4 and 8 cores
16 KB/4 way L1 Instruction and Data $
Multi-banked (16 banks) S-NUCA L2, 4x4 grid
2 MB/8-way (4 cores), 4 MB/8-way (8-cores) L2

## Slide 407: Multi-Programmed Workloads
Acceptors and Donors
Acceptors
Donors

## Slide 408: Multi-Programmed Workloads
Potential for 41% Improvement

## Slide 409: Multi-Programmed Workloads
3 Workload Mixes – 4 Cores : 2, 3 and 4 Acceptors

## Slide 410: Conclusions
Last Level cache management at page granularity
Salient features
  A combined hardware-software approach with low overheads
    Main Overhead : TT
  Use of page colors and shadow addresses for
    Cache capacity management
    Reducing wire delays
    Optimal placement of cache lines.
  Allows for fine-grained partition of caches.
Upto 20% improvements for multi-programmed, 8% for multi-threaded workloads

## Slide 411: R-NUCA: Data Placement in Distributed Shared Caches
Nikos Hardavellas, M. Ferdman, B. Falsafi, and A. Ailamaki
Int’l Conference on Computer Architecture, June 2009
Slides from the authors and by Jason Zebchuk, U. of Toronto

## Slide 412: Prior Work
Several proposals for CMP cache management
  ASR, cooperative caching, victim replication, CMP-NuRapid, D-NUCA
...but suffer from shortcomings
  complex, high-latency lookup/coherence
  don’t scale
  lower effective cache capacity
  optimize only for subset of accesses
We need:
Simple, scalable mechanism for fast access to all data

## Slide 413: Our Proposal: Reactive NUCA
Cache accesses can be classified at run-time
  Each class amenable to different placement
Per-class block placement
  Simple, scalable, transparent
  No need for HW coherence mechanisms at LLC
  Avg. speedup of 6% & 14% over shared & private
    Up to 32% speedup
    -5% on avg. from ideal cache organization
Rotational Interleaving
  Data replication and fast single-probe lookup

## Slide 414: Outline
Introduction
Access Classification and Block Placement
Reactive NUCA Mechanisms
Evaluation
Conclusion

## Slide 415: Terminology: Data Types
core
L2
core
L2
core
core
L2
core
Read
or
Write
Read
Read
Read
Write
Private
Shared
Read-Only
Shared
Read-Write

## Slide 416: Conventional Multicore Caches
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
dir
L2
L2
L2
We want: high capacity (shared) + fast access (priv.)
Private
Shared
Addr-interleave blocks
High effective capacity
Slow access
Each block cached locally
Fast access (local)
Low capacity (replicas)
Coherence: via indirection (distributed directory)

## Slide 417: Where to Place the Data?
Close to where they are used!
Accessed by single core: migrate locally
Accessed by many cores: replicate (?)
  If read-only, replication is OK
  If read-write, coherence a problem
    Low reuse: evenly distribute across sharers
sharers#
read-write
migrate
replicate
share
read-only

## Slide 418: Methodology
Flexus: Full-system cycle-accurate timing simulation
Model Parameters
Tiled, LLC = L2
Server/Scientific wrkld.
  16-cores, 1MB/core
Multi-programmed wrkld.
  8-cores, 3MB/core
OoO, 2GHz, 96-entry ROB
Folded 2D-torus
  2-cycle router
  1-cycle link
45ns memory
Workloads
OLTP: TPC-C 3.0 100 WH
  IBM DB2 v8
  Oracle 10g
DSS: TPC-H Qry 6, 8, 13
  IBM DB2 v8
SPECweb99 on Apache 2.0
Multiprogammed: Spec2K
Scientific: em3d

## Slide 419: Cache Access Classification Example
Each bubble: cache blocks shared by x cores
Size of bubble proportional to % L2 accesses
y axis: % blocks in bubble that are read-write
% RW Blocks in Bubble

## Slide 420: Cache Access Clustering
Scientific/MP Apps
Accesses naturally form 3 clusters
Server Apps
migrate
locally
share (addr-interleave)
replicate
R/W
migrate
replicate
share
R/O
sharers#
% RW Blocks in Bubble
% RW Blocks in Bubble

## Slide 421: Classification: Scientific Workloads
Scientific mostly read-only or read-write with few sharers or none

## Slide 422: Private Data
Private data should be private
  Shouldn’t require complex coherence mechanisms
  Should only be in local L2 slice - fast access
More private data than local L2 can hold?
  For server workloads, all cores have similar cache pressure, no reason to spill private data to other L2s
  Multiprogrammed workloads have unequal pressure ... ?

## Slide 423: Shared Data
Most shared data is Read/Write, not Read Only
Most accesses are 1st or 2nd access following a write
  Little benefit to migrating/replicating data closer to one core or another
Migrating/Replicating data requires coherence overhead
Shared data should have 1 copy in L2 cache
Notes: In other CMP-NUCA papers, shared data generally moved to the middle because it was accessed by all cores.

## Slide 424: Instructions
scientific and multiprogrammed -> instructions fit in L1 cache
server workloads: large footprint, shared by all cores
instructions are (mostly) read only
access latency VERY important
Ideal solution: little/no coherence overhead (Rd only), multiple copies (to reduce latency), but not replicated at every core (waste capacity).

## Slide 425: Summary
Avoid coherence mechanisms (for last level cache)
Place data based on classification:
  Private data -> local L2 slice
  Shared data -> fixed location on-chip (ie. shared cache)
  Instructions -> replicated in multiple groups

## Slide 426: Groups?
Indexing and Rotational Interleaving
clusters centered at each node
4-node clusters, all members only 1 hop away
up to 4 copies on chip, always within 1-hop of any node, distributed across all tiles

## Slide 427: Visual Summary
Private L2
Core
Core
Core
Core
Private L2
Private L2
Private L2
Shared L2
Core
Core
Core
Core
L2 cluster
Core
Core
Core
Core
L2 cluster
Private Data Sees This
Shared Data Sees This
Instructions
See This

## Slide 428: Coherence: No Need for HW Mechanisms at LLC
Fast access, eliminates HW overhead
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
core
core
core
core
L2
L2
L2
L2
Private data: local slice
Shared data: addr-interleave
Reactive NUCA placement guarantee
  Each R/W datum in unique & known location

## Slide 429: Evaluation
Delivers robust performance across workloads
  Shared: same for Web, DSS; 17% for OLTP, MIX
  Private: 17% for OLTP, Web, DSS; same for MIX
ASR (A)
Shared (S)
R-NUCA (R)
Ideal (I)

## Slide 430: Conclusions
Reactive NUCA: near-optimal block placement and replication in distributed caches
Cache accesses can be classified at run-time
  Each class amenable to different placement
Reactive NUCA: placement of each class
  Simple, scalable, low-overhead, transparent
  Obviates HW coherence mechanisms for LLC
Rotational Interleaving
  Replication + fast lookup (neighbors, single probe)
Robust performance across server workloads
  Near-optimal placement (-5% avg. from ideal)