## Slide 1
EIE: Efficient Inference Engine on Compressed Deep Neural Network
Song Han*, Xingyu Liu*, Huizi Mao*, Jing Pu*, Ardavan Pedram*, Mark A. Horowitz*, William J. Daly*†
*Stanford University †NVIDIA
Published in the Proceedings of ACM/IEEE 43rd Annual International Symposium on Computer Architecture (ISCA 2016)

## Slide 2
Motivation
Deep Neural Networks are BIG ... and getting BIGGER
  e.g. AlexNet (240 MB), VGG-16 (520 MB)
Too big to store on-chip SRAM and DRAM accesses use a lot of energy
Not suitable for low-power mobile/embedded systems
Solution: Deep Compression

## Slide 3
Deep Compression
Technique to reduce size of neural networks without losing accuracy
      Pruning to Reduce Number of Weights
      Quantization to Reduce Bits per Weight
      Huffman Encoding
“Deep Compression: Compressing Deep Neural Networks with Pruning, Trained Quantization and Huffman Coding”, Song Han et al., ICLR 2016

## Slide 4
Deep Compression
“Deep Compression: Compressing Deep Neural Networks with Pruning, Trained Quantization and Huffman Coding”, Song Han et al., ICLR 2016

## Slide 5
Pruning
Remove weights/synapses “close to zero”
Retrain to maintain accuracy
Repeat
Sparse Network

## Slide 6: Pruning Results

## Slide 10
Quantization and Weight Sharing
Quantize to fixed number of distinct values at no accuracy loss
AlexNet conv layers quantized using 8 bits (256 16-bit weights) results in zero accuracy loss

## Slide 11
Quantization and Weight Sharing

## Slide 14
Huffman Encoding
General lossless compression scheme
Encode more frequent values with less bits
Huffman, D. (1952) “A Method for the Construction of Minimum-Redundancy Codes”
AAAAAAABCDDD
Letter | Frequency | Encoding
A | 7 | 0
D | 3 | 10
B | 1 | 110
C | 1 | 111
19 bits vs 24 bits for 2-bit encoding

## Slide 15
Results
Compression Ratios (same or better accuracy)
  LeNet-300-100 – 40X
  AlexNet – 35X
  VGG16 – 49X
  LeNet-5 – 39X

## Slide 16
Efficient Inference Engine (EIE)
Compressed deep neural networks non-ideal on existing hardware
EIE specialized architecture for inference on compressed DNN
Multiple PEs
Distributed SRAM storage

## Slide 17: Fully-Connected Layers

## Slide 18: Fully-Connected Layers

## Slide 19
Distributed Weight Storage
Weight Matrix distributed across PEs by row
Activations stored distributed, but broadcast to all PEs
COLORS show assignment to PE not how computation proceeds

## Slide 20
Compressed Sparse Column (CSC)
Array of Non-zero weights (4 bit entries)
Array of Number of preceeding zeros (4 bit entries)
Array of pointer to first non-zero weight in each column of weight matrix

## Slide 22
Output activation calculation happens within a single PE

## Slide 23
SRAM
162 KB SRAM per PE
  Activations (2 KB)
  Sparse Matrix (128 KB)
  Pointers (32 KB)
93% Area

## Slide 24
Processing Element (PE)

## Slide 25
Processing Element (PE)
Non-zero Activations broadcast to all PEs
PE loads non-zero weights from SRAM
Arithmetic Unit performs multiply-accumulate
Result stored in Local Activation SRAM

## Slide 26: Processing Activations
Got to multiply with all weights along the corresponding column
The weights are distributed
Along Pes
The amount of work per PE
Varies: diff # of non-zero Ws
There will be load imbalance

## Slide 27: Skipping Zero Activations
If an activation is zero, no need to broadcast
To gain performance, must do something else
Distributed first-non-zero-activation detection
  Tree like

## Slide 28: Load Imbalance
Queueing sometimes is all you need

## Slide 29: Pointer Reads
Need pj and pj+1
How many Ws
Two single-ported Banks

## Slide 30: Input/Output Activations
Two register files
Toggle purpose (I or O) to implement feed forward
16 activations  4K activations across 64 Pes
Longer vectors  Use SRAM, do batches

## Slide 31
Processing Element (PE)

## Slide 32
Results
EIE (64 PE), 13x faster than GPU (Titan X), 3400x more energy efficient

## Slide 33
Strengths and Weaknesses
Strengths
  Good compression ratio of weights
  Good energy efficiency
Weaknesses
  Requires Retraining
  Poor performance for batch activations
  Transferring Activations between PEs can become bottleneck
  Not great on convolutional layers