## Slide 1: Delta RNN: A Power-efficient Recurrent Neural Network Accelerator
Andreas Moshovos, Feb 2019
Gao, Neil, Ceolini, Liu, Delbruck
U of Zurich & ETH
FPGA ‘18

## Slide 2: Overview
RNNs  Natural Language Processing
    Why? Temporal Sequences  Output depends on history not only current input
Vanishing Gradient Problem
    Long-Short Term Memory
    Gated Recurrent Unit  This work
  All use multiple Fully-Connected (maybe different now?)
    Bottleneck: Memory traffic for weights
Delta Network Algorithm
    Only process activation and input changes if above a threshold
    Temporal correlation
Delta RNN
    FPGA Implementation of DN

## Slide 3: Recurrent Neural Nets
FC
FC
FC
Να υπαρχεις
ή να μην
Layers
Output Depends on:
1. Current Input
2. Previous outputs
Captures Temporal Correlations
To Be or Not to Be
Temporal Sequence
vector
x(t)
h(t)
h(t-1)
“1 step delay”

## Slide 4: Vanishing Grandient Problem: Training
Impact of “long term memory” hard to capture
Attenuates severely
h(t)
FC
FC
x(t)
h(t-1)
FC
FC
x(t-n)
h(t-n-1)
FC
FC
x(t-n+1)
h(t-n)
h(t-n+1)

## Slide 5: Gated Recurrent Unit: Example Use
Their Test Network
Regular Net: 5 FCs

## Slide 6: Gated Recurrent Unit: Structure
Inputs: x(t) and h(t-1)
Output: h(t)

## Slide 7: Gated Recurrent Unit: Structure
Three “gates”:
    r: Reset
    u: Update
    c: Candidate

## Slide 8: Gated Recurrent Unit: Structure
r: Reset:
    Amount of previous hidden state added to candidate hidden state
u: Update
    h should be updated by candidate hidden state  enable long term memory
What do these mean? …

## Slide 9: Gated Recurrent Unit: Structure
Element wise
b: biases

## Slide 10: Gated Recurrent Unit: Structure
u(t):
“keep” feature’s h(t-1) value
or
Update with c(t)
Degree of each

## Slide 11: Gated Recurrent Unit: Structure
c(t): candidate
Some of x(t)/current input
or
Some of hidden state h(t)

## Slide 12: Where time goes in GRU RNNs
Weight matrices
Wxr, Whr
Wxu, Whu
Wxc, Whc
Vector-Matrix Products

## Slide 13: Where time goes in GRU RNNs: MxV
Weight matrices
x(t)
Wxr(t)
h(t) sized
Dense:
  Compute Cost: n^2
  Mem Cost: n^2 (weight) + n (vector)

## Slide 14: Sparsity Reduces Costs: Compute and Memory
Sparsity in x(t) and h(t-1): what if value is zero
x(t)
Wxr(t)
h(t) sized
“Sparse”: oc = occupancy, fraction of non-zero values
  Compute Cost: oc x n^2
  Mem Cost: oc x n^2 (weight) + oc x n (vector)
But not that much sparsity to start with

## Slide 16: Delta RN: Increase Sparsity in x(t) and h(t-1)
Key idea: update x(t) or h(t-1) iff change above threshold Θ
Intuition:
  Temporal correlation, some values don’t change much
  Magnitude of change ~ feature importance

## Slide 17: Delta RN: Increase Sparsity in x(t) and h(t-1)
Delta GRU

## Slide 18: Delta RNN: FPGA Implementation
Xilinx Zynq
FC Layers: ARM Core
DeltaRNN: GRU Layer

## Slide 19: Delta RNN: FPGA Implementation
IEU: Delta Vectors
MxV: Matrix x Vector
AP: activations

## Slide 20: Input Encoding Unit
x(t)  Dx(t)  Value/Index Sparse Representation
h(t)  Dh(t)
PT RegFile: Keep previous vectors to calculate Dx(t)/Dh(t)
    Update w/ current
x(t) 4/cycle / 64b 16b Q8.8
h(t) 32/cycle / 256b
AXI-DMA limiter

## Slide 21: Input Encoding Unit: Delta Scheduler
Encode non-zero values  value/index
    BW: 2 per cycle

## Slide 22: Input Encoding Unit: Delta Scheduler: Latency
Dh(t-1) w/ 1024 elements
  Best Case: 0% occupancy (all zeros)
    32/cycle – input bound  32 cycles
  Worst Case: 100% occupancy (all non-zero)
    2/cycle output – output bound  512 cycles
Dx(t) w/ 39 elements
  Padded to 40
  Best Case: 0% occupancy  10 cycles, 4/cycle
  Worst Case: 100% occupancy  20 cycles (output bound)

## Slide 23: MxV Unit
3 Channels: R, U, C
R: Mr(t), U: Mu(t), C: Mcx(t) & Mch(t)
128 Mul + 128 Add / 16b Q8.8 DSP + LUTs 32b

## Slide 24: Scheduling
Since h(t) tends to be longer than x(t)
First do Dx(t)  all MxV channels do Dx(t)
Overlaps with calculating Dh(t)

## Slide 25: MxV Unit: Scheduling
Weights from BRAM true dual-port
Can do two products per column
    Guessing: data width of BRAM ports?

## Slide 26: AP: can use MxV multipliers
MxV busy only when both Dx(t) & Dh(t) have non-zeros
AP BW is low  MxV will be idle  reuse it for AP
    ???

## Slide 27: AP: can use MxV multipliers
S1 / S5: 16b addition
S2: 32b addition
S2/S4: 32b mul Q16.16  Q8.8 into S5

## Slide 28: Activation Functions
Range Addressable LUT

## Slide 29: Quantization Ranges

## Slide 30: Accuracy: theta during training vs. inference
Better use the same Theta
0x80 only 1.57% loss

## Slide 31: Theta vs. Throughput & Latency
Great Benefits

## Slide 32: Sparsity and Speedup vs. Theta
better

## Slide 33: Power Measurements
Base+fan: no FPGA board  7.9W
+ Zynq w/ no programming  9.4W (9.7 above?)
w/ programming  10W
w/ prog + running  15.2W
    Zynq MPP = 15.2 – 7.9 = 7.3W
    Zynq Chip = 15.2 – 9.7 = 5.5W  Power Analyzer @ 50% activity
    PowerAnalyzer: DRNN 2.72W BRAM 2.28W
Measured @
Wall-Plug w/
Volcraft 4500Advanced

## Slide 34: Summary