## Slide 1: RePLay
Andreas Moshovos
moshovos@eecg.toronto.edu
EA310

## Slide 2: RePLay Execution Model
Frames may contain taken branches  continuous fragment of execution trace

## Slide 3: RePLay Example
while (l != NULL) {
if (l->key == value) return l;
if (l->key < value)
l = l->left;
else
l = l->right;
}

## Slide 4: RePLay Example
for (i = 0; i < N; i++) {
if ((anew[i] – aold[i]) > threshold)
anew[i] = calculate(anew[i], aold[i]);
assert (anew[i] >= min_a);
}

## Slide 5: ASSERT and Execution Model
Assert: checks whether path was followed
Assert succeeds 
  do nothing
Assert fails 
  undo all of frame execution, restart from scratch/beginning

## Slide 6: Frames Enable Optimizations
Frame executes as whole
Can be optimized
Classical optimizations
  Code motion
  Constant Propagation
  Dead-code Elimination
  Code substitution
  Etc.
Speculative, run-time optimizations
  Predict live-in values
  Treat as constants

## Slide 7: Frame trade offs
The larger the frame the more optimizations can be applied
How likely it is to complete
What fraction of the execution stream is converted to frames?

## Slide 8: RePLay Framework

## Slide 9
Frame Cache:
  Previously detected and optimized frames

## Slide 10: Sequencer
Frame Penalty:
  Depends on the length and how deep is the failing assertion
RePLay Sequencer
  Select between: Branch Predictor and Frames

## Slide 11: Sequencer Example

## Slide 12: Frame Construction
Goal: Create Atomic Regions that are likely to execute successfully.
Branch Promotion:
  Convert branches to asserts
  Uses Branch Confidence

## Slide 13: Idealistic Frame Evaluation: Frame Size
Ideal static: branch promoted if bias is >= 95%
ideal = profile = execute input
n = confidence level
Infinite branch bias table

## Slide 14: Promotion Effectiveness: Branch Breakdown + Frame Length
n=32, only very strongly biased branches
History is key

## Slide 15: Idealistic – Branch Coverage
Infinite frame cache

## Slide 16: Frame Completion Rate

## Slide 17: Average Frame Length – 64KB bias table

## Slide 18: Instruction Coverage

## Slide 19: Path History Based Prediction

## Slide 20: Frame Completion Rate

## Slide 21: Frame Sequencer

## Slide 22: Frame Predictor

## Slide 23: Frame Cache
Trace cache + trace can span multiple lines

## Slide 24: Frame Size

## Slide 25: Instruction Coverage

## Slide 26: Optimization Example

## Slide 27: Optimization Example

## Slide 28: Ex #2: Copy Bytes From Compress
# bytes copied varies but always > 9
Live-ins:
  Gp
  V0 # bytes to copy
  T5 source buffer
  Frame overwrites w/o reading: a1-a5, t3, t6 & t7
  Loop changes v0
  Loop ins:
    A4 ptr to ptr to dest buffer
    T3 # uncopied bytes
    T6 ptr to curr source byte
  Potential live outs: a1-a5, t3, t6, t7 & v0

## Slide 29: Assertions
Pointer analysis the biggest problem
Instruction 8: frame requires at least 8 bytes to copy
  Destination does not overlap forward source (insts 9-10)
  Source bytes do not overlap destination buffer (insts 11-13)
  Neither do the destination bytes (insts 11-13)
Leveraging allows the use of quad word instructions
8 iterations  single load-store combo
Insts 136  41

## Slide 32: An Instruction in a Processor’s Lifetime

## Slide 33: How to Improve Performance?
Increase concurrency
  Do more things simultaneously
Instruction Level Parallelism
  Find concurrency in instruction processing
    Within the instruction
    Across multiple instructions
Dynamic – User Transparent
    The machine discovers it
Static – User/Compiler Specifies
    Machine is build to execute multiple instructions
Parallelism – thread level
  Duplicate units / processors
  Rely on programmer to write parallel program

## Slide 34: Pipelining

## Slide 35: Sequential Semantics are Preserved

## Slide 36: Superscalar - In-order
Two or more consecutive instructions in the original program order can execute in parallel
  This is the dynamic execution order
N-way Superscalar
  Can issue up to N instructions per cycle
  2-way, 3-way, …
fetch
decode
ld
fetch
decode
add
fetch
decode
sub
fetch
decode
bne

## Slide 37: Data Dependences

## Slide 38: Superscalar vs. Pipelining
loop: ld r2, 10(r1)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
Pipelining:
sum += a[i--]
fetch
decode
ld
fetch
decode
add
fetch
decode
sub
fetch
decode
bne
time
Superscalar:
fetch
decode
ld
fetch
decode
add
fetch
decode
sub
fetch
decode
bne

## Slide 39: Superscalar Performance
Performance Spectrum?
  What if all instructions were dependent?
    Speedup = 0, Superscalar buys us nothing
  What if all instructions were independent?
    Speedup = N where N = superscalarity
Again key is typical program behavior
  Some parallelism exists

## Slide 40: “Real-Life” Performance
OLTP = Online Transaction Processing
SOURCE:
Partha Ranganathan
Kourosh Gharachorloo**
Sarita Adve*
Luiz André Barroso**
Performance of Database Workloads on
Shared-Memory Systems with Out-of-Order
Processors
ASPLOS98

## Slide 41: “Real Life” Performance - Superscalar
SPEC CPU 2000: Simplescalar sim: 32K I$ and D$, 8K bpred

## Slide 42: Issue Mechanism – A Group of Instructions at Decode
Assume 2 source & 1 target max per instr.
  comparators for 2-way:
    3 for tgt and 2 for src (tgt: WAW + WAR, src: RAW)
  comparators for 4-way:
    2nd instr: 3 tgt and 2 src
    3rd instr: 6 tgt and 4 src
    4th instr: 9 tgt and 6 src
tgt
src1
src1
tgt
src1
src1
tgt
src1
src1
simplifications
may be possible
resource checking
not shown
Program order

## Slide 43: Preserving Sequential Semantics
In principle not much different than pipelining
Program order is preserved in the pipeline
Some instructions proceed in parallel
  But order is clearly defined
Defer interrupts to commit stage (i.e., writeback)
  Flush all subsequent instructions
    may include instructions committing simultaneously
  Allow all preceding instructions to commit
Recall comparisons are done in program order
Must have sufficient time in clock cycle to handle these
See next slide

## Slide 44: Interrupts Example
fetch
decode
ld
fetch
decode
add
fetch
decode
div
fetch
decode
bne
Exception
raised
Exception
taken
fetch
decode
bne
fetch
decode
ld
fetch
decode
add
fetch
decode
div
fetch
decode
bne
Exception
raised
Exception
taken
fetch
decode
bne
Exception
raised

## Slide 45: 21164

## Slide 46: Case Study: Alpha 21164

## Slide 47: 21164: Int. Pipe

## Slide 48: 21164: Memory Pipeline

## Slide 49: 21164: Floating-Point Pipe

## Slide 50: Performance Comparison
Source:

## Slide 51: CPI Comparison: Ideal 0.25

## Slide 52: Compiler Impact
Optimized
Base
Performance

## Slide 53: Stall Cycles - 21164
No instructions
Data Dependences/Data Stalls

## Slide 54: Issue Cycle Distribution - 21064

## Slide 55: Issue Cycle Distribution - 21164

## Slide 56: Superscalar/Pipeline challenges
Must have multiple instructions in-flight
  How to find them?
    Branch/Jump instructions
Must fetch multiple instructions

## Slide 57: Instruction Decode/Issue – Alpha 21164 Solution
Up to four insts/cycle
Naturally aligned groups
  Must start at 16 byte boundary (INT16)
  Simplifies Fetch path
CPU needs:
I-Cache:
Where instructions come from?

## Slide 58: Fetching Four Instructions
CPU needs:
I-Cache:
Where instructions come from?
Software must guarantee alignment at 16 byte boundaries
Lots of NOPs

## Slide 59: Instruction Decode/Issue
Up to four insts/cycle
Naturally aligned groups
  Must start at 16 byte boundary (INT16)
  Simplifies Fetch path
All of group must issue before next group gets in
Simplifies Scheduling
  No need for reshuffling

## Slide 60: Good Design Practice
Optimize for the common case
Make sure all cases work correctly
Have a problem
  Think of the ideal solution
    Is it too expensive/complex  may lead to slower clock cycle
  Think of alternatives
    Simpler to implement  may lead to faster clock cycle
  Performance = IPC x Freq
  Reason/measure performance difference
  Which is best?

## Slide 61: Sequential Semantics - Review
Instructions appear as if they executed:
  In “program order”
    As if they executed one after the other
Program
Order
Pipelining
Superscalar
Out-of-Order

## Slide 62: Out-of-Order Execution
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
do {
sum += a[++m];
i--;
} while (i != 0);
out-of-order
loop: add r4, r4, 1
ld r2, 10(r4)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
Superscalar

## Slide 63: Sequential Semantics?
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
Execution does NOT adhere to sequential semantics
To be precise: Eventually it may
Simplest solution:
  Define problem away
  IBM 360 did this
Not acceptable today: e.g., Virtual Memory
Three-phase Instruction execution
  In-Progress, Completed and Committed
inconsistent
consistent

## Slide 64: Preserving Sequential Semantics: Three phases
Instr. exec. in 3 phases:
  In-progress, Completed, Committed
  OOO for in-progress and Completed
  In-order Commits
Completed - out-of-order: ”Visible only inside”
  Results visible to subsequent instructions
  Results not visible to outsiders
    On interrupts completed results are discarded
Committed - in-order: ”Visible to all”
  Results visible to subsequent instructions
  Results visible to outsiders
    On interrupt committed results are preserved

## Slide 65: How Completes Help w/ Performance
Time
DIV R3, _, _
ADD R1, _, _
ADD _, R1, _
In-order
commits
in-order
completes
out-of-order completes
in-order commits
complete
fetch
decode
fetch
decode
sub
bne
fetch
decode
add
fetch
decode
ld
fetch
decode
add
commit
commit
commit
commit
commit

## Slide 66: Implementing Completes/Commits
Key idea:
  Maintain sufficient state around to be able to roll-back when necessary
  Roll-back:
    Discard (aka Squash) all not committed
One solution (conceptual): History File
  Upon Complete instruction records previous value of target register
  Upon Discard, instruction restores target value
  Upon Commit, nothing to do
Focus on scheduling mechanisms

## Slide 67: Solution #2: Future File
Two states:
  Architectural
    Updated only on commit
  Speculative
    Updated on complete
Normally use Speculative
On exception:
  Flush Speculative
  Use Architectural
Implementing precise interrupts in pipelined processors
J. E. Smith and A. Pleszkun,
http://www.eecg.toronto.edu/~moshovos/ACA07/readings/smith-interrupts.pdf

## Slide 68: Out-of-Order Execution Overview
Program Form
Processing Phase
Static program
dynamic inst.
Stream (trace)
execution
window
completed
instructions
Dispatch/ dependences
inst. Issue
inst execution
inst. Reorder &
commit
In-Progress
Completed
Committed

## Slide 69: Out-of-Order Execution: Stages
Fetch: get instruction from memory
Decode/Dispatch: what is it? What are the dependences
Issue: go – all dependences satisfied
Execute: perform operation
Complete: result available to other insts.
Commit: result available to outsiders

## Slide 70: OOO Scheduling
Instruction @ Decode:
  Do I have dependences yet to be satisfied?
  Yes, stall until they are
  No, clear to issue
When Do I Wakeup?
  Producer Completes and notifies me
  If All dependences satisfied
  I can proceed
Dependence:
  (later instruction, earlier instruction) & type
We’ll first consider RAW and then move on to WAW and WAR

## Slide 71: Stalling @ Decode for RAW
Are there unsatisfied dependences?
  RAW: have to wait for register value
  We don’t really care who is producing the value
  Only whether it is available
Can use the Register Availability Vector as in pipelining/superscalar
  Also known as scoreboard
At Decode
  Reset bit corresponding to your target
  At writeback set
  Check all bits for source regs: if any is 0 stall

## Slide 72: Issuing Instructions: Scheduling
Determine when an instruction can issue
  Ignore resources for the time being
Stalled because of RAW w/ preceding instruction
Concept:
  Producer (write) notifies consumers (read)
Requirements:
  Consumers need to be able to identify producer
  The register name is one possible link
Mechanism
  Consumer placed in a reservation station
  Producers on complete broadcasts identity
  Waiting instructions observe
  Update Operand Availability
  Issue if all operands now available

## Slide 73: Reservation Station
State pertaining to an instruction
  What registers it reads
  Whether they are available
  What is the destination register
  What state is the instruction in
    Waiting
    Executing

## Slide 74: Out-Of-Order Exec. Example
loop: add r4, r4, 4
ld r2, 10(r4) 4 cycles lat
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
Cycle 0
status

## Slide 75
Out-Of-Order Exec. Example: Cycle 0
1
1
1
0
r1
r2
r3
r4
RAV
op
src1
src2
tgt
Cycle 0
add
r4/1
NA/1
r4/0
Rdy
status
loop: add r4, r4, 4
ld r2, 10(r4)
add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
Ready to be
executed

## Slide 76
Cycle 1
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Exec
status
ld
r4/1
NA/1
r2
Rdy
R4 gets produced now
Notify those waiting for R4

## Slide 77
Cycle 2
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait

## Slide 78
Cycle 3
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
0
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Rdy
No dependences

## Slide 79
Cycle 4
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Exec
r1 produced now
Notify consumers
bne
r1/1
r0/1
NA
Rdy
r1 will be available next cycle

## Slide 80
Cycle 5
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
0
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
add
r3/1
r2/0
r3
Wait
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Exec
executing

## Slide 81
Cycle 6
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
0
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Exec
Wait for r2
Result available @ cycle 6
Notify consumers
add
r3/1
r2/1
r3
Rdy
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Exec
executing

## Slide 82
Cycle 7
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Cmtd
Executing
Notify consumers
add
r3/1
r2/1
r3
Exec
sub
r1/1
NA/1
r1
Compl
Completed
bne
r1/1
r0/1
NA
Compl

## Slide 83
Cycle 8
loop: add r4, r4, 4
ld r2, 10(r4) add r3, r3, r2
sub r1, r1, 1
bne r1, r0, loop
1
1
1
1
r1
r2
r3
r4
RAV
op
src1
src2
tgt
add
r4/1
NA/1
r4
Cmtd
status
ld
r4/1
NA/1
r2
Cmtd
add
r3/1
r2/1
r3
Cmtd
sub
r1/1
NA/1
r1
Cmtd
bne
r1/1
r0/1
NA
Cmtd

## Slide 84: Window vs. Scheduler
Window
  Distance between oldest and youngest instruction that can co-exist inside the CPU
  Larger window  Potential for more ILP
Scheduler
  Number of instructions that are waiting to be issued
Window
  Instructions enter at Fetch
  Exit at Commit
Scheduler
  Instructions enter at Decode
  Leave at writeback/complete
Window >= Scheduler
  Can be the same structure
In window but not in scheduler  completed
instructions

## Slide 85: Speculative Execution
Why?
  1 every 5 insts is a branch (control flow)
  Today’s processors have a window of 128 insts
  Can’t wait until a branch is resolved to fetch next set of insts
  Solution: Speculate
Fetch branch
Resolve branch
Wrong
squash

## Slide 86: Beyond Simple OoO
A
B
C
D
E
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F2, F7, F4
E will wait for B, C and D.
WAR w/ C and D
WAW w/ B
Can we do better?

## Slide 87: What if we had infinite registers
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F2, F7, F4
A: LF F6, 34(R2)
B: LF F2, 45(R3)
C: MULF F0, F2, F4
D: SUBF F8, F2, F6
E: ADDF F9, F7, F4
No false dependences anymore
Since we do not reuse a name we can’t have WAW and WAR

## Slide 88: Register Renaming
Register Version
  Every Write creates a new version
  Uses read the last version
  Need to keep a version until all uses have read it.
Register Renaming:
  Architectural vs. Physical Registers
    more phys. than arch.
  Maintain a map of arch. to phys. regs.
  Use in-order decoding to properly identify dependences.
  Instructions wait only for input op. availability.
  Only last version is written to reg. file.

## Slide 89: Register renaming example
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p1

## Slide 90: Register renaming example
First rename input operands:
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p1

## Slide 91: Register renaming example
Then rename destination
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p4
From free list
r1
p2
ROB
For recovery purposes

## Slide 92: Register renaming example
Rename inputs
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p3
p4
p5
p5
p4
From free list
r1
p2
ROB
For recovery purposes

## Slide 93: Register renaming example
Rename destination
RAT
Architectural
Register
Physical
Register
# arch. regs
Lg(# arch. regs)
A add r1, r2, 100
B add r3, r1, r1
C sub r1, r2, r2
Original Code
A add p4, p2, 100
B add p5, p4, p4
C sub p6 p2, p2
Renamed Code
p1
p2
p5
p4
p5
p5
p4
From free list
r1
p2
ROB
For recovery purposes
r3
p3

## Slide 94: MIPS R10000 Pipeline Overview

## Slide 95: MIPS R10000 Architecture

## Slide 96: MIPS R10000 Pipelines

## Slide 97: Instruction Fetch
Must feed core with instructions
  Window is 32
Start with this

## Slide 98: Instruction Fetch
Address translation
Instruction Cache Tags
Instruction Cache Data
Branch Prediction
Instruction buffer
timeline

## Slide 99: Fetching Multiple Instructions?

## Slide 100: Fetching Multiple Instructions & the I-Cache
4 instructions (4 bytes each) out of 32-byte line
  Continuous chunk
  Alignment restrictions also limit possible cases
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
i-0
i-1
i-2
i-3
selection/alignment network
to scheduler
i-0
i-1
i-2
i-3

## Slide 101: MIPS R1000 Solution: Fetching 4 continuous insts
5
6
7
8
to scheduler
rotate
0
4
8
12
3
7
11
15
1
5
9
13
2
6
10
14
4 instructions (4 bytes each) out of 16-inst line (64 bytes)
Four banks: read one instruction from each
Calculate addr+0, …, addr+3 and send its MOD 4 to four read ports
  Only one inst. per set per cycle (for up to 4 insts fetched)
Select the 4 words
Then rotate into place
8
7
5
6

## Slide 102: Control Flow
Speculative Branches
  4-entry stack
  4-bit vector one-hot encoding of which is which
    Every instruction tagged with this
  Take snapshot of some structures
    History file – coarse grain
Resolving Branches
  Correct
    Discard entry from stack
    Clear the corresponding bit from all instructions in the pipe
  Incorrect
    Discard all instructions following branch
    Broadcast one-hot encoded branch ID
    Flush everything

## Slide 103: Register Renaming
Doing things early
Reduces critical path
Reorder buffer
From decode
To Scheduler
Link to ROB
Register
Alias
Table
scoreboard

## Slide 104: Scheduler
Reservation
Station
select
WAKEUP
Control Speculation

## Slide 105: Back-to-Back Scheduling

## Slide 106: Optimistic Scheduling
ld r1
add _, r1
F
E
M
D
W
F
E
M
D
W
Cache hit
D
M
E
D
add should start execution here
Must decide that add should execute
Start making scheduling decisions
Hit/miss known here

## Slide 107: Optimistic Scheduling #2
ld r1
add _, r1
F
E
M
D
W
F
E
M
D
W
Cache hit
D
M
E
D
add should start execution here
Must decide that add should execute
Start making scheduling decisions
Hit/miss known here
Guess Hit/Miss

## Slide 108: Data Cache Datapath