## Slide 1
PC
Memory
8
8
ADDR
Data_out
Data_in
MemRead
MemWrite
AddrSel
IR
MDR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
8
ALU1
8
8
8
ALU2
8
2
8
1
SE
8
Imm4
ZE
8
Imm5
4
5
data1
data2
dataw
8
8
RegIn
ALUop
3
MDRload
IRload
ALUout
RF
RFWrite
N
Z
FlagWrite
PCwrite
8
Imm3
ZE
0
1
1
0
1
0
000
001
010
011
100
ALU
ALUoutLD
ABLD

## Slide 2: Our Processor
256 Bytes of memory
Addresses are 8 bits
4 registers, each 8 bits, R0-R3
PC, also 8 bits
Z and N: flags, single bit registers
~10 instructions
Each instruction: encoded in 8 bits

## Slide 3: ADD Ra Rb
Ra = Ra + Rb
Set Z and N
  If (Ra == 0) Z = 1; else Z = 0;
  If (Ra < 0) N = 1; else N = 1;
PC = PC + 1

## Slide 4: SUB Ra Rb
Ra = Ra - Rb
set Z, N
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ra | Ra | Rb | Rb | 0 | 1 | 1 | 0

## Slide 5: NAND Ra Rb
Ra = Ra nand Rb (bitwise)
set Z, N
PC = PC + 1

## Slide 6: ORI imm5
R1= R1 or ZE(Imm5)
set Z, N
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IMM5_4 | IMM5_3 | IMM5_2 | IMM5_1 | IMM5_0 | 1 | 1 | 1

## Slide 7: SHIFT L/R Ra Imm3
If (L) Ra = Ra << ZE(Imm2)
else Ra = Ra << ZE(Imm2)
set Z, N
PC = PC + 1

## Slide 8: LOAD Ra (Rb)
Ra = Mem(Rb)
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ra | Ra | Rb | Rb | 0 | 0 | 0 | 0

## Slide 9: Store Ra (Rb)
Mem(Rb) = Ra
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ra | Ra | Rb | Rb | 0 | 0 | 1 | 0

## Slide 10: BNZ Imm4
if (Z is false) PC = PC + 1 + SE (Imm4) else PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IMM4_3 | IMM4_2 | IMM4_1 | IMM4_0 | 1 | 0 | 0 | 1

## Slide 11: BPZ Imm4
if ((Z is true) or (N is false)) PC = PC + 1 + SE (Imm4) else PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IMM4_3 | IMM4_2 | IMM4_1 | IMM4_0 | 1 | 1 | 0 | 1

## Slide 12: Components

## Slide 13
PC
8
Write
8
CLK
REGISTER

## Slide 14
MULTIPLEXER - MUX
8
Select
0
1
8
8

## Slide 15
DECODER
Select
00
01
10
11
2

## Slide 16
REGISTER FILE
2
reg1
reg2
regw
8
8
data1
data2
dataw
8
RF
RFWrite
2
2
CLK

## Slide 17
2
reg1
reg2
regw
8
8
data1
data2
dataw
8
RFWrite
2
2
CLK
R0
8
8
R1
8
8
R2
8
8
R3
8
8

## Slide 18
2
reg1
reg2
regw
8
8
data1
data2
dataw
8
RFWrite
2
2
CLK
MUX
MUX
R0
8
8
R1
8
8
R2
8
8
R3
8
8

## Slide 19
2
reg1
reg2
regw
8
8
data1
data2
dataw
8
RFWrite
2
2
CLK
MUX
MUX
R0
8
8
R1
8
8
R2
8
8
R3
8
8
DEC

## Slide 20
ALUop
3
N
Z
FlagWrite
ALU
8
8
8
ARITHMETIC & LOGIC UNIT
ALUOp | ALUout
000 | A + B
001 | A – B
010 | A OR B
011 | A NAND B
100 | A << B
101 | A >> C
110 | Reserved
111 | Reserved
ALUout
A
B

## Slide 21
8
ALUop
3
8
ALUout
A
B
8
MULTIPLEXER
ADDER
SUBTRACTOR
OR
NAND
RIGHT SHIFTER
LEFT SHIFTER
N
Bit 7
NOR
Z
8
1 (bit 2)

## Slide 22
DATA Memory
8
ADDRESS
DATAin
8
DATAout
DMEM
MemRead
8
CLK
MemWrite
Like the RF
256 Registers
1 Read Port
1 Write Port (CLK)

## Slide 23
8
ADDRESS
8
data1
MUX
0000 0000
8
8
0000 0001
8
8
1111 1111
8
8
This is just the read port
We will assume MemRead and MemWrite in our design
This is common for external memories.

## Slide 24
A
8
Write
8
CLK
+
8
0000 0001
1
8
New Value

## Slide 25
PC
Memory
8
8
ADDR
Data_out
Data_in
MemRead
MemWrite
AddrSel
IR
MDR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
8
ALU1
8
8
8
ALU2
8
2
8
1
SE
8
Imm4
ZE
8
Imm5
4
5
data1
data2
dataw
8
8
RegIn
ALUop
3
MDRload
IRload
ALUout
RF
RFWrite
N
Z
FlagWrite
PCwrite
8
Imm3
ZE
0
1
1
0
1
0
000
001
010
011
100
ALU
ALUoutLD
ABLD

## Slide 26: ADD Ra Rb
Read mem[PC]
Decode
Read Ra, Read Rb
  Ra = inst 7,6
  Rb = inst 5,4
tmp = Ra+Rb
Ra = tmp
set Z, N
PC = PC + 1

## Slide 27
PC
Memory
8
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
IRload
PCwrite
CYCLE 1: FETCH THE INSTRUCTION:
[IR] = Mem[ [PC] ]

## Slide 28
PC
Memory
8
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
IRload
PCwrite
CYCLE 2: DECODE
Decide what to do next

## Slide 29
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
8
8
1
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 3: READ SOURCE REGISTERS
[A] = RF[ IR7..6 ]
[B] = RF[ IR5..4 ]

## Slide 30
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
8
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 4: DO Addition/Update Flags
[ALUout] = [A] op [B]
Update Flags
8
ALUop
3
ALUout
N
Z
ALU
8
FlagWrite

## Slide 31
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
8
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 5: Write Result back to Register
RF[ IR7..6 ] = [ALUout]
8
ALUop
3
ALUout
N
Z
ALU
8
FlagWrite
8

## Slide 32
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
8
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 6: Update PC
PC = PC + 1
8
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
8
ALU2
0
1
8

## Slide 33: SUB Ra Rb
Read mem[PC]
Decode
Read Ra, Read Rb
  Ra = inst 7,6
  Rb = inst 5,4
tmp = Ra-Rb
Ra = tmp
set Z, N
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ra | Ra | Rb | Rb | 0 | 1 | 1 | 0

## Slide 34
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLES 3-6: Same as ADD
Only Difference in Cycle 4: Do SUBTRACTION instead of ADDITION
ALUOp
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
8
8
8
0
1
8
ALU2

## Slide 35: NAND Ra Rb
Read mem[PC]
Decode
Read Ra, Read Rb
  Ra = inst 7,6
  Rb = inst 5,4
tmp = Ra nand Rb
Ra = tmp
set Z, N
PC = PC + 1

## Slide 36
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
8
8
8
0
1
8
ALU2
CYCLES 3-6: Same as ADD
Only Difference in Cycle 4: Do NAND instead of ADDITION
ALUOp

## Slide 37: ORI imm5
Read mem[PC]
Decode
Read R1  Not in the instruction opcode
tmp = R1 or ZE(Imm5)
  Imm5 = Inst7,3
R1 = tmp
set Z, N
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IMM5_4 | IMM5_3 | IMM5_2 | IMM5_1 | IMM5_0 | 1 | 1 | 1

## Slide 38
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 3: READ R1
A = RF[1];
We also read a 2nd register using IR54 (see reg2 connection)
This is useless for ORI but it is not harmful
B=RF[IR54];  useless but still done
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
0
1
8
ALU2

## Slide 39
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 4: R1 OR Imm5; update flags
ALUout = A OR ZE(IR7,3); update flags
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2

## Slide 40: Zero-Extension (Imm5)
0
out7
out0
in0
in5

## Slide 41
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 5: Write Register
RF[1] = AluOUT
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2

## Slide 42: SHIFT L/R RA Imm2
Read mem[PC]
Decode
Read Ra
tmp = Ra shift ZE(Imm3)
  Imm3 = Inst5 + Inst4,3
Ra = tmp
set Z, N
PC = PC + 1
L/R! + IMM2 = Imm3 to ALU

## Slide 43
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 3: READ Ra
A = RF[IR67];
We also read a 2nd register using IR54 (see reg2 connection)
This is useless for SHIFT but it is not harmful
B=RF[IR54];  useless but still done
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
0
1
8
ALU2

## Slide 44
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 4: Calculate
ALUout = A Shift ZE(L/R + Imm2)
Set Z and N
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2
Imm3
ZE
11

## Slide 45
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 5: Write Register
RF[IR7,6] = AluOUT
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2
Imm3
ZE
11

## Slide 46: LOAD Ra (Rb)
Read mem[PC]
Decode
Read Rb
tmp = Mem(Rb)
Ra = tmp
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ra | Ra | Rb | Rb | 0 | 0 | 0 | 0

## Slide 47
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 3: READ Rb
B = RF[IR54];
We also read a 2nd register using IR76 (see reg1 connection)
This is useless for LOAD
but it is not harmful
A=RF[IR76];  useless but still done
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
0
1
8
ALU2

## Slide 48
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
CYCLE 4: Read Data from Memory
MDR = MEM[B]
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2
Imm3
ZE
11
8
8
AddrSel
0
1
MDR
MDRload

## Slide 49
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
CYCLE 5: Write MDR to Register File
RF[IR7,6] = MDR
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2
Imm3
ZE
11
8
8
0
1
MDR
MDRload
RegIn

## Slide 50: Store Ra (Rb)
Read mem[PC]
Decode
Read Ra, Rb
Mem(Rb) = Ra
PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Ra | Ra | Rb | Rb | 0 | 0 | 1 | 0

## Slide 51
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
8
CYCLE 3: READ Ra & Rb
A = RF[IR67];
B=RF[IR54];
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
0
1
8
ALU2

## Slide 52
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
CYCLE 4: Write Data to Memory
MEM[B] = A
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
00
01
8
ZE
8
Imm5
5
10
ALU2
Imm3
ZE
11
8
8
AddrSel
0
1
MDR
MDRload
RegIn

## Slide 53: BZ Imm4
Read mem[PC]
Decode
if (Z is true) PC = PC + 1 + SE (Imm4)
else PC = PC + 1
7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
IMM4_3 | IMM4_2 | IMM4_1 | IMM4_0 | 0 | 1 | 0 | 1

## Slide 54
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
CYCLE 3: PC = PC+1
PC = PC + 1
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
8
ZE
8
Imm5
5
ALU2
Imm3
ZE
8
8
AddrSel
0
1
MDR
MDRload
RegIn
SE
8
Imm4
4
000
001
010
011
100

## Slide 55
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
CYCLE 4: Update PC for taken branch
If (Z) PC = PC + SE(IR7,4)
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
8
ZE
8
Imm5
5
ALU2
Imm3
ZE
8
8
AddrSel
0
1
MDR
MDRload
RegIn
SE
8
Imm4
4
000
001
010
011
100

## Slide 56: Sign-Extension (Imm4)
out7
out0
in0
in4

## Slide 57: Using Fewer Cycles

## Slide 58
CYCLE 1: IR = Mem[PC]
CYCLE 2: Decode
CYCLE 3: A = RF[IR7,6] & B = RF[IR5,4]
CYCLE 4: AluOut = A + B, Update Z & N
CYCLE 6: PC = PC + 1
CYCLE 5: RF[IR7,6] = AluOut

## Slide 59
Observe
  All instructions do
  PC = PC+1
  In their last cycle
  The value PC is known in Cycle 1
  The value PC is not used by any other cycle before the PC = PC + 1
Conclusion:
  We can do PC=PC + 1 in the first cycle
CYCLE 1: IR = Mem[PC]
CYCLE 2: Decode
CYCLE 3: A = RF[IR7,6] & B = RF[IR5,4]
CYCLE 4: AluOut = A + B, Update Z & N
CYCLE 6: PC = PC + 1
CYCLE 5: RF[IR7,6] = AluOut
PC as left by the previous instruction

## Slide 60
CYCLE 1: IR = Mem[PC] ; PC = PC + 1
CYCLE 2: Decode
CYCLE 3: A = RF[IR7,6] & B = RF[IR5,4]
CYCLE 4: AluOut = A + B; Update Z & N
CYCLE 6: PC = PC + 1
All instructions do PC = PC + 1
CYCLE 5: RF[IR7,6] = AluOut

## Slide 61
PC
Memory
ADDR
Data_out
Data_in
MemRead
MemWrite
IR
8
2
RaSel
1
reg1
reg2
regw
2
IR5-4
IR6-7
8
8
A
B
data1
data2
dataw
8
IRload
RF
RFWrite
PCwrite
ABLD
ALUop
3
ALUout
N
Z
ALU
FlagWrite
8
8
8
ALU1
8
1
0
2
RaSel
1
2
1
0
8
8
8
8
ZE
8
Imm5
5
ALU2
Imm3
ZE
8
8
AddrSel
0
1
MDR
MDRload
RegIn
SE
8
Imm4
4
000
001
010
011
100
CYCLE 1: IR = MEM[PC] & PC = PC + 1

## Slide 62: The PC=PC+1 is an optimization that is ALWAYS useful
We are certain that all instructions need to do PC=PC+1
Next up: An optimization that will useful SOME TIMES but never harmful

## Slide 63
Observe
  The datapath is idle in cycle 2
  It’s waiting for control to look at the opcode and decide what to do in cycle 3
Can we use the datapath to do something that MIGHT be useful?
CYCLE 1: IR = Mem[PC]; PC = PC + 1
CYCLE 2: Decode
CYCLE 3: A = RF[IR7,6] & B = RF[IR5,4]
CYCLE 4: AluOut = A + B, Update Z & N
CYCLE 5: RF[IR7,6] = AluOut

## Slide 64
Observe
  The datapath is idle in cycle 2
  It’s waiting for control to look at the opcode and decide what to do in cycle 3
Can we use the datapath to do something that MIGHT be useful?
How about we read two registers just in case the instructions needs both or one of them?
  Do “cycle 3” in cycle 2
CYCLE 1: IR = Mem[PC]; PC = PC + 1
CYCLE 2: Decode
CYCLE 3: A = RF[IR7,6] & B = RF[IR5,4]
CYCLE 4: AluOut = A + B, Update Z & N
CYCLE 5: RF[IR7,6] = AluOut

## Slide 65
CYCLE 1: IR = Mem[PC] ; PC = PC + 1
CYCLE 2: Decode; R1 = RF[IR7,6] &
R2 = RF[IR5,4]
CYCLE 3: R1 = RF[IR7,6] & R2 = RF[IR5,4]
CYCLE 4 3: AluOut = R1 + R2, Update Z & N
CYCLE 5 4: RF[IR7,6] = AluOut
Which instructions benefit? ADD, SUB, NAND, SHIFT (only from Ra),
LOAD (only from Rb), STORE
ORI, and the BRANCHES execute as before

## Slide 66
SHIFT1
1
0
in0
in1
in2
in3
in4
in5
in6
in7
out0
out1
out2
out3
out4
out5
out6
out7
1
0
1
0
1
0
1
0
1
0
1
0
1
0

## Slide 67
SHIFT1
1
0
in0
in1
in2
in3
in4
in5
in6
in7
out0
out1
out2
out3
out4
out5
out6
out7
1
0
1
0
1
0
1
0
1
0
1
0
1
0
SHIFT2
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0

## Slide 68
SHIFT1
1
0
in0
in1
in2
in3
in4
in5
in6
in7
out0
out1
out2
out3
out4
out5
out6
out7
1
0
1
0
1
0
1
0
1
0
1
0
1
0
SHIFT2
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
SHIFT4
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0