## Slide 1: a = b + c: Register version
Assign variables to storage  registers
a  r9, b  R10, c  R11
ADD R9, R10, R11
unsigned char a, b, c;
a = b + c;

## Slide 2: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 0x0
R10 | 10
R11 | 20
PC | 0x100

## Slide 3: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 0x0
R10 | 10
R11 | 20
PC | 0x100
LOAD.W 0x100
1. FETCH

## Slide 4: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 0x0
R10 | 10
R11 | 20
PC | 0x100
LOAD.W 0x100
0x62D20C7A
1. FETCH

## Slide 5: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 0x0
R10 | 10
R11 | 20
PC | 0x100
LOAD.W 0x100
0x62D20C7A
2. DECODE
ADD r9, r10, r11

## Slide 6: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 0x0
R10 | 10
R11 | 20
PC | 0x100
LOAD.W 0x100
0x62D20C7A
3. READ SOURCE OPERANDS
ADD r9, r10, r11
10
20

## Slide 7: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 0x0
R10 | 10
R11 | 20
PC | 0x100
LOAD.W 0x100
0x62D20C7A
4. Perform Calculation
ADD r9, r10, r11
10
20
+
30

## Slide 8: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 30
R10 | 10
R11 | 20
PC | 0x100
LOAD.W 0x100
0x62D20C7A
5. Write Result
ADD r9, r10, r11
10
20
+
30

## Slide 9: ADD R9, R10, R11 Execution
Address | Value
0x100 | 0x62D20C7A
0x104 | 
memory
Register | Value
R9 | 30
R10 | 10
R11 | 20
PC | 0x104
LOAD.W 0x100
0x62D20C7A
6. Decide next instruction location
ADD r9, r10, r11
10
20
+
30
+
4

## Slide 10: a = b + c: with values
ADDI R10, R0, 10
ADDI R11, R0, 20
ADD R9, R10, R11
unsigned char a;
unsigned char b = 10;
unsigned char c = 20;
a = b + c;

## Slide 11: a = b + c : with larger values
ADDI R10, R0, 0x11223344
ADDI R11, R0, 0x55667788
ADD R9, R10, R11
unsigned int a;
unsigned int b = 0x11223344;
unsigned int c = 0x55667788;
a = b + c;

## Slide 12: Why can’t I have large immediates?
How is ADDI encoded:
R(B) = R(A) + Sign-Extended (IMM16)

## Slide 13: Creating a 32-bit Immediate
R9 = 0x11223344
movhi r9, 0x1122
R9 = 0000 0000 0000 0000 0000 0000 0000 0000
R9 = 0001 0001 0010 0010 0000 0000 0000 0000
ori r9, r9, 0x3344
R9 = 0001 0001 0010 0010 0000 0000 0000 0000
0000 0000 0000 0000 0011 0011 0100 0100
R9 = 0001 0001 0010 0010 0011 0011 0100 0100

## Slide 14
unsigned int a;
unsigned int b = 0x11223344;
unsigned int c = 0x55667788;
a = b + c;
movhi r9, 0x1122  r9 = 0x11220000
ori r9, r9, 0x3344  r9 = 0x11223344
movhi r10, 0x5566  r10 = 0x55660000
ori r10, r10, 0x7788  r10 = 0x55667788

## Slide 15: Immediate Macros
movi rX, Imm16 --> rx = sign-extended(Imm16)
movui rX, Imm16 --> rx = zero-extended(Imm16)
movia rX, Imm32 --> rx = Imm32
  movia r10, 0x12345678
  movhi r10, 0x1234  r10 = 0x12340000
  addi r10, r10, 0x5678  r10 = 0x12345678

## Slide 16
R9 = 0x1000 FFFF
Using movhi and addi

## Slide 17
movhi r9, 0x1000
addi r9, r9, 0xFFFF
r9 != 0x1000FFFF

## Slide 18
movhi r9, 0x1000
R9 = 0001 0000 0000 0000 0000 0000 0000 0000
addi r9, r9, 0xFFFF
0xFFFF is sign-extended
1111 1111 1111 1111
1111 1111 1111 1111 1111 1111 1111 1111
R9 = 0001 0000 0000 0000 0000 0000 0000 0000
+ 1111 1111 1111 1111 1111 1111 1111 1111
R9 = 0000 1111 1111 1111 1111 1111 1111 1111

## Slide 19
movhi r9, 0x1001
addi r9, r9, 0xffff
movhi r9, %hiadj(0x1000 ffff)
addi r9, r9, %lo(0x1000 ffff)

## Slide 20: Memory Version
unsigned int a = 0x00000000;
unsigned int b = 0x00000001;
unsigned int c = 0x00000002;
a = b + c;
Address | +0 | +1 | +2 | +3
0x00200000 | 0x00 | 0x00 | 0x00 | 0x00
0x00200004 | 0x44 | 0x33 | 0x22 | 0x11
0x00200008 | 0x88 | 0x77 | 0x66 | 0x55

## Slide 21: Loading B
Read word from memory address 0x0020 0004
movia r9, 0x0020 0004
ldw r9, 0(r9)
Address | +0 | +1 | +2 | +3
0x00200000 | 0x00 | 0x00 | 0x00 | 0x00
0x00200004 | 0x44 | 0x33 | 0x22 | 0x11
0x00200008 | 0x88 | 0x77 | 0x66 | 0x55

## Slide 22
movia r9, 0x0020 0004  r9 = 0x0020 0004
ldw r9, 0(r9)
Address | +0 | +1 | +2 | +3
0x00200000 | 0x00 | 0x00 | 0x00 | 0x00
0x00200004 | 0x44 | 0x33 | 0x22 | 0x11
0x00200008 | 0x88 | 0x77 | 0x66 | 0x55

## Slide 23
LDW Rdest, Imm16(Rbase)
  tmp = Rbase + SE(Imm16)
  Rdest = LOAD.W tmp = MEM[tmp]
STW Rsrc, Imm16(Rbase)
  tmp = Rbase + SE(Imm16)
  STORE.W tmp, Rsrc  MEM[tmp] = Rsrc

## Slide 24
movia r9, 0x0020 0004
ldw r9, 0x0(r11)
movia r10, 0x0020 0008
ldw r10, 0x0(r11)
add r8, r9, r10
movia r11, 0x0020 0000
stw r8, 0x0(r11)

## Slide 25
movia r9, 0x0020 0000
ldw r9, 4(r11)
movia r10, 0x0020 0008
ldw r10, 8(r11)
add r8, r9, r10
Movia r11,0x0020 0000
stw r8, 0 (r11)
movia r9, 0x0020 0004
ldw r9, 0x0(r11)
movia r10, 0x0020 0008
ldw r10, 0x0(r11)
add r8, r9, r10
movia r11, 0x0020 0000
stw r8, 0x0(r11)

## Slide 26
movia r9, 0x0020 0000
ldw r9, 4(r11)
movia r10, 0x0020 0008
ldw r10, 8(r11)
add r8, r9, r10
Movia r11,0x0020 0000
stw r8, 0 (r11)
movhi r9, 0x0020
ldw r9, 4(r11)
movia r10, 0x0020 0008
ldw r10, 8(r11)
add r8, r9, r10
Movia r11,0x0020 0000
stw r8, 0 (r11)

## Slide 27
.data
.align 2
a: .word 0
b: .word 0x11223344
c: .word 0x55667788
.text
movia r11, a
ldw r9, 4(r11)
ldw r10, 8(r11)
add r8, r9, r10
stw r10, 0(r11)

## Slide 28
Address | +0 | +1 | +2 | +3
0x00200000 | 0x00 | 0x00 | 0x00 | 0x00
0x00200004 | 0x44 | 0x33 | 0x22 | 0x11
0x00200008 | 0x88 | 0x77 | 0x66 | 0x55
LDW R10, 0(R9)
LDH R8, 0(r9)
LDHU R8, 0(r9)
LDB r9, 0(r9)
LDBU r9, 0(r9)

## Slide 29
unsigned int a = 0x00000000;
unsigned int b = 0x11223344;
unsigned int c = 0x22334455;
if (b == 0)
then a = b + c;
else a = b – c;

## Slide 30
B == 0
A = B - C
A = B + C
AFTER
FALSE
TRUE

## Slide 31
COND:
beq r9, r0, THEN
ELSE:
sub r8, r9, r10
beq r0, r0, AFTER
THEN:
add r8, r9, r10
beq r0, r0, AFTER
AFTER
FALSE
TRUE
B == 0
A = B - C
A = B + C
AFTER
FALSE
TRUE

## Slide 32
BEQ Ra, Rb, TARGET
  If (Ra == Rb) then PC = TARGET
  else PC = PC + 4
Bcond Ra, Rb, TARGET
BLT, BGE, BNE, BLTU, BGEU, BR

## Slide 33
unsigned int a = 0x00000000;
unsigned int b = 0x11223344;
unsigned int c = 0x22334455;
if (b == 0)
then a = b + c;

## Slide 34
COND:
beq r9, r0, THEN
br AFTER
add r8, r9, r10
AFTER
TRUE
FALSE
add r8, r9, r10

## Slide 35
COND:
bne r9, r0, AFTER
add r8, r9, r10
AFTER
TRUE
FALSE
add r8, r9, r10

## Slide 36
BEQ Ra, Rb, TARGET
  If (Ra == Rb) then PC = TARGET
  else PC = PC + 4
TARGET is a 16-bit offset
newPC = PC + SE(IMM16) + 4

## Slide 37: What would be the offsets?
beq r9, r10, lala
addi r9, r9, 1
addi r10, r10, 2
lala:
ldw r10, 0(r9)
beq r9, r10, lala
addi r10, r10, 2
lala:
ldw r10, 0(r9)
koko:
beq r0, r0, koko
addi r9, r9, 1
Imm16 = 8
Imm16 = 4
Imm16 = -4 = 0xFFFC

## Slide 38
if (va == 1 && vb == 2) then … else …
.section .text
main:
movia r11, va
ldw r8, 0(r11)
movi r10, 0x1
beq r8, r10, else
ldw r9, 4(r11)
movi r10, 0x2
beq r9, r10, else
then:
...
br after
else:
...
after: