## Slide 1: ECE 454 Computer Systems Programming CPU Architecture
Ding Yuan
ECE Dept., University of Toronto
http://www.eecg.toronto.edu/~yuan

## Slide 2: Content
Examine the tricks CPU plays to make life efficient
  History of CPU architecture
  Modern CPU Architecture basics
  UG machines
More details are covered in ECE 552
Notes: We will tell you what tricks does the cpu play to make your program fast; but we won’t go into details on how the cpu implements each of these tricks.
ECE552

## Slide 3: Before we start…
Hey, isn’t the CPU speed merely driven by transistor density?
  Transistor density increase  clock cycle increase  faster CPU
A faster CPU requires
  Faster clock cycle
  smaller Cycles Per Instruction (CPI)
    CPI is the focus of this lecture!
True
True, but
there is more…

## Slide 4: In the Beginning…
1961:
  First commercially-available integrated circuits
  By Fairchild Semiconductor and Texas Instruments
1965:
  Gordon Moore's observation: (director of Fairchild research)
    number of transistors on chips was doubling annually

## Slide 5: 1971: Intel Releases the 4004
First commercially available, stand-alone microprocessor
4 chips: CPU, ROM, RAM, I/O register,
108KHz; 2300 transistors
  4-bit processor for use in calculators

## Slide 6: Designed by Federico Faggin

## Slide 7
Intel 4004 (first microprocessor)
3 Stack registers (what does this mean)?
4-bit processor, but 4KB memory (how)?
No Virtual Memory support
No Interrupt
No pipeline

## Slide 8: The 1970’s (Intel): Increased Integration
1971: 108KHz; 2300 trans.;
  4-bit processor for use in calculators
1972: 500KHz; 3500 trans.; 20 support chips
  8-bit general-purpose processor
1974: 2MHz; 6k trans.; 6 support chips
  16-bit addr space, 8-bit registers, used in ‘Altair’
1978: 10MHz; 29k trans.;
  Full 16-bit processor, start of x86
4004
8008
8080
8086

## Slide 9: Intel 8085

## Slide 10: The 1980’s: RISC and Pipelining
1980: Patterson (Berkeley) coins term RISC
  1982: Makes RISC-I pipelined processors (only 32 instructions)
1981: Hennessy (Stanford) develops MIPS
  1984: Forms MIPS computers
RISC Design Simplifies Implementation
  Small number of instruction formats
  Simple instruction processing
RISC Leads Naturally to Pipelined Implementation
  Partition activities into stages
  Each stage simple computation

## Slide 11: RISC pipeline
Reduce CPI from 5  1 (ideally)

## Slide 12: 1985: Pipelining: Intel 386
33MHz, 32-bit processor, cache  KBs

## Slide 13: Pipelines and Branch Prediction
BNEZ R3, L1
Which instr. should we fetch here?
Must wait/stall fetching until branch direction known?
Solutions?

## Slide 14: Pipelines and Branch Prediction
How bad is the problem? (isn’t it just one cycle?)
  Branch instructions: 15% - 25%
  Pipeline deeper: branch not resolved until much later
    Cycles are smaller
    More functionality btw. fetch & decode
    Misprediction penalty larger!
  Multiple instruction issue (superscalar)
    Flushing & refetching more instructions
  Object-oriented programming
    More indirect branches which are harder to predict by compiler
Pipeline:
Insts fetched
Branch directions computed
Wait/stall?

## Slide 15: Branch Prediction: solution
Solution: predict branch directions:
  Intuition: predict the future based on history
  Use a table to remember outcomes of previous branches
BP is important: 30K bits is the standard size
of prediction tables on Intel P4!

## Slide 16: 1993: Intel Pentium

## Slide 17: What do we have so far
CPI:
  Pipeline: reduce CPI from n to 1 (ideal case)
  Branch instruction will cause stalls: effective CPI > 1
    Branch prediction
But can we reduce CPI to <1?

## Slide 18: Instruction-Level Parallelism
instructions
1
2
3
4
5
6
7
8
9
Execution
Time
single-issue
1
2
3
4
5
6
7
8
9
application
1
2
3
4
5
6
7
8
9
superscalar

## Slide 19: 1995: Intel PentiumPro

## Slide 20: Data hazard: obstacle to perfect pipeline
DIV F0, F2, F4 // F0 = F2/F4
ADD F10, F0, F8 // F10 = F0 + F8
SUB F12, F8, F14 // F12 = F8 – F14
DIV F0,F2,F4
STALL: Waiting for F0 to be written
ADD F10,F0,F8
STALL: Waiting for F0 to be written
SUB F12,F8,F14
Necessary?

## Slide 21: Out-of-order execution: solving data-hazard
DIV F0, F2, F4 // F0 = F2/F4
ADD F10, F0, F8 // F10 = F0 + F8
SUB F12, F8, F14 // F12 = F8 – F14
DIV F0,F2,F4
ADD F10,F0,F8
STALL: Waiting for F0 to be written
SUB F12,F8,F14

Not wait (as
long as it’s
safe)

## Slide 22: Out-of-Order exe. to mask cache miss delay
load (misses cache)
inst4
inst3
inst2
inst1
inst6
inst5 (must wait for load value)
Cache miss latency
IN-ORDER:
load (misses cache)
inst3
inst2
inst4
inst1
inst6
inst5 (must wait for load value)
Cache miss latency
OUT-OF-ORDER:

## Slide 23: Out-of-order execution
In practice, much more complicated
  Detect dependency
  Introduce additional hazard
    e.g., what if I write to a register too early?

## Slide 24: Instruction-Level Parallelism
instructions
1
2
3
4
5
6
7
8
9
Execution
Time
single-issue
1
2
3
4
5
6
7
8
9
application
1
2
3
4
5
6
7
8
9
superscalar
1
2
3
4
5
6
7
8
9
out-of-order
super-scalar

## Slide 25: 1999: Pentium III

## Slide 26: Deep Pipelines
TC nxt IP
TC fetch
Drv
Alloc
Rename
Que
Sch
Sch
Sch
Disp
Disp
RF
RF
Ex
Flgs
BrCk
Drv
Pentium IV’s Pipeline (deep pipeline):
Pentium III’s Pipeline: 10 stages
Notes: http://www.hardwaresecrets.com/article/Inside-Pentium-4-Architecture/235/2

## Slide 27: The Limits of Instruction-Level Parallelism
1
2
3
4
5
6
7
8
9
out-of-order
super-scalar
Execution
Time
diminishing returns for wider superscalar
1
2
3
4
5
6
7
8
9
wider OOO
super-scalar

## Slide 28
2000: Pentium IV

## Slide 29: Multithreading The “Old Fashioned” Way
1
2
3
4
5
6
7
8
9
Application 2
1
2
3
4
5
6
7
8
9
Application 1
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
Execution
Time
Fast context
switching

## Slide 30: Simultaneous Multithreading (SMT) (aka Hyperthreading)
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
Execution
Time
Fast context
switching
1
2
3
4
5
6
7
8
9
1
2
3
4
5
6
7
8
9
Execution
Time
hyperthreading
SMT: 20-30% faster than context switching

## Slide 31: Putting it all together: Intel
Year
CPI
1971
Processor
Tech.
4004
no pipeline
n
1985
386
pipeline
close to 1
branch prediction
closer to 1
1993
Pentium
Superscalar
< 1
1995
PentiumPro
Out-of-Order exe.
<< 1
1999
Pentium III
Deep pipeline
shorter cycle
2000
Pentium IV
SMT
<<<1

## Slide 32: 32-bit to 64-bit Computing
Why 64 bit?
  32b addr space: 4GB; 64b addr space: 18M * 1TB
    Benefits large databases and media processing
  OS’s and counters
    64bit counter will not overflow (if doing ++)
  Math and Cryptography
    Better performance for large/precise value math
Drawbacks:
  Pointers now take 64 bits instead of 32
    Ie., code size increases
unlikely to go to 128bit

## Slide 33: Optional materials (not covered in lectures)

## Slide 34: Branch Prediction: solution
Solution: predict branch directions: branch prediction
  Intuition: predict the future based on history
  Local prediction for each branch (only based on your own history)
  Problem?

## Slide 35: Branch Prediction: solution
Global predictor
  Intuition: predict based on the both the global and local history
  (m, n) prediction (2-D table)
    An m-bit vector storing the global branch history (all executed branches)
    The value of this m-bit vector will index into an n-bit vector – local history
BP is important: 30K bits is the standard size
of prediction tables on Intel P4!
if (a == 2)
a = 0;
if (b == 2)
b = 0;
if (a != b)
.. ..
Only depends on the history
of itself?