## Slide 1: ECE 454 Computer Systems Programming Memory performance (Part I: review of mem. hierarchy)
Ding Yuan
ECE Dept., University of Toronto
http://www.eecg.toronto.edu/~yuan

## Slide 2: Content
  Cache basics and organization
  Optimizing for Caches (next lec.)
    Tiling/blocking
    Loop reordering

## Slide 3: Matrix Multiply
What is the range of performance due to optimization?
double a[4][4];
double b[4][4];
double c[4][4]; // assume already set to zero
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i][j] += a[i][k] * b[k][j]; // work
}

## Slide 4: MMM Performance
Standard desktop computer, compiler, using optimization flags
Both implementations have exactly the same operations count (2n3)
What is going on?
160x
Triple loop
Best code

## Slide 5: Problem: Processor-Memory Bottleneck
L1 cache reference 0.5 ns* (L1 cache size: < 10 KB)
Main memory reference 100 ns (mem size: GBs)
  200X slower!
*1 ns = 1/1,000,000,000 second
For a 2.7 GHz CPU (my laptop), 1 cycle = 0.37 ns

## Slide 6: Memory Hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
on-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
Smaller,
faster,
costlier
per byte

## Slide 7: Cache Basics (review (hopefully!))

## Slide 8: General Cache Mechanics
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 9: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 10: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 11: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-3 clock cycles for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-400 cycles for main memory

## Slide 12: Lets think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits:
  99% hits:
This is why “miss rate” is used instead of “hit rate”
0.97 * 1 cycle + 0.03 * 100 cycles = 3.97 cycles
0.99 * 1 cycle + 0.01 * 100 cycles = 1.99 cycles

## Slide 13: Types of Cache Misses
Cold (compulsory) miss
  Occurs on first access to a block
  Can’t do too much about these (except prefetching---more later)
Conflict miss
  Most hardware caches limit blocks to a small subset (sometimes a singleton) of the available cache slots
    e.g., block i must be placed in slot (i mod 4)
  Conflict misses occur when the cache is large enough, but multiple data objects all map to the same slot
    e.g., referencing blocks 0, 8, 0, 8, ... would miss every time
  Conflict misses are less of a problem these days (more later)
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
    This is where to focus nowadays

## Slide 14: Why Caches Work
Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time
block
block

## Slide 15: Example: Locality?
Data:
  Temporal: sum referenced in each iteration
  Spatial: array a[] accessed in stride-1 pattern
Instructions:
  Temporal: cycle through loop repeatedly
  Spatial: reference instructions in sequence
Being able to assess the locality of code is a crucial skill for a programmer!
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;

## Slide 16: Cache Organization

## Slide 17: General Cache Organization (S, E, B)
E = 2e blocks per set
S = 2s sets
set
block
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
Cache size:
S x E x B data bytes

## Slide 18: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One block per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 19: Example: Direct Mapped Cache (E = 1)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag
Direct mapped: One block per set
Assume: cache block size 8 bytes

## Slide 20: Example: Direct Mapped Cache (E = 1)
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag
Direct mapped: One block per set
Assume: cache block size 8 bytes
int (4 Bytes) is here
No match: old line is evicted and replaced

## Slide 21: E-way Set Associative Cache (E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 22: E-way Set Associative Cache (E = 2)
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag
E = 2: Two lines per set
Assume: cache block size 8 bytes

## Slide 23: E-way Set Associative Cache (E = 2)
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag
E = 2: Two lines per set
Assume: cache block size 8 bytes
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 24: Core 2: Cache Associativity
Disk
Main Memory
L2 unified cache
L1
I-cache
L1
D-cache
CPU
Reg
Latency:
100 cycles
16 cycles
3 cycles
10s of millions
6 MB
32 KB
~4 GB
~500 GB (?)
Not drawn to scale
L1/L2 cache: 64 B blocks
8-way
associative!
16-way
associative!
Punchline: conflict misses are less of an issue nowadays
Staying within on-chip cache capacity is key

## Slide 25: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 26: Understanding/Profiling Memory

## Slide 27: Recall: UG Machine Memory Hierarchy
L2 Cache
L1
Caches
P
L1
Caches
P
Processor Chip
L2 Cache
L1
Caches
P
L1
Caches
P
Processor Chip
Multi-chip Module
32KB, 8-way data cache
32KB, 8-way inst cache
12 MB (2X 6MB), 16-way Unified L2 cache

## Slide 28: Get Memory System Details: lstopo
Run lstopo on UG machine, gives:
Machine (3829MB) + Socket #0
L2 #0 (6144KB)
L1 #0 (32KB)+Core #0+PU #0 (phys=0)
L1 #1 (32KB)+Core #1+PU #1 (phys=1)
L2 #1 (6144KB)
L1 #2 (32KB) + Core #2 + PU #2 (phys=2)
L1 #3 (32KB) + Core #3 + PU #3 (phys=3)
4GB RAM
2X 6MB L2 cache
32KB L1 cache per core
2 cores per L2

## Slide 29: Get More Cache Details: L1 dcache
ls /sys/devices/system/cpu/cpu0/cache/index0
  coherency_line_size: 64 // 64B cache lines
  level: 1 // L1 cache
  number_of_sets
  physical_line_partition
  shared_cpu_list
  shared_cpu_map
  size:
  type: data // data cache
  ways_of_associativity: 8 // 8-way set associative

## Slide 30: Get More Cache Details: L2 cache
ls /sys/devices/system/cpu/cpu0/cache/index2
  coherency_line_size: 64 // 64B cache lines
  level: 2 // L2 cache
  number_of_sets
  physical_line_partition
  shared_cpu_list
  shared_cpu_map
  size: 6144K
  type: Unified // unified cache, means instructions and data
  ways_of_associativity: 24 // 24-way set associative

## Slide 31: Access Hardware Counters: perf
The tool ‘perf’ allows you to access performance counters
  way easier than it used to be
To measure L1 cache load misses for program foo, run:
perf stat -e L1-dcache-load-misses foo
7803 L1-dcache-load-misses # 0.000 M/sec
To see a list of all events you can measure:
perf list
Note: you can measure multiple events at once